## Slide 1
Sustainability Case Study:
Plastic Books
Mike Ashby1 and the Ansys Education Division2
1 Department of Engineering, University of Cambridge
2 Ansys

## Slide 2: Plastic Books: background
Cradle to Cradle by William McDonough and Michael Braungart :
“This book is not a tree. It is…a product that can be broken down and circulated infinitely in industrial cycles. The use of (plastic) expresses our intention to evolve away from the use of wood fibers for paper”.
Plastic edition:
Weight 562 grams
Price $ 27
Paper edition:
Weight 157 grams
Price $ 13
Printed in China
Reference: https://en.wikipedia.org/wiki/Cradle_to_Cradle:_Remaking_the_Way_We_Make_Things

## Slide 3: Step 1: Objective, scale, and functional unit
Objective: Reduce demand for a natural resource by printing books on plastic
Size scale: 2.2 million titles per year, average print run 3000 = 6.6 x 109 books
Time scale: 10 years?
Functional unit: per 1000 books
Facts needed : Can plastics be recycled more times than paper?

## Slide 4: Step 2: Stakeholders and concerns
Publishers
– impact on costs, sales and margins
Printers
– material and shipping costs
Recyclers
– viability of recycling printed plastic
Environmentalists
– relative energy and carbon footprint of plastic and paper
Authors
– reaching a wide readership
Readers
– price, weight, feel of book
Stakeholders
Little Interest Great
Little Influence / Power Great
Stakeholder diagram
Printers
Authors
Recyclers
Green
lobby
Readers
Publisher
Facts needed

## Slide 5: Step 3: Fact-finding– materials and recycling
Data from the Materials Data-table of the
Granta EduPack Sustainability DB
Materials
The paper: wood-fiber paper
The plastic: proprietary, but probably a CaCO3 filled polypropylene
Demand per year
 | Average book weight, kg | Mass per 1000 books (kg) | Mass per 6x109 books (tonnes) | % of global production
Paper | 0.2 | 200 | 1.3 x 106 | 0.3
Plastic | 0.6 | 600 | 4x106 | 6.7
Recycling
Paper: globally, 65%
Plastic: globally, 5%

## Slide 6: Step 3: Fact-finding– Cost
100 books | Material | Weight kg | Energy MJ/kg | CO2 kg/kg | Cost $/kg
Paper edition | Paper | 157 | 52 | 1.2 | 1.1
Plastic edition | CaCO3 filled PP | 562 | 55 | 2.4 | 2.2
Paper edition
Plastic edition
Data from the Eco-audit tool of the
Granta EduPack Sustainability DB

## Slide 7: Ste[ 3: Fact-finding– Energy and carbon
Data from the Eco-audit tool of the
Granta EduPack Sustainability DB
Paper edition
Plastic edition

## Slide 8: Step 4: Impact on the Three Capitals (overview)
Manufacture capital
 More expensive, heavier than paper book
 Printing on plastic requires new technology
Natural capital
 No energy or carbon saving
 Based on non-renewable resource
 No evidence that recycling is improved
Human capital
 Book retailers face higher cost of both book and delivery
 Possible that the reading public might find durability attractive

## Slide 9: Step 5: Reflection
Contribution of plastic books to all three capitals is negative or neutral
Cold assessment
Best to stick with paper
Alternative strategies?
McDonough and Braungart are making a point: that product redesign can allow materials to be reuse
More reflective assessment