## Slide 1
Lecture Unit
Introduction to Finite Element Analysis with Ansys Mechanical – 1D Elements
Developed and curated by the Ansys Education Team
János Plocher & Madhumita Saravana Kumar
education@ansys.com
Notes: Introduction Finite Element Analysis (FEA) with Ansys Mechanical – 1D Analysis
The Lecture Units developed for teaching FEA in connection Ansys Mechanical.

## Slide 2: Learning objectives for this Lecture Unit
Intended Learning Outcomes | 
Knowledge and Understanding | Knowledge and understanding of FEA with 1D Elements
Skills and Abilities | Ability to use Ansys Mechanical to set up a 1D structural simulation
Values and Attitudes | Awareness of the importance of simulation in engineering design
In-Built Assessment
  Exercises:
  Quizzes
Further reading/information
  Ansys Academic
  Ansys Innovation Courses
  Ansys Education Resources
Resources
  Software: Ansys Mechanical 2022 R2
  Images: Shutterstock
  Source: Finite Element Modeling and Simulation with ANSYS Workbench (2nd Ed.); Bridge Engineering Handbook: CRC Press, 2000.
Notes: Learning Objectives
This lecture unit is aimed at teaching the fundamental concepts of FEA in 1 analyses in mechanical engineering and consolidates the understanding by employing the finite element analysis software Ansys Mechanical.

## Slide 3: Outline of lecture unit
Numerical Analysis
  Methods for solving engineering problems
  Finite Element Analysis (FEA) and Method (FEM)
  From Physical Problem to Final Product
  Structural Analysis
  FEA Workflow
  FEA Basic Equations
1D Line Elements
Equilibrium
1D FEA
  Spring Systems (single and multiple springs)
  Beam Elements
  Exercises with beam elements
Summary
Notes: Outline of lecture unit
Numerical Analysis
  Methods for solving engineering problems
  Finite Element Analysis (FEA) or Method (FEM)
  From Physical Problem to Final Product
  Structural Analysis
  FEA Workflow
  FEA Basic Equations
1D Line Elements
Equilibrium
1D FEA
  Spring Systems (single and multiple springs)
  Beam Elements
  Exercises with beam elements
Summary

## Slide 4: Numerical Analysis – Methods for Solving Engineering Problems
Numerical Methods
Finite Element Analysis is predominant
Iterative algorithm suitable for computers
Fast solutions to complex problems
Experimental Methods
Prerequisite to many numerical simulations
Follow standardized test regimes
Time- and cost-consuming approach to data acquisition
Analytical Methods
Different methodologies available
Used mainly for simple idealized cases
Time-consuming approach for complex problems
Notes: Structural Analysis – Methods for solving engineering problems
Structural Analyses are carried out in order to understand the behaviour of structures when forces are exerted on them. Two key state variables that help engineers and designers assess the structural performance and behaviour of parts are stresses and strains. To determine those, three methods are at one's disposal: (a) Analytical, (b) numerical and (c) experimental.
(*Click*)
Experimental methods are methods in which the design is manufactured in real life and tests are then carried out. These methods are required in order to calibrate and validate simulation models at important phases of development. Experimental methods are generally standardized tests. They are time consuming and can often be very expensive to create and analyze.
(*Click*)
Numerical methods are simplified iterative algebraic equations that can be solved by a computer in order to obtain results. Finite Element Method is predominantly used in analyzing engineering problems as can be easily implemented in computers. In this lecture unit we will be using Ansys Discovery, which uses finite element methods to solve engineering problems.
(*Click*)
Analytical solutions are exact and are often performed with hand calculations. Several methods are available in structural mechanics theory and will not be the object of this lecture unit. However, these exact solutions can only be found for simple idealized problems while for most engineering problems it would be problematic to be solved analytically because the models are too complex (for example from a geometrical perspective
(*Click*)
In this lecture unit we will focus on the numerical and analytical methods.
In the next slide we will specifically look at how FEA compares/compliments analytical solutions.

## Slide 5: Numerical Analysis – Methods for Solving Engineering Problems
Numerical Methods
Analytical Methods
Engineering Problem
Complexity
low
high
…
…
Solution
Method
Notes: Structural Analysis – Methods for solving engineering problems
While analytical solutions can be easily and quickly found for simple geometries and load conditions through simplification and idealization of the problem, numerical methods are required to obtain solutions for complex geometries, loading conditions and material properties (e.g. non-isotropic properties, multi-material composites, etc.) for which analytical solutions are difficult and time-consuming to obtain.
Let’s expand on the question of ‘Why to use FEA’ in the next slide.

## Slide 6: Numerical Analysis – Finite Element Analysis (FEA) and Method (FEM)
FEM is the mathematical method used to conduct FEAs, in which partial differential equations are solved to describe physical phenomena.
FEA are performed using FEM, which are implemented in CAE (computer-aided engineering) tools, providing a solution for virtual prototyping.
FEA helps to solve structural, heat transfer, fluid flow or electromagnetic problems quickly by exploiting computational power and make design changes early product development stage.
eliminate risk
increase quality
drive innovation
reduce costs
lower design cycle time
manage complexity
FEA-simulations enables you to
Finite
Element
Analysis
Finite
Element
Method
Numerical technique
Type of analysis
Notes: Finite Element Analysis (FEA) or Method (FEM)
FEM is the mathematical method used to conduct FEAs, in which partial differential equations are solved to describe physical phenomena.
FEA are performed using FEM, which are implemented in CAE (computer-aided engineering) tools, providing a solution for virtual prototyping.
FEA helps to solve structural, heat transfer, fluid flow or electromagnetic problems quickly by exploiting computational power and make design changes early product development stage.
FEA enables:
Innovation (design exploration through parameterization, optimization (e.g. Topology optimization) and general multi-physics simulation).
Cost reduction (focus in virtual rather than costly physical testing).
Management of complexity in design and physics.
Improve quality (validate design and analyze it for various conditions to ensure consistent performance).
Reduction in cycle time (product-to-market time is reduced as R&D through simulation is significantly faster than through physical testing and design iterations).
Risk reduction (Identify weak spots, e.g. for repeated/fatigue loading which may not be visible from experimental tests (e.g. crack formation)). Note: This presupposes are correct numerical mode; in most cases prototyping is still mandatory.
No simulation substitutes physical testing, but it significantly accelerates the time required to reaching to a mature product stage and lowers the likelihood of additional design iterations.
Let’s expand on the question of ‘What FEA is’ in the next slide.

## Slide 7: Numerical Analysis – Finite Element Analysis (FEA) and Method (FEM)
FEM is a numerical method that exploits computational power to calculate solutions for a range of different engineering problems, offering good approximate solution to complex problems in the field of e.g. solid mechanics (e.g., statics and dynamics).
At the core of FEM lies the discretization, which means a model is divided into a finite number of smaller bodies or elements that are connected at common points, the so-called nodes.
Each node has a limited number of degrees of freedom (DoFs), so e.g. a continuum solid becomes discretized into a finite number of DoFs, based on the number and type of elements.
For each of those elements a set of algebraic equations are solved in an iterative fashion.
Element type: Tetrahedron
node
Notes: Finite Element Analysis (FEA) or Method (FEM)
FEA is a numerical methodthat exploits computational power to calculate solutions for a range of different engineering problems (see next slide for examples). It offers e.g. good approximate solution to complex problems in the field of solid mechanics (e.g., statics and dynamics).
At the core of FEA lies the discretization, which means a model is divided into a finite number of smaller bodies or elements that are connected at common points, the so-called nodes.* Note: For this lecture unit on 1D analysis, meshing is not specifically focused on, but will be dealt with in detail in the 2D/3D analysis.
Each node has a limited number of degrees of freedom (DoFs), so e.g. a continuum solid becomes discretized into a finite number of DoFs, based on the number and type of elements. The more elements and nodes are used to model an object, the higher the accuracy.
For each of those elements a set of algebraic equations are solved in an iterative fashion. The governing equations of FEAs are differential equations and boundary conditions which will be addressed in the next slide.

## Slide 8: Numerical Analysis – From Physical Problem to Final Product
Physical Problem
Numerical Model
Physical Prototype
Final Product
Fluid Mechanics
…
e.g. bracket
e.g. pipe
e.g. heat sink
Physical principles
System of algebraic equations
Governing equations
Boundary conditions
Euler-Bernoulli beam deflection
SM
Navier-Stokes motion of viscous fluids
FM
Fourier’s law of heat transfer
TA
Insulation at x=0
TA
Parallel flow
FM
Fixed end
SM
SM
FEA approximate
Stiffness matrix
Nodal vector (disp.)
Force vector
Solid Mechanics
Thermal Analysis
Notes: Structural Analysis – From Physical Problem to Final Product
There exist many physical problems in the field of solid and fluid mechanics as well as thermal (heat transfer) mechanics that can be solved using numerical methods like FEA.
Engineering/physical problems and their associated phenomena can be expressed as a numerical model through governing equations and boundary conditions.
- Solid Mechanics: e.g. Euler-Bernoulli beam deflection with a fixed end as boundary condition
- Fluid Mechanics: e.g. Navier-Stokes motion of viscous fluids with a parallel flow boundary condition
- Thermal Analysis: e.g. Fourier’s law of heat transfer with a local insulation boundary condition
In case of a structural mechanics problem, FEA approximates the displacement of the beam based upon the applied force and the stiffness matrix, which is directly linked to the material’s Young’s modulus. The nodal vector for the displacement is given for some nodes for which a boundary condition is defined (here: fixed end), the other can be determined by creating the inverse of the stiffness matrix (Note: this is an elaborate process to conduct analytically, which is why it lends itself to exploit the computational performance for this purpose). Now, the more elements you use to represent the beam, the more nodal displacements will be calculated along its length and the better you will be able to determine the deflection curve.
Next slide: Let’s look at how a structural analysis workflow in FEA looks like.

## Slide 9: Structural Analysis – FEA Workflow
Physical Problem
Numerical Model
Physical Prototype
Final Product
Pre-processing
Post-processing
Geometry and Material
Validation
Boundary conditions (e.g. supports, forces, etc.) and analysis type (e.g. structural, modal, thermal, etc. analysis)
CAD-geometry (e.g. shape, cross-sections, assemblies) and material (e.g. steel, rubber, wood, etc.)
Numerical solution (i.e. approximation) to the system of equations at selected points obtained using FEA
Sanity check (i.e.
do the results match the expectation, are the results plausible?)
Evaluation of outputs/state variables (e.g. displacement, stresses and strains)
Mathematical model
Physical principles
Notes: Structural Analysis – FEA Workflow
Structural Analysis is carried out in order to understand the behaviour of structures when forces are exerted on them.
This structural analysis methodology can be summarised through the following steps:
(*Click*)
The process starts off with designing the geometry and defining the material of our structure. In this lecture unit for example we will be focusing on beams.
(*Click*)
Pre-processing involves defining the boundary conditions. These include loading conditions (like force, torsion, etc.) and supports (like fixed, hinged, etc.), and connecting mechanisms.
(*Click*)
Once the geometry and loading conditions have been setup the appropriate method to solve the problem needs to be decided. This can be analytical also known as hand-calculation, which means the exact solution is found for the problem or numerical, such as the Finite Element Method which are approximate solution computed by computers. The selection of the method depends on the model complexity and the available resources. In this lecture unit both methods will be covered for a cantilever beam.
(*Click*)
Once the problem has been solved, we move on to postprocessing. Here the required outputs like displacement, stress and strain can be gathered and evaluated.
(*Click*)
The last but important step, which is too often forgotten, is to validate the resulting outputs and check if they make sense. For example, are the magnitude of the results in the expected range or are they too large or too small, does the analytical solution and numerical solution match? Is the quality of the results predicted from the mesh for the stress/strain gradients observed?
As the wheel schema suggests, this process can be iterative and can take several cycles of repetition before the required end results are met. This can be very different and depend on design requirements, cost constraints, weight limitation, etc.
In the next slide, the underlying assumptions and equations of FEA will be discussed.

## Slide 10: Structural Analysis – FEA Basic Equations
Equilibrium
Internal stresses and must be in equilibrium everywhere which presupposes a local equilibrium (i.e. the sum of all forces is zero).
Compatibility
Apart from cracks in a structure, displacements/strains must continuous if the structure is continuous
Constitutive Laws
The constitutive material behavior (stress-strain and strain-displacement relationship) must be satisfied
Body and surface forces
Displacements
Stresses
Strains
*
Note: Capital letters generally refer to the global and lowercase letters to the element matrix.
* Lecture Unit: Stresses and Strains with Ansys Discovery | Ansys
† Intro to Material Elasticity - ANSYS Innovation Courses
†
Notes: Structural Analysis – Basic Equations
To solve structural solid mechanics problem requires the three basic equations must be satisfied:
Equilibrium,
Constitutive Laws and
Compatibility.
The equilibrium condition for static but also dynamic problem states that the sum of all forces must be zero, i.e. the internal stresses of a component are in equilibrium. Here, the body and surface forces are being considered and linked to the stresses and strains. As will be shown later, three equilibrium conditions define the six components of stress or strain in an infinitesimal element. (Note: In the next couple of slides, the lecture unit will expand on the topic of equilibrium).
The constitutive laws define/approximate the stress-strain relationship of materials (Young’s and bulk modulus, Poisson’s ratio, yielding, hardening, etc.) as a result of an applied force. These relation can be phenomenological (derived from experiments) in nature or derived from first principles (also assumptions or postulates).
The compatibility condition ensures that a continuum body is deformed continuously without creating gaps, meaning compatibility is guaranteed between displacements and strains (i.e. displacements are obtained by integration of the strains). Important to note is that the displacements are considered the first nodal quantitates that are being determined in FEA; stresses and strains are secondary quantities that are expressed based upon the nodal displacements.
(*Click*)
The system of equations for a structural analysis is directly based upon those basic equations and relates the applied force vector F to the stiffness matrix K and displacement vector u. Note, the use of capital and lowercase letters in this equation is used to denote global or elemental (nodal) values.
Further reading & Equilibrium Condition: Additional free online courses/lecture notes on material elasticity and stresses and strains are linked. In the next couple of slides, the lecture unit will expand on the topic of equilibrium.
Next slide: This basic structure for the system of algebraic equations is employed in the underlying mathematical models in FEA. It is adjusted accordingly to solve a range of different structural problems.

## Slide 11: Structural Analysis – FEA Analysis Types
Physical Problem
Numerical Model
Physical Prototype
Final Product
Pre-processing
Post-processing
Validation
Geometry and Material
Mathematical model
Stress/Strain Analysis
Fatigue
Fracture
Modal analysis
Rigid/flexible body
Implicit Analysis
Explicit Analysis
vs
Durability
Thermal Analysis
Structural Stability Evaluation
vs
Linear Analysis
Non-linear Analysis
Static Analysis
Dynamic Analysis
vs
Note: This is just selection and thus incomplete list of different types of analysis, models and methods that can be conduced using FEA.
Physical principles
…
Notes: Structural Analysis – FEA Analysis Types
This slide displays a selection of different types of FEAs that can be conducted or that are generally differentiated. These may include the standard stress-strain analysis and static problems, but other mathematical models (basic equations are still adhered to) exist for non-linear analysis and dynamic problems. Furthermore, one differentiates between different solvers (implicit vs explicit) that are commonly used for either static or dynamic problems.
Note: This is just selection and thus incomplete list of different types of analysis that can be conduced using FEA.
Next slide: In order to solve such specific problems, one has to consider the correct element types. Thus, an overview on the 1D elements, their DoF and the general beam theories will be covered in the next section.

## Slide 12: 1D Line Elements – Overview
1D (Line) Elements
Examples
Beam/truss
Spring
Element Representation
FEA Representation
Truss Structure
…
simplify
apply
Beam/Bar
Truss
Rod
Link
Note: A single node would be considered a point element and can for instance be used a mass element.
While line elements such as beam elements are technically 1D elements, they are referred to as 2D or 3D beam elements in Ansys Mechanical, pertaining to their nodal DoF and thus to the type of analysis.
The choice of elements is dependent – among others – on:
  DoF: Displacements/rotations in 2D or 3D space
  Beam elements/theory: Timoshenko vs Euler-Bernoulli theory based on slenderness ratio
  Material properties: Linear vs non-linear (e.g. plasticity)
  Deflection/strain magnitude: e.g. geometric non-linearity due to large deformation/rotation
  (Re-)solution accuracy: Elements with larger number of nodes will yield higher solution accuracy (i.e. p-refinement)
  The DoF of an element also determines which disciplines can be modelled, i.e. structural mechanics, thermal analysis, fluid mechanics, electromechanics, etc.
  One generally aims at running computationally efficient simulations; thus, elements should only have the required DoF and features.
  In the simulation with 1D elements, lines and curves are meshed, which is simple, as only the position and shape rather than the volume is considered. Each line element is associated with the cross-section of the actual structure.
Product Documentation (ansys.com)
Notes: Discretization – 1D, 2D and 3D elements
1D (Line) Elements
Typical examples for 3D structures which can be simplified into 1D elements in FEA are beams and trusses as well as springs. The corresponding 1D elements are likewise called beams, bars, truss, rod or links.
(*Click*)
Consequently, structures made of such constituents can be modeled using 1D elements, however one must also choose the type of analysis (2D vs 3D) and the DoF necessary to resolve the problem at hand (see next slide). This is linked to the type of element.
The choice of elements is dependent – among others – on:
  DoF: Displacements/rotations in 2D or 3D space
  [Beam elements/theory: Timoshenko vs Euler-Bernoulli theory based on slenderness ratio]
  Material properties: Linear vs non-linear (e.g. plasticity). For non-linear material properties or large strain magnitudes, the aforementioned linear relation between the stiffness, the force and the displacement is not linear for large deformations.
  Deflection/strain magnitude: e.g. geometric non-linearity due to large deformation/rotation
  (Re-)solution accuracy: Elements with larger node number will yield higher solution accuracy (i.e. p-refinement). This in turn will increases the solution memory requirements.
  The DoF of an element also determines which disciplines can be modelled, i.e. structural mechanics, thermal analysis, fluid mechanics, electromechanics, etc.
  One generally aims at running computationally efficient simulations; thus, elements should only have the required DoF and features.
  In the simulation with 1D elements, lines and curves are meshed, which is simple, as only the position and shape rather than the volume is considered. Each line element is associated with the cross-section of the actual structure.
Note: A single node would be considered a point element and can for instance be used a mass element.
Further reading: Please see the documentation for Ansys Mechanical to find out more on the different element types available, including the DoF, applicable physics, etc.

## Slide 13: 1D Line Elements – DoF and Beam Theory
*Product Documentation (ansys.com)
L
Beam
Truss/Link
2-node line
3-node line
Euler-Bernoulli
Cross-section remains perpendicular to the bending line
Shear deformation is neglected
Applicable to slender beams
Timoshenko
Cross-section can rotate in relation to the bending line
Shear deformation is considered
Applicable to stubby beams
Degrees of Freedom (DoF)
Beam Theory
1D elements in Ansys Mechanical for structural analysis*
Note: *Please see documentation for specific applicability.
†The beam element BEAM188 follows the Timoshenko _____beam theory.
Element Name | Analysis & Element Type | DoF | Application
BEAM188†/189 | 2-node/3-node in 3D space | Ux,y,z; x,y,z | Long, thin pieces of structural continua
PIPE2887289 | 2-node/3-node in 3D space | Ux,y,z; x,y,z | Straight, slender to moderately stubby pipe structures
LINK180 | 2-node in 3D space | Ux,y,z | Long, thin pieces
CABLE280 | 3-node in 3D space | Ux,y,z | Moderate to extremely slender cable structures
REINF263 | Up to 8 nodes in 2D space | Ux,y,z; z | Cable (e.g. steel rebar in concrete) or fiber (e.g. carbon fiber composites).
Element Name | Analysis & Element Type | DoF | Application
BEAM188†/189 | 2-node/3-node in 3D space |  | Long, thin pieces of structural continua
PIPE2887289 | 2-node/3-node in 3D space |  | Straight, slender to moderately stubby pipe structures
LINK180 | 2-node in 3D space | Ux,y,z | Long, thin pieces
CABLE280 | 3-node in 3D space | Ux,y,z | Moderate to extremely slender cable structures
REINF263 | Up to 8 nodes in 2D space |  | Cable (e.g. steel rebar in concrete) or fiber (e.g. carbon fiber composites).
Notes: 1D Line Elements – DoF and Beam Theory
There are different types of 1D line elements which can be differentiated based on the number of nodes, the degrees of freedom or the underlying beam theory (slenderness ratio must be considered).
Degrees of Freedom (DoF)
One differentiates between 2-node and 3-node line elements
These can be beams or trusses/links, which have dedicated DoF and this specific applicability. In Ansys Mechanical one can choose from a selection of 1D elements (see snapshot).
(*Click*)
For structural applications, the following types of elements are available (please also see the product documentation for further detail), as shown in the table. Similar to the analysis type, the recordable nodal deformations U and rotations with respect to the global coordinate axis differ between the elements. Each element type is suitable for different applications (often dependent on the dimensions of the structure that shall be represented). It is of note that e.g. BEAM188 follows the Timoshenko beam theory.
(*Click*)
Beam Theory
Many simple structures like beams or springs can be simplified into line elements in FEA. A prerequisite for this is that the ratio between the length of such a component/member is significantly greater than its dimension in the cross section (common ballpark is L/r > 20). However, one also differentiates between particularly slender or stubby beams, because for the former the Euler-Bernoulli is more applicable, whereas for the latter the Timoshenko beam theory is preferred.
Euler-Bernoulli
Cross-section remains perpendicular to the bending line
Shear deformation is neglected
Applicable to slender beams
Timoshenko
Cross-section can rotate in relation to the bending line
Shear deformation is considered
Applicable to stubby beams
Further reading: Please see the documentation for Ansys Mechanical to find out more on the different element types available, including the DoF, applicable physics, etc.
Next slide: The more elements and nodes (increased number of DoF) are used to represent a structure, the better (more accurate) its local displacements (e.g. bending line of cantilever beam) under load can be determined.
1D Line Elements – DoF and Beam Theory
There are different types of 1D line elements which can be differentiated based on the number of nodes, the degrees of freedom or the underlying beam theory (slenderness ratio must be considered).
Degrees of Freedom (DoF)
One differentiates between 2-node and 3-node line elements
These can be beams or trusses/links, which have dedicated DoF and this specific applicability. In Ansys Mechanical one can choose from a selection of 1D elements (see snapshot).
(*Click*)
For structural applications, the following types of elements are available (please also see the product documentation for further detail), as shown in the table. Similar to the analysis type, the recordable nodal deformations U and rotations 𝜃 with respect to the global coordinate axis differ between the elements. Each element type is suitable for different applications (often dependent on the dimensions of the structure that shall be represented). It is of note that e.g. BEAM188 follows the Timoshenko beam theory.
(*Click*)
Beam Theory
Many simple structures like beams or springs can be simplified into line elements in FEA. A prerequisite for this is that the ratio between the length of such a component/member is significantly greater than its dimension in the cross section (common ballpark is L/r > 20). However, one also differentiates between particularly slender or stubby beams, because for the former the Euler-Bernoulli is more applicable, whereas for the latter the Timoshenko beam theory is preferred.
Euler-Bernoulli
Cross-section remains perpendicular to the bending line
Shear deformation is neglected
Applicable to slender beams
Timoshenko
Cross-section can rotate in relation to the bending line
Shear deformation is considered
Applicable to stubby beams
Further reading: Please see the documentation for Ansys Mechanical to find out more on the different element types available, including the DoF, applicable physics, etc.
Next slide: The more elements and nodes (increased number of DoF) are used to represent a structure, the better (more accurate) its local displacements (e.g. bending line of cantilever beam) under load can be determined.

## Slide 14: 1D Line Elements – Mesh Refinement
In pursuit of increasing the solution accuracy and ensuring numerical convergence, two discretization approaches can be pursued:
Original Mesh
p-refinement
h-refinement
1 x 2-node line
2 x 2-node lines
1 x 3-node line
Increased number of elements
Increased order of the shape functions
Number of elements (/)
Stiffness (GPa)
p-refinement
h-refinement
actual stiffness
Displacement (mm)
Approximation
Actual
discrepancy
Notes: Meshing – Refinement
In pursuit of increasing the solution accuracy and ensuring numerical convergence, two discretization approaches can be pursued:
H-refinement: The same element order is employed, but the number of elements is increased.
P-refinement: The same number of elements is employed but the element order is increased.
(*Click*)
After conducting a refinement, e.g. the stiffness of a structure or any other parameter derived from the state variables will increase. The refinement is terminated once the value of the parameter converges, i.e. only changes a few percentages upon further refinement.
(*Click*)
Taking the example of a cantilever in bending, one can observe the discrepancy between the actual bending line (i.e. exact local displacements) and the discrepancies introduced due to the discretization and linear interpolation between the nodal values.
Next slide: With the specificities of 1D elements covered, the lecture unit will now focus on the general equilibrium condition that must be satisfied

## Slide 15: Local Equilibrium – Introduction
In the case of a static problem, the equilibrium condition states that the sum of all forces are zero. This means that the externally applied loads must be equal to the sum of the internal element forces at the nodes.
The local force balance (i.e., the internal forces between the elements) is termed local equilibrium and must be determined first to verify the global force balance (i.e., the distortion of the entire body).
The local equilibrium can be determined by considering an infinitesimal cube, which experiences both surface and body loads.
Infinitesimal cube
Dog-bone specimen in tension
Surface Load
Body Load
Loads acting on each of the six faces
Load induced e.g. through gravity, electric and magnetic fields or heat
g = 9,81m/s2
+
-
tension
compression
* Lecture Unit: Stresses and Strains with Ansys Discovery | Ansys
Notes: Local Equilibrium – Introduction
In the case a static problem, the equilibrium condition states that the sum of all forces toques are zero. This means that the externally applied loads must be equal to the sum of the internal element forces at the nodes.
(*Click*)
In order to find the deformations, as well as stresses and strains in a body, the local internal force balance must be solved.
The local equilibrium describes the internal force balance, which is a prerequisite to a global force balance (i.e. the global distortion of a body). The global force balance describes how the reaction forces at a boundary condition equal out the applied forces. It is generally verified after the local force balance is solved.
Considering a dog-bone specimen loaded in tension, the local equilibrium can best be explained by considering an infinitesimal cube (IC) within the sample and the load conditions on the 6 different faces.
(*Click*)
  The forces acting on the IC can be divided into surface and body loads.
  While surface loads are the forces acting directly on the 6 faces as a result of an externally applied load, the body loads describe lads that are indirectly induced, e.g. through electrical fields or gravity.
Further reading: The lecture unit on stresses and strains will provide some further background information on the fundamental state variabes.
Next, let’s describe the force and body loads for the IC in more detail.

## Slide 16: Local Equilibrium – Surface & Body Load
Surface Load
Body Load
The body force density b expresses the force on the volume
g = 9,81m/s2
+
-
Face 1
Area =
Force by
=
Force by
=
Exemplified based on one surface
Body force
=
Body 1
Volume =
Force by
=
Notes: Local Equilibrium – Surface & Body Load
Surface Loads F
In total there will be surface loads acting on all 6 faces of the IC.
Each surface has 3 forces which are determined by multiplying the stress components with the surface area. Here this is exemplified by face 1 (highlighted in green)
(*Click*)
Body load
The body load such as gravity, electric or magnetic fields act on the volume of the IC.
The force b is proportional to the volume of the cube.
b describes the body force density

## Slide 17: Local Equilibrium – Stress Component Pairs & Force Balance
Stress Component Pairs
Force Balance
Force balance is illustrated for a forces acting in y-direction
Here we focus on the stresses in y-direction only
Theory is exemplified based on one pair of opposing surfaces only
Face 1
Face 2
E.g.: Face 1 & 2
Stress components in y
Force equilibrium in y
(
Face 6
Face 4
Face 2
Face 1
Face 5
Face 3
Rate of change in x, y and z direction
Lecture Unit: Stresses and Strains with Ansys Discovery | Ansys
Note: The surface area pairs are denoted with , , and .
Notes: Local Equilibrium – Stress Component Pairs & Force Balance
Stress Component Pairs
In total there will be 3 surface pairs in the IC. Here we focus on faces 1 and 2 in y-direction.
Along the y-direction the stress value changes which is captured by the rate of change in this direction. The latter would be for the normal stress direction in y.
The same applies not only for the shear stresses on the faces 1 and 2, as highlighted in the equation on the left, but also to the two other surface pairs.
(*Click*)
Force Balance
Now, let’s establish the force equilibrium in y by summing up the forces in y (noted by the first index in the subscript and highlighted in yellow) and include the body force b.
The same applies for the force balances in x and z direction. Note: The surface area pairs are denoted with , , and .
Link/Further reading: You may also want to explore some more details on stresses and strains in lecture unit.
Next, we will summarize all force balance equations in the concise form.
Local Equilibrium – Stress Component Pairs & Force Balance
Stress Component Pairs
In total there will be 3 surface pairs in the IC. Here we focus on faces 1 and 2 in y-direction.
Along the y-direction the stress value changes which is captured by the rate of change in this direction. The latter would be (𝑑𝜎_𝑦𝑦)/𝑑𝑦 ∆𝑦 for the normal stress direction in y.
The same applies not only for the shear stresses on the faces 1 and 2, as highlighted in the equation on the left, but also to the two other surface pairs.
(*Click*)
Force Balance
Now, let’s establish the force equilibrium in y by summing up the forces in y (noted by the first index in the subscript and highlighted in yellow) and include the body force b.
The same applies for the force balances in x and z direction. Note: The surface area pairs are denoted with 𝐴_(1/2), 𝐴_(3/4), and 𝐴_(5/6).
Link/Further reading: You may also want to explore some more details on stresses and strains in lecture unit.
Next, we will summarize all force balance equations in the concise form.

## Slide 18: Local Equilibrium – Force Balance
Is the divergence of stress a scalar value like the equivalent stress?
The other two force balance equations in x and z direction can be established similarly.
All three force balance equations can the be written as follows:
Face 6
Face 4
Face 2
Face 1
Face 5
Face 3
Divergence of a tensor
3D
2D
Notes: Local Equilibrium – Force Balance
The force balance equations for a 3D/2D case can be written in the concise versions as shown on the right, yielding the local equilibrium.
Another simplification is generally conducted to represent the tensor as a single equation, whereby the divergence of the tensor is utilized.
(*Click*)
Quiz Solution: No, the divergence of stress is a tensor, expressing the rate of change in stress in the three axes of the coordinate system.
Next slide: Lets consider a very simple 1D problem first, which shall be solved analytically. This will be showcased in the next slide and is aimed at highlighting how this equilibrium condition is almost impossible to solve for complex 3D problems.

## Slide 19: Local Equilibrium – Solving 1D Solid Mechanics Problems with an Analytical Approach
Problem: Find an analytical solution for a simple 1D problem (a rod in tension by pressure P), that yields a continuous equation of the local equilibrium condition u(x).
z
x
P
A
L
= 0
Partial differential equation
= -
= -
= -
= -
= -
Equilibrium (div + b = 0)
Constitutive Law (1D Hooke’s Law)
Deformation
Boundary conditions
Under the assumption that:
Notes: Local Equilibrium – Solving 1D Solid Mechanics Problems with an Analytical Approach
The following problem of a rod in tension shall highlight the analytical approach to solving the deformation function u(x).
Analytical Process:
1. Note down all the necessary conditions for solving the solid mechanics problem: equilibrium, material model, deformation and boundary condition. Note the u(0) = zero, due to the fixture and as the pressure act at the tip of the rod. The aim is to find the expression for u(x).
(*Click*)
2. Partial differential equation: After solving the partial differential equation for the equilibrium, we find that the stress is related to the material model and strain is related to the deformation.
(*Click*)
3. Next c1 and c2 must be determined by introducing the boundary conditions. By assuming here that the parameters , an expression for u(x) can be derived.
In the next slide, we will draw a conclusions and provide and outlook in light of the equilibrium condition analytical vs numerical:
Local Equilibrium – Solving 1D Solid Mechanics Problems with an Analytical Approach
The following problem of a rod in tension shall highlight the analytical approach to solving the deformation function u(x).
Analytical Process:
1. Note down all the necessary conditions for solving the solid mechanics problem: equilibrium, material model, deformation and boundary condition. Note the u(0) = zero, due to the fixture and 𝜎(𝐿)=P as the pressure act at the tip of the rod. The aim is to find the expression for u(x).
(*Click*)
2. Partial differential equation: After solving the partial differential equation for the equilibrium, we find that the stress is related to the material model and strain is related to the deformation.
(*Click*)
3. Next c1 and c2 must be determined by introducing the boundary conditions. By assuming here that the parameters 𝐿=𝜌=𝑃=1, an expression for u(x) can be derived.
In the next slide, we will draw a conclusions and provide and outlook in light of the equilibrium condition analytical vs numerical:

## Slide 20: Local Equilibrium – Solving 1D Solid Mechanics Problems with an Analytical Approach
z
x
P
A
L
It is important to recognize that solutions for the equilibrium conditions of simple 1D elasticity problems can be calculated analytically, whereas this is almost impossible for realistic 3D problems.
Thus, finding a continuous equation that represents the deformation of a body in a real-world problem is not feasible.
Consequently, engineers use the Finite Element Analysis (FEA), whereby a piece-wise solution is sought instead, yielding an approximate solution.
Notes: Local Equilibrium – Solving 1D Solid Mechanics Problems with an Analytical Approach
Conclusions and outlook equilibrium condition (analytical vs numerical):
It is important to recognize that solutions for the equilibrium conditions of simple 1D elasticity problems can be calculated analytically, whereas this is almost impossible for realistic 3D problems.
Thus, finding a continuous equation that represents the deformation of a body in a real-world problem is not feasible.
Consequently, engineers use the Finite Element Analysis (FEA), whereby a piece-wise solution is sought instead, yielding an approximate solution.
In the next slide, we will derive the elements equations and stiffness matrices for spring systems and beam elements using the direct and energy approach.

## Slide 21: 1D FEA – Spring System (single spring)
fi
fj
i
j
k
ui
uj
x
Nodes | i, j
Nodal displacements | ui, uj [mm]
Nodal forces | fi, fj [N]
Stiffness (spring constant) | k [N/mm]
fi
i
F
fj
j
F
Force equilibrium at the nodes:
F
linear
non-linear
k
Considering the linear relationship between the spring force F and the elongation :
k = element stiffness matrix
u = element nodal displacement vector
f = element nodal force vector
Considering the equilibrium condition regarding the forces of the spring at the nodes:
Node i:
Node j:
Spring stiffness in matrix form:
Notes: 1D FEA – Spring System (single spring)
The spring system is described using the basic equations (i) Equilibrium, (ii) Compatibility and (iii) Constitutive Laws as introduced earlier.
To convey the basic underlying concept of FEA, a simple spring element (i.e. 1D case) is considered, in which two nodes (i,j) at the ends of the spring are defined by displacements and forces. Based on the spring’s stiffness and boundary conditions different forces and displacements may be recorded for each node.
(*Click*)
The spring system is considering a linear elastic relationship, meaning force and displacement are proportional.
(*Click*)
Now, the force equilibria at the two nodes can be defined.
(*Click*)
By reassembling the two expressions, the spring stiffness in matrix form is defined.
Note: As a single element (spring) is considered, the elemental stiffnesses, displacements and forces are considered.
Next slide: After considering a single element, we will now look at how the stiffness of a system of springs can defined.

## Slide 22: 1D FEA – Spring System (multiple springs)
Assembly of Element Equations
Direct Approach
1
F1
2
F2
1
F3
1
2
3
3
1
2
k1
x
k2
u1 , F1
u2 , F2
u3 , F3
Nodal forces:
Spring system stiffness in matrix form:
Notes: 1D FEA – Spring System (multiple springs)
If we consider a spring system comprised of two springs, we can initially note down the elemental stiffness matrices (see slide before).
To assemble the element equations there are two main approaches, the direct and energy approach. First we will look at the direct approach.
(*Click*)
Next the nodal force equilibria at the 3 nodes are considered again.
(*Click*)
In reassembling the 3 equations we obtain the spring system stiffness in matrix form.
Next slide: Besides the direct approach which is easier to understand, there is also the energy approach which is easier to computationally implement and is thus fundamental to FEA.

## Slide 23: 1D FEA – Spring System (multiple springs)
3
1
2
k1
u1 , F1
x
k2
u2 , F2
u3 , F3
The principal of minimum potential energy is considered with the strain energy U defined as:
Assembly of Element Equations
Energy Approach
with
Strain energy in matrix form:
Notes: 1D FEA – Spring System (multiple springs)
The more general assembly of the element equations is done via the energy approach (EA) is also considered to be the foundation for the FEA/FEM.
(*Click*)
The EA follows the principal of minimum potential energy defined by the strain energy U stored in the spring (Note, this is the area under the Force-Displacement curve). It is of note that yy applying simple matrix algebra, the terms and are re-written as and , respectively.
(*Click*)
The stored strain energy in the system is comprised of the sum of the elemental (individual spring) strain energies. By re-writing the terms and considering the terms for the nodal displacements (delta 1 and 2), the strain energy can be defined in matrix form.
Next slide: Besides the stored energy in the system, one also needs to consider the external force potential.
1D FEA – Spring System (multiple springs)
The more general assembly of the element equations is done via the energy approach (EA) is also considered to be the foundation for the FEA/FEM.
(*Click*)
The EA follows the principal of minimum potential energy defined by the strain energy U stored in the spring (Note, this is the area under the Force-Displacement curve). It is of note that yy applying simple matrix algebra, the terms 𝑘_1 Δ_1^2 and 𝑘_2 Δ_2^2 are re-written as Δ_1^𝑇 𝑘_1 Δ_1 and Δ_2^𝑇 𝑘_2 Δ_2, respectively.
(*Click*)
The stored strain energy in the system is comprised of the sum of the elemental (individual spring) strain energies. By re-writing the terms and considering the terms for the nodal displacements (delta 1 and 2), the strain energy can be defined in matrix form.
Next slide: Besides the stored energy in the system, one also needs to consider the external force potential.

## Slide 24: 1D FEA – Spring System (multiple springs)
3
1
2
k1
u1 , F1
x
k2
u2 , F2
u3 , F3
External force potential:
Assembly of Element Equations
Energy Approach
Potential energy of the spring system:
State of equilibrium (principle of min. potential energy):
Note: The global stiffness matrix represents a superposition of the elemental stiffness matrices and is (i) symmetric, as a linear system is considered and (ii) singular in this case, as no boundary conditions are applied (causes rigid body motions).
Spring system stiffness in matrix form:
Notes: 1D FEA – Spring System (multiple springs)
The potential of the external force can be written as the sum of the nodal force-displacement products.
(*Click*)
The potential energy in the spring system is the sum of the strain energy and the force potential (Note: Typical convention is that external force potential is negative when forces are acting on the body). Note, both are a function of the nodal displacements.
(*Click*)
In order to satisfy the equilibrium in the system, the potential energy must be zero. Foe this purpose, the principle of minimum potential energy can be considered.
(*Click*)
Considering the equilibrium condition the same expression for the spring system stiffness, as derived with the direct method, is obtained.
Note: The global stiffness matrix represents a superposition of the elemental stiffness matrices and is (i) symmetric, as a linear system is considered and (ii) singular in this case, as no boundary conditions are applied (causes rigid body motions).
Next slide: In order to avoid rigid body motion, boundary conditions must be considered. Let’s introduce them through a short analytical exercise in the next slide.
1D FEA – Spring System (multiple springs)
The potential of the external force can be written as the sum of the nodal force-displacement products.
(*Click*)
The potential energy in the spring system is the sum of the strain energy and the force potential. Note, both are a function of the nodal displacements.
(*Click*)
In order to satisfy the equilibrium in the system, the potential energy must be zero. Foe this purpose, the principle of minimum potential energy can be considered.
(*Click*)
Considering the equilibrium condition the same expression for the spring system stiffness, as derived with the direct method, is obtained.
Note: The global stiffness matrix [𝐊] represents a superposition of the elemental stiffness matrices [𝐤] and is (i) symmetric, as a linear system is considered and (ii) singular in this case, as no boundary conditions are applied (causes rigid body motions).
Next slide: In order to avoid rigid body motion, boundary conditions must be considered. Let’s introduce them through a short analytical exercise in the next slide.

## Slide 25: 1D FEA – Exercise: Spring System & Boundary Conditions
3
1
2
k1
u1 , F1
x
k2
u2 , F2
u3 , F3
k1 | 100 N/mm
k2 | 50 N/mm
F2=F3=P | 20 N
u1 | 0 mm
F1 | 
u2 | 50 N/mm
u3 | 20 N
?
2
Reduces to
and
3
and
Analytical Solution
4
Results in
1
Boundary condition
Notes: 1D FEA – Exercise: Spring System & Boundary Conditions
This exercise is aimed at applying boundary conditions to the spring system and solving the for the i) nodal displacements at node 2 and 3 as well as the force acting on node 1.
(*Click*)
1. For the entries in the global system of equations (Ku=F) the boundary conditions (zero displacement at node 1) is applied. Likewise, as the forces at node 2 and 3 are identical the force vector can be simplified.
(*Click*)
2. Due to the fixed node 1, the term reduces and an expression for the reaction force is obtained.
(*Click*)
3. Solving the equation in (2) for the unknow displacements and the reaction force allows for a calculation of the parameters of interest.
(*Click*)
4. As expected, the nodal displacement differ by a factor of 2, equal to the difference in the spring constants. Similarly, the reaction force is the sum of the applied forces in opposite direction (negative sign).
(*Click*)
Next slide: The spring-analogy is a good example to introduce the concept behind simple 1D elements which are commonly used in FEA software. In the following slides simple beam elements are introduced in place of the springs.

## Slide 26: 1D FEA – Beam Elements
fi
fj
i
j
E, A
ui
uj
x
Nodes | i, j
Nodal displacements | ui, uj [mm]
Nodal forces | fi, fj [N]
F
linear
non-linear
E
Linear variation of the displacement u along the bar axis is assumed:
L
Stiffness (Young’s modulus) | E [N/mm2]
Cross-section area | A [mm2]
Bar length | L [mm]
Strain:
Stress:
Note: The beam behaves like a spring.
1D Elasticity and Stiffness Matrix
Direct Approach
Note: Sum of nodal displacements with 1 DoF for each node.
Element stiffness matrix:
or
Lecture Unit: Stresses and Strains with Ansys Discovery | Ansys
Notes: 1D FEA – Beam Element
In linear elastic analyses of geometrically simple structural problems, 1D beam or truss elements can be used to approximate the behavior of a 3D solid. The basic stress-strain analysis focuses on determining the structural integrity of components (i.e. prior to failure). This means,
small deformations,
static loads and
elastic material properties are considered.
In this case, a simple 2-node beam element is considered.
In the following the 1D Elasticity and Stiffness matrix is considered with (a) the direct and (b) the energy approach.
(*Click*)
Direct Approach
First, it is assumed the that displacement u along the bar’s longitudinal axis varies linearly (referring to the nodal displacements ui, uj ).
The displacement in x-direction u(x) can thus be defined. Note: Each node has 1 DoF for the beam element.
The strain can be expressed with nodal displacements ui, uj the or the elongation .
Likewise, the stress is defined as force F over an area A, while the F is directly related to the beam stiffness and elongation. Note: As can be seen by the expression of the force F, the beam element behaves like a spring.
(*Click*)
Element Stiffness Matrix:
The stiffness of the beam is k = EA/L
Next slide: Energy approach for beam element example.
1D FEA – Beam Element
In linear elastic analyses of geometrically simple structural problems, 1D beam or truss elements can be used to approximate the behavior of a 3D solid. The basic stress-strain analysis focuses on determining the structural integrity of components (i.e. prior to failure). This means,
small deformations,
static loads and
elastic material properties are considered.
In this case, a simple 2-node beam element is considered.
In the following the 1D Elasticity and Stiffness matrix is considered with (a) the direct and (b) the energy approach.
(*Click*)
Direct Approach
First, it is assumed the that displacement u along the bar’s longitudinal axis varies linearly (referring to the nodal displacements ui, uj ).
The displacement in x-direction u(x) can thus be defined. Note: Each node has 1 DoF for the beam element.
The strain can be expressed with nodal displacements ui, uj the or the elongation ∆.
Likewise, the stress is defined as force F over an area A, while the F is directly related to the beam stiffness and elongation. Note: As can be seen by the expression of the force F, the beam element behaves like a spring.
(*Click*)
Element Stiffness Matrix:
The stiffness of the beam is k = EA/L
Next slide: Energy approach for beam element example.

## Slide 27: 1D FEA – Beam Elements
fi
fj
i
j
E, A
ui
uj
x
Nodes | i, j
Nodal displacements | ui, uj [mm]
Nodal forces | fi, fj [N]
Definition of linear shape functions:
L
Stiffness (Young’s modulus) | E [N/mm2]
Cross-section area | A [mm2]
Bar length | L [mm]
1D Elasticity and Stiffness Matrix
Energy Approach
with
i
j
i
j
Displacement u along the bar axis is:
B = element strain-displacement matrix
Note: The shape function are used to interpolate the discrete values at the nodes. For 1D elements this is generally a linear function, whereas polynomials are used for 3D problems.
Notes: 1D FEA – Beam Element
Energy Approach
Similarly, the stiffness matrix can also be established following the energy approach.
(*Click*)
For this purpose, linear shape functions Ni and Nj are introduced to interpolate the solution between the two nodes.
Note: The shape function are used to interpolate the discrete values at the nodal. For 1D elements this is generally a linear function, whereas polynomials are used for 3D problems. This allows for nodal quantities to be displayed continuously across elements.
(*Click*)
As, the expression for u(x) has previously been established, the displacement can be expressed using the shape functions.
Similarly, an expression for the strain can be derived, relating the strain to the displacement and the element strain-displacement matrix B.
Next slide: Expansion on the element strain-displacement matrix B.

## Slide 28: 1D FEA – Beam Elements
fi
fj
i
j
E, A
ui
uj
x
Nodes | i, j
Nodal displacements | ui, uj [mm]
Nodal forces | fi, fj [N]
The strain-displacement matrix B is also defined as:
L
Stiffness (Young’s modulus) | E [N/mm2]
Cross-section area | A [mm2]
Bar length | L [mm]
1D Elasticity and Stiffness Matrix
Energy Approach
Considering the strain energy U stored in the beam:
The external force potential is defined as:
The total potential of the system is the sum of the strain energy U and the external force potential :
Notes: 1D FEA – Beam Element
Energy Approach
The strain-displacement matrix B can be re-written as a function of the shape functions N and subsequently as a function of the beam’s length L: &
(*Click*)
Under consideration of the strain energy U stored in the beam, derived upon the expressions of (i) stress E = Ebu and (ii) strain
(*Click*)
The external force potential is defined as showcased (product of the transverse of the nodal displacement and the nodal force).
(*Click*)
The total potential of the system (=U+) yields the expression:
Next slide: Obtain the element stiffness matrix of this beam, by applying the principle of minimum potential energy.
1D FEA – Beam Element
Energy Approach
The strain-displacement matrix B can be re-written as a function of the shape functions N and subsequently as a function of the beam’s length L: 𝐁=𝑑/𝑑𝑥 [𝑁_𝑖 (𝜉) 𝑁_𝑗 (𝜉)]=𝑑/𝑑𝜉 [𝑁_𝑖 (𝜉) 𝑁_𝑗 (𝜉)]⋅𝑑𝜉/𝑑𝑥 & B=[■8(−1/𝐿&1/𝐿)]
(*Click*)
Under consideration of the strain energy U stored in the beam, derived upon the expressions of (i) stress 𝜎=E𝜀 = Ebu and (ii) strain 𝜀=𝑑𝑢/𝑑𝑥=[𝑑/𝑑𝑥 N]u=Bu
(*Click*)
The external force potential 𝛀 is defined as showcased (product of the transverse of the nodal displacement and the nodal force).
(*Click*)
The total potential of the system 𝚷 (=U+𝛀) yields the expression: 𝛱=1/2 u^T [∫130_𝑉▒ (B^T 𝐸B)𝑑𝑉]u−u^T f
Next slide: Obtain the element stiffness matrix of this beam, by applying the principle of minimum potential energy.

## Slide 29: 1D FEA – Beam Elements
fi
fj
i
j
E, A
ui
uj
x
Nodes | i, j
Nodal displacements | ui, uj [mm]
Nodal forces | fi, fj [N]
With the principle of minimum potential energy (), the term reduces to:
L
Stiffness (Young’s modulus) | E [N/mm2]
Cross-section area | A [mm2]
Bar length | L [mm]
1D Elasticity and Stiffness Matrix
Energy Approach
Considering the strain-displacement matrix B the element stiffness matrix k for the bar element can be written as:
f
k = element stiffness matrix
Note: This is expression is identical to the one obtained from the direct method. Recalling the expressions for i) the total potential of the system and ii) the element’s stiffness matrix, the element’s strain energy can be expresses as
,
which links the case of this beam element back to the initial spring example.
Notes: 1D FEA – Beam Element
Energy Approach
By setting , i.e. applying the the principle of minimum potential energy, it can be verified that the elements equation ku=f holds true. This expression is also true for other elements, not just the beam (or spring) element.
It if of note that the element’s stiffness can also be expressed as:
(*Click*)
Considering the strain-displacement matrix B the element stiffness matrix k for the bar element can be written as: k
Note: This is expression is identical to the one obtained from the direct method. Recalling the expressions for i) the total potential of the system and ii) the element’s stiffness matrix, the element’s strain energy can be expresses as , which links the case of this bar/beam element back to the initial spring example.
Next slide: Now, the applied knowledge on the mathematical model underlying the calculation of 1D beam elements in FEA will be tested in exercises and verified/compared with the numerical results in Ansys Mechanical.
1D FEA – Beam Element
Energy Approach
By setting 𝜕𝚷=0, i.e. applying the the principle of minimum potential energy, it can be verified that the elements equation ku=f holds true. This expression is also true for other elements, not just the beam (or spring) element.
It if of note that the element’s stiffness can also be expressed as: 𝐤=∫130_𝑉▒ (𝐁^T 𝐸𝐁)𝑑𝑉
(*Click*)
Considering the strain-displacement matrix B the element stiffness matrix k for the bar element can be written as: k =∫130_0^𝐿▒ {█(&−1∕𝐿@&1∕𝐿)}𝐸[█(&−1∕𝐿 &&1∕𝐿)]𝐴𝑑𝑥=𝐸𝐴/𝐿 [■(1&−1@−1&1)]
Note: This is expression is identical to the one obtained from the direct method. Recalling the expressions for i) the total potential of the system 𝛱 and ii) the element’s stiffness matrix, the element’s strain energy can be expresses as 𝑈=1/2 𝑢^𝑇 𝑘𝑢 , which links the case of this bar/beam element back to the initial spring example.
Next slide: Now, the applied knowledge on the mathematical model underlying the calculation of 1D beam elements in FEA will be tested in exercises and verified/compared with the numerical results in Ansys Mechanical.

## Slide 30: 1D FEA – Beam Elements Exercise 1: Beams in Tension
Consider the system of two beam elements shown below. For simplicity, each member is modelled with a single 1D line (beam) element. The beams are made up of structural steel (E1 = MPa) and copper alloy (E2 = MPa) with cubic cross-section of 50mmx50mm (A1) and 30mmx30mm (A2) and a length of 200mm (L1) and 150mm (L2), respectively. A force of magnitude 10 N is applied on node 3. Determine the displacements u1 and u2 analytically and numerically.
x
y
E1 A1 L1
E2 A2 L2
A
A
B
B
A-A
B-B
F3
Notes: FEA Beam Elements – Exercise
Consider the system two beam elements shown below (note the parallel to the spring system). For simplicity, each member is modelled with a single 1D line (beam) element. The beams are made up of structural steel (E1 = MPa) and copper alloy (E2 = MPa) with cubic cross-section of 50mmx50mm (A1) and 30mmx30mm (A2) and a length of 200mm (L1) and 150mm (L2), respectively. A force of magnitude 10 N is applied on node 3. Determine the displacements u1 and u2 analytically and numerically.
Next, we will look at the analytical solution.
FEA Beam Elements – Exercise
Consider the system two beam elements shown below (note the parallel to the spring system). For simplicity, each member is modelled with a single 1D line (beam) element. The beams are made up of structural steel (E1 = 2×10^5MPa) and copper alloy (E2 = 1.1×10^5 MPa) with cubic cross-section of 50mmx50mm (A1) and 30mmx30mm (A2) and a length of 200mm (L1) and 150mm (L2), respectively. A force of magnitude 10 N is applied on node 3. Determine the displacements u1 and u2 analytically and numerically.
Next, we will look at the analytical solution.

## Slide 31: 1D FEA – Exercise 1: Analytical Solution
E1 A1 L1
E2 A2 L2
1
2
3
E1 A1 L1
1
2.1
3
E2 A2 L2
2.2
F
F
-F
-F
F
F2 = 0 N
F3 = 10 N
F1 = -10 N
= 4
= 1.9
1
2
3
Consider the force equilibrium to determine the nodal forces, including the on at node 2 (assumed frictionless pin):
Determine the element stiffnesses k:
Determine nodal displacements u:
* Lecture Unit: Stresses and Strains with Ansys Discovery | Ansys
Notes: FEA Beam Elements – Exercise: Analytical Solution
(1) Consider the force equilibrium to determine the nodal forces, including the on at node 2 (assumed frictionless pin):
(*Click*)
(2) Considering the expression for the element stiffness matrix of a bam element introduced earlier, the element stiffness matrices can be determined.
(*Click*)
(3) Finally, the nodal displacements at node 2 and 3 can be determined from the combined stiffness matrix and boundary conditions.
(*Click*)
Further reading: The results could also be determined using Hooke’s law. Please see the lecture unit on stresses and strains for more information.
Next slide: Let’s look at the procedure for solving this problem numerically and compare the results with the analytical ones.
FEA Beam Elements – Exercise: Analytical Solution
(1) Consider the force equilibrium to determine the nodal forces, including the on at node 2 (assumed frictionless pin):
Note: The displacement at node 2 is defined as 𝑢_2=〖 𝑢〗_2.1+𝑢_2.2.
(*Click*)
(2) Considering the expression for the element stiffness matrix of a bam element introduced earlier, the element stiffness matrices can be determined.
(*Click*)
(3) Finally, the nodal displacements at node 2 and 3 can be determined from the combined stiffness matrix and boundary conditions.
(*Click*)
Further reading: The results could also be determined using Hooke’s law. Please see the lecture unit on stresses and strains for more information.
Next slide: Let’s look at the procedure for solving this problem numerically and compare the results with the analytical ones.

## Slide 32: 1D FEA – Exercise 1: Numerical Procedure
Step 1: Create a Static Structural Analysis System in Ansys Workbench and import SYS_BeamElements.scdoc (A3). Then, edit the Engineering Data (A2). | Step 2: Click on the Engineering Data Sources ribbon and select General Materials within the Data Source Table in column A. Scroll down in the Outline of General Materials table and add Copper Alloy to the engineering data by clicking the plus symbol in column B. | Step 3: Edit the Model (A4) to open up Ansys Mechanical.
Notes: FEA Beam Elements – Exercise: Numerical Procedure
Step 1: Open file FEA_BarElements.wbpj in Ansys Workbench and edit the Engineering Data (A2).
Step 2: Click on the Engineering Data Sources ribbon and select General Materials within the Data Source Table in column A. Scroll down in the Outline of General Materials table and add Copper Alloy to the engineering data by clicking the plus symbol in column B.
Step 3: Edit the Model (A4) to open up Ansys Mechanical.
Next slide: Further steps.

## Slide 33: 1D FEA – Exercise 1: Numerical Procedure
Step 4: Assign beam elements to the components of the geometry and their appropriate the correct material properties. | Optional step 5: The beam’s actual cross-sections can be visualized (sanity check). Step 6: Insert mesh sizing and as type choose ‘Number of Division’ with a value of 1, to ensure every beam segment is represented by 1 element.
Notes: FEA Beam Elements – Exercise: Numerical Procedure
Step 4: Assign the beam elements the correct material properties.
Optional step 5: As a sanity check, the beam’s actual cross-sections can be visualized.
Step 6: Insert mesh sizing and as type choose Number of Division with a value of 1, to ensure every beam segment is represented by 1 element. Choose behavior as hard.
(*Click*)
Note:
Next slide: Further steps.

## Slide 34: 1D FEA – Exercise 1: Numerical Procedure
Step 7: Insert a fixed boundary condition at node 1, a load of 10 N in x-direction at node 3. At last, add a displacement constraint at node 2 that constraints movement in y- and z-direction. | Step 8: Define an output variable to evaluate (i) the total deformation and (ii) the deformation of node 2 in x-direction by inserting a probe for tracking. Step 9: Solve the model and visualize the results
Step 8:
Notes: FEA Beam Elements – Exercise: Numerical Procedure
Step 7: Insert a fixed boundary condition at node 1, a load of 10 N in x-direction at node 3. At last, add a displacement constraint at node 2 that constraints movement in y- and z-direction.
Step 8: Define an output variable to evaluate (i) the total deformation and (ii) the deformation of node 2 in x-direction by inserting a probe for tracking.
Step 9: Solve the model and visualize the results
Next slide: Solution for the nodal deformations.

## Slide 35: 1D FEA – Exercise 1: Numerical Solution
As can be observed from the FEA results, the max. deformation (i.e. u3) and the deformation of beam element 1 (i.e. u2 as recorded by probe) are identical to the analytical solutions. They are 1.9 ×10−5 mm and 4 × 10 −6 mm, respectively.
Notes: FEA Beam Elements – Exercise: Numerical Solution
As can be observed from the FEA results, the max. deformation (i.e. u3) and the deformation of beam element 1 (i.e. u2 as recorded by probe) are identical to the analytical solutions. They are 1.9 ×10−5 mm and 4 × 10 −6 mm, respectively.
Next slide: After this simple beam analysis, we will now proceed to an exercise on an entire truss System using Ansys Mechanical.

## Slide 36: 1D FEA – Beam Elements Exercise 2: Truss System
Consider the truss system shown below. For simplicity let us model each member of the truss with a single 1D beam element. The truss system is made up of structural steel and the cross-section of each member is 50mmx50mm. Determine the maximum deformation of the structure and analyze the reaction forces at the supports using Ansys Mechanical.
1 m
1 m
1 m
1 m
1 m
50kN
50kN
50kN
Note: The truss system is solved using beam elements to account for rotations in the nodes. As an additional exercise and for comparison try to solve this problem using link/truss elements!
Notes: 1D FEA – Beam Elements Exercise 2: Truss System
Let us now analyze a truss system using Ansys Mechanical. Consider the truss system shown in the slide.
For the sake of simplicity let us model each member of the truss with a single 1D element. The truss system is made up of structural steel and the cross-section of each member is 50mmx50mm.
Note: The truss system is solved using beam elements to account for rotations in the nodes. As an additional exercise and for comparison try to solve this problem using link/truss elements!
Next slide: Let’s look at the procedure for solving this problem numerically.

## Slide 37: 1D FEA – Exercise 2: Numerical Procedure
Step 1: Create a Static Structural Analysis System in Ansys Workbench. Note that the Engineering data stays at the default Structural Steel | Step 2: Edit Properties of Geometry and activate Line Bodies | Step 3: Create geometry of the truss using SpaceClaim (Hint: Use lines and profiles tools) | Step 4: Setup the mesh (Hint: Define a very large element size so each member has only one elements)
Notes: 1D FEA – Exercise 2: Numerical Procedure
The analysis is carried out in the following steps:
Open a workbench file and create a static structural analysis system
Edit Properties of Geometry and activate Line Bodies as shown in the screenshots
Create geometry of the truss using SpaceClaim (Hint: Use lines and profiles tools)
Setup the mesh (Hint: Define a very large element size so each member has only one elements)
Next slide: Further steps.

## Slide 38: 1D FEA – Exercise 2: Numerical Procedure
Step 5: Apply boundary conditions | Step 6: Define output variable to be evaluated | Step 7: Solve the model
Notes: 1D FEA – Exercise 2: Numerical Procedure
5. Apply boundary conditions
6. Define output variable to be evaluated
7. Solve the model
Next slide: Solution total deformation.

## Slide 39: 1D FEA – Exercise 2: Numerical Solution
Total Deformation
Notes: 1D FEA – Exercise 2: Numerical Solution
The deformation in the trussed can be plotted along its members and a maximum deformation of 0.09mm is found at the centre.
Next slide: Solution reaction forces at supports.

## Slide 40: 1D FEA – Exercise 2: Numerical Solutions
Left:
Right:
Why is the force reaction along Y a very negligible number as opposed to zero?
Reaction Forces
Notes: 1D FEA – Exercise 2: Numerical Solution
As observed from the slide the total support reaction is equal to the total force applied on the truss system. This indicates that the system satisfies the laws of equilibrium.
(*Click*)
Quiz Solution: FEA is an approximation method and not an exact solution hence the approximation leads to very negligible roundoff errors. It is also important to note that in the case of 2D analysis the force value in the out of plane direction would have been zero.
Next slide: Summary of lecture unit.

## Slide 41: Summary
Finite element analysis is cost effective and saves time from design conception to manufacturing the component
In the case of structural analysis, FEA is based on 3 important equations viz., equilibrium, constitutive and compatibility equations
In this lecture unit, we focus on a 1D system, where the relationship of displacements and force is defined with the help of the stiffness matrix
At the core of FEA lies the discretization, which means a model is divided into a finite number of smaller bodies or elements (meshing). 1D elements such as beams, or trusses are used to solve 2D and 3D structural analyses in Ansys Mechanical. The element’s type and degrees of freedom (DoFs) defines which structural problems can be solved.
Ansys Mechanical has been used to solve 1D element problems ranging from a simple to a more complex system.
Notes: Summary
Finite element analysis is cost effective and saves time from design conception to manufacturing the component
In the case of structural analysis, FEA is based on 3 important equations viz., equilibrium, constitutive and compatibility equations
There are different types of FEA that can be carried out based on the application cases. Some popular types are static vs. dynamic, implicit vs. explicit and linear vs non-linear.
In this lecture unit, we focus on a 1D system, where the relationship of displacements and force is defined with the help of the stiffness matrix
At the core of FEA lies the discretization, which means a model is divided into a finite number of smaller bodies or elements (meshing). 1D elements such as beams, or trusses are used to solve 2D and 3D structural analyses in Ansys Mechanical. The element’s type and degrees of freedom (DoFs) defines which structural problems can be solved.
Ansys Mechanical has been used to solve 1D element problems ranging from a simple to a more complex system.
Next slide: Further information and resources to this and other relevant topics are linked in the next slide.
Summary
Finite element analysis is cost effective and saves time from design conception to manufacturing the component
In the case of structural analysis, FEA is based on 3 important equations viz., equilibrium, constitutive and compatibility equations
There are different types of FEA that can be carried out based on the application cases. Some popular types are static vs. dynamic, implicit vs. explicit and linear vs non-linear.
In this lecture unit, we focus on a 1D system, where the relationship of displacements and force is defined with the help of the stiffness matrix [𝑲]{𝐮}={𝐅}
At the core of FEA lies the discretization, which means a model is divided into a finite number of smaller bodies or elements (meshing). 1D elements such as beams, or trusses are used to solve 2D and 3D structural analyses in Ansys Mechanical. The element’s type and degrees of freedom (DoFs) defines which structural problems can be solved.
Ansys Mechanical has been used to solve 1D element problems ranging from a simple to a more complex system.
Next slide: Further information and resources to this and other relevant topics are linked in the next slide.

## Slide 42: Further Information and Resources
  Ansys Academic | Simulation Software for Educators, Researchers and Students.
  Ansys Innovation Courses : Free to Access to courses covering a variety of physics and software.
  Ansys Education Resources: Specifically developed for Educators.
  Ansys Discovery Forum: Learn Discovery through video-tutorials.
  Ansys Learning Forum: Ask questions to the Ansys Community!
  Ansys Learning : Ansys YouTube Channel with dedicated video playlists.