## Slide 1
Lecture Unit
Introduction to Heat Transfer with Ansys Discovery
Developed and Curated by the Ansys Education Team
Nick Stefani and David Mercier
education@ansys.com

## Slide 2: Learning objectives for this Lecture Unit
Intended Learning Outcomes | 
Knowledge and Understanding | Knowledge and understanding of basic heat transfer modes
Skills and Abilities | Ability to use Ansys Discovery to set-up simple heat transfer problems
Values and Attitudes | Awareness of importance of simulation in engineering problems
In-Built Assessment
  Simulation exercises
  Quizzes
Resources
  Books:
    Fundamentals of Heat and Mass Transfer, T. Bergmam and A.S. Lavine, 8th Edition, Wiley
    Essentials of heat transfer: principles, materials, and applications. Kaviany, Massoud. Cambridge University Press, 2011.
    Software: Ansys Discovery v22R1
Further reading/information
  Ansys Academic
  Ansys Innovation Courses
  Ansys Education Resources
Notes: Learning Objectives
These Intended Learning Outcomes are based on a taxonomy of knowledge and understanding as the basis, skills and abilities as necessary for the practical use of knowledge and understanding, followed by acquired values and attitudes enabling assessments and responsible use of these abilities.

## Slide 3: Accessing Ansys Discovery
Ansys Student: Free Student Software Downloads
Get Access to Discovery| Connect with us today
Students
Educators
Notes: If you have any questions on accessing Ansys Discovery please get in touch with the education team at education@ansys.com

## Slide 4: Outline of the lecture unit
Fundamentals
  Temperature, Internal Energy and Heat
  Heat Sources
  Measuring Heat
  Heat Transfer Modes
Conduction
  Fourier’s Law
  Visualization in Ansys Discovery
Convection
  Newton’s Law of Cooling
  Visualization in Ansys Discovery
From the Ideal to the Real World
Summary
Exercise
Notes: Heat transfer
This unit introduces heat transfer and thermal simulations using Ansys Discovery. In this presentation we will go through a number of topics. We will start with some fundamentals before distinguishing between conduction and convection using some simplified examples examples and then move towards more realistic problems example before a final summary and a final exercise.

## Slide 5: What is heat?
Heat comes from thermal energy made when molecules move.
The faster molecules move, the higher the temperature.
Temperature
A change in thermal energy can lead to a phase change (for example liquid  gas).
In other words, when the thermal energy of a substance increases, its particles move faster.
Heat sink
Heat source
Notes: What is heat?
Heat comes from thermal energy made when molecules move. The faster molecules move, the higher the temperature. In other words, heat energy is transferred from one body to another as the result of a difference in temperature. In this example, the pot on the left is frozen and water inside get colder, when the pot on the right is heated and water is starting to boil and to change in vapor.

## Slide 6: Definition of Temperature, Internal Energy and Heat
Temperature
Heat is the energy (or work) spontaneously transferred from a body to another one, by mechanisms other than thermodynamic work or transfer of matter, resulting in a temperature difference.
Temperature is the average kinetic energy of individual molecules of a body.
The internal energy is an extensive property, equal to the total energy of all the molecules within a body.
Heat Flux
Heat Flow (Heat Transfer Rate)
[ or ]
or
[ or ]
[]
Heat Energy/Work
[ or ]
With the mass of the body and the specific heat capacity. The specific heat capacity is a material property dependent of and , not like the heat capacity which is a sample property.
Notes: Definition of Temperature, Internal Energy and Heat
Temperature, internal energy and heat are defined in these slides.
The heat energy () is obtained knowing the temperature variation () in a body of a mass () and with a specific heat capacity ().
Then heat flow ( or ) and heat flux () can be determined by deriving the heat energy respectively one time and two times.
Specific heat capacity, or simply specific heat, refers to the heat capacity per unit mass of a pure substance. In other words, it is defined as the amount of heat needed to increase the temperature of 1kg of a material by 1K and is expressed in terms of J/kg·K or equivalently J/kg·°C.
Definition of Temperature, Internal Energy and Heat
Temperature, internal energy and heat are defined in these slides.
The heat energy (𝑊) is obtained knowing the temperature variation (Δ𝑇) in a body of a mass (m) and with a specific heat capacity (𝑐_𝑝).
Then heat flow (𝑄 or 𝑞) and heat flux (𝑞^′′) can be determined by deriving the heat energy respectively one time and two times.
Specific heat capacity, or simply specific heat, refers to the heat capacity per unit mass of a pure substance. In other words, it is defined as the amount of heat needed to increase the temperature of 1kg of a material by 1K and is expressed in terms of J/kg·K or equivalently J/kg·°C.

## Slide 7: Some Orders of Magnitude
Temperature scales
Specific heat capacity of pure elements as a function of atomic weight
The calorie was originally defined as the amount of heat required at a pressure of 1 standard atmosphere to raise the temperature of 1 gram of water 1° Celsius. Since 1925 this calorie has been defined in terms of the joule, the definition since 1948 being that one calorie is equal to approximately 4.2 joules.
Heat Energy/Work
Graphic obtained with Ansys Granta EduPack
The average recommended food intake for a person is 2000 Kcal. How much is that in KJ?
What is the Celsius temperature increase of 100 liters of water given by this amount of energy?
Mercury boils
Steam point
Approx. room temperature
Ice point
Nitrogen boils
Absolute zeros
°F
°C
°R
K
630
373
300
273
77
0
1134
672
540
492
139
0
357
100
27
0
-196
-273
674
212
80
32
-321
-460
Notes: Some orders of magnitude
Different temperature scales are compared to understand the link between different units. There are multiple different systems for measuring heat energy (temperature): for example Kelvin (K), Rankine (°R), Celsius (°C), and Fahrenheit (°F),. In scientific measures, it is most common to use either the Kelvin or Celsius scale as a unit of temperature measurement. The Kelvin is the SI unit of thermodynamic temperature, and one of the seven SI base units. Temperature in °C is obtained by subtracting 273.15 from the numerical value of the temperature expressed in K. The Rankine, Fahrenheit and Kelvin scales are related by the following formulaes: °R = 1.8 K and °R = °F + 459.67. Zero in both the Kelvin and Rankine scales is at absolute zero.
An Ashby map using Granta EduPack software (with « The Elements » database) is created to display the linear relationship between specific heat capacity of elements and their atomic weight. This trend highlights the Dulong–Petit law which states that the gram-atomic heat capacity (specific heat times atomic weight) of an element is a constant; that is, it is the same for all solid elements, about six calories per gram atom.
Quiz Question: 2000 Kcal are approximately 8368 kJ. This amount of energy would be enough to raise 100 liters of water by 20°C.

## Slide 8: Heat Sources
Chemical
Combustion, chemical reaction, digestion…
Electrical
Conversion of electrical energy into heat energy
Mechanical
  Friction (sliding, slipping) Impact, Explosion…
Governing Equation
Physical
Joule–Lenz law
Thermochemistry Chemical thermodynamics
Thermodynamics
Notes: Heat sources
But how heat energy is generated? ‬There are several heat sources that exist in nature, from the sun to the Earth's core, and some that are completely manmade. The most common use for a heat source is the commercial production of electricity. It is possible to classify heat sources:
Chemical ones (eg striking a match …),
Mechanical ones (eg caveman using flints or wood sticks to make fire…),
Electrical ones (eg the Joule effect in the central processing unit of your laptop…).
But, how is it to possible to quantify the heat produced or the temperature of a body?

## Slide 9: How to measure temperature or heat?
Heat energy measurement
  Calorimeter, Digital Joulemeter/Wattmeter
Without contact (often based on optical properties)
Infrared or Laser Thermometer, Thermographs, thermal imaging camera, pyrometer…
With contact
(often based on electrical resistance or expansion property)
Thermocouples, digita l thermometer, thermal strips, classical thermometers (Hg, alcohol…)…
Temperature measurement
Heat flux measurement
Heat flux can be determined using a flux sensor (usually a transducer that generates an electrical signal proportional to the total heat rate applied to the surface of the sensor). The measured heat rate is divided by the surface area of the sensor to determine the heat flux.
Notes: How to measure temperature or heat?
Several different types of experimental measurements exist on the market to determine for example a level or a gradient of temperature, or an order of magnitude of the produced heat energy. But measuring temperature can be quite challenging this is why we do simulation..

## Slide 10
Governing Equation
Conduction
Internal or body-to body energy exchange due to a temperature gradient, by direct contact
Radiation
Energy transfer from a body or between two bodies by electromagnetic waves or particles
Fourier’s Law
  Newton’s Law of Cooling
Stefan-Boltzmann Law
Convection
  Energy exchange between a body and a surrounding fluid (liquid or gas) caused by molecular motion
Heat Transfer Modes
Thermal Radiation | Ansys Innovation Courses
PP
PP
PP
Hot environment
Hot metallic pot
Water turbulence
Notes: Heat Transfer Modes
Heat is the transfer of kinetic energy from one medium or object to another, or from an energy source to a medium or object. Such energy transfer can occur in three ways: radiation, conduction, and convection.
Conduction heat transfer is the transfer of heat through matter (i.e., solids, liquids, or gases) without bulk motion of the matter. In another words, conduction is the transfer of energy from the more energetic to less energetic particles of a substance due to interaction between the particles.
Convection heat transfer is the transfer of heat between two bodies by currents of moving gas or fluid. In free convection, air or water moves away from the heated body as the warm air or water rises and is replaced by a cooler parcel of air or water.
Radiation heat transfer is a process where heat waves are emitted that may be absorbed, reflected, or transmitted through a colder body. Sun heats the earth by electromagnetic waves. Hot bodies emit heat waves.
In this lecture unit we will focus on convection and conduction. Conduction and convection are preponderant at room temperature. For example, in space there is only heat transfer by radiation (no convection, no conduction).

## Slide 11
High Temperature
Low Temperature
Heat Direction
If 5 kg of steel, at 300°C, is placed in contact with a copper sample of 500 kg at 20°C, what is the heat direction?
PP
PP
Sign Convention about heat transfer
Notes: Sign Convention about heat transfer
Heat transfer direction is defined by convention to be positive when the heat goes from the hot temperature to the cool one.
If two bodies at different temperatures are brought together, energy is transferred (i.e., heat flows) from the hotter body to the colder. The effect of this transfer of energy usually, but not always, is a decrease in the temperature of the hotter body and an increase in the temperature of the colder body.
Quiz Question: While it could be intuitive to think that heat is flowing from the object with the bigger mass, it is the temperature of the bodies that dictates the heat flow direction. In this case heat is flowing from the steel sample to the copper one.

## Slide 12
Finite Element Method is predominant
Iterative algorithm suitable for computers
Fast solutions to complex problems
Visualisation (gradients, dynamic effects…)
Prerequisite to many numerical simulations
Follows standardized test regimes
Time- and cost-consuming approach to data acquisition
Analytical Methods
Numerical Methods
Experimental Methods
Key State Variables
  Temperature
  Heat Flow and Heat Flux
Different methodologies available
Used mainly for simple idealized cases
Time-consuming approach for complex problems
Solving Heat Transfer Engineering Problems
Notes: Analytical methods are exact and are often performed with hand calculations. Several methods are available in fluid mechanics theory. However, these exact solutions can only be found for simple idealized problems. Most fluid flow problems cannot be solved analytically because the models are too complex.
Numerical methods are simplified iterative algebraic equations that can be solved by a computer in order to obtain results. Finite Element Method is predominantly used in analyzing engineering problems as it can be easily implemented using computers. In this lecture unit we will be using Ansys Discovery.
Experimental methods are methods in which the fluid flow is recreated in real life and tests are then carried out. These methods are required in order to calibrate and validate simulation models at important phases of development. Experimental methods are generally standardized tests. They are time consuming and can often be very expensive to create and analyze.
In this LU we will concentrate on Analytical and Numerical Methods.

## Slide 13
= Heat flux, = Heat flow
= Temperature
= thermal conductivity of the material
[]
Note: The minus is needed to maintain directionally of heat flow from high to low temperature.
[]
Heat Transfer is proportional to the difference in temperature:
13
Thermal Conductivity in Heat Transfer | Ansys Innovation Courses
PP
Conduction: Fourier’s Law
Notes: Conduction: Fourier’s Law
Conduction heat transfer can be expressed through Fourier’s law which is displayed in the slide in 1D and shows how the heat flow along the x direction can be computed (using the 3D version of this equation, it is also possible to determine heat along the y and z directions. The transferred heat is proportional to the difference in temperature ( a bigger temperature difference leads to higher heat transfer). Once the heat flux as been calculated the heat transfer rate can be found by taking into account the area through which heat is transferred.

## Slide 14
Conductive Heat Transfer is proportional to the difference in temperature and Thermal Conductivity k
14
Thermal Conductivity in Heat Transfer | Ansys Innovation Courses
Ansys (CES) Granta EduPack | Software for Materials Education
Thermal Conductivity
Notes: Conductive heat transfer is proportional to the difference in temperature but also to Thermal conductivity which is a material property representing the ability of a specific material to conduct heat through its body, materials with higher thermal conductivity will lead to larger heat fluxes. For example common radiators in households are made of materials with high thermal conductivity such metals and some technical ceramics, while mountain houses are usually made of wood material which have relatively small conductivity and thus provide good insulation.
The graph has been taken from Ansys Granta EduPack which is specialist software used for material comparison and selection.

## Slide 15
= 40 mm
= 15 mm
Study the conduction in a steel pipe, given = 50.4 W/m·K:
Solve the problem analytically and numerically to find the value of heat flow (.
Compare the analytical and simulation solutions for the Heat Flow.
Use simulation to visualise Temperature Field and verify that directionality of the Heat Flow direction is in line with the sign convention.
Insulated Surface
Conduction Exercise
Notes: This is a small problem on pure Conduction, in which for the given geometry it will be needed to:
Solve the problem analytically and numerically to find the value of heat flow (
Compare the analytical and simulation solutions for the Heat Flow.
Use simulation to visualise Temperature Field and verify that directionality of the Heat Flow direction is in line with the sign convention.
This is a small problem on pure Conduction, in which for the given geometry it will be needed to:
Solve the problem analytically and numerically to find the value of heat flow (𝑞)
Compare the analytical and simulation solutions for the Heat Flow.
Use simulation to visualise Temperature Field and verify that directionality of the Heat Flow direction is in line with the sign convention.

## Slide 16
Numerical solution with Ansys Discovery
()
Analytical Solution
 |  | %
70.7W | 71.4W | 1%
70.7W | 71.4W | 1%
Conduction Exercise: Analytical and Numerical Solutions
Notes: It can be observed that the analytical solution and the numerical solution provide match quite closely. The small deviation in the results can be attributed to the different models used in solving the problem: 1D analytical and 3D numerical.

## Slide 17
As per convention the displayed Heat Flux vectors show that heat flows from high temperature to low temperature.
A
Cross Section Plane A-A
x
y
A
98
40
40
80
Understanding Heat Flow and Temperature Distribution can be quite challenging for more complex geometries..
Insulated Surface
Conduction Exercise: Visualisation through Simulation
Notes: In Ansys Discovery, it is possible to display heat flux vectors across the cross-section of the geometry. By doing this it can be seen that as per the sign convention the displayed Heat Flux vectors show that heat flows from high temperature to low temperature. While in this example it can be intuitive to understand the Heat Flow and Temperature distributions, this may not always be the case. For more complex geometries with variegated loading, it can be quite challenging to do this either intuitively or with analytical solutions. This is where the visualisation capabilities of simulation tools can be of great benefits.

## Slide 18
= Heat flux, = Heat flow
= Temperature of the solid surface
= Temperature of the bulk fluid
= Heat transfer or Film Coefficient
Fluid, with velocity v
Solid
Temperature Gradient (Boundary Layer)
Heat Transfer is proportional to the difference in temperature:
Depends on:
Fluid
Contact Geometry
Motion of the fluid
Heat Transfer Coefficients | 
Free Convection | 
Gases | 2-25
Liquids | 50-1000
Forced Convection | 
Gases | 25-250
Liquids | 100-20,000
Heat Transfer Coefficients | 
Free Convection | 
Gases | 2-25
Liquids | 50-1000
Forced Convection | 
Gases | 25-250
Liquids | 100-20,000
Based solely on the values of h, would you choose a liquid or a gas to cool something?
Can be known or unknown!
Thermal Convection in Heat Transfer | Ansys Courses
Convection: Newton’s Law of Cooling
Notes: Convection: Newton’s Law of Cooling
Convection heat transfer is given by the energy exchange between a body and a surrounding fluid (liquid or gas) caused by molecular motion. The transferred heat is proportional to the different in temperature (a bigger temperature difference leads to higher heat transfer) and also to the heat transfer (or film) coefficient. While Thermal conductivity only depends on the material, the heat transfer coefficient (h) depends on many things such as the fluid properties, its motion and the contact geometry. Its value can found in table which provide information on some typical cases, based on certain assumptions, however it is often the object of heat transfer problem to find this coefficient. It can be seen that forced convection (e.g. fan blowing air), leads to higher heat transfer coefficient and thus higher heat exchanges (imagine blowing on things to cool them faster).
Question for students: Based solely on the values of h, would you choose a liquid or a gas to cool something? Answer: Liquids have higher h in both free and forced convection so they are better for cooling applications.

## Slide 19
= 0.1 m
= 100
is the length of the plate in m
Fluid Properties (Air)
, dynamic viscosity = 1.83E-05 kg/m.s
, density = 1.16 kg/m3
thermal conductivity = 0.028 W/m·K
For the shown flow of Air at 20 , with the given material properties, passing over a stationary plate at 100
Find and compare the heat transfer coefficient obtained through analytical and numerical solution
Visualise the temperature boundary layer in Ansys Discovery
Convection Exercise
Air = 1m/s, = 20
Notes: This is a small problem on pure Convection, in which a fluid is travelling at 1 m/s and 20 , before encountering a stationary plate (no-slip condition) of length 1m (for the 3d simulation consider width of 0.2 m)
Solve the problem analytically and numerically to find the heat transfer coefficient
Compare the analytical and simulation solutions for h
Use simulation to visualise Temperature boundary layer
This is a small problem on pure Convection, in which a fluid is travelling at 1 m/s and 20 °C , before encountering a stationary plate (no-slip condition) of length 1m (for the 3d simulation consider width of 0.2 m)
Solve the problem analytically and numerically to find the heat transfer coefficient
Compare the analytical and simulation solutions for h
Use simulation to visualise Temperature boundary layer

## Slide 20
With Ansys Discovery:
Analytical Solution
=
Where:
, Nusselt Number
, Prandtl Number
, Reynolds Number
, fluid velocity = 1 m/s
, viscosity = 1.83E-05 kg/m-s
, density = 1.16 kg/m3
, thermal conductivity = 0.028 W/m·K
, length of the plate = 0.1 m
, specific heat = 1020 J/kg.K
 |  | %
12.9 | 14.3 | 10%
12.9 | 14.3 | 10%
Convection Example: Analytical and Numerical Solution
Notes: The analytical solution can be computed through the equations shown above. The heat transfer coefficient is proportional to the Nusselt number which is the ratio of convective to conductive heat transfer at a boundary in a fluid. This number can be computed as a function of Reynolds number (parameter associated with the characteristics of the fluid flow) and Prandtl number (ratio of momentum diffusivity to thermal diffusivity). The various coefficients in the Nux=f(Re,Pr) equation are found through empirical correlations specific to the problem analysed (e.g. forced convection over flat plate) and would be different in other cases (e.g. natural convection, flow around cylinder etc.).
The numerical solution obtained through Ansys Discovery Simulation has been set up as shown in the video. For this it was used the refine stage, which includes monitors on heat flux for surfaces. It can be observed that there is a 10% difference between analytical and numerical solution. This is due to multiple reasons. Firstly, convection is much more complex phenomena to model compared to conduction as it is closely related to the motion of the fluid. For example the analytical solution assumes the flow to be perfectly laminar and the model to be 2D, while the numerical solution is in 3 dimensions and a turbulent-inclusive solver was used (standard Discovery Turbulent k-omega SST). Also, no consideration was given for the meshing which plays an important role when modelling these types of problems (in particular the use of boundary layer elements). A refinement of the mesh which can be done through the bottom central slider or an advanced mesh set up in Ansys Discovery will lead to improved results but this is outside of the scope for this introductory lecture unit. An increase of mesh elements in Ansys Discovery from 4000 to 32000 results in the delta dropping from 10% to 6%. For very high level accuracy it is in general recommended to use Ansys Fluent which is the Ansys flagship tool for CFD modelling and which includes advanced meshing capabilities.

## Slide 21
Convection Exercise: Visualisation through Simulation
Flat Plate Laminar Boundary Layer (FLUENT) - ANSYS Innovation Courses
Laminar Boundary Layer Theory (Fluent) | Ansys Innovation Courses
Boundary Layer Region
Notes: It can be clearly seen from the simulation the presence of a boundary layer forming in the fluid. At the bottom, the temperature of the fluid is equal to the temperature of the plate which is 100 C, then a transition zone, called boundary layer is present where temperature starts to decrease until it reaches the “inlet” temperature of the fluid which is 20 C. From the simulation it can also be plotted the velocity boundary layer which has the same shape but different height. In that case the velocity will be zero at the plate (non-slip condition) and it will increase through the boundary layer region until it reaches the velocity at the inlet in the unperturbed region. Two Ansys innovation courses are available on Boundary layer theory using Ansys Fluent (flagship Ansys tool for CFD simulation).

## Slide 22: From the Ideal to the Real World
In real world scenarios it is often necessary to model both convection and conduction at the same time and analyse temperature distribution in both solids and fluids.
This type of analysis is called Conjugate Heat Transfer (CHT).
In the case of CHT and complex problems, analytical modelling is not an easy and fast solution.
Here, numerical modelling helps to rapidly solve complex problems, to visualize gradients and distribution fields, and to perform easily parametric analysis.
Another important factor to consider is Time, which can affect the type of analysis performed.
Time independent analysis, used when:
Time behaviour is irrelevant.
Only Equilibrium results are sought.
Time-history or Time-dependent analysis, used when:
Effects of time cannot be neglected.
Results (e.g. Temperature) at a specific time are sought.
Notes: From the Ideal to the Real World
In real world scenarios it is often necessary to model both convection and conduction at the time and analyse temperature distribution in both solids and fluids. This type of analysis is called Conjugate Heat Transfer (CHT). In the case of CHT and complex problems, analytical modelling is not an easy and fast solution. Here, numerical modelling helps to rapidly solve complex problems, to visualize gradients and distribution fields, and to perform easily parametric analysis.
Another important factor to consider is Time, which can affect the type of analysis performed. In the case of time independent analysis (ie static or steady-state) the goal is to determine the long-term behavior of a system that does not change over time. For Time-dependent analysis (also called time-history analysis or transient simulation), it is possible to specify the simulation duration in seconds. If you do not specify a duration, the simulation will continue until interrupted. A time-dependent analysis, by definition, involves conditions that are a function of time.

## Slide 23
  Open with Discovery the file “Mixer_Tee_Fluid_Solid_Thermal.dsco”
  Review the different parts of the geometry and the different boundary conditions
  Run the simulation with default values, using steel S275N for the pipe material and water for the fluid flow.
  Visualize the temperature gradient inside the liquid and on the outer mixer tee surface.
  Check what is happening if you change steel for a plastic (PC, 30% PTFE lubricated)? Is there any effect on the temperature of the fluid and the temperature of the pipe?
  Compare natural and forced convections (respectively 10 and 100 on the outer mixer tee surface temperature and the liquid temperature, with steel S275N for the pipe material.
Flow Outlet
Flow Inlet
Default values
Flow Inlet
Conjugate Heat Transfer Exercise: Mixer Tee Part - 1
Notes: Conjugate Heat Transfer
After simple example of conduction and convection, conjugate heat transfer problem is discussed in this slide, with the case study of the mixer tee. 2 inlet flows (a cold one and a hot one) ar
For this computational fluid dynamics study, a simple convergent 90° T-junction (mixer tee) of different diameter has been chosen. Though it is connected to a long and complex piping system, a small portion is taken under consideration for a calculation to reduce difficulties and calculation time. In this mixing tee hot fluid enter with one end of the main pipe and cold fluid from the branch pipe. These two inlet fluids having temperature differences are mixed thermally and heat is transferred from hot to cold fluid. After mixing, the mixer liquid leaves through another end of the main pipe called outlet.

## Slide 24
Conjugate Heat Transfer Exercise: Mixer Tee Part - 1
Simulation set up | Temperature gradient into the fluid | Temperature gradient on the outer surface of the pipe
Mixer tee in steel S275N, natural convection |  | 
Mixer tee in PC, 30% PTFE lubricated; natural convection |  | 
Mixer tee in steel S275N, forced convection |  | 
Compared to Steel, change in the liquid, but better insulation of the mixer tee.
Small decrease of T inside the liquid and almost same decrease as with mixer tee in polymer.
Temperature (°C)
Temperature (°C)
Temperature (°C)
Notes: Conjugate Heat Transfer
After a vizualization step of the outer mixer tee surface and the temperature gradient inside the liquid, the material comparison for the T-junction and the type of convection (natural vs forced) are analyzed. There is no and little material influence on the temperature distribution inside the liquid, respectively when steel is replaced by a plastic and in the case of forced convention. But concerning the temperature gradient on the outer surface of the mixer tee, almost same temperature decrease is observed when steel is replaced by steel and when convection is changing from natural to forced.
In the case of the change from steel to polymer, given lower thermal conductivity of the polymer, the heat of the liquid is not easily transfered to the surface of mixer tee and thus outer tempereature decrease with a polymer.
In the case of forced convection and the mixer tee in steel, temperature decrease on the outer surface of the mixer tee is due to a good convection and thus a higher heat transfer between the pipe and the air around the tee.
As a conclusion in terms of design, changing the material of the mixer tee from steel to polymer (if possible, depending on chemical resistance, maximum temperature…) is equivalent to have a forced convection (with the addition of a fan for example) around the mixer tee.

## Slide 25
Using defaults parameters, visualize different cross-sectional views of velocity and temperature contours at different planes along with the outlet. Define the mixing region and where is the maximum of heat transfer. Why?
T (°C)
Velocity (m/s)
Heat flux (W/m²)
Max
Conjugate Heat Transfer Exercise: Mixer Tee Part - 2
Investigate and Discuss the influence of inlet 2 speed and inlet 2 temperature on the average temperature outlet.
  Parametrize Inlet 2 speed to check these conditions: 0.01, 0.1 , 1 and 10m/s
  Parametrize Inlet 2 temperature to check these conditions: 50, 100, 150 and 200°C
Quick Tip Video: How to perform parametric analysis in Ansys Discovery.
Given results obtained in the previous slide and this one, let’s propose some design improvements to optimize heat distribution and heat homogenization, without increasing energy consumption.
Notes: While passing through the mixing outlet, rapid collisions take place between hot and cold fluids. As a result, thermal mixing and heat transfer occurs, with a maximum velocity found at the mixing region as the fluids from two inlets are combined.
The faster or hotter the hot flow inlet, the hotter the average temperature outlet will be. But the relationship is only linear with the temperature of the hot flow inlet (not the speed).

## Slide 26
Governing Equation
Conduction
Internal or body-to body energy exchange due to a temperature gradient, by direct contact.
Fourier’s Law
  Newton’s Law of Cooling
Convection
  Energy exchange between a body and a surrounding fluid (liquid or gas) caused by molecular motion.
Fluid, with velocity v
Solid
Temperature Gradient (Boundary Layer)
Summary Heat Transfer Modes
Notes: In this lecture unit we focused on convection and conduction which are the heat transfer modalities that can be simulated in Ansys Discovery. For these energy transfers to take place it is necessary a temperature difference, which is proportional to the amount of heat exchanged. Conduction and Convection can be expressed through two different laws, respectively Fourier’s Law and Newton’s Law of cooling. The former is depend on thermal conductivity of the material, while the second on the heat transfer coefficient (or film coefficient) which can be a much more complicated parameter to estimate as it is dependent not only from the material properties but also from the contact geometry between the fluid and the solid and the fluid motion.

## Slide 27: Summary Thermal Simulation
Through analytical and numerical solution it is possible to obtain information on temperature distributions, heat fluxes and heat transfer coefficients.
For complex geometries and boundary conditions, simulation can be an aid to engineers in finding solutions and also by providing visualisation of fields and vectors.
Thermal problems can be modelled in different ways depending on what is the object of the investigation and the known inputs (e.g. is heat transfer coefficient known?).
In the majority of real life examples all heat transfer modes (radiation, convection and conduction) co-exist and it the role of engineer to decide what is the dominant mode and what assumptions/simplification can be made when solving the problem.
Notes: Through analytical and numerical solution it is possible to obtain information on temperature distributions, heat fluxes and heat transfer coefficients
For complex geometries and boundary conditions, simulation can be an aid to engineers in finding solutions and also by providing visualisation of fields and vectors.
Thermal problems can be modelled in different ways depending on what is the object of the investigation and the known inputs (e.g. is heat transfer coefficient known?).
In the majority of real life examples all heat transfer modes (radiation, convection and conduction) co-exist and it the role of engineer to decide what is the dominant mode and what assumptions/simplification can be made when solving the problem.

## Slide 28: Exercise Brief: Improving Insulation
Objective
Minimise Loss of Internal Temperature
Outside Air
5 ° C
Inside Air
25 ° C
Steps Summary
Open Discovery File: “Improving_Insulation_excercise.dsco”
Set up Boundary conditions
  Convection on inner face:
  Convection on outer face:
  Insulation on all outer boundaries
Run the Simulation
Create a Monitor for Average Temperature on the inside wall
Change the material in the middle between a metal, a wood and foam of your choice from the Discovery material library and make a table which includes, the name of the material, its thermal conductivity and with the average temperature on the inside wall.
Which is the best material for insulation?
Notes: The presented geometry is a small section of the wall of an house. The wall is made of 3 layers, an other one which is contact with Air at an outside temperature of 5 ° C, a middle layer which should provide insulation and an inner layer which is in contact with Air at a temperature of 25 ° C. As a measure of the insulation capability of our wall we can monitor the temperature on the inner wall surface. Follow the instruction on the slide and create the table as indicated.

## Slide 29: Exercise Solution: Improving Insulation
Material Name |  | Average on Inner Wall
Steel (S275) | 50.4 | 15.6
Wood (Maple) | 0.258 | 16.2
Phenolic Foam | 0.034 | 18.3
Material Name |  | 
Steel (S275) | 50.4 | 15.6
Wood (Maple) | 0.258 | 16.2
Phenolic Foam | 0.034 | 18.3
Best Insulation is given by the material with the lowest Thermal Conductivity
Notes: Following the instruction in the previous slide and as shown in the video, it is possible to see how the middle layer affect the temperature on the inside wall. Higher temperature on the inside wall is achieved by using materials with lower Thermal Conductivity. In this example a phenolic foam with a thermal conductivity of 0.034 lead to the highest average T on the inner wall (18.3 C)
Following the instruction in the previous slide and as shown in the video, it is possible to see how the middle layer affect the temperature on the inside wall. Higher temperature on the inside wall is achieved by using materials with lower Thermal Conductivity. In this example a phenolic foam with a thermal conductivity of 0.034 𝑊/𝑚·𝐾 lead to the highest average T on the inner wall (18.3 C)

## Slide 30: Further Information and Resources
  Ansys Academic | Simulation Software for Educators, Researchers and Students.
  Ansys Innovation Courses : Free to Access to courses covering a variety of physics and software.
  Ansys Education Resources: Specifically developed for Educators.
  Ansys Discovery Forum: Learn Discovery through video-tutorials.
  Ansys Learning Forum: Ask questions to the Ansys Community!
  Ansys Learning : Ansys YouTube Channel with dedicated video playlists.

## Slide 31
Acknowledgements
Janos Plocher, Madhumita Saravana Kumar , Mattia Montanari