## Slide 1
Lecture Unit
Structural Analysis of Beams with Ansys Discovery
Developed and curated by the Ansys Education Team
Madhumita Kumar, János Plocher
education@ansys.com

## Slide 2: Learning objectives for this Lecture Unit
Intended Learning Outcomes | 
Knowledge and Understanding | Knowledge and understanding of simple beam structural analysis
Skills and Abilities | Ability to use Ansys Discovery to set up a structural simulation
Values and Attitudes | Awareness of the importance of simulation in engineering design
Built-in Assessment
  Simulation exercises
  Quizzes
Resources
  Text: “Structural Analysis” – R. C. Hibbler
  Software: Ansys Discovery v22R1 (please note that all project files are available in the downloaded resource folder)
  Appendix Bonus Slides: Statically Determinate and Statically Indeterminate Structures
Further reading/information
  Ansys Academic
  Ansys Innovation Courses
  Ansys Education Resources
Notes: Learning Objectives
This lecture unit is aimed at teaching the fundamental concepts associated with simple beam structural analysis and consolidates their understanding by employing the easy-to-use finite element analysis software Ansys Discovery.
Through out this lecture unit, links will be present to relevant resources to supplement the learning, together with exercises and small quizzes to verify that the learning outcomes have been met.
Extra content has also been added through some bonus slides which are available after the end of the lecture unit.

## Slide 3: Accessing Ansys Discovery
Ansys Student: Free Student Software Downloads
Get Access to Discovery| Connect with us today
Students
Educators
Notes: If you have any questions on accessing Ansys Discovery please get in touch with the education team at education@ansys.com

## Slide 4: Outline of lecture unit
Structural Analysis Workflow
  Geometry: Beams
  Boundary Conditions
  Outputs
  Methods
Cantilever Beam Example
  Analytical Solution
  Simulation with Ansys Discovery
From the Ideal to the Real World
Summary
Exercise

## Slide 5: Structural Analysis Workflow
Pre-processing
Method of Solution
Post-processing
Geometry and Material
Validation
Structural Analysis is carried out in order to understand the behaviour of structures when forces are exerted on them.
Boundary conditions (e.g. supports, forces, etc.)
Geometry (e.g. shape, cross-sections, assemblies) and Material (e.g. steel, rubber, wood, etc.)
Analytical (i.e. finding the exact solution) or numerical (i.e. approximate the solution) methods
Sanity check (i.e.
do the results match the expectation, are the results plausible?)
Evaluation of outputs (e.g. displacement, stresses and strains)
Notes: Structural Analysis is carried out in order to understand the behaviour of structures when forces are exerted on them.
This structural analysis methodology can be summarised through the following steps:
The process starts off with designing the geometry and defining the material of our structure. In this lecture unit for example we will be focusing on beams.
Pre-processing involves defining the boundary conditions. These include loading conditions (like force, torsion, etc.) and supports (like fixed, hinged, etc.), and connecting mechanisms.
Once the geometry and loading conditions have been setup the appropriate method to solve the problem needs to be decided. This can be analytical also known as hand-calculation, which means the exact solution is found for the problem or numerical, such as the Finite Element Method which are approximate solution computed by computers. The selection of the method depends on the model complexity and the available resources. In this lecture unit both methods will be covered for a cantilever beam.
Once the problem has been solved, we move on to postprocessing. Here the required outputs like displacement, stress and strain can be gathered and evaluated.
The last but important step, which is too often forgotten, is to validate the resulting outputs and check if they make sense. For example, are the magnitude of the results in the expected range or are they too large or too small, does the analytical solution and numerical solution match?
As the wheel schema suggests, this process can be iterative and can take several cycles of repetition before the required end results are met. This can be very different and depend on design requirements, cost constraints, weight limitation, etc.

## Slide 6: Beams
Bicycle frame
Bridge
Crane
Geometry
Post
Validation
Method
Pre
Beams are structural elements that undergo tension, compression, bending and torsion.
Notes: As mentioned earlier, the focus of this lecture unit will be on beams.
Beams are structural elements that undergo lateral (to their axis) loading in the form of forces or moments causing them to experience tension, compression, bending and torsion.
Beam-like elements are present in all types of structures which can be observed in day-to-day life. Some of these can be seen in the picture of the slides such as, bicycle frames, bridges, cranes but also bookshelves, etc).
Each of these beam examples have a different type of loading. For example, a bicycle frame has loading only at specific areas of the frame whereas a bridge has a distributed load (due to vehicles, humans, etc.) through out its length.
In addition to geometry, it is important to define the material of the design. The impact of change of material will be discussed at a later stage in this lecture unit.
This loading is the first “input”, which we are going to explore as we progress through our structural analysis wheel now that we have identified our geometry of interest.

## Slide 7: Boundary Conditions: Common Loading Scenarios
Point Loads
Distributed Loads
Q [N/m]
Q [N/m]
Uniformly Distributed
Non-Uniform Distributed
Single Component
Multi Component
Design
Post
Validation
Method
Pre
Notes: 7
Loads and supports, which are going to explore in the next few slides, form an integral part of the boundary condition of a structural problem. There are different types of loading that a structure can undergo, with the most common type of loading being a force load. Force loads can be divided into two main categories:
Point Loads: These are loads applied at a specific point. These can be single component or multi component loads. In reality point loads do not exist, they are simply loads applied to an infinitesimally small area which can be approximated to a point. E.g. a person sitting on a bicycle could be approximated to a point load.
Distributed Loads: These are loads applied over a length or area. They can be uniform or non-uniformly distributed. E.g. cars on a bridge constitute a distributed loading condition.
Loading alone is not sufficient to the define a structural problem because without restricting the movement of the structure in some capacity, we would be looking at mechanism in motion (e.g. moving machines). Therefore something is required to restrict the motion of the structure which is subjected to load, this is known as a support.

## Slide 8: Boundary Conditions: Supports
Supports limit the degrees of freedom (DOF) of a structure. Beams have two types of DOFs viz., translation/displacement and rotation .
There are three common types of supports:
Fixed Support
Pinned/Hinged Support
Rolled Support
y
x
z
Design
Post
Validation
Method
Pre
Notes: 8
Supports limit the degree of freedom of a structure which means they remove the ability of an object to move in the 3d space. In this slide, three common types of supports along with their degrees of freedom have been described. If a degree of freedom is zero, it means that this type of motion is restricted.
There are three main kind of supports which are used in structural analysis:
Fixed support limits all displacements and rotations
Pinned support limits all displacement but allows rotation about the z-axis.
Rolled support limits translation perpendicular to the length of the beam

## Slide 9: Boundary Conditions: Common Support Scenarios
Supports are placed strategically at different locations of the design in order to restrict the degrees of freedom and rigid body motion. Common types of beams are:
Simply Supported Beam
Cantilever Beam
Fixed Beam
Can you think of any other real-world structure that represents one of these three types of beams?
Design
Post
Validation
Method
Pre
Notes: The supports presented earlier can be combined in different ways to fix a structure and limit its degrees of freedom. The total degrees of freedom (DOF) of a given structure must be <=0, otherwise the structure can undergo rigid body motion.
3 common type of support scenarios that are used in beams are:
Simply Supported: It has a hinged support on one end and a roller support on the other.
Cantilever: It has a fixed support on one end and the other end is free.
Fixed: It has fixed supports on both ends.
Note: Quiz question here is to engage students to think of real-world examples of beams and how they examples can be classified.

## Slide 10: Structural Problems: Postprocessing
The aim of a structural problem is to find the stress, strain and displacement in each point of the design. Some of these values at the boundary conditions are already known (for example, displacements are zero at the supports), while others are to be found.
Displacement () is a measure of the relative length of the movement in each point of our design.
Stress (σ) is the resistive force per unit area exerted by a body against deformation.
Strain (ε) is the ratio of change in dimension of the body to original dimension as a result of the force exerted on the body.
where,
 force acting on the body
 area over which force is exerted
where,
 change in length
 original length
Stress Analysis in Solid Mechanics | Ansys Innovation Courses, Strain in Deformation Analysis | Ansys Innovation Courses
δ
F
Design
Post
Validation
Method
Pre
Notes: 10
Having discussed the preprocessing stage in detail, it is important to understand the outputs that we are trying to find by solving the structural problem, before possible solution methods can be discussed.
Design and analysis of a structure is directly linked to its required performance. Stresses, strains and displacements represent key parameters, that engineers measure, in order to assess a structure’s integrity. Therefore, it is important to learn what stresses and strains and other key parameter related to them mean and how they can be represented mathematically.
  Displacement (𝛿) is a measure of the relative length of the movement in each point of our design.
  Stress (σ) is the resistive force per unit area exerted by a body against deformation.
  Strain (ε) is the ratio of change in dimension of the body to original dimension as a result of the force exerted on the body.
Note: Further information on stresses and strains can be obtained from the AIC courses linked in the page.

## Slide 11: Structural Problems: Relation between Stresses and Strains
In the elastic domain, stresses and strains are related by Hooke’s Law:
Young’s Modulus (E) represents the stiffness of the material and corresponds to the slope of the stress-strain curve in the elastic regime. The higher the modulus, the higher the resistance to deformation
(i.e. the lower the deflections).
Another key material property to consider is Yield Stress () which is the stress at which the material reaches plasticity for ductile materials or fracture for brittle materials. It is often used to represent the strength of a material and the stress at which our structure starts to fail.
Stress-strain curve
Intro to Material Elasticity - ANSYS Innovation Courses
Notes: 11
In the elastic domain, stresses and strains are related by Hooke’s Law.
In this equation the term E refers to Young’s Modulus which is a measure of the stiffness of the material and corresponds to the slope of the stress-strain curve in the elastic regime. The higher the modulus, the higher the resistance to deformation (i.e. the lower the deflections).
Another key material property to consider is Yield Stress which is the stress at which the material reaches plasticity for ductile materials or fracture for brittle materials. It is often used to represent the strength of a material and the stress at which a part fails (e.g. we do not want our book shelves to bend permanently). This point can be seen in the graph on the right when the curve stops being linear.
These properties along with others can be learned in more detail using the link to the Ansys innovation Course on Material Elasticity.
Now that we have discussed the desired outputs, it is time to learn about the methods of solving the problem.

## Slide 12: Methods for solving engineering problems
Analytical Methods
Different methodologies available
Used mainly for simple idealized cases
Time-consuming approach
Numerical Methods
Finite Element Method is predominant
Iterative algorithm suitable for computers
Fast solutions to complex problems
Experimental Methods
Prerequisite to many numerical simulations
Follows standardized test regimes
Time- and cost-consuming approach to data acquisition
Design
Post
Validation
Method
Pre
Notes: Now that we have defined the geometry, different input parameters like boundary conditions and the desired outputs, it is time to move onto solving the problem. Solving methods can be categorized into analytical and numerical.
Analytical solutions are exact and are often performed with hand calculations. Several methods are available in structural mechanics theory and will not be the object of this lecture unit. However, these exact solutions can only be found for simple idealized problems while for most engineering problems it would be problematic to be solved analytically because the models are too complex (for example from a geometrical perspective).
Numerical methods are simplified iterative algebraic equations that can be solved by a computer in order to obtain results. Finite Element Method is predominantly used in analyzing engineering problems as can be easily implemented in computers. In this lecture unit we will be using Ansys Discovery, which uses finite element methods to solve engineering problems.
Experimental methods are methods in which the design is manufactured in real life and tests are then carried out. These methods ae required in order to calibrate and validate simulation models at important phases of development. Experimental methods are generally standardized tests. They are time consuming and can often be very expensive to create and analyze.

## Slide 13: Cantilever Beam Exercise
Consider a solid cantilever beam (crane arm) made of structural steel with a square cross-section with a load of 50kN acting on its end.
Evaluate stresses and maximum displacement
Compare the analytical and simulation solutions
Use simulation to visualize stress and strain fields
Compare the influence of material properties and cross sectional geometry on the simulation outputs
4000 mm
50000 N
400 mm
400 mm
z
x
Design
Post
Validation
Method
Pre
Notes: 13
The discussed structural analysis process will now be applied to an engineering problem in order to see how different stages of the problem can be tackled.
This engineering problem involves designing a crane arm, make sure that stresses, strains and displacement are in the desired range and see if the design can be improved by changing material and cross-section.
The first step to discuss is to understand the geometry and the boundary conditions. A crane arm can be simplified to a cantilever beam with a point load acting on its end as shown in the picture.
We will first solve this problem analytically and then numerically using Ansys Discovery. We will then compare the solution to check if there are any differences between the outputs from the two methods.
Then will then study the influence of change in material and cross section on output parameters like stress and displacements.

## Slide 14: Cantilever Beam: Analytical Solution
δ
θ
F
L
x
Deflection:
where,
 Slope
 Deflection
 Flexural Rigidity
 Young’s Modulus
 Moment of area
 distance from the neutral axis
Slope:
Shear Force:
Max Stress:
Moment:
z
x
Booklet: Useful Approximate Solutions for standard problems | Ansys
Design
Post
Validation
Method
Pre
Notes: 14
First of all we will look at solving the problem analytically. Let us approach the problem step by step.
We know from structural mechanics theory (see standard handbooks on structural analysis and details on beam analysis) how the slope, deflection and max. stress for a cantilever beam is defined. Key parameters affecting the slope and deflection are the Young’s modulus E, and the and the moment of area I, which form the so called flexural rigidity. Generally, the max. deflection and slope is of interest, thus the maximum length L of the beam is considered for x.
Given the fact that this is a statically determinate structures (see bonus slides in teaching package), the shear force and bending moment can be determined. It is of note, that the former remains constant across the length of the beam, whereas the latter decreases to zero towards the tip of the beam.
The max. stress is additionally dependent on the beam dimensions, specifically the distance between the neutral axis and the top or bottom surface of the beam.
The actual values for those parameters will be determined in the following slide.

## Slide 15: Case study: Cantilever Beam Analytical Solution
Neutral axis
Design
Post
Validation
Method
Pre
Notes: 15
Given a beam made up of structural steel (E = 210 Gpa) as well as the dimensions and loads specified in the image, the key values of max. displacement (x=L) and max. stress can be calculated.
Depending on the beam cross-section, the definition for the moment of area changes. Here, the one for the solid quare cross-section is provided. Note, the moment of area around the y-axis is of interest here.
A small deflection of around 2 mm, with respect to the beam length, was determined. This is to be expected, as the stiffness of the material is fairly high. The max. stress equates to around 19 MPa.
For this simple geometry analytical solutions are feasible, however, if you think about real world structures in your environment, they commonly have more complex geometries, might be composed of multiple materials or experience more complex loads. Therefore, engineers are generally using FEA to rapidly obtain results for which no standard analytical solutions are present.
This simple example can be modelled in Ansys Discovery very easily and results can be obtained quickly, which will be illustrated next.

## Slide 16: Simulation Setup in Ansys Discovery
Geometry | Create the 2D sketch of the cross section | 
 | Extrude the cross section to the required length using the Pull tool | 
Supports | Define a fixed support at one end of the beam | 
Loads | Apply a load of 50kN to the face of the other end of the beam | 
Learning Solid Modeling with Ansys Discovery
Discovery: Tutorials -Ansys Discovery Forum
Design
Post
Validation
Method
Pre
Notes: 16
The table presents a quick guide to recreating the cantilever beam example in Ansys Discovery.
First the Geometry is created (use DESIGN Tab), then the BCs and loads are applied (use SIMULATION Tab). We will keep the standard structural steel as material.
[If you would like further guidance on solid modelling with Ansys Discovery, please follow the link attached in this slide.]
After setting up the model, just press solve (green icon in the bottom right corner) to run the simulation. On the right side you can choose to display different output variables.
Before we dive into the simulation output, let us take a moment to briefly look at what the software is doing after you press the run output.

## Slide 17: Numerical Solution: The Finite Element Method
This is a widely used method of numerically solving engineering problems by dividing the model into smaller elements and solving a set of algebraic equations for each of those elements.
Each geometry is divided into small elements which can have different shapes ranging from 2D (triangular, quadrilateral, etc.) to 3D (tetrahedral, hexahedral, etc.) elements through a process called discretization or meshing.
A set of algebraic equations are then solved for each of these elements in order to calculate reaction force, stress, strain, etc.
This is an iterative method where the accuracy of the results depends on the mesh quality, type of solution algorithm, etc.
Design
Post
Validation
Method
Pre
Notes: Ansys Discovery like many other structural software uses the finite element method to solve engineering problems. In this method the geometrical model is divided into smaller elements and set of algebraic equations are solved are solved for each of those elements.
Each geometry is divided into small elements which can have different shapes ranging from 2D (triangular, quadrilateral, etc.) to 3D (tetrahedral, hexahedral, etc.) elements through a process called discretization or meshing.
A set of algebraic equations are then solved for each of these elements in order to calculate reaction force, stress, strain, etc.
This is an iterative method where the accuracy of the results depends on the mesh quality, type of solution algorithm, etc.
It is important to note the results obtained from this method must always be validated as this is an approximation method that have dependencies on the mesh, the types of contacts between different components, etc. When the solution does not appear realistic a sanity check needs to be carried out from the input to the output stage.
In the context of analyzing outputs from FEAs, the next slide illustrates how state variables are displayed in Ansys Discovery.

## Slide 18: Visualise Outputs in Ansys Discovery: Displacements and Strains
Design
Post
Validation
Method
Pre
Notes: 18
This GIF provides a brief demonstration of how to navigate within the output window of Ansys Discovery after pressing the solve button. It showcases how the default output variable displacement and how it can be changed strain. We can observe however that max displacement is approximately 2mm and strains also strains are very small (10^-5 order).
Also we can clearly see a difference between displacement and strains. While the displacement is higher at the unsupported end of the beam, strains are higher at the fixed support where also stresses are larger. Recalling our slide on material properties, stresses and strains increase proportionally in the elastic range. We look at a distribution of the former in the next two slides.
Besides displacements and strain, stresses can also be readily displayed in Ansys Discovery. In contrast to analytical solutions, FEA visualises the values of the state variables across the hole domain, which makes is much easier and faster to assess the engineering problem. Let’s look at how the normal and shear stresses in the cantilever beam for instance, as will be shown in the next slide.

## Slide 19: Visualise Outputs in Ansys Discovery: Stresses
Solid Cantilever Beam
z
x
neutral axis
A-A
y
x
A
A
A-A
y
x
z
x
A
A
Stress Analysis in Solid Mechanics - ANSYS Innovation Courses
max
min
0
Design
Post
Validation
Method
Pre
Notes: 19
This GIF provides a brief demonstration of how to simulation outputs in Ansys Discovery. It showcases in particular the visualisation of stresses across different directions.
This plane-stress view (zx-plane) of the solid cantilever beam in bending explains the stresses in x-direction both schematically as well as numerically, i.e. as obtained from the simulation. This stress distribution is of particularly interest because it is the one of highest magnitude in a beam.
From this distribution, It can be highlighted, that the stresses at the neutral axis are zero, whereas tensile stresses are increasing in positive z direction from the neutral axis. Vice versa, in negative z direction compressive stresses increase with growing distance from the neutral axis.
It must be noted that the stress magnitude reduces the larger the distance from the fixed boundary where the highest stresses are found.
Plane stress plots of the AA cross-section (yx-plane) are also displayed, highlighting the edge-effect of stresses.
Note: A Link to the stress analysis Ansys innovation course is available for further exploration of this topic.
Normal stresses present in x, y and z direction and bending loads generally cause shear stresses as well, which can all be easily selected and displayed in Ansys Discovery. This is one of the great advantages of simulation software, as determining those values analytically would be extremely more time consuming.
Recalling our initial cantilever beam example for which we have determined the stress in x-direction and the maximum deflections analytically, the question now is, how do the results from FE simulation, with e.g. Ansys Discovery, compare with those? We will find out in the next side!

## Slide 20: Comparison of Analytical and Simulation Results
Results | Analytical | Simulation (GPU Mode)
Max. Deflection | 2.38 mm | 2.36 mm
Max. Stress | 18.75 MPa | 19.41 MPa
Design
Post
Validation
Method
Pre
Notes: 20
As you can notice, the max. deflection and stresses between the two methods is very close. This is achieved even when using the fast explorer mode running on the GPU available in Ansys Discovery.
It is important to notice that we have analytically determined the stress in x-direction; thus, it is critical the right output selected and displayed in our simulation.
Please note that the results presented are created using a fidelity of 13.6mm in Ansys Discovery. Depending on the capabilities of your computer beware that the default fidelity value might vary, which may cause a slight deviations in the results presented here.
In FE analysis the accuracy of results depends on the fidelity of the explore mode. This will provide a fast approximate solution, while if want to achieve high fidelity we should use the refine mode in Ansys Discovery.
Something that our analytical solutions does not provide, but that the FEA allows is the visualisation of state variables such as stress distribution across the beam faces (or internally if you were to cut specimen which you can also do in Ansys Discovery), strains and displacements.
A fair question at this point is, should we look at all the 9 stress components? Unfortunately, the answer is yes, to assess the effective stress on a structure, the entire stress state needs to be considered. However, we can use equivalent or von Mises stress to include all of those components to assess the effective stress on a structure. In the next slide we would like to elaborate briefly on this parameter.

## Slide 21: Visualise Outputs in Ansys Discovery: Von Mises
z
x
neutral axis
A-A
y
x
max
min
z
x
y
A-A
neutral axis
y
x
Design
Post
Validation
Method
Pre
Notes: 21
Here, the analysis of von Mises Stresses in Ansys Discovery shall be discussed. The von Mises stress presents an equivalent stress value for a complex stress conditions. Conveniently it reduces the 9 stress components into one single scalar value, which is generally being employed to predict the onset of yielding of a material.
This concept, allows for easy assessment on whether a material has failed or is still intact when experiencing certain stresses. Ansys Discovery calculates and displays you the von Mises stress as one of the default outputs, as show in the GIF.
This slide it also shown showcases von Mises stress distribution in the x-z and x-y planes (planes perpendicular to the cross-section).
Min./zero stress values are highlighted in blue and are to be found at the tip of the cantilever beam, whereas max. stress are located at the faces and close to the fixed boundary face, as highlighted in red. This can be observed in the A-A cross-section view.
It can be observed that the maximum stresses are located on the top and bottom surface close to the fixed surface.
Min. stresses are found at the tip of the beam as well as along the neutral axis.
It is of note, that the stress distribution in the cross-section is non-uniform, as the elements at the edges are less constraint as those in the centre, causing a different stress state.
Why is the von Mises stress such an important parameter von engineers? Well, it is also used to determine the safety factor of a structure. What this factor is will be discussed in the next slide.

## Slide 22: Introducing the Safety Factor
The safety factor (SF) is a measure of reliability of a design. It is the ratio between a structure’s strength (usually characterised as yield strength ) and the maximum stress found in the part ():
Is the SF of an automotive part identical to that of a toy?
Would you design an aircraft and a spacecraft with the same SF? Explain why or why not.
Change Geometry (e.g. Change Cross-section)
Change Material
Is the Safety Factor too high or too low?
Design
Post
Validation
Method
Pre
Notes: 22
The Safety factor determines the reliability of a design by relating the max von Mises stress to the yield strength of the material. It is an important reference for the design process, as structures must generally adhere to certain standards and regulations. A safety factor of 1 would mean a structure just about handles a load without failure, whereas a value below 1 result in failure under a given allowable load. Consequently, engineers often use the margin of safety as an alternative to SF. The SF or is dependent on how critical a part is. For instance, if it associated with risk for the life of people like in bridge constructions or aeronautical components, the SF can take values between 2-4. Likewise, the risk assessment takes into account the financial loss as a result of part failure.
We can display the safety factor as output of our Discovery simulation, by using the monitor button in the bottom right.
Quiz
Automotive parts a generally safety critical components that must ensure the safety of the passengers during a crash. From experience we know that toys on the other hand frequently fail (low lifetime).
Open discussion question: For spacecraft weight considerations are crucial and optimised to a maximum (potentially lower SF). An aircraft is in service for a long time and is critical in the safety for numerous passengers (potentially higher SF). What other considerations could students think of that might drive an engineer's decision on whether a SF is high enough or critical?
With reference to Q1, it might be obvious that the safety factors automotive components are generally very different from those of toys. The former commonly employs metallic parts for the main chassis whereas toys are often made from plastics. Having a safety factor which is too high may be an indication of a non-optimal design while having a safety factor too low relates to an unsafe design. This leads us to the question, what to do if we are not satisfied with the safety factor in our design?
If we consider that we cannot modify the external loads we can act on two aspects: either change the geometry (to either reduce stresses or save material) or change the material (for example by choosing a stronger material or a weaker one which is however cheaper).

## Slide 23: Impact of Material Properties on Simulation Outputs
Stresses, Displacements and Safety Factors as Function of Materials
Solid (Square Cross-Section) Cantilever Beam
Steel
Copper
Balsa Wood
Displacement
von Mises Stress
z
x
z
z
x
z
x
z
1
z
x
y
Intro to Material Performance - ANSYS Innovation Courses
Design
Post
Validation
Method
Pre
Notes: As an example of this we will look at our cantilever beam problem and we will see how two additional materials, namely copper and balsa wood will affect our output parameters, von Mises stress and Displacement.
The max von Mises stress and corresponding material yield stresses are detailed for the 3 materials (Note: log scale). It can be observed that a solid cantilever beam comprised of balsa wood would yield a SF < 1. Thus, it would lead to failure under service load. Together with the graph of max. displacement, highlighting a significant flexibility compared to copper and steel, it can be deduced, that balsa wood can be ruled out as a suitable material for a crane.
The schematic illustrations of the crane are reflective of the FEAs qualitatively.
Note: Further information on material performance can be obtained from the link to the AIC course.
Now, the material is not the only aspect affecting the bending performance. Many structures in our daily life use beam structures as showcased in the initial slides, but not all of them are square-shaped or solid. Thus, next the effect of cross-section geometries of beams shall be discussed.

## Slide 24: Impact of Cross Section on Simulation Outputs
Note: The safety factor decreases with a reduction in mass (solid versus hollow beam) but increases with a greater second moment of area (effect of geometry). If a beam is not loaded along its axis of symmetry (C-beam) it experiences torsion
Safety Factor as Function of Cross-Section Profile
Solid (Square Cross-Section) Cantilever Beam
Solid Beam
Hollow Beam
Solid Cylindrical Beam
Hollow Cylindrical Beam
I-Beam
C-Beam
A
A
A-A
400 mm
z
x
z
y
z
y
z
y
4000 mm
z
y
Level 3 Industrial Case Study: Material Properties and Structural Sections
400 mm
80 mm
50000 N
1
A Non-Slender Cantilever Beam under Point Tip Loading
Design
Post
Validation
Method
Pre
Notes: Taking the original cantilever beam made of steel, we will now proceed to assess and the effect of the geometry Six different cross-sections are analyzed (please note that project files are available for all of these).
Recalling the analytical solution, we know that the moment of area affects the stresses and deflections.
Similar to the example demoed before, Ansys Discovery can help to quickly find the performance of those cross-sections to compare their safety factors. Based on the findings, engineers can make informed decisions as to whether the dimensions and materials are appropriate or whether the beam is ’over-engineered’, as is the case here.
As shown in the graph on the right, we observe a performance drop when using a hollow instead of a solid beam structure. Likewise, it can be observed that I-beams that are generally used in construction are in fact having a high safety factor while using little material. If one was to divide the bending stiffness of the beams by the mass (specific stiffness), the I-beams would outperform all other designs.
Also important to note is that structures that are asymmetric with respect to the loading direction (see C-beam), experience torsion.
Note: For a detailed analysis of different beam cross-sections and materials, the case study linked in this slide is highly recommended.
Recalling the original crane example, it is obvious that this cantilever beam example is a significant simplification. This was necessary to be able to provide a analytical solution with ease, however, FEA is capable of solving much more complex problems including a realistic replication of a real crane design. The aspect that would need to be considered for such a model will be discussed next.

## Slide 25: From the Ideal to the Real World: Crane Example
Displacement
von Mises Stress
Boundary conditions:
Fixed support vs. bolted contacts?
Loading:
Loading direction and force application?
Geometry:
Solid vs. hollow beams?
Cross-section?
Material:
Stiffness and strength?
Density?
Analysis:
Safety factor?
Model quality?
Modeling the bolt and preload
Connecting Bolts with the Rest of an Assembly
Design
Post
Validation
Method
Pre
Notes: Engineering problems can be very complex, making the analytical solution very impractical. Taking a realistic replication of a real crane design, there are several other factors that need to be taken into consideration, some of which are:
Geometric complexities: Geometries rarely have a simple shape of form. There are made of parts connected by components like bolts, screws, rivets, weld lines, etc. Each of these parts and small components influence the behavior of the model
Complex loading: Loads almost never have a single concentration point. They can be multiple and be applied over different areas of the components, very often in a non-uniform manner.
Multi-body simulation: Engineering problems usually involve a large numbers of bodies moving together. The motion of each body has an influence and is influenced by the other parts connected to it.
While simulation software give us tools to model all these complexities it is the role of modern engineers to evaluate the level of complexity to include in each model and the assumptions made. For example, in the shown Ansys Discovery model, only the crane arm is analyzed, and components are considered as welded instead of screwed together (i.e. single body or permanently bonded contacts can be assumed).

## Slide 26: Summary
Pre-Processing
Geometry
&
Material
Post-Processing
Method
of
Solution
Validation
z
x
y
Fixed support DOF=0
Load
x
y
Analytical Solution
Displacement
Von Mises Stress
z
x
y
Numerical Solution (FEA)
Sanity check i.e.
do the results match the expectation,? Do I need to refine my model?
Boundary Conditions
Materials
Notes: To summarize what we have seen in this lecture unit, when dealing with structural problems we can follow this process.
First the geometry & inputs are defined
  Level of abstraction: How detailed should the real structure be replicated? What level of detail is necessary?
  Set-Up: What are the boundary conditions and loads that replicate the real-world problem most accurately? How much can the actual conditions be simplified?
  Material properties: What shall be the material of the structure? In case of second iteration – Was the safety factor obtained (output) sufficient for the initially selected material?
Subsequently, engineers must select between the solution methods. The method for finding a solution to a problem can be analytical or numerical. In most real-world structures, FEA is used as the derivation of analytical solution is difficult and time consuming. In Finite element analysis, the problem is solved numerically in an iterative fashion. Geometry must be discretized into finite elements (the higher the mesh resolution, the better the result, but the higher the computational cost). Every element is governed by a set of algebraic equations, yielding stresses and strains.
FEA can give in addition to numerical results, a visualization of the outputs can help better understand the distribution of important state variables such as displacements, strains and stresses.
These output should then be evaluated for example by comparing two solutions, or by looking at Mesh-refinement in FEA - Is the mesh-resolution fine enough to provide consistent results? Is a re-run of the analysis required?  Recall, this has to do with the model fidelity. In Ansys Discovery the fidelity can be altered within the slider on the bottom of the Explore or Refine mode. Generally, the refine mode will provide you with more accurate results at the expense of more computational time.
Finally, this lecture unit on analysis of beams shall be concluded with a brief exercise using Ansys Discovery  see next slide

## Slide 27: Exercise
With Ansys Discovery:
  Model the geometry of a circular beam of length 1m with fixed supports and a distributed load of 20kN on its surface
  Compare the results of Steel vs. Aluminium
100 mm
20 kN/m
Design
Post
Validation
Method
Pre
Notes: This exercise is aimed at familiarizing students with the use of FEA, its set-up (geometry and inputs) and the navigation between different output parameters and their validation.
Notes: Results are provided in the next slide and the model is provided with the lecture unit (in case of limited time of CAD knowledge).

## Slide 28: Solution: Ansys Discovery Results
Material | Max. Deflection | Max. Stress
Structural Steel, S275N | 2.4 mm | 104 MPa
Aluminium alloy wrought, T6 (6061) | 7.3 mm | 104 MPa
Design
Post
Validation
Method
Pre
Notes: Here, we present the solution for the aforementioned exercise.
Note: Open-discussion
Is steel or aluminum better suited for this purpose? – Consider additional aspects: cost, weight, safety factor, thermal properties
Besides safety factor some applications require a safety factor of deformation, which could rule out aluminum as a viable option in this example.

## Slide 29: Further Information and Resources
  Ansys Academic | Simulation Software for Educators, Researchers and Students.
  Ansys Innovation Courses : Free to Access to courses covering a variety of physics and software.
  Ansys Education Resources: Specifically developed for Educators.
  Ansys Discovery Forum: Learn Discovery through video-tutorials.
  Ansys Learning Forum: Ask questions to the Ansys Community!
  Ansys Learning : Ansys YouTube Channel with dedicated video playlists.

## Slide 31
Bonus Slides
Statically Determinate and Statically Indeterminate Structures
P
L
B
L
A
C
P

## Slide 32: Structural Analysis: Statically Determinate Structures
A structure is said to be statically determinate if the support reactions can be determined from the equations of equilibrium.
The equations of equilibrium in 2D are as follows:
Reaction forces in the supports are defined as follows:
where,
 force acting in the x-direction
 force acting in the y-direction
moment acting about the z-direction
y
x
z
Notes: There are different methods of determining the reaction forces at the supports of a beam. The easiest way to do this is by using the equations of equilibrium.
This method is not always possible as sometimes there are several unknown variables. When the support reactions of the structures can be determined from the equations of equilibrium, the structure is known to be statically determinate. When the number of unknowns is higher than the number of equations then the structure is known to be statically indeterminate.
In 2D, there are 3 equation of equilibrium as shown in the slide.
The reaction forces in three types of supports we discussed earlier has been shown in this slide:
Roller support: Reaction force in Y-direction
Hinged support: Reaction forces in the X- and Y-directions
Fixed support: Reaction forces in the X- and Y-directions and moment about the Z-axis

## Slide 33: Structural Analysis: Statically Determinate Structures
P
P
P
L
L/2
L/2
A
B
P
L
L
These structures are statically determinate because their support reactions can be determined from the equilibrium equations.
Notes: Using the equations of equilibrium, one can find algebraic equations of the unknown support reactions, these can be used to solve for the support reactions.
The slide shoes how the unknown support reactions of the beams were determined simply from the equations of equilibrium, so it can be concluded that these beams are statically determinate.

## Slide 34: Structural Analysis: Statically Indeterminate Structures
P
P
L
L/2
L/2
B
L
A
C
P
P
L/2
L/2
Since there are 3 equations and 4 unknowns, the support reactions cannot be determined from the equations of equilibrium. Such structures are statically indeterminate.
Notes: The slide shoes how the unknown support reactions cannot be determined from the equations of equilibrium as there are 4 unknowns but only 3 equations, so it can be concluded that this beam is statically indeterminate.
Since this structure is statically indeterminate, other methods need to be employed to determine the support reaction and other output variables like stress and strain.

## Slide 35: Quiz: Statically (In-)determinate?
A
L
Q [N/m]
P
L
L
A
B
c
Q [N/m]
Problem 1
Problem 2
Notes: Determine if the above structures are statically determinate or indeterminate.
Quiz answer:
Problem 1: determinate
Problem 2: indeterminate
The solutions can be found on the next slide.

## Slide 36: Quiz: Solution
A
L
Q [N/m]
P
L
L
A
B
c
Q [N/m]
Q*L
L/2
L/2
P
L/2
L/2
Q*L
L/2
L/2
Too many unknowns, solution cannot be determined
Notes: First the free body diagram is created. In case of distributed loads, the load acting over the given length of the beam can be simplified to an equivalent point load acting at the center of its distribution.
Problem1: The solution to the reaction forces are shown on the slide. Hence the beam is statically determinate
Problem2: The solution cannot be determined as there are more unknowns than the number of equations. Hence the beam is statically indeterminate.