## Slide 1
Greenhouse Geometry
Creation Tutorial
Alfred Oti
Ansys Academic Development Team
Notes: The 25 PowerPoint Lecture Units For 2021
The Lecture Units developed for teaching in connection with Granta EduPack are listed at the end of this presentation.

## Slide 2: Greenhouse tutorial
Hi and welcome to this tutorial. You will create a greenhouse in Ansys Discovery.
Build duration 45- 60 mins
We will take you through every step of the process let’s begin!

## Slide 3: Step 1: Basic Sketch – Front of Greenhouse
Click on the Plan View icon to see a flat sketch grid
Use the Rectangle tool to draw a box 90” x 90” (2286mm x 2286mm)
Use the Construction Line tool to draw a line vertically in the center of the square.
Right-click on the line and choose Set as Mirror Line from the menu
Draw a second vertical Construction Line 54” (1371.6mm)
Draw a third Construction Line perpendicular to the second
Use the Line tool to draw a diagonal line between the construction lines.

## Slide 4: Step 2: Basic Sketch – Front of Greenhouse
Use the Trim Away tool to erase all lines until an A-frame remains. (Remember to trim the bottom line along the red x-axis).
Hold the Ctrl key and select all the lines

## Slide 5: Step 3: Basic Sketch – Front of Greenhouse
Use the Offset Curve tool to draw a new line
Type 3” (76mm) as the offset distance
Use the Line tool to close the gaps between both lines at the bottom of the fames
Click on Return to 3D, to turn the sketch into a surface

## Slide 6: Step 4: Greenhouse Frame
Use the Pull tool to extrude the surface into a solid
Type 7.2” (184mm) as the extrude distance

## Slide 7: Step 5: Greenhouse Frame
Click on the Move tool and hold the Ctrl key to make a copy of the frame
Type 24” (609.6mm) as the copy distance
Repeat steps a to b until there are 7 frames each 24” apart

## Slide 8: Step 6: Greenhouse Frame
Use the Rectangle tool to draw a 7.2” (184mm) x 3” (76mm) box directly onto the bottom of the inner face of the leftmost frame
Use the Pull tool to extrude the box to the opposite side of the frame
Repeat steps a to b with the right most frame

## Slide 9: Step 7: Greenhouse Frame
Use the Rectangle tool to draw a 7.2” (184mm) x 3” (76mm) box directly onto the bottom far corner of the rightmost frame
Click on the Pull tool to extrude the box through (the other frames) to the rightmost frame

## Slide 10: Step 8: Greenhouse Frame
Select one of the inner diagonal faces of the rightmost frame
Click on the Sketch icon then Click on the Plan View icon to see a flat sketch grid
Use the Construction Line tool to draw a line vertically in the center of the square.
Right-click on the line and choose Set as Mirror Line from the menu
Use the Line tool to draw 3.7” (92mm) lines on both sides of the outer corners
Draw the shapes as pictured. Make sure the shapes are closed with no gaps
Click on Return to 3D. Then Select one of the shapes

## Slide 11: Step 9: Greenhouse Frame
Click on the Pull tool (see step 6) to extrude the shape through (the other frames) to the leftmost frame
Repeat steps a to b with the other shapes

## Slide 12: Step 10: Greenhouse Door Sketch
Click on the Plan View icon to see a flat sketch grid
Use the Line tool to draw a line vertically in the center of the square.
Right-click on the line and choose Set as Mirror Line from the menu
Use the Line tool to draw the sketch pictured on the right (with no gaps)
For the outer windows, use the Construction Line tool to draw a horizontal line 22.5” (571.5mm) line from the outermost edges. Then draw a perpendicular vertical line 53.5” (1359.39mm) from the bottom edge
For the doors, use the Construction Line tool to draw a vertical line 68.8” (1570.71mm) from the bottom edge
For the top window, use the Construction Line tool to draw a vertical line 80” (1932.99mm) from the bottom edge
Use the Line and Offset tools to draw the sketch pictured on the right. All parallel lines are 3” (76mm) apart.
Click on Return to 3D, to turn the sketch into a surface

## Slide 13: Step 11: Greenhouse Door Frame
Select the surface. Click on the Move tool and hold the Ctrl key to make a copy of the surface
Type 151.2” (3841.6mm) as the copy distance

## Slide 14: Step 12: Greenhouse Door Frame
Select the inner frame
Use the Pull tool to extrude the inner frame into a solid
Type 7.2” (184mm) as the extrude distance
Repeat steps a to c with the opposite inner frame
In the Model Tree right-click on the Solid icon from the menu click on Move to New Component. A new component will appear in the tree. (This will separate the greenhouse frame from the windows and door which will be made later).

## Slide 15: Step 13 : Greenhouse Doors and Windows
Click on the Move tool.
Type 3.7” (92mm) as the translate distance
Use the Pull tool to extrude the windows and doors into solids. From the right-side Heads-Up Display click on Pull both Sides
Type 1.5” (40mm) as the extrude distance
Repeat steps a to d with the opposite windows and doors

## Slide 16: Step 15: Greenhouse Side Windows
Hold the Ctrl key to select the edges of the side windows. (Edges will be highlighted in yellow)
Use the Fill tool to create surfaces
Hold the Ctrl key Select the surfaces
Click on the Move tool.
Type 1.5” (38mm) as the translate distance
Use the Pull tool to extrude the windows into solids. From the right-side Heads-Up Display click on Pull both Sides
Type 1.5” (40mm) as the extrude distance
Repeat steps a to g with the opposite windows

## Slide 17: Step 16: Greenhouse Floor
Hold the Ctrl key to select the edges of the floor. (Edges will be highlighted in yellow)
Use the Fill tool to create a surface
Click on the Move tool.
Type 1.5” (38mm) as the translate distance
Use the Pull tool to extrude the windows into solids. From the right-side Heads-Up Display click on Pull both Sides
Type 1.5” (40mm) as the extrude distance

## Slide 18: Step 17: Greenhouse Roof Windows
Select the inner face of the rightmost frame
Click on the Sketch icon then Click on the Plan View icon to see a flat sketch grid

## Slide 19: Step 18: Greenhouse Roof Windows Sketch
Use the Construction Line tool to draw a line vertically in the center of the square.
Right-click on the line and choose Set as Mirror Line from the menu
Use the Line, Offset and Trim tools to draw the shape pictured (make sure there are no gaps). The long diagonal lines are 1.5” (40mm) apart
Click on Return to 3D, to turn the sketch into a surface

## Slide 20: Step 19: Greenhouse Roof Windows Sketch
Select the surface
Use the Pull tool to extrude the roof window surface into a solid. Extrude the solid halfway across the gap
From the left-side Heads-Up Display click on Pull Up to
Then click on the inner face on the opposite side of the gap
Repeat steps 18 to 19 for the remaining roof windows

## Slide 21: Step 20: Final Greenhouse
Congratulations you have completed the greenhouse.
Your model is ready for simulation.

## Slide 22: Bonus Design Challenge
Using the steps of this tutorial build the variations of the greenhouse pictured below. Perform simulation and see how the results vary.