## Slide 1
Greenhouse Geometry
Creation Tutorial
Alfred Oti
Ansys Academic Development Team
Notes: The 25 PowerPoint Lecture Units For 2021
The Lecture Units developed for teaching in connection with Granta EduPack are listed at the end of this presentation.

## Slide 2: Project General Info
Parametric Studio : Chris Whitmer whitmer@parametricstudioinc.com
Ansys: Nick Stefani, Alfred Oti
Objective:
  Create a resource in Ansys Discovery from which data can be extracted and imported into parametric studio.
  Proof of concept to show what we can bring to introductory courses ( in future work with academics to create their examples)
Philosophy: Use visualisation and gamification to engage students and enhance understanding of underlying physics
Target audience: final year high school, college freshman
Learning outcomes:
  Understand basic underlying physics
  Appreciate importance of simulation
  Learn how to perform basic simulations
Deadline: late September/October 2022 content ready to engage with educators and test in spring semester

## Slide 3: Case Study Details
Example Chosen: Greenhouse
Physics Modelled: Thermal and Structural Analysis
Objective: Monitor the air temperature inside the greenhouse to assure that plants do not perish during the night and evaluate the structural integrity of the structure.
Case Study Sections (Tutorials)
  Geometry Creation
  Daytime Simulation: Check Internal average Temperature during day
  Night-time Simulation:
    Use the found day temperature and Check the Internal average Temperature during the Night
    Is overnight heating needed? How much?
  Structural Simulation:
    Calculate and apply snow loads
    Calculate and apply wind loads
    Can the design be improved?

## Slide 4
Geometry

## Slide 5: New Greenhouse Design
Maximum height 2.28m
Minimum height 1.4m
Length 3.8m
Glass thickness 40mm
Frame: Wood (Pine)
Panels: Glass

## Slide 6
Greenhouse Daytime Thermal Simulation

## Slide 7: Objective and Assumptions
Objective: calculate the equilibrium average temperature of the air in the greenhouse.
Physics Assumptions:
  Ansys Discovery cannot model radiation from the sun, thus as an approximation it is considered that heat flux that the ground/floor of the greenhouse sees, absorbs and releases correspond to the total released heat within the greenhouse coming from the sun.
  In reality, heat is also absorbed and released by the air, the frame, the windows and other things such as the blackbody radiation of hot objects in the greenhouse, however this has been neglected for simplicity.
  Following these assumptions, it can be computed a simple approximation of heating irradiance flux (W/m^2), light view angle, and the transmission/reflection reductions expected for this solar flux. This number would be a crude approximation of the heat that is absorbed to heat the greenhouse as the rest is reflected away either at the window or off the ground and leaves the control volume.
Data Assumptions:
  Location: Ames, IA USA
  Irradiance values assumes surfaces are normal to the incoming light’s direction.
  Time: November
  Average Outside Temperature (daytime): 9 C
November Typical Daylight Avg (2011-2021) | 139.75 | Glass 1/16 | Double Pane Glass | Acrylic (Plexiglass)
Values are in W/m2 |  | 0.9 | 0.83 | 0.79
50% Concrete/Crushed Rock | 0.375 | 78.609375 | 72.4953125 | 69.0015625
50% Moist Soil | 0.2 | 100.62 | 92.794 | 88.322
50% Black Rubber/Paint | 0.15 | 106.90875 | 98.593625 | 93.842125
50% White Paint /High reflective | 0.55 | 56.59875 | 52.196625 | 49.681125

## Slide 8: Daytime Simulation Boundary Conditions
Plastic, Acrylic [Window Panels]
Wood Pine, [Frame]
Air (Gas) Fluid Inside the greenhouse
Activate Gravity to simulate natural convection of Air in the greenhouse
Convection heat transfer on all external surfaces (Frame and Panels) with outside temperature of 9 ◦C
Initial temperature of Air (same as outside)
Ground releasing heat (49 W/m2)

## Slide 9: Video of the Set up

## Slide 10: Daytime Simulation Results
The equilibrium average temperature reached during the day is 22.2 ◦C

## Slide 11
Night Set-up

## Slide 12: Objective and Assumptions
Objective: calculate the average temperature of the night in the greenhouse.
Data Assumptions:
  Location: Ames, IA USA
  Time of the year: November
  Average Outside Temperature (Night-time): -1 C
  Initial Air temperature in the greenhouse : 20 C (Slightly lower than average day temperature)
  Constant Ground temperature: 12 C, given by the average between 20 C of the day temperature and 4 C of the soil temperature (at 4 inches depth)
Daytime temperature monitor
Average 4 inch Depth Soil Temperature in IOWA

## Slide 13: Boundary Conditions Set up – Night Simulation
Plastic, Acrylic [Window Panels]
Wood Pine, [Frame]
Air (Gas) Fluid Inside the greenhouse
Activate Gravity to simulate natural convection of Air in the greenhouse (-Y as per Global Axis)
Convection heat transfer on all external surfaces (Frame and Panels) with outside temperature of – 1 C
Initial temperature of Air
Ground not moving at steady temperature of 12 C

## Slide 14: Video of the Set up

## Slide 15: Night Simulation Results
The average temperature reached during the night is 4.35 ◦C

## Slide 16
Adding Heating during the night

## Slide 17
Introduction, Objective and Assumptions
Introduction: The night simulation has shown an equilibrium average night temperature of 4.35 degrees which is too low and could harm the plants.
Objective: How much heating (in W) is required overnight to maintain temperature above 12 C?
Data Assumptions:
  Location: Ames, IA USA
  Time of the year: November
  Average Outside Temperature (Night-time): -1 C
  Initial Air temperature in the greenhouse : 20 C (Slightly lower than average day temperature)
  Constant Ground temperature: 12 C, given by the average between 20 C of the day temperature and 4 C of the soil temperature (at 4 inches depth)
  Heater dimensions: 0.495m*0.495m*0.1m (position as per geometry)

## Slide 18: Boundary Conditions Set up – Night Simulation with heating
Plastic, Acrylic [Window Panels]
Wood Pine, [Frame]
Air (Gas) Fluid Inside the greenhouse
Activate Gravity to simulate natural convection of Air in the greenhouse (-Y as per Global Axis)
Convection heat transfer on all external surfaces (Frame and Panels) with outside temperature of – 1 °C
Heater 10 W (Parametrize value)
Ground not moving at steady temperature of 12 °C
Initial temperature of Air

## Slide 19: Video of the Set up

## Slide 20: Night Simulation with heating Results
An heating source providing 400+ W is needed to maintain an internal temperature above 12 °C during the night

## Slide 21
Structural Simulation

## Slide 22
Introduction, Objective and Assumptions
Objective: Understand if the greenhouse can withstand snow, ice and wind load
Data Assumptions:
  Location: Ames, IA USA
  Snow Load: Maximum layer of snow that can accumulate on the surface is 0.5 m which covering a roof surface of 11.2 m2, result in 5.6 m3. As snow weights approximately 50kg per cube meter, the total load on the structure is 280 KG which can be approximated to 3kN.
  Ice Load: Maximum layer of ice that can accumulate on the surface is 0.1 m which covering a roof surface of 11.2 m2, result in 1.12 m3. As ice weights approximately 920kg per cube meter, the total load on the structure is 1030 KG which can be approximated to 10kN. Given the fact that snow and ice load are on the same surface, only ice load will be simulated as this is the worst case scenario.
  Wind Load: Assuming a wind force of 35 m/s, representing gusts of 80 mph not unusual for the area, and Lateral Area of 10.9 m2 the wind force acting on the side of the greenhouse can be calculated with the equation:
      Fw = 1/2 ρ v2 A
      where
        Fw = wind force (N)
        A = surface area (m2)
        ρ = density of air (kg/m3)
        v = wind speed (m/s)
      F=0.5*1.12*(35^2)*10.9=7477-> 7.4kN
3.7 KN
3.7 KN
5 KN
Gravity
5 KN

## Slide 23: Boundary Conditions Set up – Structural Simulation
Plastic, Acrylic [Window panels]
Wood, Pine [Frame]
Activate Gravity to simulate natural density of Air outside the greenhouse (-Y as per Global Axis)
Distributed Force 3 Wind load 5 kN [right side wall only]
Distributed Force 4 Ice and Wind load 5 kN [left side wall and left side roof only]
Distributed Force 5 Ice load 5 kN [right side of the roof only]
Fixed Support [Ground not moving]

## Slide 24: Video Set up

## Slide 25: Wind and Snow Load Results
Structure is very safe
Some optimisation could be performed to reduce cost and environmental impact of the greenhouse
For example it is possible to choose less strong but cheaper material and/or reduce the thickness of the panels and the frame
In Ansys Discovery it is possible to easily compare how changing material can affect the safety of the structure and also parametrise the thickness of panels and frame and solve back to back simulation to test multiple design solutions.
(Recommended max fidelity)

## Slide 26: Choosing Cheaper Material and Making Smaller Panels
Parametrisation of the Side Panels and Frame
Changing from Pine Wood to Chipboard wood