## Slide 1
Lecture Unit
Introduction to Audio Digital Signal Processing with Ansys Sound
Alexandre Boutheon, Ansys R&D
Edited by Madhumita Saravana Kumar, Ansys Academic Development Team
education@ansys.com
Notes: Learning Objectives
This lecture unit aims at introducing elementary notions of Audio Digital Signal Processing and illustrate the theory with the help of the Ansys’ “Sound Analysis & Specification” Software.
Through out this lecture unit, links will be present to relevant resources to supplement the learning, together with exercises and small quizzes to verify that the learning outcomes have been met.
Extra content has also been added through some bonus slides which are available after the end of the lecture unit.
Be aware that it’s an introductory course, it won’t delve into details nor mathematical aspects

## Slide 2: Learning objectives for this Lecture Unit
Intended Learning Outcomes | 
Knowledge and Understanding | Knowledge and understanding of elementary Audio Signal Processing concepts
Skills and Abilities | Ability to use Ansys Sound to analyse and process an audio signal
Values and Attitudes | Awareness of the importance of simulation in engineering design
Built-in Assessment
  Simulation exercises
  Quizzes
Resources
  Text: “Understanding Digital Signal Processing” – R. Lyons
  Software: Ansys Sound v23R1 (please note that all project files are available in the downloaded resource folder)
  Appendix Bonus Slides: Simple proof of the Nyquist Theorem and Understanding computation parameters for a spectrogram
Further reading/information
  Ansys Academic
  Ansys Innovation Courses
  Ansys Education Resources
Notes: Learning Objectives
This lecture unit is aimed at teaching the fundamental concepts associated with audio digital signal processing and consolidates their understanding by employing Ansys’ Sound Analysis & Specification software.
Through out this lecture unit, links will be present to relevant resources to supplement the learning, together with exercises and small quizzes to verify that the learning outcomes have been met.
Extra content has also been added through some bonus slides which are available after the end of the lecture unit.
If you have any questions on accessing Ansys “Sound Analysis & Specification” please contact the education team at education@ansys.com

## Slide 3: Outline of lecture unit
Audio Digital Signal Processing ?
  Definition
  Sampling
  Sampling Frequency
  Nyquist Criterion
  Real life use cases
  Exercise – Sampling Frequencies
Basic Audio Digital Signal Processing Tools
  The Fourier Transform and the FFT
  Exercise – Fourier Transform
  Spectrograms
  Filtering
  Exercise – Filtering
Summary : Audio DSP Overview
Appendixes
Notes: This lecture Unit is separated in two main parts :
Definition of Audio Digital Signal Processing and the sampling theory
Main tools used in Audio DSP and a simple explanation on how they work (Fourier Transform, Spectrograms and Filters)
Several exercises are proposed along this lecture unit and also some appendixes.

## Slide 4: Section 1: Audio Digital Signal Processing ?
Notes: First part of the lecture, containing :
A Definition of Audio Digital Signal Processing
An introduction to Sampling
Definition of Sampling Frequency
The Shannon-Nyquist Theorem
Real life application of Audio DSP
An exercise on sampling frequencies

## Slide 5: Audio Digital Signal Processing - Definition
Signal Processing
Audio
Digital
The operation of analyzing, modifying or synthesizing a signal. It can be a sound, an image, an electric current etc.
A signal that represents a sound hearable by humans
As opposed to analog, the signal are processed on a computer and are represented by a series of binary numbers (0’s and 1’s)
Notes: Defining Audio Digital Signal Processing (Audio DSP)
In order to introduce properly the topic, it is necessary to define what we’re dealing with :
“Signal Processing” is an engineering field that deals with signals. A “signal” is a function that conveys information about a phenomenon, they are omnipresent in many engineering fields: such as telecommunications, medical devices, electrical engineering etc. The term “processing” means that we analyze, modify or synthetize those signals.
“Digital” refers here to the fact that we are dealing with signals represented with a finite set of values (as opposed to an infinite physical phenomenon, such as an electric current). Digital signals are found in computers and basically any device that uses an analog-digital converter.
Finally, “Audio” implies that we are studying signals that can be heard by humans. Human can hear frequencies from 20Hz to 20kHz (for a perfectly healthy person), hence, Audio signals are in this frequency range.

## Slide 6: Audio Digital Signal Processing - Sampling
Sampling: The process of converting a continuous time-signal (an electric current, pressure levels from a sensors) to a digital signal represented by binary numbers
“Real world” signal
All values are defined for every time
The signal is continuous
Time (s)
“Computer” Signal
Values are sampled at indexes n
The signal is discrete
Numbers are binary (0s and 1s)
Frequency (Hz)
Sample
Notes: Here, we explain what is sampling.
It is an essential concept to understand in order to grasp Digital Signal Processing, as all the formulas and theorems use the fact that we’re dealing with discrete, sampled values.
Sampling is the process of mapping input values from a continuous set to output values in a countable smaller set with a finite number of elements.
The first part of the animation displays a continuous analog “real life” signal. Its equation can be written of a time variable t that can have an infinite number of values.
The second part displays the same signal after sampling, now we only have a finite sequence of sampled values. Its equation depends on a sample variable n that can only use integers.
It is interesting to notice that the variable t in the analog domain corresponds to n/Fs in the digital domain.
To go further :
To be rigorously exact: the whole process of converting a “real life” signal to a “computer” signal is named “digitization” and it englobes two processes : sampling, that is explained in this slide and quantization.
Quantization refers to the fact that computers use binary numbers and that not every number can be represented with an infinite precision.
For instance, let’s say we have f(t0) = 1.60000003, the quantization process might not be able to represent exactly this number and we will obtain a digitized value f(n0) = 1.6.

## Slide 7: Audio Digital Signal Processing – Sampling Frequency
Sampling Frequency: Numbers of samples per second taken from the continuous signal to make it discrete, in Hertz (Hz)
Sampling Frequency
Time Interval (in seconds) between two samples
Notes: In order to fully understand how sampling works, one needs to understand what is the sampling frequency.
Firstly, the process of converting an analog signal to a digital signal is done with an ADC (Analog-Digital Converter).
Those ADCs will take an input continuous signals and sample it, outputting a discrete sampled digital signal.
The sampling frequency is the rate at which we sample our continuous input signal. The sampling frequency is expressed in Hertz (Hz) and often denoted Fs.
The ADC will sample the signal at a fixed rate and extract regularly spaced values, the time difference between each sample is the inverse of the sampling frequency. This is what the plots above illustrate.

## Slide 8: Audio Digital Signal Processing – Nyquist-Shannon Theorem
Nyquist-Shannon Theorem: For a given sample frequency , perfect reconstruction is guaranteed possible for a maximum frequency in the signal respecting
In other words: In order to accurately represent all the frequencies in a continuous signal after quantization, sampling frequency must be at least two times the value of the highest frequency in the signal. Otherwise, aliasing will happen.
Aliasing: An effect that causes different signals to become indistinguishable (or aliases of one another) when sampled (quantized).
An exercise: Is left to the reader as an appendix. It will allow the reader to have a first idea of where the theorem comes from.
ADC
Analog/Digital Converter with sampling frequency
Continuous Signal (e.g., Sound Pressure) with maximum frequency
Discrete Signal
Notes: The Nyquist-Shannon Theorem is essential to sampling. It is one of the foundation of digital signal processing and it’s everywhere as soon as you’re dealing with digital signals.
The theorem states that the sampling frequency of an ADC must be strictly greater than two times the highest frequency in the signal in order to be perfectly represented on a computer.
For example, if we want to sample a sine wave of frequency 440Hz, we must use a sampling frequency that is strictly greater than 880Hz.
What will happen if the theorem is not respected ? A phenomenon called “aliasing” will occur. The sampling frequency won’t be high enough to reconstruct the signal and will “mistake” some frequencies for others, hence it will create “alias” frequencies.
Proof and details of that phenomenon is beyond the scope of this lecture unit but is well documented if needed.

## Slide 9: Audio Digital Signal Processing – Real Life Applications
Audio DSP can be found in …
Video and Music Streaming
Speech Processing (Voice Assistants)
Telecommunications
Computer Music
Can you think of another application fields ?
Amazon’s Alexa
Apple’s Siri
Etc.
YouTube
Spotify
Notes: Real life applications of Audio Digital Signal Processing
Video and Music Streaming use it all the time : those services rely on “audio codecs” which are technologies used to encode and decode the transmitted data between a server and an end-user, for example a famous audio codec is the MP3. Those audio codecs need several Audio DSP operations in order to be designed and used.
Speech Processing : smart assistants such as Amazon’s Alexa or Apple’s Siri must interpret the speech commands from the user and translate it into an action. Speech processing can be seen as a subfield of Audio DSP and focuses on Speech signals.
Telecommunications : Transmitting data between smartphone such as voice or audio signals require digital signal processing.
Computer music : another interesting field for digital signal processing, several applications exist today for sound engineers, producers, musicians etc. that rely on Audio Digital Signal Processing.

## Slide 10: Audio Digital Signal Processing – Exercise
For the items below, identify what would be the fundamental frequency they could produce (approximately) and deduce what would be the minimum sampling frequency needed for an Analog-Digital Converter.
Note : base your answer only according to the fundamental frequency and not on the harmonics.
Female Voice
Acoustic Guitar
Bird (Blackpoll Warbler)
Notes: Note: for simplicity’s sake, we consider only fundamental frequencies of each of the items, of course there are harmonic content that will require a higher sampling frequency than the one proposed in the answers. The answer does not need to be rigorously exact, the important aspect is to understand how sampling frequencies work.
Answers :
Female voice is usually between 165Hz and 255Hz  An appropriate sampling frequency would be above 510Hz. Note that these are average values and of course some pitches go higher than the average, hence in real applications the sampling frequency will be way higher than 510 Hz.
An average model of guitar will be able to go to the note B5 (5th octave of the note B) which is around 996Hz, so an appropriate sampling frequency would be 2kHz, at least
The blackpoll warbler can sing up to 8kHz ! Which means an adapted sampling frequency would be at least above 16kHz
Note that this exercise is there to invite students to think about frequencies and sampling frequencies but in real life application, sampling frequencies are often standardized, and we wouldn’t have to choose a new sampling frequency each time we deal with a new signal.

## Slide 11: Section 2: Audio Digital Signal Processing Tools
Notes: Second Part of the lecture unit, dealing with the usual Audio DSP tools, such as :
The Fourier Transform (and its implementation on computers: the FFT)
An exercise on Fourier Transforms using Ansys SAS
Spectrograms
Filtering
Workflow overview of Audio DSP
An exercise on filtering

## Slide 12: Basic Audio DSP Tools – The Fourier Transform (1/2)
Fourier Transform : Fundamental mathematical transform in DSP. It decomposes a function into the frequency components that the function is made of.
Fourier Transform
Pure Sine of frequency 440Hz in the time domain
Fourier transform of the sine in the frequency domain
One peak at exactly 440 Hz
440 Hz
Notes: Fourier Transform is probably the most important thing in Audio Digital Signal Processing, it is crucial to understand what it does.
Strictly speaking, the Fourier Transform is a mathematical operation (whose definition is given in the next slides) but what is more important to understand is that the Fourier Transform allows use to look at a signal in a different way, using its frequency representation instead of its time representation.
Prerequisite in order to understand the Fourier Transform is the fact that every signal can be decomposed as a sum of sine waves with different amplitudes, frequencies and phases.
The Fourier transform decomposes a time signal into its frequency component. That’s what can be seen on the plots, the input time signal is a pure sine whose frequency is 440 Hz, when computing its Fourier Transform, we obtain only one peak at 440 Hz.
The plot obtained with the Fourier Transform is called a spectrum, its abscissae is the frequency axis, and its ordinate the amplitude one.
If we were to study another signal composed of two frequencies (440 Hz and 1000 Hz for example), we would obtain two peaks on the Fourier Transform.
Now, those signals are very simple and are there to illustrate what the Fourier Transform does but for a real-life signal we would obtain way more peaks and different amplitudes.

## Slide 13: Basic Audio DSP Tools – The Fourier Transform (2/2)
, the studied signal, time dependent
, time index
, the Fourier transformed signal, frequency dependent
, frequency index
, the imaginary unit ()
, the studied signal, sample dependent
, sample index, related to time via the sampling frequency
, the Fourier transformed signal, frequency dependent
total number of samples in our signal
Fourier Transform
(analog signal)
Discrete Fourier Transform
(digital signal)
Notes: This is the mathematical definition of the Fourier Transform.
Note that the Fourier Transform originally was not designed for Audio DSP, it comes from French mathematician Joseph Fourier in the XIXth century who originally developed this tool to study heat transfer.
The Fourier Transform is originally defined for continuous analog signals, using an integral (on the left), it outputs a continuous, frequency-dependent function.
The one that is used in Audio DSP is named Discrete Fourier Transform (or DFT) as it takes discrete signals as inputs and outputs a discrete transform.
Voluntarily, we do not detail more the mathematical aspect of the transform here as it is an introductory lecture unit but to go further, it is encouraged to study a bit more in depth how the mathematics behind the DFT work.

## Slide 14: Basic Audio DSP Tools – The Fast Fourier Transform
Fast Fourier Transform: Name of the algorithm used everywhere for the computation of the Discrete Fourier Transform
Developed in the 60’s by J. Cooley and J. Tukey, drastically improved computational time of the DFT (assuming signal length’s is a power of 2)
This is algorithm is used – most likely – in every computer or smartphones that need to compute a Discrete Fourier Transform
Notes: The Discrete Fourier Transform is not implemented “as is” on modern computers, in fact, using the formula on the previous slide will lead to extremely long computational times.
Fortunately, an algorithm named “Fast Fourier Transform” developed during the 60’s by James Colley and John Tukey exists.
The algorithm uses some symmetry properties of the DFT and reduces the complexity of the Algorithm from O(N²) to O(Nlog(N)) operations. It is remarkable that the output of the FFT is the same as the DFT, simply faster.
The computation is highly efficient when the signal length’s is a power of 2, in real applications we can add zeros to the end of the signal to reach a power of 2 if needed.
Nowadays it is used most likely everywhere a DFT is needed.
Trivia story of the algorithm: Tukey had the idea of the algorithm while attending a meeting of President Kennedy’s Science Advisory Committee. He was using DFT to detect possible nuclear tests done by the Soviet Union during the cold war, but the DFT algorithm was too slow to be usable in “real time” (or at least in a time that was short enough to be useful). Eventually he came up with the FFT Algorithm with Colley. They didn’t patent the algorithm which ended up in the public domain, probably for the best as it brought considerable improvements in signal processing.

## Slide 15: Basic Audio DSP Tools – Exercise 1 with Ansys Sound
Time Domain Signals | In Ansys Sound, Open the time signals provided with this lecture Unit using the File > Open… menu Note : You can listen to the time signals using the playback controls in the bottom panel | 
Frequency Domain Spectrums | For each of the opened sound, right click on the waveform and select “calculate spectrum” | 
Frequency Domain Analysis | For each spectra computed, analyze the frequency content : How many peaks are there for each signals ? What’s the frequency with the highest magnitude ? | 
Signals to use :
pure_sine.wav
pure_sine2.wav
bell.wav
flute.wav
white_noise.wav
Notes: 15
This is the first exercise with Ansys Sound Analysis & Specification.
The idea here is to invite students to think about what see in a spectrum.
Note: Don’t forget to listen to the signals (press the “Play” button in SAS once a signal is opened), listening is important !
Here some comments on the spectrums obtained with the available signals:
pure_sine.wav: This is a pure sine wav with a 440Hz frequency. The resulting spectrum only contains one distinct peak at exactly 440Hz.
pure_sine2.wav: This signal contains two sine wav one after the other, the first one is at 200 Hz and the second at 1Khz. There are two distinct peaks in the signal.
bell.wav: It now becomes trickier, it’s not a synthetized signal (compared to the two previous ones) but a real one, you can observe that the spectrum is more chaotic, but you can distinguish clearly some peaks at 900 Hz, ~1.6kHz, ~2.5kHz, 3.5kHz etc. these are the different harmonics of the bell signal !
flute.wav: Same analysis as the bell sound but this spectrum is a bit easier to read, the peaks are more distinct from the rest of the spectrum.
white_noise.wav: This one is a “trap”, there is no observable peaks ! And the reason for that is that we’re looking at a white noise signal. One property of white noise is that its spectrum is “flat”, amplitudes of the spectrum are more or less the same for all frequencies.

## Slide 16: Basic Audio DSP Tools – Spectrograms
Short Time
Fourier Transform
Bell sound, in the time domain
Spectrogram of the bell
X axis : Time
Y axis : frequency
Z axis : Magnitude
A spectrogram is another way of computing the Fourier Transform by computing several “small” Fourier Transform on the input signal, thus allowing the user to visualize the evolution of the frequency content of a signal
It is particularly useful for non-stationary signals (i.e., whose frequency content is time dependent)
Notes: Spectrograms are another very important tool in Audio Digital Signal Processing.
In order to compute a Spectrogram, we use the “Short Time Fourier Transform”, we compute Fourier Transforms on small portions of the signals and we repeat the operation for the whole signal. Once this is done, we can concatenate the transforms in such a way that we obtain the nice plot on the right of the slide.
It allows the user to see how the frequency content of a signal evolves over time.
In simple terms: it can be seen as a “Spectrum in 3 dimensions”, the third dimension being the time.
If you’re dealing with non-stationary signals, i.e., signals whose frequency content evolves over time, it is the appropriate tool to use.

## Slide 17: Basic Audio DSP Tools – Spectrograms
Notes: This video’s purpose is to demonstrate what is a spectrogram using Ansys Sound Analysis and Specification.
Here we open the signal bell.wav and compute its time-frequency representation (spectrogram) using the right click menu.
First, it is interesting to notice the bursts of energy when the bell is hit, on the spectrogram it can be seen starting at 0,2s, the vertical lines with high amplitudes.
Second interesting thing to notice is that, once we hit the bell, we still have some horizontal lines with high amplitudes staying until the end of the signal, this correspond to the actual frequency of the bell and its harmonic.
The tool used in the video is the “time slice”, on the right of the spectrogram you can observe the spectrum corresponding to a given time, the goal here is to make understand students that a spectrogram is basically a concatenation of spectrums in order to observe how frequency content of a signal evolves.

## Slide 18: Basic Audio DSP Tools – Filtering
Filtering : Mathematical operation on a (digital) signal whose goal is to attenuate or amplify certain components (i.e., frequencies) of the signal.
Original Unfiltered Bell Signal
Filtered Bell Signal
Filtering
Notes: Filtering is the last concept presented in this lecture unit.
Filtering is an operation performed on signals whose purpose is to change the frequency content of a signal.
It is used in order to extract, attenuate, amplify some frequencies in a signal.

## Slide 19: Basic Audio DSP Tools – Main Filter Types
Filter Type | Application
Low-Pass | Will only keep low frequencies (Bass for example) and remove high frequency content.
Band-Pass | Only keeps a certain frequency “band”, useful if you need to isolate only a certain set of frequencies in your signal
High-Pass | The opposite of a low-pass, will only keep high frequencies
All-Pass | Will keep all frequencies but affect the phase of each component
Low Pass
Band Pass
High Pass
Below, a parametric equalizer (EQ) used in music production composed of several filters
Notes: Filters are usually classified in different types list in this slide.
Low-pass filter: Only allow the low frequencies to pass and hence will attenuate the high frequencies.
Band-pass filter: Allows only a band of frequencies to pass. It will most likely attenuate high and low frequencies and keep only frequencies in-between.
High-pass filter: The opposite of a low-pass, it will allow the high frequencies to pass and attenuate the low ones.
All-pass filter: Less common but it exist as well, it will allow all frequencies to pass but affect their phases.
The picture on the right is an equalizer, it is used in music production (and in other areas) to adjust the frequency components of a sound, you can observe the first three types of filters in the picture.

## Slide 20: Basic Audio DSP Tools – Filter Categories
In general : Filters are defined by their impulse responses in the time domain. The impulse response is the output produced by the filter when the input signal is an impulse. The Fourier transform of the impulse response leads to the transfer function.
Finite Impulse Response Filters (FIR)
The impulse response is finite in time
The output only depends on previous inputs
Output signal can be expressed using the following expression:
are the filter coefficients (deduced from the impulse response)
Infinite Impulse Response Filters (IIR)
The impulse response is infinite in time
The output depends on previous inputs and outputs !
Output signal can be expressed as the following :
- and are the filter coefficients
The two categories above are the main ones for designing filters in Audio DSP, each of them have their pros and cons but it is important to know that they exist.
Notes: This slide gives a brief and incomplete overview about digital filter categories.
Be aware that the category (IIR, FIR) of a filter is different from its type (high-pass, low-pass etc.). In fact, you can have Low-pass FIR filters as well as low-pass IIR filters.
Mathematically, a filter is defined by is impulse response. The impulse response is the output produced by the filter when the input is an impulse.
For a FIR filter, the impulse response will have a finite length whereas for an IIR filter the length of the impulse response will be infinite.
There are several difference and subtilities between IIR and FIR filters, the takeaway messages here are :
Know that these two categories exist and are mainly using in digital filtering
There’s a difference in the impulse response length
Depending on the application one category of filter will be more appropriated than the other

## Slide 21: Basic Audio DSP Tools – Exercise 2 with Ansys Sound (1/2)
Time Domain Signals | In Ansys Sound, Open the signal bird_and_voice.wav and listen to it | 
Frequency Domain Analysis | Compute either the spectrum or the time frequency representation of the signal, can you identify which frequencies correspond to the voice and to the bird ? Make sure to use an FFT size of 4096 points (to change this parameter go to File > Preferences and then Spectrum or Time-Frequency Tab and change to the appropriate value.) | 
Notes: 21
Second Exercise with Ansys Sound Analysis and Specification.
The goal here is to use frequency domain representation (spectrums and spectrograms) and to filter a signal.
The signal used for this exercise contains a bird chirp and human voice speaking, the final goal is to isolate one of those with a filter.

## Slide 22: Basic Audio DSP Tools – Exercise 2 with Ansys Sound (2/2)
Filtering | In the menu Modules, choose “Frequency Filtering” this will open a filter editor that you can apply to the previous signal. The goal here is to “draw” a filter that will either suppress the voice sound or the bird sound from the signal. Hint : Find the frequency domain of the bird and the voice, from there define a “limit” frequency such that the voice is below this frequency and the bird is above it. Then, design a filter using the “Free Hand Edition Mode” that will cut off everything above/below this frequency (depending on what sound you want to keep) | 
Listening | Try different filters on your signal, and every time listen to the results ! Your ears are one of the most important tools when doing Audio Digital Signal Processing  | 
An example of filter that can be done in the filtering module. This will attenuate frequencies below 2kHz by 20 dB
Notes: 22
In order to solve this problem, one must :
Compute the spectrogram of the input signal (spectrum can work as well but it’s easier with a spectrogram)
Determine where is the frequency “limit” between the human voice and the bird chirp
Open the filtering module in Ansys Sound Analysis and Specification
Design a filter whose cut-off frequency is at the previously found limit and apply a negative gain to the part you want to isolate
Apply the filter to the signal and list to the result

## Slide 23: Summary : Audio DSP Overview
Notes: Summary of the lecture unit that sums up what has been seen

## Slide 24: Basic Audio DSP Tools – Simple Workflow Overview
Time Domain Signal
Fourier Transform
Frequency Domain Analysis
Inverse Fourier Transform
Filtering
Hereafter is a simple workflow overview on how to use the tools presented in this lecture unit to convey some simple Audio Digital Signal Processing Operations
Listening to our signal in the time domain and viewing its waveform
Converting the signal from frequency domain back to the time domain
Converting the signal from time domain to frequency domain, using DFT or STFT
Removing / Extracting / Amplifying specific frequencies in the signal
Studying Spectrums and/or Spectrograms to analyse the frequency components of a signal
Notes: This slide serves as a summary of what has been introduced in this lecture unit.
When dealing with a digital audio signal :
First, it’s always a good idea to use one’s ears and look at the waveform
Then computing the DFT or the STFT to obtain a spectrum or a spectrogram
Analyse the previously obtain spectrum/spectrogram, extract information regarding the frequency components of the signal
Apply filtering on the signal depending on what is to be achieved
The convert the signal back to the time-domain

## Slide 25: Further Information and Resources
  Ansys Academic | Simulation Software for Educators, Researchers and Students.
  Ansys Innovation Courses : Free to Access to courses covering a variety of physics and software.
  Ansys Education Resources: Specifically developed for Educators.
  Ansys Learning Forum: Ask questions to the Ansys Community!
  Ansys Learning : Ansys YouTube Channel with dedicated video playlists.

## Slide 27: Appendix 1 : A simple proof of the Nyquist-Shannon Theorem
Notes: This first appendix offers a simple “proof” of the Nyquist-Shannon Theorem, rigorously speaking the proof is not complete but it allows the student to grasp where the theorem comes from

## Slide 28: Appendix 1 – Exercise with the Nyquist-Shannon Theorem (1/2)
Starting point: Study the periodicity of
  With being the fundamental frequency
  And being the sampling frequency
Exercise: , what can you deduce ?

## Slide 29: Appendix 1 – Exercise with the Nyquist-Shannon Theorem (2/2)
Solution: Let
We can rewrite this as with (because is periodic)
Cleverly factoring, we obtain : , with (for simplicity)
The result above means that : When sampling at a rate of samples/second, if is any positive or negative integer, we cannot distinguish between the sampled values of a sinewave of Hz and a sinewave of Hz.
This result is a first step towards the Nyquist-Shannon theorem

## Slide 30: Appendix 2 : Impacts of computational parameters for a spectrogram
Notes: This second appendix is a simple exercise that will allow students to manipulate Ansys Sound Analysis & Specification and make them understand what are the different parameters in a spectrogram computation

## Slide 31: Appendix 2 – The Parameters of the spectrogram computation (1/2)
The computation of a spectrogram relies on several parameters :
  The size of FFT used
  The window used
  The Overlap used
In Ansys Sound Analysis and Specification, try different values for each of these parameters, compute the spectrogram of a sound of your choice and try to explain their impact on the resulting spectrogram.
The parameters can be modified in File > Preferences… > Time-Frequency tab
Notes: Here, any sound can be used, don’t hesitate to use one of the previous signal associated with this lecture unit. Important thing is for the student to try out different parameters.

## Slide 32: Appendix 2 – The Parameters of the spectrogram computation (2/2)
Spectrogram Parameters Impact | 
Parameter | Importance
FFT Size | Will Impact the size of the FFT. The higher the size, the finer the frequency resolution but the lower the time resolution. More info here
Window Type | Windows are used to avoid a phenomenon called “Spectral Leakage”. A window is a mathematical function applied to our signal prior to computing the FFT, different window will have different impacts. More info here
Overlap | Overlap quantifies how much the successive FFT frames will “overlap” between each other, a high overlap value will ensure a smooth signal but will increase the number of points in the STFT.