## Slide 1
Forced Convection in External Flows
Lesson 2: Velocity & Thermal Boundary Layers
Created by Ansys ACE
Edited by Ansys Academic Development Team

## Slide 2: Velocity and Thermal Boundary Layers
The problem of determining local or averaged HTCs is complex as they depend on various fluid properties and surface geometry.
This dependency is a result of the convection heat transfer being determined by the boundary layers along the surface.
Thus, it is important to give a quick review of the velocity boundary layer concept and introduce its thermal counterpart.
The concept of the velocity boundary layer was introduced by Prandtl in 1904. The boundary layer is the thin region next to wall where viscous effects dominate.
As a result of the no-slip condition, a sharp gradient of velocity exists next to the wall, resulting in skin friction drag and other effects.
Within the boundary layer, the continuity and momentum equations can be reduced to simpler forms, which permitted solutions for simple geometries (e. g. flat plates).
Steady-state velocity boundary layer model for flow over a flat plate
Inviscid zone
Viscous zone
Boundary layer edge
Notes: The concept of boundary layers is essential for understanding the convective heat transfer, especially for fluids flowing along a solid surface, where the heat transfer coefficient depends on both fluid properties as well as the surface geometry. Similar to the velocity boundary layer which is generated due to a sharp gradient that exists because of the no-slip condition on the solid surface, a thermal boundary layer is also generated where a temperature gradient is observed. In this lesson, we will learn about these velocity and thermal boundary layers.

## Slide 3: Thermal Boundary Layers
The idea behind velocity boundary layers can be extended to thermal problems .
In an analogous fashion, sharp gradients of temperature are observed in a layer of fluid next to a wall boundary in a viscous flow. The thickness of this layer is denoted .
The temperature gradients result in heat fluxes (Fourier’s Law) and, therefore, heat transfer between the fluid and the wall.
Steady-state thermal boundary layer model for flow over a flat plate
Inviscid zone
Viscous zone
Thermal Boundary layer edge
Notes: Let us take an infinitely long flat plate. When the thermal boundary layer is formed near the wall, the fluid temperature varies between the wall temperature, , and the free stream temperature, , at the boundary layer edge and the thermal boundary layer thickness is given as . From Fourier’s law of heat conduction, any temperature gradient at the flat plate wall results in heat transfer between the fluid and the wall.
Let us take an infinitely long flat plate. When the thermal boundary layer is formed near the wall, the fluid temperature varies between the wall temperature, 𝑇_𝑠, and the free stream temperature, 𝑇_∞, at the boundary layer edge and the thermal boundary layer thickness is given as 𝛿_𝑡. From Fourier’s law of heat conduction, any temperature gradient at the flat plate wall results in heat transfer between the fluid and the wall.

## Slide 4: Laminar Boundary Layer Approximations
The 2-D governing equations can be simplified by applying well-known boundary layer approximations:
Under these assumptions, the steady incompressible boundary layer equations for laminar flows are:
viscous dissipation
The viscous dissipation term is typically small compare to advection terms and can be neglected in most incompressible flows.
Notes: Using boundary layer approximations, the 2D governing equations of fluid motion are simplified. Based on these approximations, we obtain the following boundary layer equations for steady incompressible laminar flows. It is to be noted that the viscous dissipation term in the energy equation is small compared to the advective terms and, therefore, can be neglected.

## Slide 5: Laminar Boundary Layer Approximations
For constant property flows, the continuity and momentum equations are decoupled from the energy equation, and the boundary layer velocity field can be calculated without knowledge of the temperature.
The temperature and velocity field are coupled, and velocities must be known before the equation for temperature is solved.
This decoupled nature of the velocity field allows us to utilize well-known relations and solutions for the velocity boundary layer to derive corresponding thermal layer relations.
Laminar Boundary Layer over a Flat Plate
Boundary Layer over a Sphere
Notes: A closer look at these equations tell us that the temperature and velocity fields are coupled. This means that they are interdependent, and a temperature solution is necessary to solve for the fluid velocity. Having said that, for fluids with constant flow properties, the energy equation is decoupled from the continuity and momentum equations. This allows us to obtain the velocity solution first, and we, then, use this obtained solution to solve for the temperature field in the boundary layer.

## Slide 6: Non-Dimensional Boundary Layer Equations
The non-dimensional form of the boundary layer equations is obtained by normalizing independent and dependent variables by characteristic length, velocity and temperature scales:
Here , and are nondimensional numbers:
Reynolds Number
Prandtl Number
Brinkman Number
Usually small and can be neglected
  The product of Reynolds and Prandtl numbers in the thermal diffusion term is sometimes defined as the Peclet Number, .
Notes: Let us non-dimensionalize the laminar boundary layer equations. We will use the highlighted length of the flat plate, free stream velocity, and free-stream temperature as the characteristic scales to normalize the independent and dependent variables. We obtain the following equations in their non-dimensional form. A closer look at these equations will show these non-dimensional numbers – Reynolds number, Prandtl number and Brinkman number. The last term in the energy equation is often small compared to the other terms and is neglected. The following boundary conditions are needed to solve these equations. At the walls, we impose a no-slip condition. On the thermal side, we either need the knowledge of the wall temperature or wall flux. At the edge of the boundary layer, both fluid velocity and temperature equal their respective free stream values. Although we will not look at the final solution of these equations in this lesson, it is important to understand the physical meaning behind these conditions.

## Slide 7: Physical Interpretation of Non-Dimensional Parameters
The value of the Prandtl number reflects the relative growth of velocity and thermal boundary layers. For laminar flows,
For gases, , and velocity and thermal boundary layers have approximately same thicknesses.
For liquids, , and the thermal layer is much thinner than the velocity layer.
For liquid metals, , and the velocity layer is much thinner than the thermal layer.
This observation has important implications in numerical simulations of convective heat transfer as thermal laminar layers in liquids and liquid metals require much different near wall resolution than the velocity layers, whilst no special considerations for resolving thermal layers are needed in gas flows.
Notes: One important observation can be made from the dimensionless numbers. The ratio of velocity to thermal boundary layer thickness is proportional to the nth power of the fluid Prandtl number. This implies that the velocity boundary layer is much thicker than the thermal boundary layer for high Prandtl number fluids such as liquids. On the other hand, for low Prandtl number fluids, such as liquid metals, the thermal layer is thicker than the velocity. For most gases with Prandtl numbers approximately equal to 1, the velocity and thermal layer thicknesses are nearly equal. These observations are extremely important in modern-day CFD when deciding the near-wall resolution of the computational meshes. It is crucial to highlight that for most practical turbulent flows, the velocity and thermal boundary layers have nearly similar thicknesses.

## Slide 8: Boundary Conditions
Viscous flow problems with the boundary layer equations can be solved by:
  Computing the pressure field 𝑑𝑝/𝑑𝑥 around the body using inviscid methods (e.g. potential flow).
  Computing the viscous flow field near the walls using the boundary layer equations.
The addition of the energy equation requires:
  A thermal wall boundary condition (specified temperature or heat flux).
  Temperature achieves freestream conditions outside the boundary layer.
Thus, for the boundary layer equations (including the energy equation), the boundary conditions become:
No Slip BC
Thermal wall BC
Freestream conditions at
boundary layer edge

## Slide 9: Reynolds Analogy
It can be noted from the of the governing boundary layer equations that when and pressure gradient is zero, the momentum and energy equations have identical non-dimensional form. This is a form of the Reynolds Analogy stating the velocity and temperature profiles have the same shape.
While, strictly speaking, valid for and zero-pressure gradient, it is a good approximation for gases in both laminar and turbulent flows.
The Reynolds analogy allows us to relate wall heat flux (in terms of non-dimensional Nusselt number) and skin friction (in terms of non-dimensional skin friction coefficient):
where
The significance of this relationship lies in the fact that, for a known velocity field, it provides an estimate for the Nusselt number (or heat transfer coefficient) for the flow.
Notes: For zero pressure gradients and the Prandtl number is equal to 1, it is clear from the non-dimensional form of boundary layer equations that the momentum and energy equations are identical. This is popularly called the Reynolds analogy where the velocity and temperature profiles have identical shapes. Using this analogy, the wall heat flux and skin friction coefficient are related through the following equation. Here, the heat flux is represented in a non-dimensional sense as the Nusselt number. If the velocity field is known, we can use this relationship to estimate the heat transfer provided that two conditions are satisfied – zero pressure gradient and .
For zero pressure gradients and the Prandtl number is equal to 1, it is clear from the non-dimensional form of boundary layer equations that the momentum and energy equations are identical. This is popularly called the Reynolds analogy where the velocity and temperature profiles have identical shapes. Using this analogy, the wall heat flux and skin friction coefficient are related through the following equation. Here, the heat flux is represented in a non-dimensional sense as the Nusselt number. If the velocity field is known, we can use this relationship to estimate the heat transfer provided that two conditions are satisfied – zero pressure gradient and 𝑃𝑟=1.

## Slide 10: Reynolds Analogy
The Reynolds analogy can be re-written in terms of the Stanton number, , as,
where
The Reynolds analogy can be corrected by a correction to expand its applicability to a wide range of Prandtl numbers. A popular form is Chilton-Colburn analogy:
- Colburn factor
For laminar flows, this analogy is appropriate only if:
Notes: This analogy is therefore most applicable for gas flows. This equation is rewritten in terms of the Stanton number. The analogy can be expanded to a wider range of Prandtl numbers by adding a small correction. The following Chilton-Colburn analogy is applicable for Prandtl numbers ranging between 0.6 and 60.

## Slide 11: Turbulent Boundary Layer Equations
A laminar boundary layer along a flat plate transitions to the turbulent regime at to .
Governing equations for a turbulent boundary layer can be derived by representing a flow variable () as a sum of its mean () and instantaneous fluctuating component (), , and applying the classical Reynolds averaging technique. For an incompressible flow with constant properties, the turbulent boundary layer equations are:
This term is assumed to be small across the boundary layer (~0.4% of freestream dynamic pressure)
Reynold’s stress term
Notes: Let us now turn our attention to turbulent boundary layers. Unlike the laminar boundary layer flow, the turbulent flow variables have two components – a mean component and an instantaneous component . We apply the classic Reynolds averaging technique and obtain the following governing equations for an incompressible fluid with constant properties. The highlighted term in the y-momentum equation is almost always small across the boundary layer compared to the free-stream dynamic pressure and can be neglected.
Let us now turn our attention to turbulent boundary layers. Unlike the laminar boundary layer flow, the turbulent flow variables have two components – a mean component 𝜙 ̅ and an instantaneous component 𝜙′. We apply the classic Reynolds averaging technique and obtain the following governing equations for an incompressible fluid with constant properties. The highlighted term in the y-momentum equation is almost always small across the boundary layer compared to the free-stream dynamic pressure and can be neglected.

## Slide 12: Turbulent Boundary Layer Equations
Extra terms appearing in the momentum and energy equations, and , represent contributions of turbulent mixing to the total shear stress and total heat flux:
These expressions confirm that transport rates of momentum and heat are enhanced by the presence of turbulence.
and are additional unknowns which require additional modeling.
Notes: There are two extra terms in the momentum and energy equations respectively and these are highlighted here. Both terms are the result of turbulent mixing and they individually contribute towards the total shear stress as well as the total heat flux. The presence of these turbulent terms results in an enhancement of momentum and thermal transport rate as shown here. Both these terms require additional modeling, and we make use of the most common modeling approach – the Boussinesq hypothesis.

## Slide 13: Turbulent Boundary Layer Equations
The most common (but not exclusive) approach to modeling these terms is the Boussinesq hypothesis which relates the Reynolds stress to gradients of mean flow velocity and temperature through an eddy (or turbulent) viscosity, , and eddy diffusivity, :
Methodologies of determining and are defined by the science of Turbulence Modeling.
In general, there is no universal turbulence model which is applicable to all types of turbulent flows, and the choice of a turbulence modeling approach depends on specific flow physics and application.
Even though the turbulent boundary layer equation resembles the laminar one, we rely on experiments as well as modern-day CFD to obtain the solution.
Turbulent Boundary Layer Equations
Substituting in the BL equations
Notes: In this approach, the Reynolds stress is related to the gradients of mean flow velocity using an eddy viscosity and the gradients of temperature through eddy diffusivity. These relationships are as follows. Here and are eddy viscosity and diffusivity, respectively. Substituting these back into the energy equation, we obtain the following final turbulent boundary layer equations. The determination of eddy viscosity and diffusivity is part of what is called the ‘science of turbulence modeling’ and there is, unfortunately, no universal model for all turbulent flow problems. This choice is primarily dependent on the flow-physics as well as the type of application. Unlike the laminar boundary layer equations, we rely either on experiments or modern-day CFD to solve for the turbulent boundary layers. With this note, let us conclude this lesson.
In this approach, the Reynolds stress is related to the gradients of mean flow velocity using an eddy viscosity and the gradients of temperature through eddy diffusivity. These relationships are as follows. Here 𝜈_𝑇 and 𝛼_𝑇 are eddy viscosity and diffusivity, respectively. Substituting these back into the energy equation, we obtain the following final turbulent boundary layer equations. The determination of eddy viscosity and diffusivity is part of what is called the ‘science of turbulence modeling’ and there is, unfortunately, no universal model for all turbulent flow problems. This choice is primarily dependent on the flow-physics as well as the type of application. Unlike the laminar boundary layer equations, we rely either on experiments or modern-day CFD to solve for the turbulent boundary layers. With this note, let us conclude this lesson.

## Slide 14: Summary
We learned about the thermal boundary layer region and understood the general nature of the temperature profile.
We simplified the 2D governing equations to obtain the final form of laminar boundary layer equations. We also non-dimensionalized these equations. The non-dimensional solution helped in understanding the relative thickness between velocity and thermal boundary layers for different Prandtl numbers.
For and zero pressure gradients along the flow, we discussed the Reynolds Analogy and developed a relationship between Skin Friction coefficient and Nusselt number.
We also outlined the turbulent boundary layer equations and defined the additional terms eddy (or turbulent) viscosity and eddy diffusivity that appear because of the Boussinesq approximation.
Next, we will look at forced convection in flow over a flat plate.

## Slide 15: What have we covered…What’s next?
Introduction to Forced Convection
Dimensionless Numbers and Correlations
Velocity and Thermal Boundary Layers
Boundary Layer Equations and Conditions
Forced Convection over a Flat Plate
Flow Types: Laminar & Turbulent
Cross Flow: Cylinder, Tube Bank & Jet Flow