## Slide 1
Forced Convection in External Flows
Lesson 1: Introduction to Forced Convection
Created by Ansys ACE
Edited by Ansys Academic Development Team

## Slide 2: Introduction to Forced Convection
In general, convection is the process of thermal energy transfer that occurs due to fluid motion.
  For example, if air is blown across a heated plate, it can be noticed that the downstream air is hotter – thermal energy has been transferred into the fluid and carried by it to another location.
  How does the heat enter the fluid? How much thermal energy can be transferred? How does the nature of the fluid flow affect the rate of heat transfer? These questions are addressed by the science of convective heat transfer.
Notes: Have you ever noticed how blowing on a hot beverage, say a cup of coffee, cools it down much faster than if you just left it on the table? What you are unconsciously doing is employing forced convection to cool your coffee faster. Let’s take a deeper look at what forced convection is all about.

## Slide 3: Introduction to Forced Convection
Convection is classified into forced and natural (free) convection based on a mechanism responsible for creating the fluid flow:
  In forced convection, the flow is generated by external means, e. g. wind or fan, or by object’s motion through the fluid.
  In natural convection, the heat transfer itself is the primary mechanism behind the fluid motion which is generated by the buoyancy forced due to temperature gradients.
In this course, we will focus our discussion on forced convection.
Air Flow
Temperature distribution in the air as it flows over a hot heat sink to extract heat through the process of forced convection
Notes: Convection is the mode of heat transfer where energy is transferred to or from a cold or hot body by fluid motion. Back to the coffee example, the air you blow extracts heat from the coffee and convects it away from the mug. Based on how the fluid flow is created, convection can be classified into Natural or Forced convection. In forced convection, the fluid flow is generated by external means i.e. by a fan or because of an object’s motion. Cooling of electronic components, localized space heaters are a few examples of forced convection. In natural convection, a fluid flow is created because of buoyancy forces, caused by temperature gradients, due to the energy transfer between the body and the surroundings. Cooling of a hot coffee left on a table, heating a room through heaters are examples of heat transfer via natural convection. In this course, our focus will be on forced convection.

## Slide 4: Newton’s Law of Cooling/Heating Revisited
Consider the Newton’s Law of cooling/heating at a point on our heated plate. Let the local convection heat flux be represented using the heat transfer coefficient the incoming fluid temperature by , and wall temperature by .
At the wall, there is no motion due to the no-slip condition and the conduction heat flux in the fluid is described by the Fourier’s Law.
These two fluxes must be equal at the wall (neglecting radiation), thus:
Conduction
Convection
fluid
solid
Notes: Consider a hot plate at a temperature of Tw. If the incoming fluid is at temperature T∞ and the heat transfer coefficient is ‘h’, according to Newton’s law of cooling, the convection heat flux can be calculated using the following equation. At the surface of the plate, there is no fluid motion due to the no-slip condition and therefore, there will be only conduction from the plate into the fluid, which is calculated using the Fourier’s law as shown here. Neglecting radiation, these two fluxes must be equal at the wall and as a result, we get the following flux balance. Here, q’’ is local heat flux and therefore, ‘h’ is generally referred to as a local heat transfer coefficient.

## Slide 5: Local and Average Heat Transfer Coefficients
In general, heat transfer is a function of space, and likewise the heat transfer coefficient will vary (sometimes substantially) over a surface.
Accordingly, a local heat transfer coefficient can be defined based on the local heat flux and wall temperature, , as shown on the previous slide.
For engineering purposes, an average heat transfer coefficient value for a surface is often needed in order to estimate the heat transfer. Therefore, the local value can be area-averaged (denoted by the overbar) as follows:
Note that the sign of the local heat flux should be consistent with the local temperature difference such that is always a positive number.
The essence of the problem of convection is determining the local and averaged heat transfer coefficients, which can subsequently be used to calculate the local flux or the total heat transfer rate.
It is common to abbreviate the terms “heat transfer coefficient” as HTC, and we will be using this abbreviation throughout this course.
Then, the total heat transfer rate is:
Notes: In general, heat transfer is a function of space and hence the heat transfer coefficient will vary over the surface. For engineering estimates, the averaged value of heat transfer coefficient for a surface can be defined as shown here. Subsequently, the total heat transfer rate is defined by the following relation. Note that ‘h’ is always a positive number and therefore the sign of ‘q’ will depend on the temperature difference Tw and T∞. The essence of any convection heat transfer problem is determining the local and averaged heat transfer coefficients, which can subsequently be used to calculate the local flux or the total heat transfer rate.

## Slide 6: The Nusselt Number
Let us now non-dimensionalize the wall heat flux balance equation using (reference length), and (reference temperature). All the parameters (, , , ) are assumed to be constant. Denoting non-dimensional quantities with *, the heat flux balance can be rewritten as:
The term on the left is known as the Nusselt Number (𝑁𝑢). We will use the Nusselt number as a non-dimensional measure of convective heat transfer relative to heat transfer that would occur by conduction into the fluid.
As defined, the Nusselt number is local if the heat transfer coefficient is local. If we employ the average heat transfer coefficient, we obtain the average Nusselt number:
Notes: Let’s go back to the heat flux balance at the wall. If we now non-dimensionalize this equation using reference length (L) and reference temperature (T∞), the heat flux balance can be rewritten as shown here. Note that Tw, T∞, h and Kf are assumed to be constant. The circled term here is generally referred to as the Nusselt number (Nu). It is a non-dimensional measure of convective heat transfer relative to the heat transfer that would occur by conduction into the fluid. If the heat transfer coefficient used to define the Nusselt number is local, then the Nusselt number is also local. To obtain the average Nusselt number, one can instead use the average heat transfer coefficient.

## Slide 7: The Reynolds and Prandtl Numbers
The Nusselt number is found to correlate with two dimensionless parameters associated with the momentum and energy equations, namely:
  The Reynolds Number
  The Prandtl Number
The Reynolds number represents the ratio of inertial forces (represented by ) in a flowing fluid to the viscous forces (represented by ) .
The Prandtl number represents the ratio of viscous diffusion of momentum (represented by ) to thermal diffusion in the fluid (represented by ).
Notes: Experiments have shown that the Nusselt number correlates with the Reynolds number, which represents the ratio of inertial to viscous forces in a fluid flow, and the Prandtl Number which represents the ratio of viscous diffusion of momentum to thermal diffusion in the fluid.

## Slide 8: The Reynolds and Prandtl Numbers
One of the central themes in convection heat transfer is determining the heat transfer coefficient for specific flow configurations e. g. flow over a heated cylinder, flow in a pipe, etc.
This can be accomplished in two ways:
  Run a series of experiments where key geometric and thermal parameters are varied and measured carefully. For example, we can measure the heat flux from a cylinder of diameter which is maintained at a specific surface temperature and exposed to a fluid flow at a given freestream temperature and velocity.
  Run simulations wherein the governing equations are solved using CFD techniques for specific geometries and flow/thermal boundary conditions. This is akin to doing an “experiment” except now we are simulating the flow field numerically.
It is impractical to perform experiments or run simulations for every conceivable geometry and flow/thermal condition. Is there a way to generalize the physics? The answer is yes! We can use Similarity Methods and Dimensionless Groups to develop correlations for common geometries and flow configurations.
Notes: To determine the heat transfer coefficient, there are two ways.
Through a series of experiments where key geometric and thermal parameters are varied, and fluxes are measured carefully.
Through simulations wherein the governing equations are solved using CFD techniques for specific geometries and flow/thermal boundary conditions. This is akin to doing an “experiment” except now we are simulating the flow field numerically.
However, it is impossible to perform experiments or simulations for every conceivable geometry and flow condition. To address this issue, engineers make use of similarity methods and dimensional groups to develop correlations for common geometries and flow configurations.

## Slide 9: Geometric and Dynamic Similarity
Consider a flow over two objects, where the smaller object represents a physical model of the larger.
Geometric similarity refers to the requirement that the ratio of all corresponding lengths of the two objects (L1/L2, W1/W2) are the same.
  Another way of saying this is that the two objects are perfectly scaled geometrically.
Dynamic similarity is the requirement that if the two objects are geometrically similar, then they also have similar flow patterns i.e. the velocities and velocity gradients, fluid forces, and streamlines all scale with the geometry.
For heat transfer problems, we will also require that the temperatures, temperature gradients, and heat fluxes scale with the geometry.
L1
L2
W1
W2
Notes: There are two types of similarities: Geometrics and Dynamic.
Geometric similarity means that two bodies are geometrically similar if they are perfectly scaled versions of each other. Consider the following two objects. If they are geometrically similar, then it is required that the ratio of corresponding lengths of the two objects i.e L1/L2, W1/W2 etc. are the same.
Dynamic similarity requires that, for geometrically similar bodies, the flow patterns are also similar i.e. the velocities and velocity gradients, fluid forces, and streamlines all scale with the geometry.

## Slide 10: Geometric and Dynamic Similarity
As in Fluid Dynamics, formal methods can be used to determine the relevant dimensionless groups for convection heat transfer.
  The Nusselt number is a non-dimensional representation of the heat transfer.
  The Prandtl number represents the relative sizes of the thermal and velocity gradients.
  The Reynolds Number is a non-dimensional representation of the fluid dynamics (ratio of inertial to viscous forces).
The requirement for similarity then is that the dimensionless groups (both flow and thermal) are the same for a geometrically similar system.
For the case of forced convection, two geometrically similar systems are dynamically similar if their Nusselt, Reynolds, and Prandtl Numbers are the same.
  Therefore, if an experiment is run with a model geometry at a given Reynolds and Prandtl number to determine a Nusselt number, then the Nusselt number results can be applied to a scaled-up version of the model provided the Reynolds and Prandtl number are the same.
Notes: For heat transfer problems, it is also required that the temperatures, temperature gradients, and heat fluxes scale with the geometry. For the case of forced convection, two geometrically similar systems are dynamically similar if their Nusselt, Reynolds, and Prandtl Numbers are the same.

## Slide 11: Heat Transfer Correlations
Let’s consider a convection scenario such as flow over a heated object of size with the objective to experimentally determine how the heat transfer varies with the geometry size and flow conditions.
From the similarity discussion, a test matrix would be set up where the Reynolds and Prandtl numbers are systematically varied and the Nusselt number is calculated from the data obtained from the tests.
Could a relationship between the Nusselt Number and Reynolds and Prandtl Numbers be found? That is:
It turns out, the results for a given fluid (i. e. fixed ) fall close to a straight line on a scale, and the expression for a global Nusselt number can be represented by an empirical correlation:
Specific values of , and oftentimes are independent of the fluid, but they depend on the geometry of the surface and flow type.
Notes: Is it possible to formulate a relationship between these dimensionless numbers? In order to determine that, multiple experiments can be setup at varying Reynolds and Prandtl numbers, to calculate the corresponding Nusselt numbers. And as it turns out, researchers have found that for a fixed Prandtl number i.e. for a given fluid, an empirical correlation of the following form can be written to calculate the global Nusselt number.

## Slide 12: Heat Transfer Correlations
Non-dimensional empirical correlation of heat transfer measurements
Notes: On a log-log scale, this correlation looks like a straight line as shown here. The values of ‘C’, ‘m’, and ‘n’ are dependent on the geometry of the object and the flow type, and are oftentimes independent of the fluid itself. That was a quick brief on the basics of forced convection.

## Slide 13: What have we covered…What’s next?
Introduction to Forced Convection
Dimensionless Numbers and Correlations
Velocity and Thermal Boundary Layers
Boundary Layer Equations and Conditions
Forced Convection over a Flat Plate
Flow Types: Laminar & Turbulent
Cross Flow: Cylinder, Tube Bank & Jet Flow