## Slide 1
Forced Convection in External Flows
Lesson 3: Forced Convection over a Flat Plate
Created by Ansys ACE
Edited by Ansys Academic Development Team
Notes: Our journey to understand the fundamental concepts of external forced convection takes us first to the canonical flat plate problem. From an engineering standpoint, forced convection over a flat plate provides the foundation for understanding heat transfer applications such as electronics cooling and metallurgy. In this lesson, we will learn about the fundamental concepts governing heat transfer over a flat plate.

## Slide 2: Laminar & Turbulent Flow Regimes
The flow over a flat plate transitions from laminar to turbulent due to the interactions of naturally occurring unsteady flow structures or small disturbances within the boundary layers.
The key to understanding and estimating convection is to identify the flow regime over the flat plate.
We will investigate two thermal conditions:
  Flat Plate with Isothermal Wall (constant wall temperature)
  Flat Plate with Constant Heat Flux
L
Turbulent
Laminar
Transition
Flow Regime |  | Flow Characteristics
Laminar Flow Regime | - | Smooth highly ordered flow
Transitional Flow Regime* |  | Flow changes with time, sometimes laminar sometimes turbulent
Turbulent Flow Regime |  | Highly irregular random flow dominated by chaotic mixing
Flow Regime |  | Flow Characteristics
Laminar Flow Regime |  | Smooth highly ordered flow
Transitional Flow Regime* |  | Flow changes with time, sometimes laminar sometimes turbulent
Turbulent Flow Regime |  | Highly irregular random flow dominated by chaotic mixing
Boundary layer flow over an infinitely long flat plate has three distinct region based on the flow behavior:
* The Rex where transition occurs varies based on flow conditions, surface disturbances, and flow application.
Notes: The fluid flow over an infinitely long flat plate is categorized depending on the flow behavior as laminar, transitional, and turbulent. A boundary layer is formed at the leading edge, and the flow near this leading-edge is smooth and highly ordered. This is the laminar region where the Reynolds number, based on the length of the plate, is lower than approximately 3.5 x 105. As the fluid flows further downstream away from the leading edge, the flow becomes unsteady due to small disturbances in the boundary layer, sometimes exhibiting laminar characteristics and other times turbulent. This region is often referred to as the transitional region and the characteristic Reynolds number ranges between 3.5 x 105 to ~ 3 x 106. Further downstream, the fluid flow is characterized by highly irregular random motion dominated by chaotic flow mixing and this is the turbulent region. Identifying these flow regimes is an important aspect of understanding convective heat transfer over a flat plate and we will first look into the laminar flow before venturing into the turbulent flow regime. Also, we will investigate two thermal conditions for a heated flat plate – the constant wall temperature and the constant heat flux.

## Slide 3: Hydrodynamic Boundary Layer: Blasius Solution (Laminar Flow)
Blasuis developed a similarity solution based on the observation that the velocity profile remains geometrically similar along the boundary layer.
New independent and dependent variables and are defined in terms of stream function, and these variables are used to reduce the flat plate boundary layer partial differential equations (PDEs) into a single ordinary differential equation (ODE).
The appropriate boundary conditions are also converted in terms of the similarity variables.
A solution to the ODE is obtained by series expansion or numerical integration and the Hydrodynamic Boundary Layer profile is obtained.
Inviscid zone
Viscous zone
Boundary layer edge
)
Notes: For a laminar flow over a flat plate, the velocity boundary layer solution is obtained using the similarity analysis, popularly known as the Blasius solution. The governing equations are transformed into ordinary differential equations using similarity variables and , so we can obtain a relationship for the boundary layer thickness. A thermal boundary layer is created when the fluid flows over a heated flat plate.
For a laminar flow over a flat plate, the velocity boundary layer solution is obtained using the similarity analysis, popularly known as the Blasius solution. The governing equations are transformed into ordinary differential equations using similarity variables 𝜂 and 𝑓(𝜂), so we can obtain a relationship for the boundary layer thickness. A thermal boundary layer is created when the fluid flows over a heated flat plate.

## Slide 4: Blasius Results (Laminar Flow)
Hydrodynamic Boundary Layer Thickness:
Wall shear stress is obtained from the velocity gradient at the wall :
The friction coefficient is computed as follows:

## Slide 5: Laminar Flow over an Isothermal Flat Plate
Let us assume a heated flat plate at a constant temperature, .
We define the dimensionless temperature,
Inviscid zone
Viscous zone
Thermal Boundary layer edge
The thermal boundary layer equation is transformed into the following ODE. This equation is dependent on the hydrodynamic conditions, .
The corresponding boundary conditions are:
Similarity Solution
and
At ,
At ,
Notes: In this case, the plate temperature is held constant at Ts. To obtain the heat transfer solution, we take the energy equation into account. First, we define the dimensionless temperature T*, which is also a function of , in terms of both surface temperature, Ts, and free stream temperature, . Following the same similarity approach, we rewrite the boundary layer energy equation into the following ODE. For laminar flows, it is important to note that the thermal boundary layer solution is dependent on the Prandtl number. We need the following two boundary conditions to solve this ODE.
In this case, the plate temperature is held constant at Ts. To obtain the heat transfer solution, we take the energy equation into account. First, we define the dimensionless temperature T*, which is also a function of 𝜂, in terms of both surface temperature, Ts, and free stream temperature, 𝑇_∞. Following the same similarity approach, we rewrite the boundary layer energy equation into the following ODE. For laminar flows, it is important to note that the thermal boundary layer solution is dependent on the Prandtl number. We need the following two boundary conditions to solve this ODE.

## Slide 6: Thermal Boundary Layer Solution for Higher Prandtl Numbers
For , Pohlhausen correlated the first derivative of at using the following correlation.
The local convective heat transfer coefficient is rewritten in terms of variables and :
The local Nusselt Number (at any x) is:
For different values of Prandtl numbers, the ODE is numerically solved.
Comparing the solutions of hydrodynamic and thermal boundary layer thicknesses, we obtain
For ,
For
Thermal BL is much thinner compared to the Hydrodynamic BL for fluid with Prandtl Numbers greater than 1.
Notes: Let us first consider fluids with Prandtl numbers greater than 0.6. Pohlhausen correlated the first derivative of T* at using the following relationship, which is used to determine the thermal boundary layer thickness. When this is compared with the hydrodynamic boundary layer thickness for a laminar flow, we obtain the following ratio. If the fluid Prandtl number is high, the hydrodynamic boundary layer is thicker than the thermal boundary layer. The local heat transfer coefficient is expressed in terms of the first derivative of the temperature at and the following relationship is obtained. Rewriting this in terms of Nusselt number, we obtain the following relation for fluids with a Prandtl number greater than or equal to 0.6. This relationship is a function of x and is dependent on the length of the plate.
Let us first consider fluids with Prandtl numbers greater than 0.6. Pohlhausen correlated the first derivative of T* at 𝜂=0 using the following relationship, which is used to determine the thermal boundary layer thickness. When this is compared with the hydrodynamic boundary layer thickness for a laminar flow, we obtain the following ratio. If the fluid Prandtl number is high, the hydrodynamic boundary layer is thicker than the thermal boundary layer. The local heat transfer coefficient is expressed in terms of the first derivative of the temperature at 𝜂=0 and the following relationship is obtained. Rewriting this in terms of Nusselt number, we obtain the following relation for fluids with a Prandtl number greater than or equal to 0.6. This relationship is a function of x and is dependent on the length of the plate.

## Slide 7: Average Nusselt Number for Laminar Flow
The local Nusselt number expressions are obtained assuming an infinite flat plate.
For the laminar region , average heat transfer coefficient is determined by integrating the local heat transfer coefficient along the plate.
For , the average heat transfer coefficient for laminar flow is:
The corresponding average Nusselt number for laminar flow over a flat plate is:
For Laminar Flow over a Flat Plate, the Average Nusselt Number is twice the Local Nusselt Number.
Note: We can replace ‘x’ with ‘L’ if the flow is laminar over the entire flat plate.
Notes: Assuming we know the length of the laminar boundary layer region (x), we can integrate the local heat transfer coefficient along the plate to obtain an average value. It is observed that the average heat transfer coefficient is exactly twice the local heat transfer coefficient at any given length of the plate x. Similarly, the average Nusselt number over a specified length L is twice the local Nusselt number at that specific location L.

## Slide 8: Thermal Boundary Layer Solution for Low Prandtl Number
For smaller Prandtl numbers (mainly liquid metals), the thermal boundary layer develops faster compared to the hydrodynamic boundary layer .
In the limiting case , because of thin hydrodynamic boundary layer, we assume a uniform velocity throughout the thermal boundary layer. This allows use to set in the thermal boundary layer equation.
Differentiating the thermal boundary layer equation, we obtain:
1
The solution of the above equation gives:
For
Even though the above local Nusselt number is for a limiting case of , the result holds for
Peclet Number,
Notes: Now, for low Prandtl number fluids such as liquid metals, the thermal boundary layer is much thicker than the hydrodynamic layer. And because of this, we can assume a uniform velocity u = throughout the thermal boundary layer. Using this condition and solving the appropriate ODE, we obtain the following solution for the first derivative of T*. This translates to the following local Nusselt number relationship. For low Prandtl number fluids, the Nusselt number is proportional to the square root of the Prandtl number, whereas, for higher Prandtl number fluids, it goes as one-third power of the Prandtl number.
Now, for low Prandtl number fluids such as liquid metals, the thermal boundary layer is much thicker than the hydrodynamic layer. And because of this, we can assume a uniform velocity u = 𝑉_∞ throughout the thermal boundary layer. Using this condition and solving the appropriate ODE, we obtain the following solution for the first derivative of T*. This translates to the following local Nusselt number relationship. For low Prandtl number fluids, the Nusselt number is proportional to the square root of the Prandtl number, whereas, for higher Prandtl number fluids, it goes as one-third power of the Prandtl number.

## Slide 9: Turbulent Flow over an Isothermal Flat Plate
The flow Reynolds number (Re) for turbulence is generally greater than .
Unlike laminar flow, we cannot use similarity variables to obtain the relationships for the turbulent flow regime. In such cases, we rely on experimental correlations to calculate the local coefficient of friction:
In this flow regime, the heat transfer is dictated by random fluctuations as opposed to molecular diffusion, and therefore, the boundary layer growth is not related to the Prandtl number of the fluid.
The thermal and hydrodynamic boundary layer thickness grow at a similar rate and their thickness is obtained from:
The local Nusselt Number for turbulent flow is obtained by invoking the Chilton-Colburn analogy and using the above local coefficient of friction
Turbulent boundary layer grows faster than laminar boundary layer
Notes: In the case of a turbulent flow regime, the heat is transported across the boundary layer by the random chaotic motion of turbulent eddies, and not by molecular diffusion of heat. Because of this, the thermal boundary layer growth is independent of the Prandtl number of the fluid, and its thickness is comparable to that of the velocity layer. The thermal and hydrodynamic boundary layer thickness for turbulent flow over a flat plate is given by the following expression. When compared to laminar flows, it is observed that the boundary layer growth in the turbulent flow regime is faster. One major difference between the laminar and turbulent flow analysis is that we cannot use the similarity approach and have to rely on experiments to obtain the local friction coefficient along the plate. This is given by the following relationship. This relationship is used by the Chilton-Colburn analogy to obtain the local Nusselt number for the turbulent flow along a flat plate.

## Slide 10: Mixed Boundary Layer Conditions
Laminar relations are useful when the flow over the flat plate is either entirely laminar or marginally transitional quite close to the trailing edge of the plate (in the last ~5% of the plate length).
If the transitional region occurs reasonably close to the leading edge of the flat plate, using laminar relations for predicting the convective heat transfer will produce erroneous results. The heat transfer in such cases is effected by both laminar and turbulent boundary layers.
If the transition occurs at a length (laminar region: and turbulent region: ), it is useful to estimate the average heat transfer coefficient over the entire plate as:
Substituting for the local laminar and turbulent heat transfer coefficients and integrating, we obtain the following relationship for the Average Nusselt Number.
where, A is a constant estimated from the critical Reynolds Number,
Notes: Between the laminar and turbulent flow regimes, there is a region of transition. If this transition occurs much downstream of the plate, closer to the trailing edge, we can rely on the laminar boundary layer correlations to predict the heat transfer. However, if this transition region occurs much closer to the leading edge, the heat transfer is affected by both laminar and turbulent boundary layers. In such cases, where the flow transition occurs at length , we calculate an average heat transfer coefficient over the entire length of the plate using the following relationship. Here, the laminar region is between 0 and and the turbulent region is between and L. Substituting for both laminar and turbulent heat transfer coefficients, we obtain the following relation. Here, A is a constant based on the critical Reynolds number.
Between the laminar and turbulent flow regimes, there is a region of transition. If this transition occurs much downstream of the plate, closer to the trailing edge, we can rely on the laminar boundary layer correlations to predict the heat transfer. However, if this transition region occurs much closer to the leading edge, the heat transfer is affected by both laminar and turbulent boundary layers. In such cases, where the flow transition occurs at length 𝑥_𝑐, we calculate an average heat transfer coefficient over the entire length of the plate using the following relationship. Here, the laminar region is between 0 and 𝑥_𝑐 and the turbulent region is between 𝑥_𝑐 and L. Substituting for both laminar and turbulent heat transfer coefficients, we obtain the following relation. Here, A is a constant based on the critical Reynolds number.

## Slide 11: Laminar & Turbulent Flow: Constant Heat Flux
In certain heating and cooling applications, such as electronics and food processing industries, the wall heat flux is known. For such applications, the local wall temperature distribution becomes the key variable of interest.
The local Nusselt number relations for a flat plate with a constant heat flux are:
Laminar Flow:
Turbulent Flow:
Comparing these with the isothermal relations:
  Laminar Flow: The Nusselt number is ~36% higher for the constant heat flux condition.
  Turbulent Flow: The Nusselt number is ~4% higher for the constant heat flux condition.
The wall temperature is determined using the local heat transfer coefficient in the following expression:
Notes: Until now, we have discussed convection heat transfer relations for flow over an isothermal flat plate. Now, let us learn about a different condition – when the applied wall heat flux is known. This condition is useful for electronics cooling where constant thermal power is generated by the electronics. Another application is cooling hot metal or steel. In such applications, the wall temperature distribution becomes the variable of interest. The local Nusselt number relationships for laminar and turbulent flow over a flat plate with a constant heat flux are as follows. When these are compared with the isothermal relationships, it is observed that the Nusselt number is 36% higher for the constant heat flux condition in case of a laminar flow. For a turbulent flow, it is only 4% higher when a constant heat flux condition is applied. The obtained heat transfer coefficients are used to estimate the local wall temperature of the flat plate using the following expression. With that, let us wrap up this lesson.
Until now, we have discussed convection heat transfer relations for flow over an isothermal flat plate. Now, let us learn about a different condition – when the applied wall heat flux is known. This condition is useful for electronics cooling where constant thermal power is generated by the electronics. Another application is cooling hot metal or steel. In such applications, the wall temperature distribution becomes the variable of interest. The local Nusselt number relationships for laminar and turbulent flow over a flat plate with a constant heat flux 𝑞_𝑠^′′ are as follows. When these are compared with the isothermal relationships, it is observed that the Nusselt number is 36% higher for the constant heat flux condition in case of a laminar flow. For a turbulent flow, it is only 4% higher when a constant heat flux condition is applied. The obtained heat transfer coefficients are used to estimate the local wall temperature of the flat plate using the following expression. With that, let us wrap up this lesson.

## Slide 12: Summary
For a flat plate under isothermal conditions,
  Laminar flow:
    For high Prandtl numbers , the hydrodynamic BL is thicker than the thermal BL.
    For low Prandtl numbers , the thermal BL is thicker than the hydrodynamic BL.
  Turbulent Flow:
    The thermal and hydrodynamic BL thickness are nearly equal, and the BL growth is independent of the Prandtl number.
    Heat transfer is primarily governed by random fluctuations (as opposed to molecular diffusion).
We discussed relationships for local and average Nusselt numbers relations for flat plate in both isothermal and uniform heat flux conditions.
In the transitional regime, it is useful to estimate the average heat transfer coefficient from both laminar and turbulent relationships.

## Slide 13: What have we covered…What’s next?
Introduction to Forced Convection
Dimensionless Numbers and Correlations
Velocity and Thermal Boundary Layers
Boundary Layer Equations and Conditions
Forced Convection over a Flat Plate
Flow Types: Laminar & Turbulent
Cross Flow: Cylinder, Tube Bank & Jet Flow