## Slide 1
Forced Convection in External Flows
Lesson 4: Cross Flow Geometry
Created by Ansys ACE
Edited by Ansys Academic Development Team

## Slide 2: Introduction
In this lesson, we will analyze the forced convection heat transfer in some representative external flows.
In cases such as fluid flow over a flat plate, flow over a cylinder etc., the presence of a boundary layer has a strong impact on the heat transfer characteristics.
The nature of the boundary layer i.e. whether it is laminar or turbulent or transitional, can significantly alter the amount of heat transferred to/from the body.
In this lesson, we will extend our discussion from the last lesson, and analyze the heat transfer behavior for three different cases:
  Flow across a Tube Bank
  Impinging Jet Flow
  Cylinder in Cross Flow
Notes: Now that we have a good understanding of forced convection heat transfer over a flat plate, let us extend this analysis and study certain other external flows. The first configuration we will be looking at is that of a circular cylinder in a crossflow, as shown here. Due to the ease of manufacturing, circular pipes are widely used as a part of tube banks in heat exchangers. Before we discuss heat transfer for this case, let us quickly recap the related fluid dynamic concepts.

## Slide 3: Cylinder in Cross Flow
As the flow turns around the cylinder, it accelerates accompanied by the reduction in fluid pressure i.e. – favorable pressure gradient. The boundary layer also begins to grow around the cylinder.
At a certain circumferential location, and the flow reaches its maximum velocity. Beyond this point, because of an adverse pressure gradient i.e. , the flow starts to decelerate.
At a further circumferential location, the flow momentum is not strong enough to overcome the adverse pressure gradient. As a result, the boundary layer detaches from the surface of the cylinder. At this location, called the separation point is 0.
The motion of a fluid normal to the axis of a cylinder is considered a cylinder in cross flow. Because of ease of manufacturing, circular cylinder is the most used tube shape in heat exchangers.
Let us quickly recap some fundamental aspects of flow over a cylinder.
The flow stagnates as it first encounters the cylinder. The forward stagnation point is so named because the flow is brought to a complete stop at this location. Consequently, the fluid pressure is maximum at this location.
Notes: As the fluid flow hits the cylinder, it comes to a complete stop at a location referred to as the stagnation point. At this location, the velocity of the flow is zero and consequently, according to Bernoulli’s principle, the pressure is maximum. Due to a favorable pressure gradient, the flow starts to accelerate and a boundary layer begins to form on the wall, as the flow turns around the cylinder. At a certain circumferential location where , maximum flow velocity is reached. Beyond this point, because of an adverse pressure gradient that is 𝑑𝑝/𝑑𝑥>0, the flow starts to decelerate. At a further circumferential location, the flow momentum is not strong enough to overcome the adverse pressure gradient. As a result, the boundary layer detaches from the surface of the cylinder at a location called the separation point.
As the fluid flow hits the cylinder, it comes to a complete stop at a location referred to as the stagnation point. At this location, the velocity of the flow is zero and consequently, according to Bernoulli’s principle, the pressure is maximum. Due to a favorable pressure gradient, the flow starts to accelerate and a boundary layer begins to form on the wall, as the flow turns around the cylinder. At a certain circumferential location where 𝑑𝑝/𝑑𝑥=0, maximum flow velocity is reached. Beyond this point, because of an adverse pressure gradient that is 𝑑𝑝/𝑑𝑥>0, the flow starts to decelerate. At a further circumferential location, the flow momentum is not strong enough to overcome the adverse pressure gradient. As a result, the boundary layer detaches from the surface of the cylinder at a location called the separation point.

## Slide 4: Cylinder in Cross Flow
The nature of the boundary layer strongly influences the location of the separation point.
Let’s define a Reynolds number based on the cylinder diameter (D) as .
For , experiments show that boundary layer is laminar, and the separation point is around .
For , the boundary layer is turbulent, and the separation point is around .
Separation is delayed because the presence of high momentum fluid in the turbulent boundary layer helps to sustain the adverse pressure gradient over a longer circumferential distance.
Notes: The circumferential location of this separation point is strongly influenced by the nature of the boundary layer. Let’s define a Reynolds number based on the diameter of the cylinder. Experiments show that the boundary layer is laminar for Reynolds number less than 200,000, and the separation point is around θ=80 degrees. For Reynolds number greater than 200,000 when the boundary layer becomes turbulent , flow separation is delayed due to the enhanced fluid momentum that withstands the adverse pressure gradient for longer, and as a result, the separation location is around θ=140 degrees.
BL or flow?

## Slide 5: Cylinder in Cross Flow
The convective heat transfer, represented by the local Nusselt number (), is strongly influenced by the nature of the boundary layer.
For , decreases with increasing circumferential distance i.e. .
At the separation point i.e. , the local Nusselt number attains its minimum value. Due to enhanced mixing from vortices, increases beyond the stagnation point.
For , still shows a decreasing trend from the stagnation point. Between and , because of laminar-turbulent transition, a sharp increase is observed. Beyond , again decreases till the separation point, beyond which it increases again because of enhanced mixing.
For and , the following correlation can be used to calculate the local Nusselt number at stagnation point
Notes: The convection heat transfer levels are also significantly influenced by the nature of the boundary layer. For Re < 100,000 where the boundary layer is entirely laminar, the local Nusselt number decreases with increasing circumferential angle, as seen in this plot. Close to the separation location i.e. θ=80 degrees, the Nu number attains its minimum value. However, due to enhanced mixing from the vortices in the separated flow, the Nu number starts to increase. This situation is slightly different for Re greater than 100,000. Initially, the Nu number profile still shows a decreasing trend till about θ=80 degrees. Between, 80 and 100 degrees however, a sharp increase in the heat transfer levels is observed, which is due to the laminar-turbulent transition. Beyond θ=100 degrees, the profile once again shows decreasing trends till the separation location, after which it again increases because of enhanced mixing. For low Reynolds number flows, that is Re < 2000, and for Pr > 0.6, one can use the following correlation to calculate the local Nusselt number at the stagnation location.

## Slide 6: Cylinder in Cross Flow
Hilpert proposed the following empirical correlation () for the overall average conditions
Here and are constants that vary with .
Zukauskas proposed a modified correlation of the following form:
Here, all quantities are evaluated at , expect , which is evaluated at . For , and for , .
A comprehensive correlation was proposed by Churchill and Bernstein which is valid for all and for .
Re
For
valid for
Please refer to Chapter-7 of Fundamentals of Heat and Mass Transfer by Incropera, DeWitt, Bergmann and Levine for a details regarding the constants used in these correlations
Notes: Different researchers have proposed correlations, which are valid for specific situations, to calculate the average Nusselt number. The most frequently used ones proposed by Hilpert, Zukauskas, and Churchill are plotted here on this graph.

## Slide 7: Flow across a Tube Bank
Tube bank is a set or collection of tubes carrying a hot/cold fluid. These are commonly seen in devices such as heat exchangers where a second hot/cold fluid is passed over the tube bank to add/remove heat from the fluid inside the tubes.
The heat transfer to/from the tube bank is significantly impacted by the arrangement of the tube rows of the bank, which can take two major forms:
  Aligned
  Staggered
If multiple such rows are arranged such that the successive rows are only longitudinally displaced from the previous row, such a setup is called an aligned arrangement
If the successive rows are displaced both longitudinally and transversely, relative to the previous row, such a setup is called a staggered setup
Notes: Let us now look at a different case: Flow across a tube bank. A tube bank is a set or collection of tubes carrying a cold/hot fluid. These are commonly seen in devices such as heat exchangers, where a second hot/cold fluid is passed over the tube bank to add/remove heat from the fluid inside the tubes. These tubes can be arranged either in an aligned or staggered form. In the aligned arrangement, successive rows are longitudinally displaced from each other as shown here. In a staggered arrangement, in addition to longitudinal offset, the tube rows are also offset in the transverse direction as illustrated in this figure.

## Slide 8: Flow across a Tube Bank
In both the arrangements, the flow around the first row of tubes is equivalent to that of a crossflow over a singular cylinder, which we saw earlier.
  If the cylinders are closer, the presence of the neighboring cylinders affects the separation pattern and therefore the heat transfer levels.
In the aligned arrangement, the successive tube rows are in the turbulent wake of the previous row. Due to the turbulent nature of the fluid, for a specific range of the longitudinal distance, , the downstream tube rows exhibit higher convection coefficients.
This convection coefficient increases till about the 5th tube row beyond which it remains relatively constant.
For values of , the downstream rows are shielded from the flow by the upstream rows and as a consequence, the heat transfer levels are dramatically reduced.
This issue is not as pronounced in the staggered arrangement and therefore, the downstream tube rows exhibit enhanced levels of heat transfer.
Notes: For the first row of both the arrangements, the flow is equivalent to that of the crossflow over a singular cylinder which we looked at earlier. However, if the cylinders of the same row are very close to each other, they can influence the separation patterns of adjacent cylinders and therefore the heat transfer levels. In the aligned arrangement, as the flow passes over the tube rows, its turbulent character increases and consequently, the downstream tube rows exhibit higher convection coefficients than the previous rows. However, this behavior does not go on indefinitely and, instead, saturates around the 5th tube row, beyond which the heat transfer coefficients remain relatively constant. If the longitudinal offset of rows is small compared to the lateral distance between the cylinders, the downstream rows can be shielded from the flow by the upstream rows and the heat transfer levels are substantially reduced.

## Slide 9: Flow across a Tube Bank
To determine the average heat transfer coefficient across the entire tube bundle with number of rows (), Grimison proposed the following correlation based on film temperature:
Here, , and and are dependent on the ratio of , , and the type of tube arrangement.
The above equation can be extended to any fluid using a factor
For , the above formula can be modified using a correlation factor
valid for
valid for
Please refer to Chapter-7 of Fundamentals of Heat and Mass Transfer by Incropera, DeWitt, Bergmann and Levine for a details regarding the constants used in these correlations
Notes: This issue is not as pronounced in the staggered arrangement. Grimison proposed the following correlation to calculate the average Nusselt number for both the arrangements. Here, the constants C1 and m are dependent on the type of tube arrangement, and the longitudinal and lateral distances between the cylinder’s axes. This formula can be extended to any fluid, and to tube bundles with less than 10 rows using the following correlations. The variable ‘V_max’ can be calculated from mass conservation principles and varies with the type of tube arrangement.

## Slide 10: Flow across a Tube Bank
The is based on the maximum fluid velocity in the bank. Based on conservation of mass for an incompressible fluid, for the aligned arrangement, can be written as
In the staggered arrangement, the maximum velocity can occur either in the transverse () or the longitudinal () plane. The maximum velocity will occur in longitudinal () plane if the following relation holds
The formula for the aligned arrangement can be used if the maximum occurs in , if not, the following relation can be used to compute
Zukauskas proposed a correlation where all properties, except , are based on the arithmetic mean of inlet and outlet temperature
This modified correlation accounts for significant temperature differences between the inlet and outlet temperature.
valid for
Please refer to Chapter-7 of Fundamentals of Heat and Mass Transfer by Incropera, DeWitt, Bergmann and Levine for a details regarding the constants used in these correlations

## Slide 11: Impinging Jet flow
A fast-moving flow impinging on a solid surface is referred to as an impinging jet flow.
Such flow configurations are used to achieve enhanced heat transfer rates in applications such as glass tempering, metal annealing, deicing of aircrafts etc.
A typical configuration of an impinging jet is shown the figure on the right
  A nozzle, which can either be circular/round or rectangular/slot, is used to discharge the jet.
  The fluid exits the nozzle with a uniform velocity distribution. As it interacts with and entrains the ambient fluid, the jet starts spreading laterally.
  The potential core or the inviscid central region of the jet starts to contract and eventually collapses. Beyond the core collapse region, the velocity profile across the jet is entirely non-uniform.
Notes: Let us now shift gears and look at a different type of external flow: an impinging jet flow. When a fast-moving fluid exhausting from a nozzle or pipe impinges on a solid surface, it is called an impinging jet flow. An illustration of such a flow is shown here. These types of flows are used to achieve enhanced heat transfer rates in applications such as milling, glass tempering, deicing of aircrafts and other applications. The entire flow-field of an impinging jet configuration can be broadly classified into 3 zones.

## Slide 12: Impinging Jet flow
The entire flow-field of an impinging jet can be broadly classified into three zones
  Free jet zone – In this region, the impact of the impingement surface is not felt, and jet develops freely.
  Stagnation/impingement zone – This region is significantly influenced by the presence of the impingement surface.
    The fluid flow is decelerated in the wall-normal direction, and closer to the plate the flow is forced to change direction.
    A stagnation point with zero velocity exists where the jet hits the surface. The linear momentum of the jet is transformed into a horizontal acceleration.
  Wall jet zone – The region in which stagnation flow transforms into a wall jet flow
    The accelerating horizontal flow in the stagnation zone starts entraining fluid from the ambient.
    As a result, the flow starts spreading radially outward and takes the form of a wall jet.
Notes: Free jet zone is a region in which the effect of the surface is not felt by the fluid flow. Stagnation or impingement zone is a region which is significantly influenced by the surface. Before impinging on the surface, the flow is decelerated in the wall-normal direction and closer to the plate, the flow is forced to change direction. At impingement, a stagnation point with zero velocity exists where the jet hits the surface. From this point on, the linear momentum of the jet is transformed into a horizontal acceleration. The wall jet zone is the region in which the local flow takes the form of a wall jet. The accelerating horizontal flow in the stagnation zone starts entraining fluid from the surrounding and spreads radially outward to take the form of a wall jet.

## Slide 13: Impinging Jet flow
Most configurations of impinging jets used for heating/cooling applications have multiple jet arrays.
Due to the interaction of adjoining jets, secondary stagnation zones can also be formed.
Once the fluid from the jet impacts and extracts/imparts the heat from/to the surface and can no longer be used for heat transfer purposes, this fluid is called spent gas. The temperature of the spent gas is in between that of the nozzle exit and the surface. The overall heat transfer from/to the surface strongly depends on how the spent gas is vented from the system.
For the configurations shown here, if the spent gas is allowed to escape through the vents between the nozzles, equivalent local and average values of convection coefficients exist in close proximity (dotted region) near the nozzle.
For single/isolated nozzle, the heat transfer coefficients are dependent on the lateral distance away from the nozzle.
Array of Slotted Jets
Aligned Round Jets
Staggered Round Jets
Top view of Slotted Jets
Notes: Most configurations of impinging jets used for heating/cooling applications have multiple jet arrays. Due to the interaction of adjoining jets, secondary stagnation zones can also be formed. Once the fluid from the jet extracts or imparts the heat from or to the surface, and can no longer be used for heat transfer purposes, this fluid is called spent gas. The overall heat transfer from/to the surface strongly depends on how the spent gas is vented from the system. For the configurations shown here, if the spent gas can escape through the vents between the nozzles, equivalent local and average values of convection coefficients exist in close proximity (dotted region) of the nozzle.

## Slide 14: Impinging Jet flow
According to Newton’s law of cooling, for a surface temperature of and nozzle exit temperature of , the heat flux can be written as
For a single round nozzle, and for a single slot nozzle, , where is the width of the slot.
When the distance between the nozzle exit and surface is large i.e. , heat transfer is maximum at the stagnation point, and decreases with increasing distance.
For smaller separations, the number distribution exhibits a second maximum. This is due to the rise in turbulence levels associated with the transformation of the accelerating stagnation region flow to a wall jet.
  Additional maxima are also possible due to phenomena like vortex formation, laminar-to-turbulent wall jet transition etc.
For jet arrays, interaction of adjoining jets also results in secondary maxima. For such configurations, the heat transfer distribution is also 2D i. e. variations of heat transfer coefficient can be observed in both directions parallel to the surface.
Notes: The plot here shows the Nu number distribution along the plate starting with the stagnation point. When the distance between the nozzle exit and surface is large, that is 𝐻/𝐷ℎ > 5, the heat transfer is maximum at the stagnation point, and decreases with lateral distance along the plate. Due to the rise in turbulence levels associated with the transformation of the accelerating stagnation region flow to a wall jet, for smaller separations, the 𝑁𝑢 number distribution exhibits a second maximum. For jet arrays, interaction of adjoining jets also results in secondary maxima. For such configurations, the heat transfer distribution is 2D which means that variations of heat transfer coefficient can be observed in both directions parallel to the surface.

## Slide 15: Impinging Jet flow
To obtain average numbers, the local values are integrated over an appropriate surface area.
For a single round jet, Martin proposed the following correlation
For an array of round jets,
For a slot jet, the following correlation can be used to obtain averaged number
For an array of slot jets,
where
Valid for
where
Valid for
where
Valid for
where
Valid for
Please refer to Chapter-7 of Fundamentals of Heat and Mass Transfer by Incropera, DeWitt, Bergmann and Levine for a details regarding the constants used in these correlations
Notes: Different correlations exist depending on the nozzle geometry and whether the configuration is a single nozzle or an array of nozzles. The parameters that appear in these correlations such as nozzle exit area, nozzle-plate separation distance, and Reynolds number, have a specific range over which the correlations are valid. With that, let’s wrap up this lesson.

## Slide 16: What have we covered?
Introduction to Forced Convection
Dimensionless Numbers and Correlations
Velocity and Thermal Boundary Layers
Boundary Layer Equations and Conditions
Forced Convection over a Flat Plate
Flow Types: Laminar & Turbulent
Cross Flow: Cylinder, Tube Bank & Jet Flow