## Slide 1
Simulation Example 1:
Convective Heat Transfer – Tube Bundle
Created by Ansys ACE
Edited by Ansys Academic Development Team

## Slide 2
Forced Convective Heat Transfer in a 2D Staggered Tube Bundle - Set Up - YouTube

## Slide 3: Results
The contours of static temperature plotted below clearly show air extracting heat from the cylinders and convecting downstream.
The contours of velocity magnitude plotted below show flow field of air in the tube bundle.
  The air accelerates as it squeezes between the cylinders due to the venturi effect.
Contours of Static Temperature
Contours of Velocity Magnitude

## Slide 4: Results
The variation of heat transfer rate for each of the rows, for both the 4 rowed and 6 rowed configurations, is shown below.
The upstream rows act as turbulators and increase the turbulent intensity of the fluid, which results in higher heat transfer rate for the downstream rows.
  However, this behavior is not sustained and saturates around the 5th tube row
Chart: Row Number
| wall-tube1 | wall-tube2 | wall-tube3 | wall-tube4 | wall-tube5 | wall-tube6
6 rowed configuration | 165.9798 | 183.4435 | 188.5371 | 202.359 | 203.0794 | 201.4635
4 rowed configuration | 165.2941 | 181.4984 | 187.9141 | 200.9681