## Slide 1
Simulation Example 1:
Round Impinging Jet
Created by Ansys ACE
Edited by Ansys Academic Development Team

## Slide 2
Round Jet Impinging on a Heated Flat Plate - Set Up - YouTube

## Slide 3: Jet Velocity Field
As the jet exits the nozzle, the jet starts spreading due to viscous effects in its shear layer, as can be seen in the velocity contour plot.
The middle portion of the jet, represented by red color, is the potential core of the jet and it often referred to as the Inviscid Core.
The region outside the Inviscid Core is the Free Jet region. This region of the jet is not affected by the impingement.
The velocity of the jet is sharply reduced to zero at the stagnation point. The upstream jet flow decelerates in the normal direction, and the plate forces the fluid to change the flow direction (observed by the velocity vectors). This is the Stagnation / Impingement Zone.
Further downstream along the plate is the Wall Jet region, where the fluid is accelerating horizontally. Here, the ambient air is entrained by the jet as it flows radially outward along the plate.
Air Flow
Inviscid Core
Free Jet
Stagnation Point
Wall Jet
Wall Jet
Entrained Air
Stagnation/Impingement Zone
Velocity Contours

## Slide 4: Jet Temperature Field
Cold air impinges on the hot plate. Thermal energy from the plate is transferred to the moving fluid. Convection is the primary mode of heat transfer in this problem.
The fluid temperature increases as it flows radially outward along the flat plate. This is clear from the plot of the fluid wall adjacent temperature along the length of the flat plate.
A sharp temperature gradient is observed between the flat plate and the ambient fluid very close to the wall (as seen in the magnified Temperature contour plot). This is the primary region of interest for heat transfer. There is no heat transfer away from this region.
Total thermal power removed from the flat plate by the impinging jet is 633.14 W.
axis
Hot Wall
Stagnation Point
Wall Adjacent Temperature, K
Radial Distance along the plate, m
wall-impinge-fluid-out
wall-impinge-fluid-jet
Air Flow
Temperature Contour

## Slide 5: Average Surface Nusselt Number
The average Nusselt Number for a single round jet is estimated using the following correlation.
H
D
In Ansys Fluent, the Surface Nusselt Number is defined as follows:
As observed in the plot, the average Nusselt number estimated from the simulation shows good agreement with the correlation at various values.
This decrease in the average Nusselt number is because of increasing mean temperature of the fluid as it flows downstream along the plate.
= reference length, m (0.02 m)
= heat transfer coefficient,
= surface heat flux, ,
= local wall temperature, , and
= reference temperature, (= 300 K)