## Slide 1
Fluid Kinematics Lesson 2
Description of Fluid Motion
Created by Ansys ACE
Edited by Ansys Academic Development Team

## Slide 2: Mathematical Description of Fluid Motion
Using the notion of a continuum, we can develop mathematical models of fluid motion, where the goal is to know the state of the fluid (e. g., velocity, pressure, density, temperature, etc.) at any given point in space and time.
We can thus mathematically describe any fluid property with respect to a spatial coordinate system, such as the Cartesian coordinates , and at a given time .
x
z
y
The goal of mathematical fluid dynamics is to solve models of fluid motion to determine, for all times, the state of the fluid at every point in space within a given region of interest.
Notes: The final goal of studying fluid dynamics is to understand the flow field and translate these learnings into developing any engineering application or product. For example, we study fluid dynamics to understand the behavior of the flow field around an aircraft. This provides insightful information on how its design should be modified to generate the larger force for the aircraft to fly. This force is called the lift force . Similarly, we understand the flow around an impeller in a mixing tank so we can get more uniform mixing . A good understanding of the flow variables such as velocity, pressure, density, temperature in the flow field help engineers make products better. The need for understanding these flow fields brings us to the mathematical description of fluid motion. Here, we use mathematics as a tool to describe the flow field in both time and space. To do this, we invoke the continuum assumption, using which, we treat flow variables such as velocity, pressure, temperature, and density as continuous functions in time and space.

## Slide 3: What is Fluid Kinematics?
Before we start developing the governing equations of fluid flow, it is helpful to talk about ways of describing fluid motion. This topic is often referred to as fluid kinematics.
Fluid kinematics focuses on fluid motion itself and examines quantities like positions, velocities and accelerations. It does not consider forces acting on the fluid which make it flow, or conservation laws that the fluid must obey. These belong to the realm of fluid dynamics.
In this lesson, we will introduce common concepts, definitions and terminology of fluid kinematics.
Notes: Before describing the governing equations for fluid motion and different ways of solving them, we will first venture into the topic of fluid kinematics. Fluid kinematics does not consider forces acting on the body. It only examines the motion of the fluid. The parameters of interest here are position, velocity, and acceleration.

## Slide 4: Fluid Velocity Field
Fluid flow
Recall that the velocity of a fluid at a point can be represented mathematically using a vector field which is a function of space and time. In the stationary coordinate system, we can write this as:
If we know the velocity at each point in space, we have a description of the flow, much like tufts of thread in an airflow as shown in the picture (which shows the surface airflow over a winglet on a jet aircraft wing).
Notes: Let us first start with the velocity field. Fluid velocity is a vector quantity, which means it has both magnitude as well as direction. It can be described in the form of 3 components in the cartesian coordinates which are X, Y and Z. Fluid velocity can be a function of both space and time. Knowledge of this variable at each point in space helps us describe the bulk motion of the fluid.

## Slide 5: General Description of Fluid Motion
A general motion of a fluid element can be described as a superposition of four components:
  Translation
  Volumetric deformation
  Angular deformation
  Rotation
A
B
C
A’
D’
C’
D
B’
Translation
Rotation
Angular Deformation
Volumetric Deformation
Notes: If we visualize each fluid particle as a fluid element in the flow field, depending on the flow, one or more things can happen do this fluid element. This element can undergo translation or rotation or angular deformation or volumetric deformation. In a real flow field, the fluid element can simultaneously experience one or more of any of these components in the flow field. In this lesson we will discuss each of these components in detail.
Translation of a fluid element involves linearly displacing this element from one point to another. In pure translation, the shape of the fluid element does not change. It merely moves from one location to another.

## Slide 6: Rotational Motion
Rotational motion of the fluid element is described by its angular velocity . Consider a plane fluid element of initially perpendicular sides OP () and OQ () lying on the plane. The velocity components at O are and . Using Taylor’s series, we obtain the velocity components at P, Q and R as shown below.
Over a time the displacements PP’ and QQ’ are:
Corresponding angles of deformation per unit time are obtained by
The average angular velocity of the fluid element about the z-axis is:
Notes: When a fluid element undergoes pure rotation, it is rotating about its respective element axis. This rotation is given by a physical quantity called angular velocity. We take a regular 3D fluid element aligned along the XY plane with dimensions: delta_x and delta_y. The velocity components at each point are given by u(x,y) and v(x,y). If we take u and v to be the velocity components at O, then the x and y velocity components at P can be obtained using Taylor series. We can similarly obtain the velocity components at other points P, Q, and R. The rate of deformation for d_theta_1 can be expressed by the following limit. Since d-theta-1 is small, this ratio is further simplified in terms of the net displacement of point P to P' over delta_x. As displacement occurs from P to P' over a small time dt, we can write this displacement PP' using the v component of velocity. When we replace PP', we obtain the final value of deformation per unit time for d_theta_1.
In a similar manner, the displacement QQ' can be written for a small time dt. Here the negative sign indicates displacement is in the negative x direction. Following a similar approach, we can arrive at the deformation per unit time for d_theta_2.

## Slide 7: Rotational Motion
Applying similar considerations to the and -components of the angular velocity , its final expression can be written as:
From vector calculus:
where is called the flow vorticity, which is twice the rotational speed of the fluid element.
In nature, we see phenomena represented by vorticity everywhere, from swirling eddies in a river to vortices being shed from behind a bluff body.
2
Notes: The overall angular velocity about the z-axis is defined as the average angular velocity of these two deformations per unit time. Other components of angular velocity can also be defined in the same manner.
In fluid dynamics, vorticity is defined as the measure of rotation of a fluid element and mathematically, it is equal to twice the angular velocity or rotational speed of that element. A more detailed discussion on vorticity and vortex flows is presented in the next lesson.

## Slide 8: Angular Deformation
Angular deformation of a fluid element can be described as a change in its shape wherein a straight line connecting two points within the element before the deformation is not parallel to the straight line connecting them after deformation.
The figure below shows that, in addition to rotation, velocity derivatives may lead to the angular deformation (change in shape) of the fluid element.
The rate of change in the right angle formed by the lines OP () and OQ () due to angular deformation is called the rate of shearing strain and is given by :
These are the six components of the symmetric rate of shearing strain or rate of angular deformation.
Notes: Angular deformation is the third type of fluid motion and can be described as changing the angle between the two mutually perpendicular segments of the fluid element. For the fluid element shown, it is defined as the rate at which the angle between the line segments OP' and OQ' decreases. Over a time period delta t, the change in this angle due to angular deformation is because of rate of shearing strain. This expression is only applicable in the xy plane. We can similarly define the other components. Together, these six components are called symmetric rate of shearing strain or rate of angular deformation.

## Slide 9: Volumetric Deformation
Volumetric deformation involves a change in element’s shape wherein a straight line connecting two points within the element before the deformation is parallel with a straight line connecting them after the deformation.
The fluid element will change its shape in the direction via a volume deformation only if , which represents the component of longitudinal rates of strain in the direction.
Consider the -direction,
Similar terms will result for the and components, giving:
Notes: The last and the final type of fluid motion commonly found in fluid elements is volumetric deformation. The shape of the fluid element is defined by the angle between the line segments. During volumetric deformation, this angle remains constant. This retains the original shape of the element. However, length of the element in x and y directions change. To change the length of the fluid element in the x direction, it will require a non-zero value of u velocity gradient along the x direction. Similarly, changes in length in the y-direction will require dv/dy to be non-zero. This analysis can be extended to the z-direction as well. These individual terms are called components of longitudinal strains in x, y, and z directions respectively. The total rate of volumetric strain is given by the following equation.

## Slide 10: Angular and Volumetric Deformations
Together, angular and volumetric rates of strain describe general deformations of a fluid element and they can be combined into the strain rate tensor .
This is a symmetric tensor with diagonal terms representing volumetric deformations and off-diagonal terms describing angular deformations. In three dimensions, the strain rate tensor is written as:
Notes: The angular and volumetric strains together form the overall strain tensor. The off diagonal terms of this tensor describe the angular deformation whereas the main diagonal terms represent volumetric deformation .

## Slide 11: Streamlines
For a flow field which is steady-state (velocity field is a function of space only), we can define a streamline as a path in space which an imaginary particle would take if it were “riding” along with the flow.
Such a curve has the property that the velocity vector is tangent at each point along the streamline. This fact will permit us to develop an equation for the curve based on the velocity field.
Mathematically, the requirement of tangency results in the following mathematical definition of the streamlines:
This can also be written in the compact vector form:
Streamline
Fluid
velocity
vector
Notes: Until now, we have learnt about the velocity vector and the different types of motion undergone by a fluid element. Let us now switch gears and look at tools to visualize the flow field. At any given instant in time, we can draw lines in the flow field such that they are tangential to the local direction of flow at every point. In other words, these lines are tangential to the local velocity vectors in the flow field. These lines are called streamlines. In case of steady flows, velocity is not a function of time and remains only a function of space. Therefore, the streamlines do not change in time. If we define an imaginary particle on a streamline in steady flows, it will remain on this streamline as if it were riding along.

## Slide 12: Pathlines and Streaklines
For an unsteady fluid flow, if we release a particle in the fluid, we can track its position as a function of time. The curve that is traced out as we follow the particle is called the pathline.
In experimental analysis, typically a tracer is released from a fixed point to visualize the motion of the fluid. The tracer shows the current location of all the particles that passed through the emission point in the past. The resulting path is called a streakline.
Mathematically, they are given by:
pathline
streakline
denotes the position of a given fluid particle at time
denotes the position of a given fluid particle at the emission time
  Note that if the velocity is a function of time, the pathlines, streaklines and streamlines will NOT be the same!
Notes: In addition to streamlines, we also use pathlines and streaklines to describe the motion of a fluid. A pathline is the line traced out by the trajectory of a moving particle as it flows in the flow field. To define a streakline, we have to focus our attention to a particular region in the flow field. If we release fluid particles at this exact location in the flow field, the line connecting all the individual particles crossing this unique location will form a streakline . In most experiments, we use color dyes to visualize the flow field. Such dyes are released at one particular location in the flow field. After a considerable amount of time, the dye streak represents a streakline.

## Slide 13: Visualizing Streamlines
Under the assumption that the flow has a steady behavior, streamlines can be visualized in real flows by injecting dye, smoke or tiny particles into the fluid. Indeed, for steady-state flows, pathlines, streaklines and streamlines are the same.
Using smoke injection to visualize streamlines around a car
Notes: It is important to understand that, for steady flows, the streamlines, path lines, and streaklines can all be represented by one single line. In the next lesson, we will learn more about these lines and how to visualize them.

## Slide 14: Lagrangian Description of Fluid Motion
A fluid flow field can be thought of as comprising a large number of finite-sized fluid parcels which have mass, momentum, internal energy and other properties.
A way of looking at fluid motion is to “ride” along with the parcel. We can use the center of mass of the parcel to describe the parcel velocity:
We can apply physical laws to each fluid parcel to develop models of fluid motion. This is called the Lagrangian description of fluid motion.
Fluid
Parcel
Fluid parcel path
Notes: But, before we get there – let us wrap up by talking about two different types of mathematical descriptions to understand the flow field. The first one is the lagrangian description of the flow field. In this description, the fluid is assumed to be a collection of a large number of fluid parcels. The idea in the lagrangian description is to follow these individual fluid parcels through the flow field. The trajectory of these parcels will help us understand the flow. In fact, the motion of these fluid parcels is described as a function of time. This helps the analyst estimate the position, velocity, and acceleration of each fluid parcel in time .

## Slide 15: Eulerian Description of Fluid Motion
We can also consider how flow properties change at a fixed region in space, , rather than following individual fluid particles. The velocity of a fluid at a point can be represented mathematically using a vector which is a function of space and time:
Physical laws can then be applied to the region (control volume). This is the Eulerian description of fluid motion.
Control
Volume
Notes: The second type of mathematical description is the Eulerian description. In this, we focus on a particular region in space rather than on individual fluid particles. These regions in space are commonly referred to as control volume and its boundaries are referred to as control surfaces. Fluid is viewed as it enters and exits these control surfaces. Flow parameters and fluid properties are described to be a function of both time and space .

## Slide 16: Is one better than another?
The fundamental laws of fluid motion are easily formulated in the Lagrangian framework.
However, the solution of these equations for a specific flow is more easily carried out using the Eulerian framework, as it permits them to be expressed as a system of differential equations.
We will therefore develop the fundamental equations of fluid mechanics as follows:
  Formulate the governing equations using the Lagrangian system
  Transform the equations from the Lagrangian system to the Eulerian system using a fundamental principle called Reynolds Transport Theorem.
  The resulting differential equations can then be solved for specific flow fields of interest, given suitable initial/boundary conditions.
Our goal is to develop a mathematical model for fluid flow in each region of space and to apply this model to practical problems.
Notes: Naturally, the next question would be: “is one description better than the other?” The answer is no. We can pretty much use either of the two formulations to describe the fluid flow. We can derive the fluid equations using either of the two formulations and, if solved correctly, both formulations give the same exact solution.

## Slide 17: Summary
In this lesson we introduced the concept of fluid kinematics, described the fluid velocity field and explained general representation of fluid motion.
Four basic components of fluid element motion (translation, rotation, angular and volumetric deformations) and their mathematical description (vorticity, strain rate tensor) were discussed.
Streamlines, pathlines, and streaklines were outlined as methodologies to represent and visualize the velocity field.
The Lagrangian framework, which follows a fluid parcel, and the Eulerian framework, which monitors a fixed region in space, were introduced.
The Lagrangian framework can be used to formulate the governing equations, while the Eulerian approach can be used to obtain solutions for flow fields.