## Slide 1
Fluid Kinematics Lesson 3
Fluid Flow Rotation
Created by Ansys ACE
Edited by Ansys Academic Development TeamLesson 3
Notes: Certain flows show a significant amount of rotation while others do not. What cause these flows to be rotational? In this lesson, we will be learning about the rotationality of fluid element. It is important the conditions under which the fluid flow is rotational. Some of the concepts outlined in this lesson were the basis for predicting lift forces on an aircraft after the first flight by Wright Brothers in 1903. In those days, we did not have the computing power (we have today) to solve mathematical models or measurement techniques to optimize aircraft wings. The physicists and mathematicians therefore relied on these techniques to come up with approximate solutions for such engineering problems.

## Slide 2: Irrotational Flow
The definition of vorticity () is:
A fluid velocity field is said to be irrotational if the vorticity is zero everywhere.
An example of irrotational versus rotational flow is shown on the right
  As the irrotational flow moves downstream, a marker in the flow does not change orientation (no rotation)
  If the flow is rotational, the marker would rotate as it moves downstream
When is a flow irrotational?
  If the flow entering a region is irrotational, we will see that (in the absence of viscous effects) the flow will remain irrotational. This is approximated for smooth flows outside boundary layers.
Irrotational
Rotational
Notes: we defined vorticity as the measure of the rotation of a fluid element. In the case of irrotational flows, each individual fluid particle does not change its orientation in the flow field. In other words, these particles do not rotate as they travel through the flow field. This happens only when the fluid particle is under the influence of either body force or normal pressure force. Rotational component requires the action of shearing force or shear stress. In fluid dynamics, shear is related to the rate of angular deformation. Therefore, a fluid cannot rotate without undergoing angular deformation. The relationship between shear stress and angular deformation is given by viscosity. Therefore, a flow is rotational only if it is viscous. For irrotational flows, vorticity is equal to zero. Because of this, the fluid velocity can be expressed as a function of the gradient of a scalar variable, phi. This variable is defined as the velocity potential.

## Slide 3: Irrotational Flow
From vector calculus, the condition for the vorticity to be zero in an irrotational flow is given as:
This requires that the velocity field is a potential field, i.e. the velocity vector is expressed in terms of a potential function as:
This simplifies formulations of governing equations and makes certain classes of irrotational flows open to be solved analytically. We will discuss this in more detail in subsequent lessons.
One property of an irrotational flow is that its circulation along any closed contour is zero:
And, as a result, a streamline in an irrotational flow cannot be closed on itself.
Notes: The circulation over any closed curve or contour is defined as the line integral of the tangential component of velocity about this closed curve. For irrotational flows, circulation is also equal to 0. As a consequence, streamlines cannot form closed curves in irrotational flows.

## Slide 4: Rotational Flow
A flow is rotational if fluid elements undergo rotation about their axis while flowing along streamlines.
The flow is rotational when its vorticity vector is non-zero in some of its regions.
If the flow is rotational everywhere, then the divergence of the vorticity vector is zero:
By applying the Gauss Divergence Theorem to the above equation, we can conclude that the vorticity flux across any closed surface is zero:
Notes: In almost all flows that occur in nature, the individual fluid elements rotate about their respective axes as they travel through the flow field. Such flow fields are called rotational. For these flows, the vorticity vector is non-zero. In fact, from the basics of vector calculus, the divergence of the vorticity vector for fully rotating flows is 0. This means that the vortex field is solenoidal. There are no sources or sinks in this vector field. For fully rotational flows, the vorticity field lines are completely closed loops. By extension, we can say that the vorticity flux crossing over any close surface is also 0. This means that the net outflow of vorticity through any close surface is 0.

## Slide 5: Vortex Lines and Vortex Tubes
Similar to the streamline definition, a vortex line can be defined as a curve with the property that the vorticity vector is tangent at each point along the vortex line.
Mathematically, the requirement of tangency results in the following mathematical definition of the vortex lines:
Vortex lines passing through each point of a closed contour form a so-called "vortex tube."
The conditions of zero vorticity flux through a closed surface yields:
Notes: Similar to the way we introduced streamlines to visualize the flow field, we can introduce vorticity lines to visualize the rotationality of the flow field. The tangent of a vorticity line is parallel to the local vorticity vector. These lines can be defined by the following expression. If we consider a closed loop or curve and draw the vortex lines passing through all points on this curve, the obtained 3D shape is called a vortex tube. In fact, the flow of vorticity through any cross-sectional surface of a vortex tube is a constant all along the tube. This is true at every instant of time.

## Slide 6: Vortex Lines and Vortex Tubes
The integral quantity
  is called the “strength” of the vortex tube, or simply vortex strength*, and it is the same everywhere along the tube.
A tornado is a fascinating example of a devastating vortex tube observed in nature.
* Vortex strength is sometimes confusingly called vortex flux, which is not accurate, since it does not refer to the advection of vorticity.
Notes: The integral shown here refers to the strength of the vortex or simply vortex strength.
A tornado is an excellent example of a vortex tube occurring in nature.
Another example is smoke ring created in air. Dolphin create vortex tubes in the form of bubble. If we take a linear vortex tube and join the two ends, it would resemble a smoke ring or bubble ring.

## Slide 7: Helmholt’z Vortex Theorems
Helmholtz's theorems, named after Hermann von Helmholtz, state the following about vorticity fields:
Vortex lines move with the fluid, i.e. fluid elements lying on a vortex line at some instant continue to lie on that vortex line.
The strength of the vortex tube is constant along its length and in time.
Fluid elements initially free of vorticity, remain free of vorticity.
Vortex tubes can only extend to infinity, form a closed loop or end at a solid boundary.
While rigorous mathematical proofs of these theorems is beyond the scope of this course, they can be formally derived in the framework of fluid kinematics by ignoring fluid compressibility and viscous (and other) forces.
Helmholtz theorems played an important role in developing the classical lifting line theory for lining bodies (airfoils, wings), attributed to Prandtl (1921).
While statements in Helmholtz's theorems may at first glance appear theoretical, they find confirmation in nature. A tornado always attempts to touch the ground as the most optimal way to satisfy the 4th statement above.
Notes: A German physicist Herman von Helmholtz came up with a series of theorems that defined the motion of a vortex tube. Prandlt, in 1921, made use of these mathematical theorems developed by Helmholtz to develop the classical lifting theory for line bodies such as airfoils and wings. He was able to solve for the overall lift force generated on these line bodies. Helmholtz theorem states four main facts for pure rotating flows.
Vortex lines move with the fluid, that is fluid elements lying on a vortex line at some instant continue to lie on that vortex line. This is valid for an ideal rotational flow. As seen in this example of the smoke ring, the fluid particles which are on the vortex lines will remain on those lines.
The strength of the vortex tube is constant along its length and in time. This is true unless acted upon by a dissipative force such as viscous resistance. Smoke rings die out because of this resistive force applied by the surrounding air. In an ideal world without any air resistance, once the rings are generated by an external means, their strength should not change.
fluid elements initially free of vortex remain free of vortex. The fluid elements which are outside these vortex tubes will remain outside. This is true unless the vortex tube is acted up on by an external disturbance.
vortex tubes can extend to Infinity, form a closed loop (like in the case of smoke rings or dolphin bubble rings) or end at a solid boundary. In fact, a practical example of this is a tornado. It always attempts to touch the ground somewhere.

## Slide 8: Summary
Irrotational and rotational flow approximations provide simplifications to fluid flow descriptions, which make possible analytical solution approaches to certain classes of problems.
Rotation flows are characterized by the vorticity vector, which can be represented and visualized by vortex lines and vortex tubes.
Helmholtz’s vortex theorems represent formal statements of vortex kinematics. They provided an important basis for the theory of lifting bodies developed in the first half of the 20th century.