## Slide 1
Fluid Kinematics Lesson 4
Fluid Flow Visualization
Created by Ansys ACE
Edited by Ansys Academic Development Team– Lesson 4
Notes: In the previous lesson, we understood the difference between rotational and irrotational flows. We also learnt about vortex motion and the importance of vorticity. Naturally, the next question that comes to mind is - How can we visualize the flow? How do we visualize a vortex ? Can we experience what happens to flow around an aircraft wing when it is at the cruising altitude? In this lesson, we are going to discuss some flow visualization techniques used in the engineering design cycle to develop products.
In most scenarios, flow visualization provides a qualitative visual understanding of what the flow looks like. In some cases, like in the case of modern computational flow visualizations, the resultant information is useful to quantify these flows for various engineering applications. In this lesson, we will limit ourselves to the qualitative aspects of flow visualization. Broadly speaking, visualization techniques can be classified as experimental and computational.

## Slide 2: Wind Tunnel
A wind tunnel uses the concept of streamlines to understand the aerodynamics of an automobile or an aircraft by mimicking its motion.
A scaled model is kept stationary and high-speed air is blown on the model using a large rotating fan.
Smoke is used to create streamlines around these scaled models.
The interaction of the smoke lines with the body helps the engineer understand the impact of its shape, providing a macroscopic understanding of the overall flow around the body.
A general sense of the airflow and the generated vortices can be obtained from these smoke lines.
Smoke lines over an automobile
Model of an aircraft in a wind tunnel
Notes: Most visualizations analyze the flow behavior through surface flow patterns. Experiments conducted in wind-tunnel facilities use the concept of streamlines to understand the aerodynamic shape of an aircraft or an automobile. Wind-tunnels mimic the motion of these means of transportation. Generally, a scaled model of an automobile or an aircraft is used in these wind-tunnel tests. Sometimes, the object of interest is only a small portion - such as an aircraft wing or an automobile spoiler. The scaled model is fastened in a wind-tunnel facility and is maintained stationary. High-speed air is blown on these models using a large rotating fan. The air moving around this stationary object gives us an understanding on what would happen if the object were moving at a certain speed.
White smoke jets are released at specific locations to create streamlines around these scaled models. These smoke jets are released from either one or a rake of multiple smoke generators in the wind-tunnel. The generated smoke blows around the body being tested. [7] The interaction of these smoke lines with the body of the aircraft or automobile helps the engineer understand the impact of its shape. These smoke lines provide a macroscopic understanding of the overall flow around the body. A general sense of where the air is flowing and where the vortices are being generated can obtained from these smoke lines [8].

## Slide 3: Tufts
Tufts are used to understand and visualize flow very close to the body.
Tufts are small strips of yarn or stings about long. One end is securely glued with the surface of the model being tested while the other end is free to move with the flow.
Length and weight of tuft is carefully selected so that they can provide a good understanding of the flow very close to the body without altering the flow.
It helps to obtain qualitative information on cross-flow, reverse flow and flow separation close to the body being analyzed.
These flow behaviors influence the overall resistance offered by the flow.
Tufts being used for Flow Visualization in Wind Tunnel
Courtesy: NASA
Notes: Tufts
In addition to white smoke, fluid engineers make use of flow tufts to understand and visualize the flow close to the body. Tufts are small strips of yarn or strings about 15 cm long. One end of the tuft is securely glued to the surface of the model to be tested before it is placed inside the wind-tunnel. As air blows over these flow tufts, the loose end of these tufts is free to move with the flow. Because the length and weight of these tufts are carefully selected, they provide a good understanding of the flow very close to the body without actually altering the flow. These are particularly crucial in obtaining qualitative information on crossflow, reversed flow, and flow-separation close to the solid body of the aircraft. These flow behaviors influence the overall resistance offered by the body to the flow. In addition to wind-tunnel testing, tufts are also used to understand flow patterns during actual in-flight tests. This is done by recording a video of these tufts during the flight and subsequently analyzing the obtained flow patterns.

## Slide 4: Surface “Oil Flow” Visualization
The surface of the body of interest is coated with a viscous oil which is transported by high-speed air flowing around the body, creating streaks on the surface.
The resulting streaks can be used to visualize the flow on the surface of the body of interest.
These oil streaks act as good indicators of flow separation.
The initial thickness of the oil film is an important parameter to obtain useful results.
Courtesy: NASA
Courtesy: NASA
Notes: Another popular flow visualization technique employed in high-speed wind tunnels is to observe oil-flow steaks over surfaces. The surface of the test object such as wing of an aircraft are coated with viscous oil. The oil is transported by the flowing high-speed air, leaving oil streaks on the surface of the test object. These oil streaks are good indicators of flow separation over the body. After a considerable amount of testing, the wind-tunnel is stopped and photographs of the oil streak patterns on the surface are taken. The initial thickness of the oil film is an important factor to obtain meaningful results from this flow visualization technique.

## Slide 5: Water Tunnel Visualization
Dye injection in water
Water tunnels are used to visualize and evaluate the hydrodynamic behavior of submerged bodies under water.
Like wind tunnels, the model is kept stationary as water flows over it.
Colored dyes are injected into the flow, which helps to visualize macroscopic flow around the bodies and the locations of vortices.
Certain water tunnels can increase or decrease the static pressure to perform cavitation studies, which play a crucial role in the design process of propeller blades of submarines and ships.
Notes: Wind-tunnels are a great way of visualizing external air flow over bodies. In a similar manner, water tunnels are used to visualize and test hydrodynamic behavior of submerged bodies under water. For these submerged bodies, it is important to understand the lift or drag forces acting on them. In these water tunnels, the model to be tested in kept stationary in flowing water and the flow over these submerged bodies is visualized by injecting colored dyes into the flow. Similar to the white smoke lines in a wind-tunnel, the lines obtained by injecting these colored dyes provide information about the macroscopic flow around the submerged body. In addition, it also provides information related to the whereabouts of vortices. Certain water tunnels have the ability to increase or reduce the internal static pressure to perform cavitation studies. These studies are extremely important for designing propeller blades of a submarine or a ship.

## Slide 6: Schlieren Photography
Schlieren photography is an optical visualization technique that distinguishes fluids of varying densities.
It uses the principle of refraction, i.e., light rays bend when traveling from a denser medium to a rarer medium and vice-versa.
The setup consists of a bright source of light, a knife edge for focusing the light and two concave mirrors on either side of the flow being visualized.
This method was primarily developed for studying high-speed supersonic flows.
Light source
Concave mirror #1
Concave mirror #2
Image plane
Measurement section
Schlieren setup
Bow shock & normal shock
(Ansys Fluent simulation)
Notes: Schlieren photography is an optical visualization technique which distinguishes fluids with varying densities. It uses the principle that light rays bend differently when passing from a denser medium to a rarer one or vice versa. It uses a bright source of light, a knife-edge - for focusing the light better, and two concave mirrors on either side of the flow being visualized. It was primarily developed for studying high-speed supersonic flows. Shock waves are common in supersonic flows and this visualization technique was developed to capture these shock waves. A shock wave is a thin narrow region with high gradients of pressure, density, and temperature. The rays of light passing through this shock waves are bent and are stopped by the knife edge and do not reach the recording device. They are therefore captured as dark lines on the image. Schlieren photography can also be used visualize the flow around a hot body.

## Slide 7: Visualization in Simulation
While experimental visualization techniques provide invaluable insight into the flow physics, the information they provide is oftentimes limited by:
  The amount of information they can provide
  Placement of the instrument
  Optical blockage
  The flow regimes of the measurement devices used
Experimental visualizations are also expensive, both in terms of time it takes to set up the apparatus, conduct and post-process the experiment, and the cost of equipment and staff time.
On the other hand, visualization of a numerical flow field calculated with a high-fidelity Computational Fluid Dynamics code is free of these limitations and can present a complete virtual visualization of the fluid flow, oftentimes at a fraction of the cost of the experiment
Heat sink: contours of
velocity magnitude
Room with air conditioning vents – velocity vectors
Notes: All these experimental visualization techniques require careful calibration and instrumentation. In fact, most of these experimental set-ups are expensive and can only be operated by trained staff. Moreover, not all aspects of flow physics are brought out through these experimental techniques. Therefore, in this modern age, computer models are capable of providing insights into flow physics that cannot be captured experimentally. For fluids, these models are generally referred to as computational fluid dynamics, (CFD, in short).

## Slide 8: Visualization in Simulation
A multitude of options is available to visualize and examine details of a simulated flow field:
  Contour plots of flow variables on arbitrary defined surfaces
  Distribution of vector fields
  Streamlines, pathlines, particle tracks
  Animations of flow fields
  Visualization of 3D flow structures such as vortices and turbulent eddies
  3D submerged virtual reality, or virtual travel through the fluid system
Pulsing pathlines in a cyclone separator
Notes: The results obtained from these models are capable of analyzing flow data and finally display the flow as surface plots such as contours, vector plots, streamlines, pathlines, and particle tracks plot. With the invention of virtual reality, users can now get an immersive experience of the flow field. We are now able to travel along a streamline or visualize the vortex in the flow-field from its center. The beauty of computational visualization lies in the fact that the engineer can now understand aspects of the flow which might not be possible with experimental techniques.

## Slide 9: Visualization in Simulation
These animation examples illustrate the power of virtual visualization of numerical simulation results which would be difficult or impossible to obtain using experimental techniques:
Generation and propagation of sound waves by supersonic impinging jet
Details of instantaneous turbulent structures behind a landing gear
Notes: In fluid dynamics, it is important to use both these sets of flow visualizations. In fact, in most industries, experiments and computations go hand in hand during the product design cycle.

## Slide 10: Summary
Experimental visualization of fluid flows provides important insights into flow physics and expands our understanding of fluid dynamics.
Visualization of simulation results calculated by a high-fidelity CFD code adds capabilities to examine flow features otherwise not observable by the experimental techniques and further contributes to broadening our knowledge of fluid flows.
Mixing of fluids at different temperatures in a mixing elbow