## Slide 1
Fluid Kinematics Lesson 5
Fluid Flow Measurement
Created by Ansys ACE
Edited by Ansys Academic Development Team– Lesson 5

## Slide 2: Introduction
As we explore the science of fluid mechanics, it is important to understand how we can measure the characteristics of real flow fields — pressure, velocity, temperature, etc.
Flow measurement is the cornerstone of experimental fluid mechanics. It not only provides us with information about the flows observed but enables us to determine how well our theories match up to the real world.
In this lesson we will highlight some of the important methods and measurement techniques for three key flow parameters:
    Pressure
    Velocity
    Temperature
Notes: Flow visualization and flow measurement are different. Most flow visualization techniques provide a general macroscopic understanding of the flow field. However, flow measurement techniques provide ways of precisely measuring the flow variables such as pressure, velocity, or temperature . These techniques allow engineers and product designers to quantify the flow. Model results obtained by solving the flow on computers using CFD are carefully calibrated against these measurements obtained by experimentalists.

## Slide 3: Steady Versus Unsteady Measurements
Nearly all fluid flows we observe are inherently unsteady due to turbulence, wave motion and instabilities.
When we measure fluid flow properties, the readings may in fact be mildly unsteady even if the system boundaries are at steady conditions.
However, for many applications, we merely wish to know the mean or average flow properties at a point in space or spatially averaged on a surface.
For most of the descriptions in this lesson, we will focus on measurements intended for steady-state analysis and therefore represent a mean value.
However, we will also look at a few methods where the flow unsteadiness is measured, thus requiring a system which can record and log the time history of the flow variable.
Unsteady signal
Pressure measurement
Time-averaged signal
Notes: Most flows we see in nature are unsteady. The flow field variables, whether it is velocity, pressure, or temperature, vary continuously with time. However, under certain flow conditions, these variables can be assumed steady. Whether the flow is steady or unsteady, we are generally interested in the mean values of these parameters. We want to measure either the spatial or temporal (which is time-average) average values of various flow variables during our experiments. In this lesson, we'll talk about steady ways of measuring pressure, velocity, and temperature.

## Slide 4: Pressure Measurement Methods
Fluid pressure is a key variable in all fluid flows.
The pressure variation on surfaces wetted by fluids gives rise to forces and moments which mechanically impact the bodies associated with those surfaces. For example:
  Lift forces on an aircraft wing
  Pressure drop in a gas pipeline
  Drag force on a race car
  Torque and power on the blades of a wind turbine
Two devices commonly used for measuring pressure are the manometer and the barometer. These rely on the effect the pressure has on the height of a liquid in a tube situated in the earth’s gravitational field.
We will now look at examples of other methods of measuring pressure.
Notes: When it comes to measuring the lift force generated by an aircraft wing or the downforce generated on a Formula One racing car, or the torque and power generated by a turbine blade, it all comes down to the pressure force exerted by the fluid on the surface of these individual parts. It is because of this that measuring pressure becomes important in understanding and designing various products. The simplest way of measuring pressure is to use a barometer or a manometer.

## Slide 5: Static Pressure Taps
Relating to the manometer, it is important to understand how pressure measurements are set up in a real-world flow system.
One of the most common ways of sensing pressure is to install a static pressure tap.
The static pressure tap is a hole drilled into the wall of a flow system such as a pipe. A manometer or other pressure sensor is connected at this point.
The pressure tap allows the pressure of the fluid at a specific point on the wall to be measured and recorded (usually with an electronic data logger).
Pressure taps installed on the wall
Notes: In addition to these, static pressure taps measure the pressure at a point in the flow field. The recorded value of pressure is processed through an electronic data logger.

## Slide 6: The Bourdon Tube Pressure Gage
A Bourdon Tube pressure gauge is a device consisting of a curved tube, with one end closed and the other connected to the pressure measurement source.
When fluid pressure is imposed on the open end of the tube, an elastic deformation of the tube occurs. The amount of deflection is measured by a spring-loaded needle, which points to a calibrated scale to indicate the pressure.
This type of gauge is often used for measuring pressures in closed tanks, tires, pressurized vessels and similar systems.
Bourdon Pressure Gauge
Bourdon Tube
Pointer
Socket
Bourdon Pressure Gauge – Working Principle
Notes: Another way of measuring pressure is through a Bourdon pressure gauge. These are primarily used for measuring pressures in closed systems such as pressure vessels and automobile tires. They are a mechanical way of measuring pressure and rely on the deformation of a circular tube. This straightening and deforming tube causes a deflection in a spring-loaded needle which provides the necessary pressure measurement.

## Slide 7: Velocity and Flowrate Measurement Methods
Along with pressure and velocity, flowrate measurements are essential in understanding the state of a fluid flow in real systems.
Flowrate measurements are concerned with measuring the volume or mass flow rates, usually in a bulk sense (e.g., flow passing through a pipe with a given cross-sectional area).
Velocity measurements attempt to determine the magnitude and direction of the local velocity.
  In some cases, only velocity magnitude can be readily determined.
  More sophisticated measurements can obtain both magnitude and direction.
Notes: Velocity measurements in a flow field gives us an idea of what the flow field looks like. In fact, knowledge of velocity helps us estimate the overall resistance offered by a body as it is moving through a fluid. This is extremely important for making the body of an aircraft or a formula 1 car. The entire field of aerodynamic shapes stems from this requirement to reduce the overall resistance offered by the flow. Velocity can be measured directly or indirectly. An indirect way of measuring velocity is to obtain the overall flow rate. Flow rate provides an indication of the rate at which a certain fluid volume is being transported across the system. Knowledge of this flow rate can help us understand the average velocity of the fluid.

## Slide 8: Bernoulli’s Equation
Many flow and velocity measurement methods infer the velocity (or mean velocity) from a pressure difference which can be measured (e. g., by a manometer). We can relate pressure differences to the velocity through various forms of Bernoulli’s equation.
One form defines the velocity in terms of a total and static pressure difference ():
Another form infers velocity from a static pressure difference () and a loss coefficient :
In either case, these devices must be calibrated. That is, the loss coefficient is calibrated such that the pressures measured yield the correct flowrate.
Notes: Most velocity measurements are based on an important principle in fluid dynamics called the Bernoulli's principle. According to this, velocity in the system can be calculated based on the total pressure and difference between the static pressures measured at 2 specific points. It is important to note that this principle can be applied to flow fields under certain conditions. For now, it is sufficient to know that we can calculate the velocity of the fluid using the following equation.

## Slide 9: The Pitot Tube
The pitot tube is a device for measuring velocity at a point and has applications in experimental fluid mechanics (wind tunnels) and aviation (air velocity sensors).
The device is a pointed tube with openings for pressure measurement at the tip and at the side of the tip.
The tip pressure is the total (or stagnation) pressure, while the side opening is the static pressure. Both can be measured at once and the difference recorded.
Using Bernoulli’s equation (previous slide), we can determine the velocity knowing the fluid density.
Pitot Tube
Pitot Tube – Working Principle
Notes: The simplest way of measuring the local velocity of the fluid is to use a pitot tube. A pitot tube is an L-shaped tube where measurements are taken both at the tip and on its sides. The total pressure or the stagnation pressure of the fluid is measured at its tip and the static pressure measurements at taken on the side. The local fluid velocity is calculated using these measurements based on the Bernoulli's principle.

## Slide 10: The Venturi Tube
A Venturi tube is a device for measuring flowrate, again using two pressure measurements.
The device is essentially a tube with a narrow constriction (or throat).
As the flow passes from the upstream to the throat, the pressure drops. The level of pressure drop along with knowing the fluid density and area difference between the upstream pipe and throat allows us to determine the volume flow rate using the following equation:
Venturi Tube
Notes: Venturi tube is another common way of measuring the fluid velocity. The venturi tube has a narrow section where the flow gets restricted. This section is commonly referred to as the throat of the venturi. Velocity is calculated based on pressure drop measurements across the throat and by taking the area ratios between the upstream section and the throat.

## Slide 11: Orifice Plates and Flow Nozzles
Like a Venturi tube, orifice plates and flow nozzles infer flowrate from the measurement of pressure difference across an orifice opening or a flow nozzle.
In both cases the orifice or nozzle is an obstruction to the flow which causes a pressure drop. The flowrate can be calculated knowing the density of the fluid and the pressure drop, assuming the geometry of the orifice or nozzle (and therefore the loss characteristics) is known.
Orifice Plate
Notes: A similar principle for measuring the mean velocity of the flow is provided by devices such as orifice plate and flow nozzles.

## Slide 12: Turbine Flowmeters
Turbine flowmeters are based on the idea that a flowing fluid can turn a simple turbine rotor. Attaching the shaft of the rotor to an electric pulse detection sensor (to obtain the rotor RPM), we can calibrate the electrical signal thus produced with the fluid flowrate.
With their rugged construction, turbine flowmeters are used in harsh environments for measuring flows (e. g., high pressures and temperatures).
Notes: Turbine flow meters and rotameters are other common velocity measuring instruments.

## Slide 13: The Rotameter
A rotameter is a flow measuring device that uses a float in a tube of varying cross section to determine volume flowrate.
The basic principle is that the tube, which is oriented vertically, directs the fluid flow around the float, which pushes the float upwards due to the drag force acting on the surface of the float. The weight of the float acts in the opposite direction. As a result, an equilibrium position is established. This position can be calibrated with flowrate and a scale created for the device based on the fluid properties.
Obviously, the orientation of the rotameter and calibration of the flowrate scale are important when applying it to specific measurement applications.
Flow Rotameter
Notes: Turbine flow meters and rotameters are other common velocity measuring instruments.

## Slide 14: Hot Wire Anemometers for Velocity Measurement
A hot wire anemometer is a probe designed to sense velocity magnitude by measuring the heat transfer and temperature of an electrically heated thin wire which is immersed in the flow.
The heat flux from the wire can be expressed as a function of calibration parameters (), local fluid velocity (), freestream temperature () and wire temperature () as follows:
Since the wire is heated electrically, we can measure the electrical current through the wire and relate the heat flux with the wire resistance, temperature and calibration parameters. Thus, we can determine the fluid velocity from the equation above.
Hot wire anemometers are very sensitive to change in velocity and thus are used for measuring rapidly fluctuating turbulent flow transients.
Notes: Hot wire anemometer is another intrusive way of measuring the local velocity in the flow field. In this method, we insert a thin long wire into the flow. This wire is electrically heated and attempts to measure the local flow temperature. Based on the overall heat flux and the temperature difference between the wire and the fluid , a local velocity is calculated. This method, however, makes use of carefully calibrated coefficients to estimate the velocity of the flow. The final velocity measurements are noisy and requires time-averaging.

## Slide 15: Laser Doppler Anemometer (LDA) Velocity Measurement
One of the problems with the flow measurement devices discussed to this point is that they disturb the flow in some way (e.g., a flow nozzle is an obstruction in a pipe flow).
If precise measurements of the undisturbed flow field are required, then optical methods must be used.
The Laser Doppler Anemometer (LDA) (also called Laser Doppler Velocimetry - LDV) is an optical method with the precision to obtain quantitative measurements.
Basically, the LDA works by focusing a laser beam on a point in a flow which is seeded with a low concentration of particles. The particles scatter the light such that a Doppler shift can be detected, which is related to the velocity of the fluid at the point of measurement.
Laser Doppler Anemometer (LDA)
Notes: Until now all the velocity measurement devices that we discussed are intrusive. That is, they cause minor disturbances to the flow field. To avoid this and to get a precise measurement, we use optical techniques called the Laser Doppler Velocimetry and particle image velocimetry. A laser Doppler velocimeter focuses a beam of laser on a point in the flow field which is seeded by a certain concentration of seed particles. These particles scatter the light from a laser and the scattered light gives us a sense of the local velocity at that point. Unlike LDV which is a point measurement, we are able to capture 2D and 3D flow fields using particle image velocimetry.

## Slide 16: Particle Image Velocimetry (PIV) Measurement
Particle Image Velocimetry (PIV) is another optical method used to measure flow velocities.
Unlike the LDA which measures the velocity at a point, the PIV produces two-dimensional or even three-dimensional velocity fields.
The PIV process focuses two subsequent light pulses from a laser through a flow seeded with trace particles on a camera. This provides information for reconstructing a two-dimensional velocity field.
The addition of the second camera enables stereoscopic imaging of the flow, resulting in a three-dimensional representation of the velocity field .
Particle Image Velocimetry (PIV)
Notes: In PIV, we use two light pulses from the laser through the trace particles. These light pulses are captured by a recorder and the 2D or 3D flow fields are reconstructed.

## Slide 17: Temperature Measurement Methods
Temperature is a very important flow parameter, particularly for compressible flows and flows with heat transfer.
There are many ways to measure temperature and most fall into three categories:
  Mechanical temperature measurement
  Electrical temperature measurement
  Radiation temperature measurement
We will briefly consider these three types of temperature measurements.
Notes: Temperature measurements are important when it comes to solving either a compressible flow or a heat transfer problem. Knowledge of temperature gives us an idea of how hot or cold a certain flow is. This is extremely important in applications such as electronics cooling or thermal management of battery packs in electric vehicles. In these applications, the knowledge of fluid temperature helps engineers provide better heat transfer solutions.

## Slide 18: Mechanical Temperature Measurement
This temperature measurement method uses the change in size or dimension of a solid or fluid as an indication of temperature.
  Mercury Liquid-in-Glass Thermometer
    Mercury expands/contracts in the tube in response to temperature.
  Bimetallic Strip
    Two pieces of metal with different coefficients of thermal expansion are bonded together.
    The strip bends in two directions depending on the temperature.
Thermometer
Bimetallic Strip Thermostat
Notes: There are different ways of measuring temperature and they can be broadly classified as mechanical, electrical, and radiation based. A common thermometer, which works on expansion or contraction of a liquid in a glass tube, is one way of measuring temperature. A bimetallic strip, which is commonly used in temperature regulators in homes and offices, relies on the principle that different metals have different coefficients of thermal expansion. A bimetallic strip has 2 metal strips and they bend in different directions depending on the temperatures they sense.

## Slide 19: Electrical Temperature Measurement
There are two main categories of electrical temperature measurement:
  Electrical resistance thermometer — This device consists of a resistance element of a known metal or a semiconductor. The electrical resistance of the material is a function of temperature and can be read precisely and converted to a calibrated temperature.
  Thermocouples — When two dissimilar metals are joined, a voltage is created which is a function of temperature (this is known as the Seebeck Effect). This voltage can be read and converted to a calibrated temperature. Thermocouple circuits require special care in their installation and need compensation for other voltages that may arise due to connections away from the point of measurement.
Thermistor
Thermocouple
Notes: Thermistors and thermocouples are common examples of electrical means of measuring temperature. Thermistors rely on the fact that electrical resistance of metals and semiconductors change with temperature. An increase or decrease in the value of electrical resistance of these metals or semiconductors help us estimate the temperature. Thermocouple, on the other hand, operates on the principle of Seebeck effect. Two different metal strips produce an electromotive force or voltage when there is a temperature gradient between them. The thermocouple senses this voltage and passes it to a data logger which provides the final temperature reading. It is important to note that these temperature measuring devices only provide a point measurement.

## Slide 20: Radiation Temperature Measurement
Mechanical and electrical devices for temperature measurement are somewhat intrusive as we need to insert the measurement element into the flow, thereby disturbing it.
There are optical methods which avoid this and infer temperature by sensing the infrared radiation emitted by the fluid.
It is beyond the scope of this lesson to explore this in detail, but it should be noted that infrared cameras have now become commonplace and can be used to qualitatively show regions of high and low temperature.
IR Image of an Engineering System
IR Image of an Electronic Printed Circuit Board
Notes: An infrared Camera senses the infrared radiation emitted by a body and converts it to a temperature field. This is a non-intrusive way of measuring temperature. In contrast to all the other devices discussed earlier, an infrared Camera can help us provide the entire temperature field map. Usually, hot spots are identified by red and cold spots by blue.

## Slide 21: Summary
This lesson described methods for measuring flow properties experimentally.
Experimental data is highly valuable as the testing helps further our knowledge of fluid mechanics and provides reference information to assist in the development of numerical simulation methods.
Notes: There are many other ways of measuring flow variables to calibrate the flow field. These measurement techniques are used by engineers across all fields to test and come up with design modifications to develop cheaper, efficient, and safer products.