## Slide 1
Simulation Examples 1
Propagation of Car Exhaust Gas in a Ventilated Garage
Created by Ansys ACE
Edited by Ansys Academic Development Team

## Slide 2: Problem Statement
Overview
Ventilations are widely used to circulate air where harmful gases exist (like in parking garages)
The model consists of a car parked inside a garage. The ventilation system is kept on the wall. The garage door is kept open
The working fluid is a mixture of air and exhaust gas
All walls are considered to be adiabatic (thermal insulation)
Problem Description
Boundary conditions
  Inlet-exhaust: mass flowrate
  Outlet–vent-1: mass flowrate
  Outlet–vent-2: mass flowrate
  Outlet-door: Pressure outlet
  All walls: no-slip adiabatic wall
A fully turbulent flow is developed from the exhaust (
A steady-state solution can be obtained using the pressure-based coupled pseudo-transient solver in Ansys Fluent

## Slide 3: Flow Pathlines From the Car Exhaust
Pathlines of the car exhaust flow, colored by the mass fraction of the exhaust gas, are show here.
Most of the pathlines starting from the exhaust end at the vent, showing that most of the exhaust gas is ventilated.
The dilution of the exhaust is fast as more air-exhaust mixture is being vented compared to the gas exhausted by the car.
Flow pathlines of the exhaust flow with mass fraction representation

## Slide 4: Flow Pathlines from the Door
Reversed flow occurs through the door outlet as the air is induced into the garage through the door by the ventilation effect.
A large vortex is formed inside the garage because the ventilation unit is not on the same line with the door.
The fresh air coming through the door will first mix with (and hence dilute) the exhaust gas, then circulate along the vortex near the ventilation and finally be sucked out of the garage.
Flow pathlines of the outflow at the ventilation from door

## Slide 5: Concentration of Exhaust Gas
Visualization of exhaust gas distribution in a volume can be implemented by creating various iso-surfaces of its mass fraction.
In this specific case, three iso-surfaces of the exhaust gas concertation corresponding to the iso-values of 0.1 (red) , 0.01 (green) and 0.001 (blue) are created:
  Most of the garage has the exhaust mass fraction on the scale of 0.01
  The immediate region downstream of the exhaust pipe has higher exhaust gas concentration (0.1)
  the region downstream of the door has relatively low exhaust concentration due to the fresh air being induce in by the ventilation.
Iso-surface representation of mass fraction of the exhaust

## Slide 6: Wall Temperatures
A hot spot can be observed on the garage floor just downstream of the exhaust.
Garage ceiling temperature is higher than that on the side walls due to the buoyancy effect and the ventilation.
Temperature contour on the garage floor
Temperature contour on garage ceiling and side walls

## Slide 7: Summary
A detailed simulation of ventilation is carried out using Ansys Fluent
  It was observed that most exhaust is ventilated out through the outlet
  The exhaust gas is diluted almost instantly because of the ventilation
The detailed problem setup and result discussion can be observed by following the link.

## Slide 8
Appendix
Propagation of Car Exhaust Gas in a Ventilated Garage

## Slide 9: Steady State Solution: Monitors
Small-amplitude oscillations in the residuals and monitors indicate the solution is mildly unsteady, and steady-state solution cannot be fully converged. Since monitor oscillations are small, the solution can be considered nearly steady for first-order qualitative analysis
The mass imbalance is within 2% of the exhaust gas flow rate.
The oscillation of temperature monitor is also small: