## Slide 1
Simulation Example 2
Cyclone Separator
Created by Ansys ACE
Edited by Ansys Academic Development Team

## Slide 2: Problem Statement
Overview
Cyclone separators are mainly used in oil and gas and cement industry
They use terminal velocity to separate fine and coarse and lighter and heavier particles.
Objective
Simulate the motion of air inside a cyclone separator and understand the physics of swirling/rotating flows.
Only air motion will be observed in this simulation and not the motion of the particle
Problem description
Cyclone separator dimensions –
  Inlet diameter -
  Outlet diameters - (overflow) (underflow)
Operating fluid is air –
  ,
  inlet velocity,
  Boundary Conditions
    Velocity – inlet
    Pressure outlet
    Walls for separator surfaces
  Steady State Simulation is performed in Ansys Fluent with pressure-based coupled solver

## Slide 3: Results
Iso-surface of Q-criterion inside the cyclone separator depicting the vortex core
Pathlines inside the cyclone separator
Because the air is tangentially introduced into the cyclone, a high-speed rotating flow is established within the separator.
The velocity vectors shown here exhibit the spiral motion pattern of air.
As the air reaches the bottom of the cylinder, it stops swirling and gathers at the center of the separator. From there, the air travels upwards along the axis of separator and exits through the overflow outlet.
The pathlines shown here indicate the path, resembling the shape of a cyclone, taken by air in the separator.
Using Q-criterion, we can identify the vortical structures in the flow. Here is the iso-surface of Q-criterion which shows the "eye" of the cyclone.
Velocity vectors inside the cyclone separator

## Slide 4: Results
The swirling flow of air establishes an air vortex with low-pressure region along the center of the separator, as can be seen in the contours of static pressure
At the eye of the cyclone, the tangential velocity is quite small. However, it increases in magnitude as the radius increases before falling off near the surface of the separator
Contours of static pressure along the center plane of the cyclone separator
Contours of tangential velocity along the center plane of the cyclone separator
Note: The axis of rotation is the negative z-direction

## Slide 5: Summary
An Ansys Fluent Simulation was successfully run to understand the flow of air inside a vortex separator.
The swirling and flow of air was captured and studied. It was seen that the air came stopped swirling at the underflow outlet.
A detailed explanation on simulation setup and post processing can be observed by following the link.

## Slide 6
Appendix
Cyclone Separator

## Slide 7: Setup Changes
Modifications from the default Ansys Fluent 2020 R1 settings are outlined here
  Viscous Model
    Realizable k-ε (default : k-ω SST): The Realizable k-ε (RKE) considers the effects of mean rotation on computing the turbulence viscosity, and it performs better in simulating flows with small to moderate levels of swirl/rotation in the fluid when compared to other k-ε and k-ω models.
    Enhanced Wall Treatment (default : Standard wall functions) : The y+ range of the mesh used for this example is between 0.1 and 6. Standard wall functions require the minimum y+ to be greater than 30. To ensure accuracy of computation, y+ insensitive Enhanced Wall Treatment is used.