## Slide 1
Homework 1:
Flow Through a 90-degree Bend Pipe
Created by Ansys ACE
Edited by Ansys Academic Development Team

## Slide 2: Problem Statement
Objectives
Understand the flow of turbulent flow around a pipe bend
Check the re-circulation vortex in separation zone
Understand flow structures
Problem Description
Dimensions of the pipe:
  Diameter
  Arc radius at the bend
  Length upstream of bend
  Length downstream of the bend
Working fluid is air
Boundary and initial conditions
  Inlet:
  Outlet: pressure outlet (gauge pressure relative t atmospheric
  Pipe walls are no-slip walls
The Reynolds number , Hence a SST turbulence model was utilised.
A steady state solution was used using the pressure-based coupled pseudo-transient solver in Ansys Fluent.

## Slide 3: Velocity Magnitude
The velocity magnitude contour on the symmetry plane shows how the air flow accelerates as it flows over the bend and separates form the wall past the inner bend side, forming a low-speed zone recirculation zone.
Flow velocity over the outer bend side is lower as the flow turns to follow the bend.
Inner bend
outer bend

## Slide 4: Static Pressure
The static pressure contour on the symmetry plane shows higher pressure on the outer side of the bend corresponding to lower velocity in that region, as per conservation of momentum.
The area of low pressure on the inner bend side is associated with the flow separation regions.
The pressure distribution across the pipe becomes nearly uniform away from the bend downstream.

## Slide 5: Velocity Vector Analysis
A boundary layer is formed along the wall. The velocity is uniform at the inlet, and the fully-developed pipe profile is not established in this model because pipe sections before and after the bend are relatively short.
The recirculation flow pattern in the zone past the inner bend side can be identified by its vortex structure clearly seen in the velocity vector plot.
The flow begins to gradually recover downstream of the bend but does not have enough pipe length to fully re-establish before reaching the outlet.

## Slide 6: Summary
A turbulent flow across a 90 Degree bend pipe was analyzed
It was seen that there was a boundary layer formation near the walls which can be observed in the streamline plots.
The effect of the bend on the pipe was visualised where a recirculation was observed right after.
The flow recovered after the recirculation further downstream.
More on how to recreate the setup and the results can be followed by clicking on the link.

## Slide 7
Appendix
Flow Through a 90-degree Bend pipe

## Slide 8: Set up Changes
Modifications from the default Ansys Fluent 2023 R1 settings:
  The stop criteria for residuals are all set to to obtain a better converged solution in this simple case.