## Slide 1
Internal Compressible Flows Course Lesson 1
Introduction to Internal Compressible Flows
Created by Ansys ACE
Edited by Ansys Academic Development Team

## Slide 2: Introduction
Rocket Engine Nozzles
  There are different ways to classify internal compressible flows, and one of them is by defining the intended purpose of an internal flow system. Three such basic purposes are:
    Transporting compressible fluid (gas) from one point to another
      Gas pipelines
    Accelerating the flow
      Nozzles in jet engines and rocket engines
      Wind tunnels
    Decelerating the flow
      Inlets
      Diffuser section of a wind tunnel
  There is one common objective in all the above applications, and that is to achieve required goals with minimal losses due to compressible waves and friction.
Notes: Understanding the physics of internal compressible flows is important for several engineering applications ranging from aircraft inlets to designing engine exhaust nozzles and wind-tunnel facilities. Internal compressible flows are confined wall-bounded flows where compressibility of the fluid plays a major role.

## Slide 3: Gas Transportation Pipelines
  The transportation system of natural gas is a complex network of pipelines for transporting it from the origin to points of consumption.
  In general, a national gas transportation network consists of a gathering system, the interstate pipeline system, the distribution system and the storage system.
  The gas is compressed for transportation, so it occupies less volume. It is transported either in the gaseous form or in the liquefied form.
  Natural gas is inevitably gaseous and compressible through a part of the transportation systems, e. g. during transportation of raw gas to processing plants, compression of gas into its liquid form or gasification of liquid gas back into its gaseous form.
  Thus, the analysis of internal compressible flows plays an important role in the design and operation of gas transportation systems.
Oil pipeline
Notes: Transportation of compressed natural gas from one location to another is an excellent example of such an internal flow. A compressed gas occupies less volume, and the natural gas is either compressed into its liquid state or is gasified from its liquid state back to the gaseous form during its transportation. A good understanding of the internal compressible flow is important for the design and operation of these transportation networks. In this course, we will focus our attention on such internal flows.

## Slide 4: Nozzles
  In the aerospace industry, the goal of a nozzle is to generate thrust by increasing the kinetic energy of the exhaust gas at the expense of pressure and internal energy.
  Most modern aircraft and spacecraft use nozzles as a part of their propulsion systems.
  There are many different nozzle configurations ranging from classical convergent-divergent nozzles designed to accelerate supersonic aircraft and space vehicles to separate jet exhaust nozzles used in modern high bypass ratio jet engines for commercial aircraft.
  Analysis of compressible flows through nozzles is crucial to designing effective nozzles with minimal losses.
Exit Nozzles of Concorde Supersonic Aircraft
Notes: Most aerospace vehicles use nozzles to generate a greater thrust force. They increase the kinetic energy of the exhaust gas by changing its pressure and internal energy. There are several types of nozzle configurations - the converging-diverging nozzles are a common design in supersonic aircraft and space vehicles. Similarly, separate jet exhaust nozzles are used commonly in modern commercial aircraft for high bypass ratios. In this course, we will learn extensively about compressible flows in converging-diverging nozzles and study the importance of inlet-exit pressure ratios for such nozzles.

## Slide 5: Inlets
  Inlets of flight vehicles are designed to decelerate incoming airflow and direct it to a compressor or a combustor at a subsonic speed, free of disturbances and non-uniformities to assure on-design performance of the engine.
  The design of a supersonic inlet is complex as it needs to slow down supersonic flows through a series of shocks and expansions so that the flow becomes subsonic before entering a compressor.
  Since the incoming airflow is affected by factors such as free-stream turbulence, the inlet design must be versatile and robust enough to operate at a wide range of ambient conditions.
  Inlets into turbofan jet engines of commercial airliners operate in transonic flow conditions, and their design must account for a potential development of a shockwave due to the flow accelerating past the inlet lip.
  The inlet is designed to diffuse the shock and restrict it from being “digested” by the engine rotor.
Inlet of a Turbofan engine
Notes: Engineers designing aircraft engine inlets also rely heavily on the principles of internal compressible flows. The inlet is designed to decelerate the incoming airflow to subsonic speed and direct this flow into the compressor. This is done to remove flow disturbances and ensure a uniform flow into the combustor, thereby increasing the engine’s performance. The deceleration of the incoming supersonic flow occurs through a series of oblique shocks, expansion waves, and a terminal normal shock, beyond which the flow is fully subsonic. Similarly, the inlets of turbofan engines used in commercial aircraft, which generally operate in transonic flow regimes, are designed to diffuse, or restrict the shockwave developed at the inlet lip. This shockwave potentially occurs due to the flow acceleration past the inlet lip and is detrimental to the engine rotor.

## Slide 6: Wind Tunnels
  Wind tunnels are experimental facilities used to test aerodynamics of aircraft, ground vehicles and other objects where external aerodynamics is of utmost importance.
  There are different types of wind tunnels, but all of them operate on the principle of accelerating initial stagnant air to the required speed in the test section.
    Low speed wind tunnels use a fan or an array of fans to accelerate air. This design, however, cannot generate high-speed transonic or supersonic flows.
    A different type of wind tunnel consisting of a large nozzle to accelerate the flow to supersonic speeds and a diffuser to decelerate this flow past the test section is used for high-speed flow tests.
Schematic of a Supersonic Wind Tunnel
Notes: Wind tunnel facilities are commonly used to conduct experimental aerodynamic tests on aircrafts, ground vehicles, and other objects during their design phase. Even though the object being designed is for external flow applications, the wind-tunnel facility itself is an example of an internal compressible flow system where the incoming air is accelerated to the required speed in the test section. These facilities make use of large nozzles to achieve high-speed transonic and supersonic flows before the test section. Beyond the test section, the air is decelerated to low subsonic velocities using diffusers. In this course, we will understand how these nozzles and diffusers are arranged in a modular fashion to generate the necessary supersonic flow conditions inside these wind-tunnels. Furthermore, we will also understand the method of characteristics to design these internal flow structures. With that, let’s wrap up this lesson.

## Slide 7: Course Outline
  The focus of this course will be to discuss some practical concepts of internal compressible flows.
  Our analysis will be 1-D or quasi-one-dimensional, but that will not be a hindrance for us to obtain useful and practical relations for the analysis of compressible flows through inlets, nozzles, wind tunnels and long pipes.
  In the following lessons of this course, we will cover:
    1-D flows with heat addition (Rayleigh flows) and with friction (Fanno flows) .
    Quasi 1-D analysis of internal variable area flows.
    Analysis of a converging-diverging nozzle.
    Diffusers and wind tunnels.
    Method of characteristics in internal flow designs.