## Slide 1
Internal Compressible Flows Course Lesson 5
Diffusers and Wind Tunnels
Created by Ansys ACE
Edited by Ansys Academic Development Team

## Slide 2: Introduction
  Any duct designed to slow down an incoming gas flow to a lower velocity is called a diffuser.
  Incoming flow can be either subsonic or supersonic based on the application.
  A diffuser is designed such that the loss in total pressure is minimal during the slowing down of the flow.
  Diffusers are commonly used in propulsion systems such as air breathing engines, rocket engines etc.
  Diffusers are also integral components in many wind tunnel designs.
2
,
Notes: Let’s say we want to conduct an experiment to study how an object interacts with a Mach 2.5 flow. To do this experiment, we would need to create a uniform Mach 2.5 flow, so we start with a converging-diverging nozzle with an area ratio of 2.6, and we need to establish a pressure ratio of 17.09 across the nozzle for a shock-free expansion to Mach 2.5 at the exit. If we exhaust the nozzle directly into the lab, then the Mach 2.5 flow passes on to the test model as a free jet. For the jet to be free of any shock or expansion waves, the nozzle exit pressure pe must be equal to the back pressure pb, which in this case would be the ambient pressure in the lab or the atmospheric pressure. This would mean that the inlet of our C-D nozzle would need a pressure reservoir of 17.09 atm. Such a set up would be very expensive to build and operate due to the higher costs associated with such high-pressure devices and storage systems. So, the question is, can we accomplish this more efficiently and economically? Let’s Find out!

## Slide 3: Ideal Vs Real Diffuser
  An ideal diffuser is one in which the incoming flow is slowed by an isentropic compression to lower velocities.
  The supersonic flow entering the diffuser at is isentropically compressed in a convergent duct to Mach 1 at the throat () and is then further isentropically compressed in a divergent duct to a low subsonic Mach number at the exit.
  However, in the converging portion of the diffuser, the flow will generate oblique shocks as the supersonic flow is turned into itself.
  Due to viscosity, there will be an entropy increase within the boundary layers on the walls of the diffuser.
  For this reason, an ideal diffuser can never be constructed for engineering applications.
3
,
Notes: Let us modify our setup so that the nozzle exits the flow into a constant area section instead of a free jet into the lab and this constant area section contains a normal shock wave standing at the end of the constant-area section. As a result, the pressure downstream of the normal shock is 1 atmosphere. At M=2.5, the static pressure ratio across the shock will be 7.125, which means the pressure at the nozzle exit is 0.14 atm. Therefore, the pressure required at the nozzle inlet to ensure proper isentropic flow reduces from 17.09 to 2.4 atmosphere!
In this case, the normal shock wave helps by slowing the air from Mach 2.5 to Mach 0.51 behind the shock. As a result, this setup is also referred to as a ‘Normal Shock Diffuser’.
Any duct designed to slow down incoming gas flow to a lower velocity is called a diffuser. This incoming flow can be either subsonic or supersonic depending on the application. It is designed in such a way that the loss in total pressure is minimal during the slowing down of the flow.
Diffusers are commonly found in propulsion systems such as air breathing engines, rocket engines, and in wind tunnels. In fact, diffusers are an integral part of many wind tunnel designs.

## Slide 4: Ideal Vs Real Diffuser
  An actual supersonic diffuser slows down an incoming flow by a series of reflected oblique shocks in the convergent section and the throat (usually in the form of a constant area section).
  Interaction of shock waves with the viscous flows near the wall weakens and diffuses the reflected shock patterns, which ends up in the form of a weak normal shock wave at the end of the constant area throat.
  The subsonic flow downstream of the throat is subsequently slowed down via a diverging section.
  As the flow is no longer isentropic, the entropy at the exit is higher and the total pressure is lower.
  Design problem of a diffuser - design the converging, constant area and the diverging section to obtain the desired exit Mach number with least possible total pressure loss. (In other words, trying to keep as close to unity as possible.)
4
,
Normal shock
(Weak)
Note that due to entropy increase across shock waves and boundary layers, the real diffuser throat area,
Notes: If we consider an ideal diffuser, the one in which the incoming flow is slowed via an isentropic compression to lower velocities, the supersonic flow entering the diffuser at M_1 is isentropically compressed in a convergent duct to Mach 1 at the throat (area=A^∗) and is then further isentropically compressed in a divergent duct to a low subsonic Mach number at the exit. However, the flow will inherently generate oblique shocks in the converging portion of the diffuser as the flow is being turned into itself. Moreover, as the flow is viscous, there will be an entropy increase within the boundary layers on the walls of the diffuser. For this reason, an ideal diffuser can never be constructed for engineering applications. So how does an actual diffuser work?
An actual supersonic diffuser slows down an incoming flow by a series of reflected oblique shocks in the convergent section and the throat, which is usually in the form of a constant area section. The interaction of the shock waves with the viscous flows near the wall weakens and diffuses the reflected shock patterns.
Many times, it ends up in the form of a weak normal shock wave at the end of the constant area throat. The subsonic flow downstream of the throat is subsequently slowed down via a diverging section. As the flow is no longer isentropic, the entropy at the exit is higher and the total pressure is lower, as shown here. Therefore, the design problem of a diffuser can be summed up as the process of designing the converging, constant area, and the diverging section to obtain the desired exit Mach number with the least possible total pressure loss.
Now that we have some understanding of the design and operating principles of diffusers, let us revisit our wind tunnel.

## Slide 5: Wind Tunnel Design and The Role of Diffusers
  Let's assume we want to create a uniform Mach 2.5 flow for an experiment. We need a converging-diverging nozzle with an area ratio and we need to establish a pressure ratio of across this nozzle for a shock-free expansion to at the exit.
  If we exhaust the nozzle directly into the laboratory, the Mach 2.5 flow passes on to the test model as a free jet as shown.
  For the free jet to not have any shock or expansion waves, the nozzle exit pressure must be equal to the back pressure .
  As the back pressure is the atmospheric pressure in the lab, atm, implying that at the inlet we would need a pressure of atm.
  This setup would be very expensive to build and operate due to the higher cost associated with such high-pressure devices and storage systems.
5
Test Model
=
Nozzle exhausting directly into the atmosphere
Notes: Hold on! Before we can start building this setup for our experiment, there are few issues that we still need to consider – firstly, a normal shock is the strongest possible shock which creates the largest pressure loss, so maybe if we can replace it with weaker shocks then we can help reduce the total pressure loss and the required reservoir pressure.

## Slide 6: Normal Shock Diffuser
  Let's change the setup so that the nozzle exits the flow into a constant area section instead of a free jet into the laboratory as shown here.
  The constant area section contains a normal shock wave standing at the end of the constant-area section.
  As a result, the pressure downstream of the normal shock wave is . At , the static pressure ratio across the shock will be .
  Thus, at the nozzle exit. In order to ensure proper isentropic flow through the nozzle, requiring a pressure ratio of , we would now need a reservoir with a pressure of only !
  This is considerably less than atm required in the previous design.
  The normal shock wave acts as a diffuser by slowing the air at to the subsonic value of behind the shock.
6
Test Model
Normal Shock
Constant Area
Nozzle exhausting into a constant area duct with a normal shock at the exit
Notes: Moreover, the flow unsteadiness and instabilities can cause the normal shock to move and fluctuate constantly, giving rise to uncertainty about the quality of the flow in the constant-area duct. And lastly, the introduction of the test model in the test section would cause oblique shock waves from the model to propagate downstream making the flow three-dimensional and causing the normal shock to vanish. How do we address these concerns while keeping the reservoir pressure requirements low?

## Slide 7: Normal Shock Diffuser
  The addition of the diffuser allows us to produce the required flow more efficiently. However, this approach has some problems:
  A normal shock is the strongest possible shock and creates the largest pressure loss. Replacing it with weaker shocks can help reduce the total pressure loss and the required reservoir pressure .
  Flow unsteadiness and instabilities cause the normal shock to move and fluctuate constantly. This would give rise to uncertainty about the quality of the flow in the constant-area duct.
  The introduction of the test model in the test section would cause oblique waves from the model to propagate downstream making the flow three-dimensional causing the normal shock to vanish.
7

## Slide 8: Oblique Shock Diffuser
  Replacing the normal shock diffuser with an oblique shock diffuser as shown, we have a converging-diverging diffuser which slows the flow down to a low subsonic speed.
  This arrangement is referred to as a supersonic wind tunnel. The main source of pressure loss in a supersonic wind tunnel is the diffuser.
  Reducing the velocity of a supersonic flow progressively via consecutive oblique shocks to a low supersonic value and further reducing it to subsonic speeds across a normal shock results in a smaller total pressure loss compared to a single strong normal shock.
  An oblique shock diffuser is usually more efficient than a normal shock diffuser. However, due to the presence of shock wave – boundary layer interactions and the skin friction exerted on the surface, adds to inefficiencies.
8
Test Model
Test Section
Normal (weak) shock
Diffuser
Nozzle
1
2
8
Notes: Let's replace the normal shock diffuser with an oblique shock diffuser as shown here. In this setup, we have a converging-diverging diffuser which slows the flow down to a low subsonic speed. This way we are effectively reducing the velocity of the supersonic flow via consecutive oblique shocks to a low supersonic value and further reducing it to subsonic speeds across a normal shock results in a smaller total pressure loss compared to a single strong normal shock. This arrangement is referred to as a supersonic wind tunnel. The main source of pressure loss here is the diffuser.

## Slide 9: Two Throats of a Supersonic Wind Tunnel
  As seen from the schematic, the supersonic wind tunnel has two throats:
    Nozzle throat with area called the first throat
    Diffuser throat with area called the second throat
  For steady flow through the wind tunnel:
  Since the thermodynamic state of the gas is irreversibly changed when going through shock waves, the properties at the two locations will differ and thus the two throats must have a different areas.
  Assuming sonic flow at both stations 1 and 2, we can get the following relation using the isentropic equations:
  As the total pressure always decreases across shock waves, , the second throat must always be larger than the first throat, .
9
Notes: As we can see, our supersonic wind tunnel has two throats - the nozzle throat with an area At1, called the first throat and the diffuser throat with an area At2 called the second throat. For maintaining a steady flow through the wind tunnel, we must ensure the following condition. Since the thermodynamic state of the gas is irreversibly changed when going through shock waves, the properties at the two locations will differ and thus the two throats must have different areas. If we assume sonic flow at both stations 1 and 2, we can get the following relation using the isentropic equations. Since the total pressure always decreases across shock waves p02 is less than p01 and thus the second throat must always be larger than the first throat.

## Slide 10: Efficiency of Diffusers
  Efficiency of a diffuser can be evaluated based on several figures of merit.
  The most commonly used definition (related to wind tunnel work) is based on the comparison of the actual total pressure ratio across the diffuser , with the total pressure ratio across a hypothetical normal shock wave at the test section Mach number :
  For typical supersonic diffusers, the efficiency is very sensitive to the second throat area as shown in the plot.
    As decreases from a large value, first increases up to a peak value and then rapidly decreases.
    The peak efficiency is obtained by a value of slightly larger than the value obtained from the equation on previous slide ().
    Below the flow is choked, and the efficiency drops significantly.
10
Choking
Starting
Notes: Now that we have our diffuser ready for the wind tunnel, we now need some metric to evaluate its performance. The most commonly used definition of Diffuser efficiency (related to wind tunnel work) is based on the comparison of the actual total pressure ratio across the diffuser, with the total pressure ratio across a hypothetical normal shock wave at the test section Mach number. For typical supersonic diffusers, the efficiency is very sensitive to the second throat area At2 as shown here. As we can see, the peak efficiency is obtained for a value of At2 slightly larger than the value At2* obtained using this expression. For any value below At2* the flow is choked and the efficiency drops significantly.
An oblique shock diffuser is usually more efficient than a normal shock diffuser. However, this may not always be true due to the presence of shock wave – boundary layer interactions and the skin friction exerted on the surface.

## Slide 11: The Starting Problem
  When the flow through a wind tunnel is first started, a complicated transient flow pattern is established, which, after some time, settles to a steady flow as we have discussed in this lesson.
  In most cases, the starting process is usually accompanied by a normal shock wave traversing through the entire duct – from the nozzle entrance to the diffuser exit.
  When this starting shock wave is at the inlet to the diffuser, the second throat area must be large enough to allow the passage of the mass flow behind a normal shock. This value is given by corresponding to the total pressure ratio across a normal shock at the test section Mach number, .
    This starting value of throat area is always larger than that corresponding to the peak efficiency.
    If is less than this starting value, the normal shock will remain upstream of the diffuser, and the wind tunnel will not start properly.
    If is equal to or more than this value then the normal shock will proceed through the diffuser section and the wind tunnel will start properly.
  This is the reason why many advanced wind tunnels use variable-geometry diffusers.
11
Notes: So let's start our wind tunnel and see what happens.
As the flow through a wind tunnel is first started, a complicated transient flow pattern is established, which after some time, settles to a steady flow as we have discussed. In most cases, the starting process is usually accompanied by a normal shock wave traversing through the entire duct – from the nozzle entrance to the diffuser exit. When this starting shock wave is at the inlet to the diffuser, the second throat area must be large enough to allow the passage of the mass flow behind a normal shock. This value is given by At,2∗ corresponding to the total pressure ratio across a normal shock at the test section Mach number, p0,2/p0,1.
One very important thing to note here is that this starting value of the throat area is always larger than that corresponding to the peak efficiency. If At,2 is less than this starting value, the normal shock will remain upstream of the diffuser, and the wind tunnel will not start properly.
If At,2 is equal to or more than this value, then the normal shock will proceed through the diffuser section and the wind tunnel will start properly. This is the reason why many advanced wind tunnels use variable-geometry diffusers.

## Slide 12: Summary
  In this lesson we analyzed flows through diffusers and wind tunnels where diffusers play a vital role.
  We looked at the differences between an idealized and a real diffuser.
  We also looked at the two throats of a supersonic wind tunnel and how they give rise to the starting problem and the means with which it can be addressed.
12
Notes: With this, we have reached at the end of this lesson!