## Slide 1
Internal Compressible Flows Course Lesson 3
Quasi 1-D Flows
Created by Ansys ACE
Edited by Ansys Academic Development Team

## Slide 2: Introduction
  In this lesson we will analyze quasi one-dimensional flows.
  Unlike a truly one-dimensional flow, the area of the passage varies in such flows. However, the variation , is gradual and therefore it is sufficiently accurate to neglect the and variations, and to assume that the flow properties are functions of only.
  In such flows, it is the area change that causes the properties to vary along the direction.
  A wide range of engineering applications such as wind tunnels, rocket engines, etc. can be analyzed with a fair degree of accuracy using the methods discussed in this lesson.
Wind Tunnel
Rocket Engine
Notes: The most common applications of compressible internal flow problems are often represented by geometries with varying cross-sectional areas. Propulsion systems or advanced wind tunnels used in research facilities take advantage of the variations of their cross-sectional area in order to accelerate subsonic flows to supersonic speed or decelerate supersonic flows to a subsonic state. In this lesson we will analyze the underlying relations that describe and govern these kinds of flows. Let’s explore quasi 1D flows.

## Slide 3: Basics of 1-D and Quasi 1-D Flow
  The flow is considered compressible and has attained steady-state.
  Working fluid is assumed to be an ideal gas with known thermodynamic properties.
  Property variations assumed to be isentropic (except across shock waves).
  Velocity and thermal property profiles are uniform across the passage
  No separated or reversed flow
  No heat transfer or work input to the fluid
  The duct cross-sectional area:
    Is constant for 1-D flows
    Is a function of for Quasi 1-D flows
1-D Flow
Quasi 1-D Flow
Notes: Quasi 1-D flows are very similar to the 1D flows we analyzed before. We assume the flow is compressible and steady. The gas behaves as an ideal gas and its property variations are assumed to be isentropic, except across shockwaves. Viscous effects are neglected, the solid boundaries are adiabatic and there is no work done to or by the fluid. The main difference between 1D and Quasi 1D flows is the cross-sectional area of the passage. For quasi 1D flows, it is no longer constant, but is a function of the x location. The properties of the flow are assumed to be uniform across the passage and only vary in the x direction.

## Slide 4: Governing Equations for 1-D Flow
Mass
Momentum
Energy (First Law)
Entropy (Second Law)
        Equation of state (ideal gas)
  Stagnation relations
Notes: The general form of the governing equations for quasi 1D flows does not differ from the one we have for 1D flows. We have mass, momentum and energy conservation, as well as the relations for ideal gas and isentropic flow. The only thing to remember is that when applying the mass equation between two locations, we cannot simplify the area term anymore. We can also recall the isentropic relations of the stagnation quantities, for our convenience.
The continuity equation and the isentropic relations can be combined to obtain an expression for the mass flow rate.

## Slide 5: Mass flow rate
  The Quasi 1-D continuity equation and the isentropic equations can be manipulated to give the following equation for the mass flow rate:
  This form shows that the mass flow rate is proportional to the fluid total pressure and the duct area, while is inversely proportional to the total temperature of the fluid
  Typically, the inlet conditions for a quasi 1-D model are set assuming that the fluid originates from a tank at the stagnation (zero velocity) pressure and temperature.
  The fluid is assumed to accelerate isentropically to the inlet of the passage, and we can define the inlet condition as known stagnation (total) flow properties (etc.).
Quasi 1-D Flow
Notes: As we can see, the mass flow rate can be increased if we increase the flow total pressure and the section of the passage, or if we decrease the total temperature of the fluid. Often, when discussing quasi 1D flows, it is assumed that the incoming fluid is stored in a pressurized tank at stagnation conditions. Then, the fluid accelerates isentropically to the inlet of the duct, so that the stagnation conditions are still valid at the inlet.

## Slide 6: Area – Velocity Relation
  Governing equations in differential form:
  Using the continuity equation we can get:
  For an isentropic flow, any change in pressure is accompanied by a corresponding isentropic change in density :
  Combining these equation and manipulating, we get the Area – Velocity Relation:
V increasing
V decreasing
V increasing
V decreasing
Notes: Now, let's explore one of the most important relations of quasi 1D flows - the area velocity relation. In the differential form of the continuity equation we have three terms: the density one, the velocity one and the one related to the area. Now, using the momentum equation in its differential form and the definition of speed of sound based on isentropic assumptions, we can find an expression for the density term.
Substituting the expressions into the continuity equation we obtain the final area-velocity relation. We can see that area changes are proportional to velocity changes and, depending on the Mach number, the proportionality can be direct or inverse.
Let's analyze this.
If we consider a subsonic flow, we can see that the proportionality coefficient will be negative. This means that for a subsonic flow moving through a converging geometry, the velocity will increase, while a subsonic flow in a diverging geometry would decelerate. This is the reason why when we blow on something, we contract our mouth to accelerate the air, instead of just blowing with open mouth. We can also test the opposite trend simply blowing air in an open cone, the air exiting the cone would be slower than just blowing it with our mouth.
If the Mach number is larger than one, we have a supersonic flow. In this case the coefficient is always positive, meaning that when we increase the area of a duct the flow will accelerate and if we decrease the area of the duct the flow will decelerate instead. This may not be immediate to grasp, since we do not commonly deal with supersonic flows in our everyday lives. Here is a simple analogy to remember this. Think about a highway with road works. As the lines available get reduced the cars slow down, like the supersonic flow would in a converging geometry. Past the roadworks the cars accelerate as the road opens up and the numbers of lines increases back, exactly like a supersonic flow would in a diverging duct.
The area velocity relation and its implications are really what is “behind the scenes” of supersonic wind tunnels and propulsive systems. If we take those pieces (the converging and diverging geometries sketches) and combine them together we can achieve something that those pieces alone would not. If we use these configurations, we can accelerate a subsonic flow into a supersonic flow and decelerate a supersonic flow into a subsonic one.

## Slide 7: Critical State in Compressible Flow
  As the gas accelerates, its velocity (and Mach number) increases, while the static pressure and temperature decrease. When the fluid velocity reaches Mach number = 1, an important limiting effect is imposed on the passage mass flow rate.
    This flow state is the Critical State and is denoted with the superscript * (e.g. etc.).
    For our 1-D passage we denote the area at which sonic conditions are achieved as
  Let’s consider a converging nozzle, from the energy equation:
  The passage mass flux () can then be defined as:
  Let’s denote the minimum area of the duct as throat.
  For a given mass flow rate, the maximum mass flux must occur at the throat, since it is the smallest section of a duct.
Flow
Minimum Area
(Throat)
Converging Nozzle
Stagnation Conditions
(Inlet)
Notes: Let’s now look at another aspect: the critical state.
Let's assume a subsonic flow going through a converging nozzle. As the flow accelerates, it will eventually reach Mach equal to 1. In this case, we have reached the maximum mass flow rate that can go through the passage and the flow reached a critical state. Since the flow has reached sonic conditions the state quantities and the area of the passage can be denoted by using the star superscript.
The energy equation can be used to obtain an expression for the velocity, by combining the definition of enthalpy and the isentropic relations. As expected, the lower the pressure, the higher will be the velocity. We can also introduce a new variable that defines the mass flux to the passage by simply dividing the mass flow rate by the area. Now, assume that the minimum area is at the end of this converging nozzle and let's call this location as the throat of the duct.
By the definition of mass flux, for a given mass flow rate the maximum mass flux will occur at the smallest section of the duct.

## Slide 8: Choking
  We denote the area and flow properties there with a subscript .
  We can now write:
  From the 1-D momentum equation:
  Under the assumption of isentropic flow, combining the above yields:
  This shows that when the throat is small enough so that the velocity becomes equal to the speed of sound (or Mach number = 1), then the throat is the point of maximum mass flux. This physical effect is called choking, as it represents the maximum mass flow rate which can be achieved in a converging passage from a given stagnation condition.
Note that the derivative of the mass flux is zero at the throat.
Notes: Let's denote the flow properties of the throat with the subscript ‘t’. Then doing the logarithmic differentiation of the mass flux expression and dividing by dX, we can achieve an interesting conclusion. The derivative of the mass flux is zero at the throat, also combining this equation with the momentum equation and the assumption of isentropic flows, we find that the velocity at the throat is equal to the speed of sound. This means that, if the converging section of the duct is small enough so that the flow reaches the speed of sound, then the throat becomes the point of maximum mass flux. This physical effect is called choking and the mass flow rate at this location is the maximum that can be achieved in the geometry for a given stagnation condition. We cannot exceed the mass flow rate that we achieve in choking conditions.

## Slide 9: Choking and Flow Measurement
  Since throat conditions are at sonic velocity, they are also critical conditions and can be denoted by the * superscript (e. g. , , etc.).
  The critical (choking) mass flow rate can be calculated substituting M= 1 in the relation presented earlier:
  This equation provides the basis for flow measurement using choked converging passage nozzles.
    The choked mass flow equation can be used to determine mass flow rate from the upstream total pressure and temperature, the nozzle throat area , and known gas thermodynamic properties ().
    The total pressure and temperature can be measured using pitot-static tubes and thermocouple probes.
    The downstream pressure ratio /should be less than the choking threshold (for example, 0.528 for air).
Sonic (throat) relations
1
2
Flow
Notes: With the throat at sonic conditions we can easily estimate the fluid temperature, pressure and density using the sonic relations. Also, the expression we found before for the mass flow rate can be simplified using Mach equal to 1. The mass flow rate for a chocked flow is function of the total conditions and the choking area. This equation can be useful to estimate the mass flow rate in a duct using choked converging passage nozzles. The mass flow rate can be found if we measure the upstream total pressure and total temperature using a static tube and a thermocouple, assuming that the nozzle throat area is known. This approach is valid as long as the flow is chocked.

## Slide 10: Critical Area Ratio and 1-D Flow Solution
  Using the continuity equation, we can develop an equation for the passage area to critical (throat) area ratio :
  Notice that as , – that is, the passage area approaches the critical (throat) area. We can now formalize the 1-D flow calculation procedure:
Specify flow conditions at the inlet (stagnation properties and inlet Mach number).
Passage geometry is known, .
At the inlet Mach number, calculate the area ratio Since is known, calculate
For any downstream station calculate and use the area ratio equation to solve for the Mach number at the station. (This can be done numerically, or one can consult tables.)
Knowing the Mach number, use the isentropic relations to obtain all flow properties.
This can be easily set up in a spreadsheet or computer program, thus avoiding the use of tables or charts.
Notes: We can use the continuity equation to find that the ratio of the duct area to the critical throat area is a function of the Mach number. As the Mach number goes to 1 the area ratio goes to 1 as well. Now why is this relation so important? Using this equation we can estimate the local Mach number at each section of known geometry.
Assume we know the passage geometry, hence A(x), the inlet conditions or stagnation properties and the Mach number. We can then calculate the value of A*. Using the ratio of A/A*, for a specific location in the duct, we can extrapolate the Mach number using tables or numerical methods. Then we can use the isentropic relations to estimate all the flow properties based on the inlet total conditions, since the flow is isentropic.
The critical area is based on the inlet conditions, but the actual passage can present a minimum area that is larger than A*. In that case the flow will not choke at the throat. On the other hand, if the minimum area is smaller than A*, then the Mach number prescribed will not be possible. The throat will reach sonic conditions and the inlet Mach number will change accordingly.

## Slide 11: Quasi 1-D Flow Solution
  Note that is calculated based on the inlet conditions. However, in our actual passage geometry, the physical minimum area may be larger than. If this is the case, then the flow will not choke at the throat.
  It is also possible that the minimum area is smaller than. In this case, the prescribed inlet Mach number is not possible! In fact, for the prescribed stagnation pressure and temperature, the inlet Mach number will be lower and the physical throat in the passage will be choked.
  Let's analyze this issue further by looking at the variation in Mach number with passage area. Using the quasi 1-D governing equations and isentropic relations, we can develop the following relation:
  These equations lead to four limiting cases analyzed in the next slides.
Notes: Let’s analyze this in detail. From the continuity equation we can obtain this relation between Mach and area variations.

## Slide 12: Converging Passage
  Subsonic Inflow
Mach increases
  Supersonic Inflow
Mach decreases
Flow
Outflow
Inflow
A converging passage is a nozzle for subsonic inflow and a diffuser for supersonic inflow
A sonic flow cannot enter a converging passage!
(up to 1)
(down to 1)
  Sonic Inflow, Supersonic Outflow
Impossible!
  Sonic Inflow, Subsonic Outflow
Impossible!
Notes: Let's start with a converging passage. If we have a subsonic inflow, we would have an area variation less than 0 and a Mach variation larger than 0, hence the exit Mach number will be larger than the inlet Mach Number. For a supersonic inflow the Mach variation is negative hence the Mach decreases along the channel. This means that a converging passage is a nozzle for a subsonic inflow and a diffuser for a supersonic inflow. Let's assume now that we have a sonic inflow and a supersonic outflow. In this case the area variation is still less than zero and the Mach variation would be negative too, meaning that the Mach at the end of the throat will be less than the inflow, hence this situation is impossible. Now, if we assume to have a sonic inflow and a subsonic outflow, we would have a Mach variation larger than zero so the flow at the exit would be faster than the inlet , and this again is impossible. The conclusion is that a Sonic flow cannot possibly enter a converging passage.

## Slide 13: Diverging Passage
  Subsonic Inflow
Mach decreases
  Supersonic Inflow
Mach increases
  Sonic Inflow, Supersonic Outflow
Mach increases
  Sonic Inflow, Subsonic Outflow
Mach decreases
Flow
Outflow
Inflow
A diverging passage is a diffuser for subsonic inflow and a nozzle for supersonic inflow
A sonic flow can enter a diverging passage!
Note that the outflow may be subsonic or supersonic.
Notes: Now we can analyze a diverging passage, hence the area variation would be larger than zero. If we have a subsonic inflow the Mach variation would be less than zero, meaning that the flow decelerates along the duct. On the other hand, with a supersonic inflow the Mach variation is larger than 0 meaning that the Mach number increases through the duct. The conclusion is that the diverging passage is a diffuser for a subsonic inflow and a nozzle for a supersonic inflow. Now let's see what would happen if we have a sonic inflow. In this case both supersonic and subsonic outflows would be possible, as verified by the Mach variation for each scenario. Hence a sonic flow can enter a diverging passage and the outflow can be either subsonic or supersonic.

## Slide 14: Summary
  In this lesson we learned how to analyze quasi 1-D compressible flow problems having variable area.
  The concepts of choking and critical flow properties were introduced.
  We also saw that there are physical limitations on the type of flow that is permissible in a converging or diverging passage.
Notes: This concludes our lesson on the analysis of quasi 1D flows.