## Slide 1
Simulation Example 1
Compressible Flow Through a Converging Nozzle
Created by Ansys ACE
Edited by Ansys Academic Development Team

## Slide 2: Problem Statement
Overview
The amount of thrust generated by jet engine to propel an aircraft depends on the velocity difference between the outgoing gases and incoming air.
To impart high velocities to the exhaust gases, engines are fitted with nozzles. Exhaust gases expand as they flow through the nozzle.
Objective
Simulate the compressible air flow through a converging nozzle, operating at a nozzle pressure ratio of 2.
To calculate variables such as thrust and discharge coefficient and compare them with the experiments.
Problem description
Nozzle geometry –
  2D axisymmetric converging nozzle
  Nozzle exit radius = 1.5 inches.
Operating fluid is air –
  Air is modelled as a compressible ideal gas.
  Nozzle Pressure Ratio (NPR) = 2.

## Slide 3: Problem Statement
  Boundary Conditions
    No-slip wall for the walls of nozzle.
    Pressure-inlet for the nozzle inlet.
      Gauge Total Pressure – 202650 Pa
      Supersonic/Initial Gauge Pressure – 101325 Pa
      Temperature – 288 K
    Pressure-outlet for the domain exit.
      Gauge Pressure – 101325 Pa
  A Steady State Simulation is performed using 2D axisymmetric session of Ansys Fluent with the density-based solver.
Nozzle wall
Nozzle

## Slide 4
  At a Nozzle Pressure Ratio (NPR) of 2, the flow becomes mildly supersonic beyond the exit of the nozzle.
  The contours of Mach number clearly show the jet formation and eventual collapse of the potential core.
  The undulations in the profile of variation of Mach number along the axis (centerline) are due to existence of weak shock cells.
  Around x/D=9, the potential core of the jet collapses, which is indicated by the dramatic falloff in the centerline velocity.
4
4
4
Results
Contours of Mach number
Variation of Mach number with axial distance along the jet centerline

## Slide 5: Results
  The discharge coefficient (Cd) is the non-dimensional mass flow rate calculated as:
  Here, is the choked mass flow rate given by:
  From the simulation, at the exit of the nozzle is . Using the above formula and obtaining , we can calculate Cd to be.
  The discharge coefficient obtained from experiments is .
  The error between the simulation and experiment1 is around , which indicates an excellent agreement between the two results.
5
5
5

## Slide 6: Results
  The thrust coefficient (Cv) is the non-dimensional thrust force generated by the nozzle. It is calculated as:
  From the simulation, the numerator of the above equation is obtained as . Using the above formulae and calculating , we can calculate Cv to be.
  The thrust coefficient obtained from experiments is .
  The error between the simulation and experiment1 is around , which indicates an excellent agreement between the two results.
6
6
6
1 R. L. Thornock, E. F. Brown, “An Experimental Study of Compressible Flow Through Convergent-Conical Nozzles, Including a Comparison With Theoretical Results,” J. Basic Eng. Dec 1972, 94(4): 926-930.

## Slide 7: Summary
  An Ansys Fluent simulation was carried out to investigate the flow characteristics through a convergent nozzle for specified Nozzle Pressure Ratio (NPR) of 2.
  The formation of jet and eventual collapse of the potential core is clearly observed from the contours of the Mach number.
  The discharge coefficient estimated from simulations compares fairly well with that from the experiments1.
  The error between the Thrust coefficient estimated from the simulation and experiment1 is around 0.1%, indicating an excellent agreement between the two results.
7