## Slide 1
Simulation Example 2
Compressible Flow Through a Converging-Diverging (CD) Nozzle
Created by Ansys ACE
Edited by Ansys Academic Development Team

## Slide 2: Problem Statement
Overview
Converging-Diverging (CD) nozzles are used to accelerate compressible flows to supersonic speeds and are commonly used in propulsion systems of rockets and jet engines.
The nozzle has a converging section, a throat and a diverging section.
Objective
Simulate the compressible air flow through a converging-diverging nozzle, operating at two different nozzle pressure ratios.
To visualize formation of normal shock and subsequent shock-induced boundary layer separation.
Problem description
Nozzle geometry –
  2D axisymmetric converging-diverging nozzle
  , , .
Operating fluid is air –
  The ideal gas law is used to calculate density.
  Viscosity is modelled using the Sutherland viscosity law.

## Slide 3: Problem Statement
  Boundary Conditions
    No-slip wall for the walls of nozzle.
    Pressure-inlet for the nozzle inlet.
      Gauge Total Pressure – 150000 Pa
      Supersonic/Initial Gauge Pressure – 101325 Pa
      Temperature – 300 K
    Pressure-outlet for the domain exit.
      Gauge Pressure – 101325 Pa
  A Steady State Simulation is performed using 2D axisymmetric session of Ansys Fluent with the density-based segregated solver.
L = 0.11 m
rin = 0.0284 m
L = 0.012 m
rout = 0.01375 m
L = 0.0762 m
inlet
wall
axis
outlet

## Slide 4: Mach Number Contours: Shock vs. Design
  For both the cases
    The air accelerates through the converging section of the nozzle and reaches the sonic speed (M = 1) at the nozzle throat.
    Downstream of the throat, the flow continues accelerating to become mildly supersonic.
  In the 1st (Shock Case), the prescribed exit pressure at the nozzle outlet, p2 = 101,325 Pa, is greater than the theoretical isentropic exit pressure calculated using the provisional exit M = 1.5, p2’ = 40,860 Pa. Thus, the flow undergoes a normal shock in the diverging section, as postulated by the theory.
  For the Design Case, p2 = 101,325 Pa and p2’ ~ 101,325 Pa, thus p2 p2’. This is a branching point for the flow to either continue isentropically or create a shock. The flow, however, accelerates through the diverging section isentropically as creating a shock would require additional “effort”.
4
4
4
4
Contours of Mach number
Shock Case
Design Case
Normal Shock

## Slide 5: Shock-Induced Boundary Layer Separation
  When the shock impinges on the wall, it induces a small separation region (highlighted in blue color) in the boundary layer.
  This causes an increase in the subsonic region thickness in the boundary layer immediately downstream of the normal shock.
  Engineers designing CD nozzles for aerospace and space applications must account for this phenomenon otherwise overlooked by the inviscid theory.
5
5
5
Normal Shock
Boundary Layer Separation
Contours of Mach number
Shock Case

## Slide 6: Summary
  An Ansys Fluent simulation was carried out to investigate the flow characteristics through a convergent-divergent nozzle for two different Nozzle Pressure Ratios (NPRs).
  The air is observed to accelerate through the converging section of the nozzle and reaches sonic speed (M=1) at the nozzle throat.
  In the first case, since the exit pressure is greater than that estimated from isentropic flow calculations, the flow undergoes a normal shock in the diverging section of the nozzle.
  Subsequent shock-induced boundary layer separation post shock impingement on the nozzle walls is observed from the contours of Mach number.
6