## Slide 1
Internal Compressible Flows Course Lesson 4
Converging – Diverging Nozzle
Created by Ansys ACE
Edited by Ansys Academic Development Team

## Slide 2
  In this lesson we will analyze the flow in a converging-diverging (C-D) Nozzle.
  A C-D Nozzle is a variable area passage which is used to accelerate gases to higher supersonic speeds.
  It consists of a converging section with minimum area occurring at a specific location, called throat.
  Downstream of the throat, the cross-sectional area starts to increase, thus creating the diverging section of the C-D nozzle.
  It is most commonly used in propulsion systems such as rocket engines and after-burners of jet engines.
  It is also used in supersonic wind tunnels.
Introduction
Rocket Engine
Converging Section
Diverging Section
Throat
Notes: The focus of this lesson will be on analyzing compressible gas flow through converging-diverging nozzles. Also known as De-Laval Nozzles, these are devices that are used to accelerate fluids to very high speeds. CD nozzles are commonly used in propulsion systems of supersonic aircraft and spacecraft, and in supersonic wind tunnels.
A CD nozzle is shaped such that the cross-sectional area varies with axial distance along the length of the nozzle, as shown in the image here. The shape of a CD nozzle resembles that of an hourglass. There is a minimum area section called the throat, which is preceded by a converging section, and succeeded by a diverging section.

## Slide 3
  Using the continuity and the isentropic relations, we can get the following equation relating the Area with Mach number:
  This equation is called the area – Mach number relation, and it shows that *, i. e., the Mach number at any location in the duct is a function of the ratio of the local duct area to the sonic throat area.
  Note that there are two values of that corresponds to a given area ratio *, a subsonic and a supersonic value.
  The solution to this equation is plotted in the graph on the right, clearly showing the subsonic and the supersonic branches.
Area – Mach Number Relation
Super-sonic
Sub-sonic
Variation of Mach Number with Area
Notes: Using continuity and isentropic relations, we can obtain the following relation for the variation of Mach number with nozzle cross-sectional area. This equation is called the Area-Mach number relation. Notice the presence of a variable called A* which is the sonic throat area. From this equation, it is clear that the Mach number at any location in the nozzle is a function of the ratio of the local duct area to the sonic throat area. Here is a plot of Area-Mach number relation. If you notice, there are two values of Mach number that satisfy the equation for any given area ratio, a subsonic value, and a supersonic value.

## Slide 4
1-D Flow through a C-D Nozzle
Inlet total conditions fixed
(, , )
  Consider a C-D nozzle such that the area ratio at the inlet /. The inlet station feeds from a large reservoir operating at the and (stagnation properties).
  In the convergent portion of the nozzle, the subsonic flow is accelerated, and the Mach number is dictated by the local value of /. At the throat, where , we get .
  In the divergent portion of the nozzle the flow expands supersonically, and again the Mach number (supersonic now) is governed by the local value of /.
  The resulting variations of the pressure, temperature and Mach number follow a monotonic increase or decrease as shown on the right.
  , and are the pressure, temperature and Mach number at the nozzle exit. In an ideal situation the exit pressure is equal to the ambient pressure at the exit (back pressure, ) – this situation is referred to as “design condition”
  Next, we will evaluate the effect of different pressure ratios () across a given nozzle.
Notes: Let us now understand a generic 1-D flow through the CD nozzle. Consider a CD nozzle with a very high area ratio at the inlet. The inlet station feeds from a large reservoir operating at stagnation conditions of p0, rho0, and T0. When the ambient or back pressure at the exit of the nozzle is small enough, a supersonic flow will be established. In the converging section, the flow is always subsonic and the exact value depends on the local area ratio. At the throat, the area ratio is 1 i.e. At=A* and therefore the flow attains a sonic velocity. This sonic flow then enters the diverging section where it is further accelerated. The variation of pressure, temperature, and Mach number through the nozzle is shown here. Notice that pressure and temperature decrease whereas the Mach number increases, monotonically. The variables with subscript e refer to the conditions at the nozzle exit. Except for two special conditions which we will discuss later, the exit pressure will always be equal to the back pressure. For our discussion, we will be using the two terms interchangeably and make the distinction when necessary.

## Slide 5
  For our analysis, we will use the physical model of the C-D nozzle as shown in the figure.
  The nozzle is connected to a tank supplying the inlet station with fixed total pressure and temperature.
  A valve attached to the nozzle exit is adjusted to vary back pressure.
  Except for two special conditions which we will discuss later, the nozzle exit pressure will always be equal to the back pressure. For the purpose of our discussion, we will be using the two terms interchangeably and make the distinction when necessary.
  Let us analyze what happens to the flow as we open the valve and reduce the back pressure from
C-D Nozzle Model
Pressurized tank
C-D Nozzle
Pressure control valve
Low pressure environment
Notes: Let us now analyze the flow behavior at different values of the pressure ratio. Here, the pressure ratio is referred to as the ratio of the exit pressure to the inlet total pressure. For our analysis, we will consider the setup shown here where the CD nozzle is connected to a tank supplying the inlet section with air at a fixed total pressure and temperature.
A valve attached to the system beyond the nozzle exit is adjusted to vary the back pressure. Initially, let us assume that the back pressure is equal to the total pressure at the inlet. At this condition, no gas flow is possible.

## Slide 6
  Initially, . Therefore, there will be no flow in the nozzle.
  When back pressure is slightly reduced such that , a low speed flow is established in the nozzle, as indicated by Case
  As we start decreasing the back/exit pressure, , from to, this flow starts accelerating as shown by case .
  If the flow in the entire nozzle is subsonic, then the flow at any axial station within the nozzle can be analyzed using the relations derived previously.
  As the exit pressure is further decreased, the flow is accelerated more, leading to a higher Mach Number throughout the nozzle with the highest being at the throat. Consequently, the pressure is also lowest at the throat.
  At a certain value of , the flow just becomes sonic at the throat (Case C). At this point and .
Fully Subsonic Flow
A
B
C
A
B
C
Notes: Let us now reduce the back pressure slightly such that pb=pe=peA. At this condition, a low speed flow is established inside the nozzle. As the back pressure is further decreased, the flow is accelerated more, leading to a higher Mach Number throughout the nozzle, with the highest being at the throat. In the diverging section beyond the throat, the flow is decelerated.

## Slide 7
  Decreasing the exit pressure from to , the mass flow through the nozzle () increases until sonic conditions are reached at the throat corresponding to .
  The mass flow rate through the C-D nozzle corresponding to the condition C, i.e., sonic flow attained at the throat, is given by:
Choked Flow – Converging Section
C
.
1
Mass flow rate
  If the back pressure is further reduced, the Mach number at the throat cannot increase beyond 1.0 and the mass flow remains constant, this condition is referred to as choked flow.
  For , the sonic flow at the throat corresponds to the pressure ratio of .
Notes: The acceleration of the flow continues up to a back pressure, say pb=pe=peC, where the flow becomes sonic at the throat i.e. M=1 and At=A*. At this value of exit pressure, the mass flow rate through the nozzle attains its maximum value. Even with any further reduction of the exit pressure, the Mach number at the throat will always be 1.0 and the mass flow rate will remain constant. This situation is referred to as a choked flow. For a calorically perfect gas at gamma=1.4, the sonic flow at the throat corresponds to a throat pressure ratio i.e. p*/p0 of 0.528.

## Slide 8
  If the exit pressure, is further decreased to a value below the sonic condition, , the flow remains unchanged in the converging section. However, interesting flow phenomenon occurs in the diverging section of the nozzle.
  No isentropic solution is possible in the divergent duct until the nozzle exit pressure is adjusted to the specified low value as shown earlier for the design condition case.
  For values of exit pressure above the supersonic design condition value, but below (sonic condition), a normal shock wave is observed inside the diverging section as shown.
  The region ahead of the shock in the diverging section is supersonic while behind the shock, the flow is subsonic. As a result, the Mach number decreases, and the static pressure increases towards the exit.
Choked Flow – Diverging Section
Normal Shock
Isentropic Solution (Supersonic)
Isentropic Solution (Subsonic)
Isentropic Solution (Supersonic)
Notes: Now, if the back pressure is decreased below the value of peC, there will not be any change in the flow characteristics in the converging section. For values of back pressure less than peC but greater than design condition, which we will refer to as pb=pe=peD, a normal shock is formed in the diverging section of the CD nozzle. The flow in front of the shock is supersonic, while behind the shock it is subsonic. The plots here show the representative pressure and Mach number distribution for the condition where a normal shock exists in the diverging section. Before the shock, the Mach number of the flow increases through the diverging section, and subsequently, the pressure reduces. Beyond the shock, the flow becomes subsonic and starts decelerating as it flows through the rest of the nozzle, while the pressure dramatically increases across the shock and keeps increasing till the nozzle exit, where it becomes equal to the prescribed back pressure, peD. If the value of peD is closer to peC, the normal shock is located closer to the throat of the nozzle. As peD is decreased, the shock wave moves downstream and closer to the nozzle exit.

## Slide 9
  The location of the normal shock is such that it allows the exit pressure to attain the prescribed value at the nozzle exit.
  The flow accomplishes this via the increase of static pressure across the shock wave and the pressure increase due to the subsonic flow in the remaining diverging section.
  As we decrease the exit pressure further from , the shock wave moves downstream and closer to the nozzle exit.
  At a certain value the shock will be located precisely at the exit.
  Note that in this figure represents the proper isentropic value for the design exit Mach number and it exists just upstream of the normal shock.
  From this condition, the back pressure and exit pressure will be distinct.
  Now let's reduce the backpressure even further and see what happens to the shock at the exit.
Choked Flow – Diverging Section
Notes: At a certain value of back pressure, the shock sits exactly at the nozzle exit. At this condition, the nozzle exit pressure and the back pressure will become distinct. The back pressure, say peE, is the static pressure behind a normal shock at the design Mach number of the nozzle. In this figure, peF represents the proper isentropic value for the design condition and it exists just upstream of the normal shock. From this point on, the nozzle exit pressure remains unchanged at peF, irrespective of the back pressure. Since we know that peF is the design condition exit pressure, let us look at how the flow behaves for back pressure values between peE and peF.

## Slide 10: Overexpanded and Underexpanded Nozzles
  When the downstream backpressure is further reduced such that then the flow inside the nozzle is fully supersonic and isentropic. However, the nozzle exit pressure is maintained at
  The increase of exit pressure () to the backpressure () takes place across an oblique shock attached to the nozzle exit, outside the duct itself as shown. The nozzle in this case is said to be overexpanded, because the pressure at the exit has expanded below the back pressure ().
  If the back pressure is further reduced, we reach a stage where . At this point the nozzle is said to be operating at design conditions, as we get perfect supersonic expansion.
  If the back pressure is further reduced to , the flow adjustment takes place across expansion waves outside the duct as shown.
  In this case, the nozzle is said to be underexpanded, because the exit pressure is higher than the back pressure, () and the flow is capable of further expansion after exiting the nozzle.
Oblique Shocks
Overexpanded Nozzle
Underexpanded Nozzle
Expansion Waves
Design Condition
Notes: As soon as the back pressure is reduced below peE, the shock wave moves out of the nozzle, and the flow inside the nozzle is fully supersonic and isentropic. However, since the exit pressure (peF) is still less than the back pressure, oblique shock waves are formed at the nozzle lip through which the gas pressure is increased. In such a case, the nozzle is said to be overexpanded.
On further reduction of exit pressure such that pb=peF, we arrive at the design condition of the nozzle. At this condition, there is a perfect supersonic expansion and no shock waves are present either inside or outside the nozzle. For this condition, the back pressure and exit pressure will match identically.
Now, if the back pressure is further reduced below peF, the nozzle is said to be underexpanded and in order for the exit pressure (peF) to be made equal to the back pressure, expansion waves are generated at the nozzle lip.

## Slide 11: Effect of Backpressure on CD nozzle Flow
Subsonic
throughout
Normal Shock in diverging section
Over-expanded
Under-expanded
Stagnant
Subsonic except for throat
Shock at the exit plane
Perfect supersonic expansion –
Design condition
Underexpanded into a vacuum
Notes: Till now, we have analyzed the qualitative flow behavior in a CD nozzle at different pressure ratios. It is now time to understand the overall process quantitatively.

## Slide 12: 1-D Flow Solution for C-D Nozzle
  Now that we understand the flow physics of a C-D nozzle, lets look at the overall process of analyzing the flow quantitatively.
  We begin the analysis by assuming the flow through the nozzle is entirely isentropic. Therefore, total properties are constant: , ,
  Using the isentropic relations and the known exit pressure , we can compute
  We now calculate from the area ratio equation, using and . This is a provisional critical value which we will use to determine if in fact the flow is isentropic and fully subsonic.
  Next, we compare the actual throat area with Two possibilities exist:
     This indicates that the throat is too large for sonic flow and thus the entire nozzle flow is subsonic.
     This indicates that the throat is too small for subsonic flow and thus the nozzle is choked. For this scenario, we can split the analysis into two parts: (A) the converging section, and (B) the diverging section.
  Let’s consider each of the above cases in detail.
Notes: Let us begin by assuming that the flow through the nozzle is entirely isentropic. As a result, the total conditions can be considered constant throughout the nozzle. For a known value of exit pressure p2, the following expression can be written using the isentropic relations, from which exit Mach number M2 can be calculated. Using A2 and M2, we can calculate A* from the area ratio equation. This calculated value A* can be compared with the actual cross-sectional area of the throat, At. If At is greater than A*, it indicates that the throat is too large for a sonic flow and thus the entire nozzle flow is subsonic. If At is less than A*, it indicates that the throat is too small for subsonic flow and thus the nozzle is choked.
Let us now look at each of these conditions in more detail.

## Slide 13: Fully Subsonic Flow
  If the flow in the entire nozzle is subsonic, then calculating the flow at any axial station within the nozzle is straightforward. Just use the computed from the first step as a reference quantity.
    For any station, compute the area ratio and calculate the Mach number from the area ratio equation. You can use tables, charts, or solve the equation numerically for .
    Knowing the total properties and Mach number, calculate all flow properties and the mass flow rate. As a check, make sure your calculated mass flow rate is consistent at each station.
Note that you only consider the subsonic solution here.
Inlet total conditions fixed
(, , )
Choked pressure
Nozzle throat
Exit
Notes: When the flow is fully subsonic in the nozzle, using A* as the reference quantity, we calculate the area ratio at any location in the nozzle. From Mach number – area ratio relation, we obtain the corresponding flow Mach number at this location. Knowing the total properties and the Mach number, it is straight forward to calculate all the flow properties and the mass flow rate.

## Slide 14: Choked Flow – Converging Section
  If the throat is choked, then the physical area and the reference area are the same.
  Note that the flow in the converging section is subsonic and isentropic. Hence, we can calculate any station from the inlet to the throat as defined previously for the fully subsonic case.
    For any station, compute the area ratio and calculate the Mach number from the area ratio equation. Use the subsonic solution.
    Knowing the total properties and Mach number, calculate all flow properties and the mass flow rate. Make sure your mass flow rates are consistent with the inlet as a check.
Choked pressure
Nozzle throat
Exit
Inlet total conditions fixed
(, , )
Notes: For the condition where the throat is choked, i.e. At=A*, we know that the flow in the converging section is subsonic and isentropic. Hence, we can use the same procedure as we just discussed to obtain the flow properties at any location in the converging section.

## Slide 15: Choked Flow – Diverging Section
  In the diverging section of the nozzle, there are two possibilities:
    The flow at the exit is supersonic.
    The flow at the exit is subsonic.
  As discussed previously, in the subsonic case, there must be a normal shock wave in the diverging section as the flow is supersonic when it enters the diverging section.
  The subsonic flow downstream of the shock will then diffuse (slow down).
Note that which case will occur depends entirely on the prescribed exit pressure!
Choked pressure
Nozzle throat
Exit
Inlet total conditions fixed
(, , )
Supersonic
Subsonic
Notes: For the diverging section however, things are a little different. There are two possibilities based on the prescribed back pressure.
The flow at the nozzle exit is subsonic and
The flow at the nozzle exit is supersonic.
In the case of a subsonic exit flow, as discussed earlier, there must be a normal shock wave in the diverging section.

## Slide 16: Choked Flow – Diverging Section
  Let’s look at the case of supersonic flow at the exit.
    We first compute a provisional exit supersonic Mach number knowing the exit area ratio . We will denote this as .
    From this provisional Mach number, we calculate the theoretical exit pressure using the isentropic relation for pressure ratio (since no shocks exist in the diverging passage and ).
    Then compare the computed with our prescribed :
      - For this case, the flow expands outside of the nozzle, and thus the actual pressure that will exist at the nozzle exit plane is . Hence, our previous analysis for the supersonic exit condition is used.
      - For this case, it is clear that the flow must undergo a normal shock wave somewhere in the diverging passage and then diffuse subsonically to the prescribed exit pressure. We will discuss this case next.
Choked pressure
Nozzle throat
Exit
Inlet total conditions fixed
(, , )
Fully Supersonic
Normal Shock
Note that we want the supersonic solution to the area ratio equation.
Notes: For a supersonic flow at the exit, we first compute the design condition exit Mach number using the exit area ratio A2/A*. For this Mach number, we can compute the exit pressure, let us say p2’, using isentropic relation for pressure ratio. If we compare the value of p2’ to our prescribed back pressure, we encounter two scenarios.
If p2 is less than p2’, the flow needs further expansion, in order for the exit and back pressures to match, which happens outside the nozzle. This is the underexpanded condition that we discussed previously.
If p2 is greater than p2’, there must be a normal shock in the diverging section and the flow must pass through this shock and further diffuse subsonically to the prescribed back pressure.

## Slide 17: Normal Shock in the Diverging Section
  The problem in this case is that we don’t know the exact location of the normal shock wave. However, we can compute the position using a trial and error process in conjunction with the shock wave relations, shown below for reference. For clarity, we will denote each side of the shock by the letters A (upstream) and B (downstream).
A
B
Shock wave
Choked pressure
Nozzle throat
Exit
Inlet total conditions fixed
(, , )
Fully Supersonic
Normal Shock
Notes: In this case, there is one problem though. How do we determine the location of the normal shock? Well, we have to use a trial and error strategy. Let us look at this using the following flowchart.
We first assume a location for the normal shock in the diverging section of the nozzle. Let us consider the location just in front of the normal shock as A and just behind the normal shock as B. Since the flow from the nozzle inlet to point 𝐴 is isentropic, we know the total properties at 𝐴. From the area-ratio equation we can calculate 𝑀𝐴 using the supersonic solution. Using 𝑀𝐴 and the total properties at 𝐴, we then calculate the static properties at 𝐴 (𝑝𝐴, 𝑇𝐴, 𝜌𝐴). We can now use the normal shock wave relations to obtain the static properties at location B from the known values of MA and static properties at A. We can obtain the total quantities at B which will prevail through the remainder of the nozzle (where the flow is isentropic). Using MB and the Area-Mach number relationship, we can calculate a new reference critical area AB*. This critical area will also prevail from the downstream side of the shock to the exit. Using the exit area 𝐴2, we calculate 𝐴2/𝐴B* and then obtain a provisional subsonic 𝑀2, again using the area-ratio equation.

## Slide 18: Trial and Error Method for Finding The Shock Wave Position
Begin by guessing an axial position in the diverging passage. A shock wave is fixed at this position with upstream downstream stations and .
Since the flow from the nozzle inlet to point is isentropic, we know the total properties at . From the area ratio equation we can calculate using the supersonic solution.
Using and the total properties at we then calculate the static properties at (, , ).
Now apply the shock wave equations to obtain , , , and knowing and the static properties. We can obtain the total quantities , , which will prevail through the remainder of the nozzle (which flows isentropically).
From the area and we now calculate a new This reference critical area will also prevail from the downstream side of the shock to the exit.
Using the exit area , we calculate and then obtain a provisional subsonic , again using the area ratio equation.
Finally, using the isentropic relation for total to static pressure ratio, we solve for a provisional exit pressure .
If is greater than the prescribed exit pressure , the shock must be closer to the throat and the assumed axial position is reduced;
Otherwise, we increase . A small increment is chosen for these adjustments.
Update
Notes: Finally, using the isentropic relation for the total to static pressure ratio, we solve for a provisional exit pressure 𝑝2′. If 𝑝2′ is greater than the prescribed exit pressure 𝑝2, the shock must be closer to the throat and the assumed axial position 𝑥 is reduced and rerun the analysis. Otherwise, we increase 𝑥 and rerun the analysis. A small increment Δ𝑥 is chosen for these adjustments.

## Slide 19: Summary
  In this lesson, we analyzed 1-D compressible flow in a converging-diverging (C-D) nozzle.
  Several solutions are possible depending on the boundary conditions (particularly the exit static pressure).
  The solution methods can easily be codified in a computer program, spreadsheet, or similar tool.
  Despite the widespread use of numerical methods for flow solutions, these methods are useful for quick design calculations as well as illustrating key features of the C-D nozzle flow field.
Fully supersonic
Choked pressure
Normal shock
Fully subsonic
Choked subsonic
Nozzle throat
Exit
Inlet total conditions fixed
(, , )
Notes: That brings us to the end of this lesson.