## Slide 1
Homework 1
Rayleigh Flows
Created by Ansys ACE
Edited by Ansys Academic Development Team

## Slide 2: Problem Statement
Overview
Chemical lasers are in the industry for precise cutting and drilling. The flow moving in the cavities of the glass resonator that generates the laser beam is subject to heat addition due to chemical reactions and molecular vibrational energy.
These types of flows are examples of the physics described by Rayleigh flows.
Objective
Simulate the Rayleigh flow inside a duct using the density-based solver in Ansys Fluent.
To explore the physics of heat addition to a compressible inviscid flows.
Problem description
Duct geometry –
  2D axisymmetric duct
  , .
  Zone 1 – No heat addition.
  Zone 2 – Heat is added to the fluid through a volumetric energy source of .
Operating fluid is air –
  The air is modelled as an inviscid ideal gas.

## Slide 3: Problem Statement
  Boundary Conditions
    Wall - No-slip and adiabatic wall.
    Inlet – Velocity inlet.
      Velocity magnitude =
      Supersonic/Initial Gauge Pressure – 101325 Pa
      Temperature – 288.15 K
    Outlet – Pressure outlet.
      Gauge Pressure – 101325 Pa
      Backflow Total Temperature – 372.12 K
  A Steady State Simulation is performed using 2D axisymmetric session of Ansys Fluent with the density-based segregated solver.
Velocity
Inlet
Pressure
Outlet
Axis
U = 408.35 m/s
Adiabatic No-slip Wall
Zone 1 (1m)
Zone 2 (2m)

## Slide 4: Results
  The total temperature contours show how the energy source adds heat to the fluid and increases its temperature, both for the supersonic and the subsonic case.
  The total temperature remains constant in the upstream region without the heat source.
4
4
4
4
Contours of Total Temperature for the Subsonic Case
Contours of Total Temperature for the Supersonic Case

## Slide 5: Results
  The Mach number contours show that the heat addition affect the subsonic and the supersonic flows in the opposite manner, as described by the theory. The subsonic flow is accelerated while the supersonic flow is slowed down.
  The fluid passing through the region without heat source maintains its velocity constant.
5
5
5
5
Contours of Mach number for the Subsonic Case
Contours of Mach number for the Supersonic Case

## Slide 6
Appendix
Rayleigh Flow

## Slide 7: Boundary Conditions
  The pressure outlet requires the backflow total temperature to be set.
  No reversed flow develops in this problem, thus the temperature setting at the outlet is not applied.
  Still, it is a good practice to apply realistic values of the backflow total temperature at the outlet.
  In order to estimate the total temperature, we can estimate the heat per unit mass from the value of the energy source () and knowing the heated volume () and the mass flow rate (). Then, we can obtain the expected total temperature at the outlet:

## Slide 8: Solution Controls
  The overall convergence rate of this particular problem is somewhat slow when using default settings. Since the flow field is very simple and devoid of strong flow gradients, we can accelerate the solution convergence increasing the Courant number in the solution controls section.
  In this case we increase the value from 5 (default) to 50, greatly reducing the simulation time, without causing the solution to diverge.