## Slide 1
Internal Compressible Flows Course Lesson 6
Method of Characteristics
Created by Ansys ACE
Edited by Ansys Academic Development Team

## Slide 2: Introduction
  In this lesson we will discuss the method of characteristics for solving the governing equations of supersonic steady inviscid and irrotational flows, and illustrate an application of this method in a design of a divergent section of a supersonic nozzle.
  Combining the Continuity and Euler's equations, under the assumption of two-dimensional irrotational flow, we can derive the velocity potential equation:
  In a supersonic flow, this equation is of hyperbolic type, and can be solved by the method of characteristics.
  It is not our goal here to go over the entire mathematical theory of hyperbolic equations. Instead, we will simply refer to PDE textbooks for the main results needed for this lesson.
2
2
Notes: In this lesson we will discuss the method of characteristics for solving the governing equations of supersonic steady inviscid and irrotational flows and also see how this method can be applied to design the diverging section of a supersonic nozzle.

## Slide 3: Main Postulates
  A PDE is hyperbolic if the coefficients of its highest-order derivatives satisfy a certain relation. For the velocity potential equation, this relation is:
  A hyperbolic equation is characterized by the existence of certain directions (or lines) in the plane called characteristics. For the velocity potential equation, characteristics are the Mach lines.
  The normal derivatives of the velocity components (2nd derivatives of the velocity potential) are indeterminate on a characteristic and can even be discontinuous in some cases, but the velocity itself (or 1st derivatives of the velocity potential) is continuous.
  Since the normal velocity derivative is allowed to be discontinuous on a characteristic, different flows can be patched together at characteristic lines.
  On characteristics, the velocity potential satisfies a certain relation called the compatibility equation.
3
3
Notes: Combining the Continuity and Euler's equations, under the assumption of two-dimensional irrotational flow, we can derive the velocity potential equation. For a supersonic flow this equation becomes hyperbolic in type, since the square of the velocity magnitude divided by the speed of sound is larger than 1. [(phix^2+phiy^2)/a^2 >1]
A hyperbolic equation presents particular directions in the space called characteristics. Along the characteristics the flow properties are continuous, the derivatives are indeterminate and can be discontinuous. Also, the velocity potential relation satisfies the compatibility equation.

## Slide 4: Method of Characteristics
  Let’s go back to the 2-D velocity potential equation.
  Since the velocity potential and its derivatives are functions of and , we have:
  As these equations represent three equations with three unknowns, using Cramer’s rule we get:
4
4
Notes: The velocity potential equation can be combined with the chain rule for the potential derivatives to obtain a system of three linear algebraic equations. This system can be solved using Cramer’s rule, for example we can solve for phi_xy.

## Slide 5: Characteristic Lines
  If the denominator is chosen such that , then the numerator must also be zero , as we know that has a specific defined value at every point in the flow.
  Thus, we can say that there is some direction at every point () along which is indeterminate which is the characteristic line. Precise direction of these lines can be calculated as following:
  Consider the point in the flow field and set the denominator to zero. Expanding the determinant and setting it to zero, we get:
  Here represents the slope of the characteristic lines and is given by the roots of this quadratic equation:
5
5
Notes: If we set the denominator to be equal to zero then also the numerator must also be zero, since the phi_xy must have a finite value in every point of the flow. This means that phi_xy is indeterminate, hence we found a characteristic line.
Let’s see how we can define these lines. If we set the denominator to zero and expand its expression, we obtain the following equation in terms of velocity components. In this case, we can solve for dy/dx that is the slope of the characteristic lines of the problem.

## Slide 6: Characteristic Lines
  Since and , and the local Mach angle is given by , the slope becomes:
  After some algebraic and trigonometric manipulation, we get:
  This equation states that the two characteristic lines running through the point have slopes equal to shown by and depicted by .
  The characteristic lines through the point are simply the left and right running Mach waves through the point, i. e. the characteristic lines are Mach lines.
  Note that the characteristic lines are curved in space because the local Mach angle depends on the local Mach number which is a function of both and . Moreover the local streamline direction also varies throughout the flow.
6
6
Characteristic Line
Streamline
Notes: Now, we can further manipulate this expression into something much simpler. We can define the components of the velocity u and v through the angle that the velocity vector has with respect to a horizontal line. If we replace these expressions in the formula for the slope, we obtain this relation that can be simplified into this final relation through algebraic and trigonometric manipulations. The slope of the characteristic lines is equal to the tangent of the angle between the characteristic line and a horizontal line, as you can see in the graph.
This means that for a point A in the space where the velocity of the particle is V, two characteristic lines would pass through A with a slope given by tan(theta-mu) and tan(theta+mu). We can see that the characteristic lines are inclined by an angle mu with respect to the velocity vector, hence these lines are simply two Mach lines. Depending on the position in the flow, the fluid could have a different Mach number and velocity vector orientation. This causes the characteristic line to have a different orientation based on the position in the flow.

## Slide 7: Compatibility Equations
  Along the characteristic lines, the governing partial differential equation describing the flow reduce to ordinary differential equations known as compatibility equations.
  These can be found by setting the numerator determinant to zero, , giving:
  Substituting here the slope of the characteristic lines, and and after some algebraic manipulations we get the following ODEs:
7
7
Notes: Along the characteristic lines the governing equations that describe the fluid reduce to what we call compatibility equations. We can simply obtain these equations setting the numerator N equal to zero.
This gives us this relation that can be re-casted into two equations after some manipulations using the relations for the characteristic lines slope.

## Slide 8: Compatibility Equations
  These equations can be integrated to obtain a result in terms of the Prandtl-Meyer function as shown:
  Here and are different constants along different and characteristics.
  The above compatibility equations are now reduced to algebraic equations. In general inviscid supersonic steady flow, the compatibility equations are ODEs.
  In the case of a 2-D irrotational flow they further reduce to algebraic equations.
  The equations can be combined to obtain simple expressions to calculate and .
  Next, we discuss how we can use these results for calculating the supersonic flow inside a nozzle and determine a proper wall contour so that no shock waves appear inside the nozzle.
8
8
Notes: These are two ordinary differential equations that can be integrated into simple angular algebraic relations for irrotational 2D flows, where the sum or difference between the flow direction angle and the value of the local Prandtl-Mayer function is equal to a constant. K- and K+ are two different constants along the C- and C+ characteristics.
Combining the two relations we can also obtain simple expressions to calculate theta and nu based on the two constants at a point in the domain.

## Slide 9: Supersonic Nozzle Design
  Design problem:
Design the wall contour for a converging-diverging nozzle to allow shock-free isentropic expansion of a gas from rest to a given supersonic Mach number at the exit.
9
9
  For the convergent section, there is no particular contour which gives better results than the others. Thus the design of this part of the nozzle is usually based on experience and industry best practices.
  Let’s consider a 2-D flow for simplicity, as shown on the next slide. The sonic line is located at the throat.
  The limiting characteristic is such that any characteristic line originating downstream of this line does not intersect the sonic line.
  Based on the calculations of the convergent profile, we know the flow properties in the throat region and thus we can use the limiting characteristic as the initial data line.
  The diverging section is divided into two regions: Expansion section and Straightening section.
Notes: Let’s now analyze how we can use the characteristics to design a supersonic nozzle. Our design problem we want to solve is to “ Design the wall contour for a converging-diverging nozzle to allow shock-free isentropic expansion of a gas from rest to a given supersonic Mach number at the exit.” For the convergent section there is not a particular contour that gives better results than others, and industry best practices are sufficient. For the diverging section of the nozzle the methods of characteristics should be used.

## Slide 10: Supersonic Nozzle Design
10
10
Expansion Section
Sonic Line
Limiting Characteristic
Straightening Section
Supersonic nozzle profile design using method of characteristics
Notes: Let’s consider a 2D problem for simplicity, this is a converging diverging nozzle geometry. The sonic line is located at the throat. The limiting characteristic is defined such that any characteristic originating downstream the throat cannot cross or intersect the limiting line. The flow conditions at the nozzle throat are known based on the convergent geometry. Hence the information on the limiting characteristic is known.
Here, we can see that the divergent zone of the nozzle can be divided into two sections: the expansion section and the straightening section. Let’s define theta_w the angle between the wall and the horizontal line. In the expansion section the theta angle increases constantly up to a maximum theta_max. Past this point the straightening section starts and the wall angle keeps decreasing until it goes back to zero at the nozzle exit.
The shape of the expansion section is arbitrary and is usually in the form of a circular arc of large radius.
Let’s add to the picture some characteristic lines. Point s 1,5 and 8 are defined by the flow properties and the wall angle given by the expansion section geometry chosen. The flow properties and direction in point 2 are also known. We would need to find the flow properties in points 12 and 13 to define the shape of the straightening section of the nozzle. This grid of characteristics is coarse in order to help highlight the process and having a clear picture. The solution of the method of characteristics is an exact solution for an infinite number of characteristic lines. In practice, a finite number of lines is used and small errors due to resolution and simple approximations, like straight connecting segments between the points, would affect the final results. However, with a good number of lines it is possible to have just small percent errors.
The solution is obtained solving the flow at the different intersection points of the grid. The points shown in here in blue are what we call internal grid points. The yellow points are wall grid points, that would define the shape of the wall. Only the points on one side of the symmetry axis can be solved since the points on the other side would be the exact reflection of the previous ones.

## Slide 11: Supersonic Nozzle Design
  If we define as the angle between a tangent to the wall and the horizontal, then the section where is increasing is called the expansion section. This section ends at the point of .
  Downstream from this point is the straightening section where decreases to zero at the nozzle exit.
  The shape of the expansion section is arbitrary and is usually in the form of a circular arc of large radius.
  Therefore, for our analysis we know the flow properties along the limiting characteristic line and the slope at points , and . Now we simply need to apply the method of characteristics to design the contour of the straightening section, i. e., from points through . Points below the axis are simply the reflections of the points above the axis.
  It should be noted that the characteristic mesh sketched here is very coarse and in actual calculations, the mesh should be much finer.
  The method of characteristics is an exact solution of inviscid, nonlinear supersonic flow. However, in practice, there are numerical errors associated with the finite grid: the approximation of the characteristics mesh by straight-line segments between grid points is one such example.
  In principle, the method of characteristics is truly exact only in the limit of an infinite number of characteristic lines.
11
11
Notes: The procedure to solve this problem is to march downstream from the initial data line at the throat to the nozzle exit and solve each point one by one.

## Slide 12: Internal Points
  The calculation procedure consists of analyzing the flow at grid point which are the points of intersection of characteristic lines.
  There can be two types of grid points:
    Internal Grid Points
    Wall Grid Points
  Lets first analyze the internal grid points as shown. We know the location and flow properties at points 1 and 2.
  Point 3 is simply on the centerline. The characteristic and characteristic are coming from point 2 and 2’ respectively and are symmetric.
12
12
  The constants along the given and characteristics are the same and opposite . The flow angle is zero since the point is on the centerline. Hence can be calculated as:
Notes: Let’s start with point 3. The C- characteristic is the same as point 2 because they are on the same line. Since the point also lies on the centerline the K+ and the K- constants are the same and opposite. Hence, theta is equal to zero and nu can be directly calculated.

## Slide 13: Internal Points
  Using and , we can calculate the remaining flow properties:
13
13
Obtain using
Calculate and from and previously known ,
Using , Compute and then
Notes: From the Prandtl-Meyer relation we can obtain the Mach number and then the flow properties using the isentropic relations. From the Mach number and the temperature, we can also estimate the speed of sound and so the local velocity.

## Slide 14: Internal Points
  Point 4 is located at the intersection of the characteristic and characteristic through points 1 and 3 respectively. Therefore, we can say:
  𝐾_− and 𝐾_+ are constant along the given and characteristics, and at point 4 we can write:
  Solving these two algebraic equations we obtain the following solution:
Using and , we can calculate the remaining flow properties as done for point 3.
14
14
Notes: Next, we can move to point 4. Point four is located at the intersection of the C- characteristic and the C+ characteristic through point 1 and 3 respectively. Hence, K-4 is equal to K-1 and K+4 is equal to K+3. From these known values we can calculate theta and nu for point four. Once nu is known we can estimate the flow variables as done for point 3.

## Slide 15: Wall Points
  Let's consider an internal point () which is close to the wall. The characteristic through point 4 intersects the wall at point .
  Assume the slope of the wall at point is known, i. e., . Then we can obtain the flow properties at this wall point using the properties at point as is constant along the characteristic :
  Since we already know and , we can easily compute and follow the procedure outlined in the previous slide to obtain the remaining flow variables.
  Note that for both internal and wall points, our analysis started using the known properties at specific grid points.
  Therefore, we begin our analysis from the initial data line and compute the flow properties by marching downstream along the grid defined by the intersection of characteristic lines.
15
15
Notes: For the wall points the procedure is similar. Let’s consider point 5, for this point we know the wall slope theta_5 and that the K+5 constant is equal to K+4 since they lay on the same characteristic line. So, nu-5 can be directly estimated and so the remaining flow variables.

## Slide 16: Wall Points
  Let's consider the wall points on the straightening section of the nozzle. These points are needed to define the shape of the nozzle profile.
  The slope of the wall at points and is not known in this case.
  However we know that the straightening section of the nozzle is designed in such way that we have expansion waves cancellations at the wall. Hence, no characteristic line would be generated.
  This means that the flow properties are the constant along the characteristic lines coming from points 9 and 11.
16
16
and
and
  To draw the nozzle profile start from point 8 and draw a straight line at an angle of that intersects the line from point 9. The intersection point is point 12.
  Then using an angle of repeat the process from point 12 to intersect the line from point 11 and identify point 13.
Notes: Solving for the different points in the domain we finally reach the wall points in the straightening section where the wall angle is not known like for point 12 or 13. The purpose of the straightening section is to cancel any expansion wave impinging on the wall. For this reason, the characteristic lines from point 9 and 11 are completely straight lines and end at points 12 and 13. At the walls the K+ and K- values, and so theta and nu, are the same as the last connected point, in this case point 9 and 11 respectively.
The wall of the nozzle is then obtained moving from point 8 to 12 and then to 13 drawing a straight line with an average slope ½ (theta-8 + theta-12) and ½ (theta-12 + theta-13) respectively until the next characteristic line is intersected. It must be noted that the Mach number at points 11 and 13 would be the exit Mach number for the nozzle.

## Slide 17: Supersonic Nozzle Design
  The procedure outlined in the previous slide can be easily put into a computer program which can be used to compute the optimum profile for a supersonic nozzle.
  The figure below represents the nozzle design for air flow () at a given exit computed using 50 characteristic lines.
17
17
Notes: This process can be automated into a computer program to get the optimum profile for a supersonic nozzle. Here is an example of the 50 characteristic lines used to obtain the shape of a Mach 2.5 nozzle. In this case only the points on the wall of the expansion section are used as starting points for the method.

## Slide 18: Summary
  In this lesson we discussed the method of characteristics.
  We also showed how this method can be used to design the wall profile for a supersonic nozzle.
  Method of characteristics allows us to analyze the flow along the characteristic lines easily as the partial differential equations convert to ordinary differential equations along these lines.
  In the next section, we will cover external compressible flows.
18
Notes: This highlights the importance of the method of characteristics in the design phase for a supersonic nozzle.