## Slide 1
Lesson 3: Introduction to Direct Modeling in Ansys Discovery, Part 3
Developed and curated by the Ansys Education Team
education@ansys.com
Adaptation and compilation led by Alfred Oti
Based on curriculum by Kenneth Alfano, Teaching Professor in Engineering Undergraduate Education at the University of Michigan

## Slide 2: Learning objectives for this unit
Intended Learning Outcomes | 
Knowledge and Understanding | Understanding of the fundamental tools used to create and edit geometry in Ansys Discovery: model stage
Skills and Abilities | Ability to create and edit simple geometric 3D models
Values and Attitudes | Insight into how the fundamental style of modeling used in Ansys Discovery
Resources
Software: Ansys Discovery 2022 R2
University of Michigan personnel.
Built-in Assessment
  Step-by-Step guide
Further reading/information
  Ansys Academic
  Ansys Innovation Courses
  Ansys Education Resources

## Slide 3: Camera Exterior Tutorial
This tutorial will take you through the steps to create an exterior of a 3D camera model as shown below, based on a Nikon D7500 (we will make some simplifying assumptions here).
Notes: Now, let’s begin with a brief overview of modeling.
Computer-Aided Design more often termed as CAD – C A D.
Gives us the ability to our designs in 3D,
explore and make mistakes with less cost than physical prototypes.
For example, it might not necessarily be feasible to build a large-scale prototype,
but with CAD we can put in our desired specifications and metrics
and see how it would look in a virtual space.
Additionally, CAD models can also be used with simulation,
C A E or Computer Aided Engineering programs.
This allows for more and faster design iterations,
by saving time when testing with virtual prototypes.
For example, it isn’t necessarily feasible to prototype a whole item or a whole object.
Whether it’s an aircraft, a bridge, a car engine
Putting that object into a simulated space
can allow us to have an example of how that object may react when physically prototyped.
REFERNCES
https://www.engineering.com/DesignSoftware/DesignSoftwareArticles/ArticleID/16587/Whats-the-Difference-Between-Parametric-and-Direct-Modeling.aspx#:~:text=In%20a%20nutshell%2C%20parametric%20design,3D
https://www.ptc.com/en/cad-software-blog/parametric-vs-direct-modeling-which-side-are-you-on

## Slide 4: Camera Exterior Tutorial (Casing)
Step 1: Using the Rectangle tool, draw a box measuring 135.5 mm by 104 mm. Then click on Return to 3D to create a surface.
Step 2: Using the Pull tool, extrude the box by 72.5 mm to form a 3D box.

## Slide 5: Camera Exterior Tutorial (Casing)
Step 3: Select the top-left edge of the box, then use the Pull tool and select Round from the right Heads-Up Display (HUD). Extrude the edge with a radius of 25 mm.
Step 4: Using the Circle tool, draw a circle with a diameter of 20 mm. The circle should be 20 mm from the top-right edge and centered from the top and bottom edges.

## Slide 6: Camera Exterior Tutorial (Casing)
Step 5: Using the Pull tool, extrude the circles by 20 mm to create buttons.
Step 6: Using the Rectangle tool, on the rear face of the camera casing (when looking at it, the button is on the top face on the right side) draw a screen measuring 75 mm by 15 mm. Place the screen 27 mm above the bottom edge and 15 mm from the left edge of the casing. Then click Return to 3D, and use the Pull tool to extrude the screen by a depth of 3 mm.

## Slide 7: Camera Exterior Tutorial (Casing)
Step 7: On the right side of the camera casing, using the Rectangle tool, draw a slot measuring 2.1 mm by 24 mm (for the SD Card). This slot should be placed 52 mm below the top edge, and 10 mm from the left edge of the casing. Then click on Return to 3D.
Step 8: Use the Pull tool to extrude the slot by a depth of 32 mm. Be sure to click on the correct face, for the extrusion.

## Slide 8: Camera Exterior Tutorial (Casing)
Step 9: Finally, using the Circle tool, draw a circle with a diameter of 70 mm on the front face of the camera casing. Then click on Return to 3D to create a surface. This surface will be used to attach a lens. Save the file as camera casing.

## Slide 9: Camera Exterior Tutorial (Lens)
Step 1: Open a new file. Using the Circle tool, draw a circle with a diameter of 70 mm. Then click on Return to 3D to create a surface. Using the Pull tool, extrude the circle surface by 72 mm to create a lens.
Step 2: On the top face of the lens, draw a circle with a diameter of 64 mm. Then click Return to 3D. Using the Pull tool, extrude the circle to a depth of 3 mm. Ensure the inner circle is at the center of the outer circle.

## Slide 10: Camera Exterior Tutorial (Lens)
Step 3: On the bottom face of the lens, using the three point rectangle tool, draw a box from the center measuring 49.5 mm by 49.5 mm. Using the Pull tool, select the square and extrude it by 1 mm. This completes the camera lens model.

## Slide 11: Camera Exterior Tutorial (Assembly - Beginning)
Step 1: Open your camera casing file. From the file menu, select ‘Insert Geometry’ and open your camera lens model; it will appear in the casing file.
Step 2: Select the Align tool found in the Assemble section of the Design Ribbon. Then click on the square surface of the camera lens, and then select the circle surface on the camera casing. Next, select the circular edge at the bottom of the lens, and then select the circular edge on the front of the camera casing. The lens should move to the center of the casing. Work on this assembly will resume in the next lesson.

## Slide 12: Additional Discovery Tutorials (Optional/As-Needed)
Learning Solid Modeling with Ansys Discovery — Course Overview
  Helpful intro to geometry in Discovery, very good for before you try things on your own
Ansys Discovery Forum Getting Started Tutorials
  Great extra tutorials focused on different concepts/features
Lecture Unit: Creating and Editing Geometries in Ansys Discovery
      The unit covers the creation and editing of 3 models from their initial 2D sketches to their final 3D shapes with no prior modeling experience necessary
SpaceClaim/Discovery Keyboard Shortcuts

## Slide 13
Acknowledgements
Ansys: Ethan Rabinowitz, Madhumita Saravana Kumar, Josh Suneby
University of Michigan: Lizzie Kagan, Sarah Wholihan, Naomi Kantor, Leo Lavigne, Nadya Barghouty