## Slide 1
Lesson 4: Introduction to Direct Modeling in Ansys Discovery, Part 4
Developed and curated by the Ansys Education Team
education@ansys.com
Adaptation and compilation led by Alfred Oti
Based on curriculum by Kenneth Alfano, Teaching Professor in Engineering Undergraduate Education at the University of Michigan
Notes: Note: This lesson directly builds upon the previous one, which thus must be completed before.

## Slide 2: Learning objectives for this unit
Intended Learning Outcomes | 
Knowledge and Understanding | Understanding of the fundamental tools used to create and edit geometry in Ansys Discovery: model stage
Skills and Abilities | Ability to create and edit simple geometric 3D models
Values and Attitudes | Insight into how the fundamental style of modeling used in Ansys Discovery
Resources
Software: Ansys Discovery 2022 R2
University of Michigan personnel.
Built-in Assessment
  Step-by-Step guide
Further reading/information
  Ansys Academic
  Ansys Innovation Courses
  Ansys Education Resources

## Slide 3: Continuing the Camera Exterior Tutorial (Accompanying SD Card)
Step 1: Using the Rectangle tool, draw a box measuring 24 mm by 32 mm. Then click on Return to 3D to create a surface. Using the Pull tool, extrude the surface by 2.1 mm to create a 3D box.
Step 2: Using the Rectangle tool, draw the following boxes: a) at the bottom edge, 6 mm by 1 mm; b) on the right edge, 1 mm by 2 mm, at 10 mm down from the top edge; c) on the left edge, 1 mm by 7 mm, at 8 mm down from the top edge. Then, click on Return to 3D to create a surface. Using the Pull tool, extrude the boxes to create holes through the original 3D box.

## Slide 4: Camera Exterior Tutorial (Accompanying SD Card)
Step 3: Select the top-right edge. Using the Pull tool, select Chamfer from the right Heads-Up Display (HUD) menu. Then extrude the edge by 4.35 mm.
Step 4: Using the Rectangle tool, draw the following boxes: a) on the left edge, 2 mm by 0.5 mm; b) on the right edge, 1 mm by 0.5 mm. Then, click on Return to 3D. Using the Pull tool, extrude the boxes to create holes through the original 3D box.

## Slide 5: Camera Exterior Tutorial (Accompanying SD Card)
Step 5: Select the large face of the left indent. Using the Rectangle tool, draw a box measuring 8 mm by 0.6 mm. Then click on Return to 3D to create a surface. Using the Pull tool, extrude the surface by 0.5 mm to create a ridge.
Step 6: Select the top face of the left indent, and click on the Sketch icon.

## Slide 6: Camera Exterior Tutorial (Accompanying SD Card)
Step 7: Sketch the C-shape shown above. Make sure the C shape has no gaps; use CTRL-Z as needed. Then click on Return to 3D to create a surface. Using the Pull tool, select the Square and extrude the C shape by 20 mm. This completes the SD card component model.

## Slide 7: Camera Exterior Tutorial (Assembly – Continuing from prior lesson)
Step 3: From the File menu, select ‘Insert Geometry’ and open your camera’s SD Card model. It will appear in the camera casing file. Using the Move tool, rotate the SD card so that it faces the camera casing (as shown). Note: the mating may be more intuitive for those familiar with SD cards; if needed, please do a brief search about it.
Step 4: Select the Align tool found in the Assemble section of the Design Ribbon. Then click on the top-left corner edge of the SD card, and select the top edge on the camera casing slot. This will align the height of the SD card with the height of the slot.

## Slide 8: Camera Exterior Tutorial (Assembly)
Step 5: Finally, use the Move tool to place the SD card partially into the camera casing’s slot. This completes your assembly.

## Slide 9: Some tips/notes about the mating
Start with orienting your piece! Proper orientation will ensure the easiest step by step mating
Ctrl+Z is your friend! You can always reverse/undo a mate
Try out or “play” with some different mating styles, to see what works best
Go back and double check using the “Move” tool, to ensure the attachment doesn’t budge

## Slide 10: Additional Discovery Tutorials (Optional/As-Needed)
Learning Solid Modeling with Ansys Discovery — Course Overview
  Helpful intro to geometry in Discovery, very good for before you try things on your own
Ansys Discovery Forum Getting Started Tutorials
  Great extra tutorials focused on different concepts/features
Lecture Unit: Creating and Editing Geometries in Ansys Discovery
      The unit covers the creation and editing of 3 models from their initial 2D sketches to their final 3D shapes with no prior modeling experience necessary
SpaceClaim/Discovery Keyboard Shortcuts

## Slide 11
Acknowledgements
Ansys: Ethan Rabinowitz, Madhumita Saravana Kumar, Josh Suneby
University of Michigan: Lizzie Kagan, Sarah Wholihan, Naomi Kantor, Leo Lavigne, Nadya Barghouty