## Slide 1
Lesson 2: Introduction to Direct Modeling in Ansys Discovery, Part 2
Developed and curated by the Ansys Education Team
education@ansys.com
Adaptation and compilation led by Alfred Oti
Based on curriculum by Kenneth Alfano, Teaching Professor in Engineering Undergraduate Education at the University of Michigan

## Slide 2: Learning objectives for this unit
Intended Learning Outcomes | 
Knowledge and Understanding | Understanding of the fundamental tools used to create and edit geometry in Ansys Discovery: model stage
Skills and Abilities | Ability to create and edit simple geometric 3D models
Values and Attitudes | Insight into how the fundamental style of modeling used in Ansys Discovery
Resources
Software: Ansys Discovery 2022 R2
University of Michigan personnel.
Built-in Assessment
  Step-by-Step guide
  Video context notes
Further reading/information
  Ansys Academic
  Ansys Innovation Courses
  Ansys Education Resources

## Slide 3: Continuation of CAD modeling with Discovery
Open Discovery, and start a new file.
Today we are going to deepen our understanding of modeling features: Mirror, Fill, Combine, Pull Edges, Smoothen, etc.
To do this, we are going to create a (vintage!) boombox stereo exterior, with some simplifications

## Slide 4: Boombox Stereo Tutorial
Step 1: Open a new file. Click on the Plan View icon to enter the sketch grid.
Step 2: Using the rectangle tool, draw a box measuring 820 mm by 300 mm. Then click on Return to 3D to create a surface. (Remember to click on “Draw from center” in the right-side HUD menu.)

## Slide 5: Boombox Stereo Tutorial
Step 3: Using the Construction line tool, draw a line vertically through the middle of the box. Then right-click on the line and select Set as Mirror Line from the menu.
Step 4: Using the line tool, draw a line measuring 260 mm from the origin point (where both axes cross). Note that line direction can go either left or right.

## Slide 6: Boombox Stereo Tutorial
Step 5: Using the Circle tool, draw a circle with a diameter of 175 mm. (A second circle should appear on the other side of the mirror line.) Then click on Return to 3D to create surfaces.
Step 6: Using the Rectangle tool, draw a box measuring 101.6 mm by 63.5 mm, approximately 63.5 mm from the bottom at the center of the large box. Then draw a second rectangle, measuring 150 mm by 25 mm, in the center of the large box.

## Slide 7: Boombox Stereo Tutorial
Step 7: Using the Line tool, draw a line measuring 820 mm across the face of the large box. Using the Dimension tool, click on the top edge of the large box and the newly drawn line. This will give you a figure. Click on the figure, and type 50 mm. The newly drawn line will move 50mm from the top edge of the large box.
Step 8: Using the Circle tool, draw three circles with a diameter of 25 mm. The circles should be 25mm apart. (You can use mirror line and construction lines to aid the placement of the circles.) Then click on Return to 3D to create surfaces.

## Slide 8: Boombox Stereo Tutorial
Step 9: Delete the construction lines. (To delete, click on a construction line and press the “Delete” button on your keyboard. Alternatively, right-click on a construction line and use the Discovery Tools to delete.) Afterwards, the front of the Boombox should look like this (as shown).
Step 10: Expand the Model Tree in the top-left corner of the screen. Select both large circles. To select both faces, navigate to the structure tree and select both of the circle elements. Using the Pull tool, extrude the large circles surfaces by 20 mm to form cylinders.

## Slide 9: Boombox Stereo Tutorial
Step 11: Using the Pull tool, CTRL-click on the top edges of the cylinders and select Round from the right Heads-Up Display (HUD) menu. Then extrude the edge towards the Boombox by 15 mm. For the extrusion, pull towards the center of the speakers.
Step 12: Expand the Model Tree in the top-left corner of the screen. Select the small boxes and circles by using the Shift key and clicking your mouse to select the faces. Using the Pull tool, extrude the remaining box and circle surfaces. Extrude all by 10 mm.

## Slide 10: Boombox Stereo Tutorial
Step 13: Select the large box, and use the Pull tool to extrude it by 200 mm.
Step 14: Select the top edge at the front of the Boombox. Using the Pull tool, select Chamfer from the right HUD menu. Then extrude the edge towards the Boombox by 50 mm. (Remember to delete the original line we placed earlier at 50mm.)

## Slide 11: Boombox Stereo Tutorial
Step 15: On the top surface of the Boombox, use the Rectangle tool and select Draw from center from the right HUD to draw a box measuring 540 mm by 40 mm.
Step 16: Using the Pull tool, extrude the box upward by 80 mm.

## Slide 12: Boombox Stereo Tutorial
Step 17: Select the front face of the new box, and use the Rectangle tool to draw a box measuring 480 mm by 40 mm.
Step 18: Finally, select all the edges of the Boombox. Using the Pull tool, select Round from the right HUD and extrude the edges to a depth of your choice. This will create a more pleasing aesthetic.

## Slide 13: Additional Discovery Tutorials (Optional/As-Needed)
Learning Solid Modeling with Ansys Discovery — Course Overview
  Helpful intro to geometry in Discovery, very good for before you try things on your own
Ansys Discovery Forum Getting Started Tutorials
  Great extra tutorials focused on different concepts/features
Lecture Unit: Creating and Editing Geometries in Ansys Discovery
      The unit covers the creation and editing of 3 models from their initial 2D sketches to their final 3D shapes with no prior modeling experience necessary
SpaceClaim/Discovery Keyboard Shortcuts

## Slide 14
Acknowledgements
Ansys: Ethan Rabinowitz, Madhumita Saravana Kumar, Josh Suneby
University of Michigan: Lizzie Kagan, Sarah Wholihan, Naomi Kantor, Leo Lavigne, Nadya Barghouty