## Slide 1
Lesson 6: Introduction to Structural Simulation in Ansys Discovery, Part 2
Developed and curated by the Ansys Education Team
education@ansys.com
Adaptation and compilation led by Alfred Oti
Based on curriculum by Kenneth Alfano, Teaching Professor in Engineering Undergraduate Education at the University of Michigan

## Slide 2: Learning objectives for this unit
Intended Learning Outcomes | 
Knowledge and Understanding | Understanding of the mechanics of a simple cantilever beam simulation in Ansys Discovery
Skills and Abilities | Ability to perform a simple cantilever beam simulation in Ansys Discovery
Values and Attitudes | Insight into the methods used for a simple cantilever beam simulation in Ansys Discovery
Resources
Software: Ansys Discovery 2022 R2
University of Michigan personnel.
Built-in Assessment
  Step-by-Step guide
Further reading/information
  Ansys Academic
  Ansys Innovation Courses
  Ansys Education Resources

## Slide 3: Static Structural Simulation
Things are made of things – and thus, they react to certain things :)
Material is important for analysing how objects in the world around us are built
Examples of where material choice can be critical:
  Bridges
  Device Casings
  Roads
  Medical Implants
  Buildings
  What else can you think of?
Notes: (Bracket examples, by Ansys)

## Slide 4: Scenario for a cantilever beam: “Captain Hook” needs a plank
Some things to consider:
How does it respond to weight?
How durable is it?
How costly is it?
What should we make it from?
Pyle, H. Walking the Plank by Howard Pyle. World History Encyclopaedia. Retrieved from https://www.worldhistory.org/image/14536/walking-the-plank-by-howard-pyle on July 20, 2023.

## Slide 5: Considerations when Selecting Materials
Performance Needs
Weight
Budget/Cost
Rigidity (Stiffness)
Durability
And many more!

## Slide 6: Cantilever Beam Simulation
Step 1: Using the dimensions specified on the accompanying slide, construct the plank. Click on of the end faces of the plank, then click on the Simulation ribbon at the top of the screen. Click on ‘Structure’ from the drop-down list, choose ‘Support > Fixed’ and click on the green checkmark to confirm the face as a fixed support.
Step 2: Select the face of the plank opposite the fixed support, then click on the Simulation ribbon at the top of the screen. Click on ‘Structure’ from the drop-down list, and choose ‘Force > Distributed’. We are using a distributed force – as these are spread out over a length, area, or volume. This includes the weight of the materials and the force of anything pushing on it. From the right HUD menu, choose Use Force Components. Enter -780N for the Y value, then click anywhere on screen to commit the value.

## Slide 7: Plank Specifications
Design Constraint: Support the load of one person (max) at any point in time = 80kg ≅ 0.78kN
For the purpose of this assignment, we are going to model this as a point load at the end of the plank.
The plank is essentially a cantilever beam meaning that it has a fixed support at one end (the ship). Fixed means that the support has no translational or rotational movement.
The load is then placed on the face opposite the fixed support of the plank.

## Slide 8: Cantilever Beam Simulation
Step 3: In the model tree at the top-right of the screen, right-click on the green solid label. On the left side of the screen, a materials drop-down menu will appear. Type or select your desired material name. The model will take on the properties of your material choice. Try using various materials!
Step 4: Click on the green solve button at the bottom-right of the screen to run the simulation. Change the units in the legend to mm. To view the extent of the displacement, click on the Scaled Deformation button to the left of the green ‘solve’ button. To view an animation of the displacement, click on the ‘show animation’ button top-left of the green ‘solve’ button. The Displacement Value can also be changed to view different material behaviours such as stress and strain. Repeat steps 3 and 4 with different materials and compare the results (e.g. displacements).

## Slide 9: Additional Discovery Tutorials (Optional/As-Needed)
Learning Solid Modeling with Ansys Discovery — Course Overview
  Helpful intro to geometry in Discovery
Ansys Discovery Forum Getting Started Tutorials
  Great extra tutorials focused on different concepts/features
Lecture Unit: Structural Analysis of Beams with Ansys Discovery
      This lecture covers basic concepts of structural analysis and its workflow through the study of simple beams. It also showcases how to set up a structural simulation in Ansys Discovery and provides a comparison of analytical and numerical solution for a cantilever beam.
SpaceClaim/Discovery Keyboard Shortcuts

## Slide 10
Acknowledgements
Ansys: Ethan Rabinowitz, Madhumita Saravana Kumar, Josh Suneby
University of Michigan: Lizzie Kagan, Sarah Wholihan, Naomi Kantor, Leo Lavigne, Nadya Barghouty