## Slide 1
Lesson 5: Introduction to Structural and Thermal Simulation in Ansys Discovery, Part 1
Developed and curated by the Ansys Education Team
education@ansys.com
Adaptation and compilation led by Alfred Oti
Based on curriculum by Kenneth Alfano, Teaching Professor in Engineering Undergraduate Education at the University of Michigan

## Slide 2: Learning objectives for this unit
Intended Learning Outcomes | 
Knowledge and Understanding | Understanding of the processes used to conduct simple thermal and (static) structural simulations in Ansys Discovery
Skills and Abilities | Ability to perform simple thermal and (static) structural simulations in Ansys Discovery
Values and Attitudes | Insight into the methods used for simple thermal and (static) structural simulations in Ansys Discovery
Resources
Software: Ansys Discovery 2022 R2
University of Michigan personnel.
Built-in Assessment
  Step-by-Step guide
Further reading/information
  Ansys Academic
  Ansys Innovation Courses
  Ansys Education Resources

## Slide 3: From CAD (modeling) to CAE (simulation)
CAE (computer-aided engineering) builds upon CAD (computer-aided design), by simulating physical conditions such as heat, mechanical forces, etc. being applied to a 3D model
Physical simulation enables “virtual prototyping” to explore/predict effects of potential design choices such as different dimensions, materials, or configurations
Simulation can save time and money before investing in actual physical prototyping or fabrication, particularly for costly or complex items
Conventional CAE tools are more complex and can require much training and specialized expertise to use effectively; Discovery simplifies simulation, making it a more directly usable tool for a wider range of design engineers (and students)

## Slide 4: First, Thermal Simulation
Step 1: Open your “mug” model from the first/earlier tutorial. In the physics tree, double-click on the structural steel label. The material Heads-Up Display (HUD) will appear. In the right HUD, change the material type to “porcelain, clay-based” (type or choose from the drop-down list).
Step 2: Select the inner cylindrical face of the mug. Click on the handle of the mug. Then in the Simulation ribbon, select Solid Thermal from the physics tools. From the drop-down menu, click on Temperature. In the right HUD, enter 83 degrees into the temperature box. This is where our hot liquid would be making contact with the mug surface. Select the bottom inner face of the mug, and type 83 degrees into the temperature box again.

## Slide 5: Thermal Simulation
Step 3: Click on the green ‘solve’ button at the bottom-right of corner of the screen. The simulation will run and display the heat distribution for the material.
Alternative Thermal Method

## Slide 6: Next, Structural Simulation:
Step 1: With your mug model still open, click on the handle of the mug. Then in the Simulation ribbon, select Structural from the physics tools. From the drop-down menu, click on Support. Choose ‘Fixed’ from the menu. Click on the green tick to confirm your choice. (This simulates holding the Mug by its handle.)
Step 2: Click on the bottom of the mug. Then in the Simulation ribbon, select Structural from the physics tools. From the drop-down menu, click on Pressure. In the right HUD box, enter 0.5. Change the unit to lb/in2. Click on the green ‘solve’ button to run the simulation. In the legend on the right of the screen, change the result from temperature to stress.
Alternative Thermal Method

## Slide 7: Some points to note:
The mug handle provides support when a user is holding the mug; thus, we apply a simulation force in such a manner
  Note there may be various stresses at the top and/or bottom of handle attachment points
Try to model realistic forces
  For example, 0.5 lb/in^2 was noted as a small force in a range of what might realistically be present
A fixed support is best for a rigid simulation where support does not change with movement
  A mug handle remains rigidly attached to the mug, at a particular location and in a particular configuration
  Something more flexible, like a backpack strap, by contrast, may shift based on where/how it is being held, and thus is not necessarily as representable with fixed support (though the seams where it attaches to the backpack itself would of course remain fixed)

## Slide 8: Thermal Simulation (Alternative Method)
Step 1: Open your “mug” model from the earlier tutorial. In the physics tree, double-click on the ‘structural steel’ label. The material HUD will appear. In the right HUD, change the material type to “porcelain, clay-based” (type or choose from the drop-down list).
Step 2: Select the inner faces of the Mug.

## Slide 9: Thermal Simulation (Alternative Method)
Step 3: Click on the handle of the mug. Then in the Simulation ribbon, select Solid Thermal from the physics tools. From the left HUD, click on Heat. In the right HUD, click Total Heat, then enter 1W in the box.
Step 4: Discovery will automatically apply convection to all the outer faces of the mug. By default, convection is set to 10 W/m²·°C. Change this to 5.

## Slide 10: Thermal Simulation (Alternative Method)
Step 6: Click on the green ‘solve’ button to run the simulation. The plot and legend show that the cup is has an average temperature of 84.7C. This is in the normal range for a hot beverage.
Step 5: In the Simulation ribbon, select Monitors from the results tools. From the drop-down menu, choose Custom, then select Temperature from the left HUD variable list. In the right HUD, click on Average. A chart will appear with the title Average Temperature 1. Right-click and re-name the title as Average Temperature Mug Depression.

## Slide 11: Structural Simulation (Alternative Method)
Step 1: Click on the outer bottom face of the mug. Then in the Simulation ribbon, select Structural from the physics tools. From the drop-down menu, click on Support. Choose ‘Fixed’ from the menu. Click on the green tick to confirm your choice. (This simulates the mug resting on a flat surface.)
Step 2: Click on the inner bottom face of the mug. Then in the Simulation ribbon, select Structural from the physics tools. From the drop-down menu, click on Pressure. In the right HUD box, enter 0.5. Change the unit to lb/in2. Click on the green ‘solve’ button to run the simulation. In the legend on the right of the screen, change the result from temperature to stress (as we had started with a temperature simulation).
Return to Step 1

## Slide 12: Additional Discovery Tutorials (Optional/As-Needed)
Learning Solid Modeling with Ansys Discovery — Course Overview
  Helpful intro to geometry in Discovery
Ansys Discovery Forum Getting Started Tutorials
  Great extra tutorials focused on different concepts/features
Lecture Unit: Creating and Editing Geometries in Ansys Discovery
      The unit covers the creation and editing of 3 models from their initial 2D sketches to their final 3D shapes with no prior modeling experience necessary
SpaceClaim/Discovery Keyboard Shortcuts

## Slide 13
Acknowledgements
Ansys: Ethan Rabinowitz, Madhumita Saravana Kumar, Josh Suneby
University of Michigan: Lizzie Kagan, Sarah Wholihan, Naomi Kantor, Leo Lavigne, Nadya Barghouty