## Slide 1
Lesson 1: Introduction to Direct Modeling in Ansys Discovery, Part 1
Developed and curated by the Ansys Education Team
education@ansys.com
Adaptation and compilation led by Alfred Oti
Based on curriculum by Kenneth Alfano, Teaching Professor in Engineering Undergraduate Education at the University of Michigan

## Slide 2: Learning objectives for this unit
Intended Learning Outcomes | 
Knowledge and Understanding | Understanding of the fundamental tools used to create and edit geometry in Ansys Discovery: model stage
Skills and Abilities | Ability to create and edit simple geometric 3D models
Values and Attitudes | Insight into how the fundamental style of modeling used in Ansys Discovery
Resources
Software: Ansys Discovery 2022 R2
University of Michigan personnel.
Built-in Assessment
  Step-by-Step guide
Further reading/information
  Ansys Academic
  Ansys Innovation Courses
  Ansys Education Resources

## Slide 3: Modeling
CAD - Computer Aided Design
2 main types
  Parametric
  Direct
Gives us the ability to see our designs in 3D, explore possibilities and make “mistakes” before proceeding to prototyping
CAD models also can be used with simulation (Computer Aided Engineering or CAE) tools
  Allows more/faster design iterations by saving time when “testing” with various “virtual prototypes”
  Also, e.g. it isn’t feasible to prototype a whole airplane/bridge/etc. and rely solely on physical tests

## Slide 4: Parametric Modeling (“History-Based”)
Uses features and constraints
Best for tasks that involve very precise requirements and manufacturing criteria
Useful for minor modifications and continuous iterations
Can create “families” of parts
  Each part is a set of ordered
  features (kind of like steps);
  an assembly is a combination
  of parts
Takes more time for major changes

## Slide 5: Direct Modeling (Non-History-Based)
Creates “geometry” rather than “features”
Like working with modeling clay
  More conceptually intuitive
Define and capture geometry quickly
Not based on the history or development of a model
Directly manipulate faces of the model by pushing and pulling
More difficult to edit dimensions in some cases
More useful as computing power increases
Ansys Discovery uses direct modeling

## Slide 6: Getting Started with CAD modeling: “Mug” Tutorial
(screenshot)

## Slide 7: Mug Tutorial
Step 1: Open a new file. Click on the Plan View icon to enter the sketch grid.
Step 2: Using the Circle tool, draw a circle diameter of 26 mm. Start the circle from the (0,0) coordinate where the axis intersect.

## Slide 8: Mug Tutorial
Step 4: Using the Pull tool, extrude the surface into a cylinder by 30 mm.
Step 3: Click on Return to 3D. The circle should become a surface.
Alternative Method 1
Alternative Method 2

## Slide 9: Mug Tutorial
Step 5: Click on the Sketch tool, then select the top of the cylinder. Using the Circle tool, draw a circle with diameter of 24 mm.
Step 6: Using the Pull tool, extrude the inner circle down by 28 mm (extrude inwards).

## Slide 10: Mug Tutorial
Step 8: Using the View Arc and the Plane tool, place a second plane perpendicular to the first, 13 mm from the central axis.
Step 7: Click on the central axis, then select the Plane tool in the create section of the design ribbon. A plane will appear in the middle of the cylinder.

## Slide 11: Mug Tutorial
Step 10: Select the second plane and move it forward 13 mm. Keep it perpendicular to the first plane.
Step 9: Select the original plane. Then click on the Sketch icon. Click on the construction line tool, and draw a horizontal line at the midpoint of the cylinder. Right-click on the construction line, and choose ‘Set as Mirror line’. Then click on the construction line tool and 10mm line from the midpoint. After this, use the three-point arc tool to draw a semi-circle with a diameter of 20mm at an angle of 180 degrees.

## Slide 12: Mug Tutorial
Step 12: Using the Pull tool, select the Sweep icon from the Heads-Up Display (HUD). Then select the oval surface and the semi-circle arc. Then select the Full Pull icon to sweep the oval along the arc, to form a handle.
Step 11: Select the plane again, and click on the Sketch icon. Using the Oval tool, sketch an oval measuring 4 mm by 2 mm.

## Slide 13: Mug Tutorial
Step 14: Select the handle, then click on the DISPLAY tab. Click on the Color tool, then choose a color. The handle will change to the selected color. Delete the planes and curves.
Step 13: Using the Move tool, select the handle and move it into the cylinder by a distance of 0.1 mm. This will close the gap between the handle and the cylinder.

## Slide 14: Mug Tutorial (Alternative Method 1)
Step 2: Click on Return to 3D, and the L shape should become a surface. Select the Pull tool, then the Revolve icon. Click on the L surface, then the central y-axis, then select the Full Pull icon to revolve the L surface around the y-axis to form a cylinder. Return to step 7 of the mug tutorial.
Step 1: Using the rectangle tool, draw a box measuring 13 mm by 30 mm. Then draw a second box measuring 11 mm by 28 mm, starting at the top left corner.
Return to step 8

## Slide 15: Mug Tutorial (Alternative Method 2)
Step 1: Using the Shell tool found in the create section of the design ribbon, click on the top surface of the cylinder, then enter 2mm in the label box. The cylinder will be become a shell with a uniform thickness. Return to step 7 of the mug tutorial.
Return to step 8

## Slide 16: Some common helpful notes for this tutorial:
Ctrl+Z is your friend!
  Use it to quickly undo/reverse an action when needed
Save your work early and often
Check your work: Rotate your drawing at various points, to ensure that everything is lined up and extrusions are the right depth
  E.g., you don’t want to make a hole in your mug!
  Hint: The mug handle needs to be fully flush with the mug’s external side
    Remember that the handle shouldn’t be made to go too far into the mug, either

## Slide 17: Additional Discovery Tutorials (Optional/As-Needed)
Learning Solid Modeling with Ansys Discovery — Course Overview
  Helpful intro to geometry in Discovery, very good for before you try things on your own
Ansys Discovery Forum Getting Started Tutorials
  Great extra tutorials focused on different concepts/features
Lecture Unit: Creating and Editing Geometries in Ansys Discovery
      The unit covers the creation and editing of 3 models from their initial 2D sketches to their final 3D shapes with no prior modeling experience necessary
SpaceClaim/Discovery Keyboard Shortcuts

## Slide 18
Acknowledgements
Ansys: Ethan Rabinowitz, Madhumita Saravana Kumar, Josh Suneby
University of Michigan: Lizzie Kagan, Sarah Wholihan, Naomi Kantor, Leo Lavigne, Nadya Barghouty