## Slide 1
Dipole Theory and Simulation
Developed and curated by the Ansys Education Team
Based on the Ansys Innovation Course: Design of the Half-Wave Dipole
Original Developer: Kathryn Smith
Updated and curated by Dimitrios Tzagkas and Celia Gomez Molina
education@ansys.com

## Slide 2: Learning Objectives for this Lecture Presentation
Intended Learning Outcomes | 
Knowledge and Understanding | Understanding fundamental concepts on Dipole Antenna
Skills and Abilities | Ability to create and simulate a basic dipole antenna on Ansys Electronics Desktop - HFSS
Values and Attitudes | Awareness of wavelength and frequency for signal transmission
Resources
  “Elements of Electromagnetics,” by Matthew N.O Sadiku, 5th ed. (2010)
  “Engineering Electromagnetics,” by Nathan Ida, 3rd ed. (2015)
  “Microwave Engineering,” by David Pozar, 4th ed. (2012)
  “Antenna Theory”, by Constantine A. Balanis, 4th ed. (2016)
  Software: Ansys Electronics Desktop v23R2 (please note that all project files are available in the downloaded folder)
Built-in Assessment
  Simulation instructions
  Exercise
Further reading/information
  Ansys Academic
  Ansys Innovation Courses
  Ansys Education Resources

## Slide 3: The Half-Wave Dipole Antenna
Half-wave dipole antennas are among the most common antenna topologies. They
  are simple to design and fabricate
  offer symmetrical radiation pattern
  with linear polarization
However, they have some limitations as
  Narrowband response
  Native directivity is limited
Cannot be unnoticed especially on a Yagi-Uda antenna

## Slide 4: Half-Wave Dipole Antenna Design
Consists of 2 sectors of same length
Separated by small distance (feeding gap)
Overall length L is λ/2
Radius can affect the bandwidth (with trade-offs)
L
Feed

## Slide 5: The Current Structure
The current structure on a half-wave dipole (when driven by a sinusoidal source) is approximately sinusoidal. When driven at exactly the half-wave frequency, the current magnitude forms a standing half-sinusoid along the length of the dipole, with nulls at either end of the dipole and a maximum at the center.
Current nulls observed at ends, where maximum current is observed at center
1. Increasing the radius of the wire used for the dipole, makes is harder to effect a smooth transition of current from the feed line to the antenna body
2. Increasing the radius of the wire used for the dipole, makes the antenna being more affected by fringing fields

## Slide 6: Fringing Fields
Fringing fields occur due to the abrupt truncation of the current path at the ends of the dipole. The high density fringing fields make the effective length of the dipole antenna slightly longer than its physical length . The effect of the apparent lengthening of the dipole is to increase its inductance, and thereby reduce its resonant frequency.
Physical length
Potential effective length
This effect is typically very small, and can be compensated for by slightly reducing the physical length of the dipole

## Slide 7: Example of dipole dimensions and frequency response
Let us consider a dipole antenna that we would like to operate at 2.4 GHz. The dipole dimensions would be:
Dipole dimension
Shortening the dipole to:
Notes: As the desired frequency is the 2.4 GHz, we can calculate the wavelength for that operating frequency, and dividing it by 2 we can get the dipole dimensions. If we create the dipole with the estimated length of λ/2, then due to fringing effects, the operating frequency will appear to be smaller, and in this case close to ~2.2 GHz instead of 2.4 GHz. If we shorten by a bit the dipole and simulate again, we can get the appropriate length needed for the specific frequency.

## Slide 8: The Theoretical Far-Field Radiation Pattern
Directivity of the dipole antenna for φ=0 deg
3D Directivity plot
Vertical cut of the 3D Directivity plot
φ
θ

## Slide 9: The Theoretical Far-Field Radiation Pattern
Top view plot
Directivity of the dipole antenna for θ=90deg

## Slide 10
Simulation of a 2.4 GHz Dipole Antenna in Ansys HFSS

## Slide 11: Create a new HFSS project and change the solution type

## Slide 12: Create the dipole antenna
Draw a cylinder with the following properties

## Slide 13: Create the gap
Copy the cylinder and assign the following properties
Subtract the gap to the dipole
Preserve the gap object
For simplicity we use the size of the gap to be equal to the radius of the dipole

## Slide 14: Assign materials
Select the dipole and assign PEC as material

## Slide 15: Excitation: Lumped port
Create a rectangle in YZ plane
Separate both cylinders as different objects as shown below

## Slide 16: Excitation: Lumped port
Then, assign Terminal Lumped Port excitation to the rectangle sheet
Select any of the conductors as reference

## Slide 17: Create the solution setup
Add a solution set up with frequency equal to 2.4GHz
Add a solution sweep from 1.2 GHz to 3.6GHz
Then, validate and analyze the model

## Slide 18: Plot S and Z parameters
Create two rectangular plots, one for Z parameter and the other one for S parameter

## Slide 19: Z parameter
At this frequency, the real part is 66.65Ω
The imaginary part of the input impedance is 0Ω at the center frequency of the antenna (2.4GHz)
Needed for next step

## Slide 20: S parameter
Renormalizing the port impedance, the S parameter remains as shown
Minimum of S11 parameter at the design frequency (2.4GHz)
Calculated on previous step

## Slide 21: 3D Directivity
Create a 3D Polar Plot
Plot the total directivity in linear units
Minimum directivity in Z direction and maximum for θ=90deg

## Slide 22: Exercise: Plot Directivity in dB
The 3D Directivity plot that was generated previously was in linear plot.
Task: How could we plot the 3D Directivity in dB this time???

## Slide 23: Exercise: Plot Directivity in dB (solution)
Create a 3D Polar Plot
Plot the total directivity in dB
Solution:

## Slide 24: Radiation pattern in the antenna
Plot the Radiation Field in the antenna model to visualize them together with the dipole

## Slide 25: 2D directivity
Create a Radiation Pattern plot
Plot the total directivity in the Elevation plane
Minimum directivity in θ=0deg direction and maximum for θ=90deg

## Slide 26: 2D directivity
Create a Radiation Pattern plot and plot the total directivity in φ
For θ=0deg and θ=180deg
Omnidirectional

## Slide 27: Exercise: Plot the 2D directivity in the antenna

## Slide 28: Exercise: Plot the 2D directivity in the antenna (solution)
Plot the Radiation Field in the antenna model to visualize them together with the dipole
Solution:

## Slide 29: Conclusions
The tutorial provided in this Academic Resource includes the instructions to follow and fully populated model for reference.
The solutions can be seen only after the analysis is executed for each model, and this can be done by the “Analyze” function.
The model including all the designs is named: “Dipole_antenna_model_all.aedt”
or here 

## Slide 30: Ansys Education Resources Feedback Survey
Here at Ansys, we rely on your feedback to ensure the educational content we create is up-to-date and fits your teaching needs.
Please click the link below to fill out a short survey (~7 minutes) to help us continue to support academics around the world utilizing Ansys tools in the classroom.
Feedback Survey Link
Notes: Feedback Survey link for copy-paste method  https://ansys.typeform.com/to/jcattJI5