## Slide 1
Selecting Materials for Musical Instruments:
a Case Example with a Xylophone
Kaitlin Tyler, Ph.D. and Elisabeth Hülse, M.S.
Ansys Academic Development Team
education@ansys.com

## Slide 2: What is music?
Any rhythmic, melodic, or harmonic grouping of sounds that is specifically composed and that forms a unity so as to convey a message, to communicate, or to entertain1
Music has been a part of human history for tens of thousands of years 2,3
Notes: Optional activity: crowd source a definition from the class before revealing the “technical” definition

## Slide 3: What is sound?
Mechanical energy that is transmitted by longitudinal pressure waves in a material medium (such as air) and is the objective cause of hearing2

## Slide 4: What is a musical instrument?
Violoncello for the “Medici” Quintet, 1690
Photo taken by Author in the Academia Galley in Florence, Italy 2023
Any device used to create music.
The major classifications are woodwinds, brass, percussion, and stringed instruments.
Keyboard instruments are sometime a separate category, although they produce sounds either by vibrating strings (as in the case of the piano, harpsichord, virginal, etc.) or by the flow of air (as in the organ).
Electronic instruments, developed in the 20th century, form a new classification of instruments1.

## Slide 5: Make your own musical instrument!
Take the next five minutes and use whatever is around you to make an instrument!

## Slide 6: Make your own musical instrument!
Take the next five minutes and use whatever is around you to make an instrument!
TIMES
UP!
1 minute remaining
2 minutes remaining
3 minutes remaining
4 minutes remaining
5 minutes remaining

## Slide 7: Hornbostel-Sachs Instrument Classification System1
Membranophones
Idiophones
Aerophones
Electrophones
Chordophones
Produce sound by vibrating themselves
Produce sound by a vibrating membrane
Produce sound by vibrating strings
Produce sound by vibrating
a column of air
Produce sound
electronically

## Slide 8
Membranophones
Idiophones
Aerophones
Electrophones
Chordophones
Take the next five minutes to group your instruments into the five categories above!
Group your homemade instruments

## Slide 9
Membranophones
Idiophones
Aerophones
Electrophones
Chordophones
Take the next five minutes to group your instruments into the five categories above!
TIMES
UP!
1 minute remaining
2 minutes remaining
3 minutes remaining
4 minutes remaining
5 minutes remaining
Group your homemade instruments

## Slide 10: What materials did you make your instrument out of?
What other materials do you know instruments are made of?
What materials were instruments made of in the past?
Notes: NOTE: if you are not doing the “make your own instrument” activity, simply delete the first question from this slide

## Slide 11: Instruments of the past
Flutes made of swan bones and mammoth ivory found in the Geiβenklösterle Café in southwestern Germany -- Dated to be around 35,000 years old!5
Made from available materials
 what would those have been?

## Slide 12: Instruments of Today
What materials do we see here?
Do you play an instrument?
What material(s) is it made of?

## Slide 13: Why do we make instruments out of certain materials?
Properties
Structure
Processing
Performance
Materials Tetrahedron
Notes: (Animation 1 )A material’s performance is how a material behaves once in service in a product
(animation 2) This is determined by a material’s properties – traits that describe how a material reacts or behaves under specific conditions or stimuli
Well, material properties can be controlled,
(animation 3) by altering a materials atomic structure
(animation 4) Through various processing techniques
(animation 5) These four areas are connected to one another in what is commonly referred to as the materials tetrahedron. It means that if we change one area, it will have an effect on the other three.

## Slide 14: How do materials need to perform in instruments?
It depends on the instrument class!
Some vibrate the material of the instrument itself (idiophones)
Some vibrate a membrane material component of the instrument (membranophones)
Some vibrate a string material component of the instrument (chordophones)
Some facilitate the vibration of air within the instrument (aerophones)

## Slide 15: Instrument of interest today: xylophone
Idiophone
 The bars vibrate when struck by a mallet

## Slide 16: Material performance for xylophone bars
Bars themselves are vibrating
Need a material with good acoustic performance
  that will have good sound quality, volume, and the “tone” of the sound
What does sound “tone” mean?
In this question, tone does not refer to the note being played!
Notes: By tone, we are referring to the “color” or “temperature” of the sound. Ask students if they have heard of warm sounds vs. cool sounds. If I hit a piece of wood or a piece of metal, they have different tones!

## Slide 17: Material properties for xylophone bars
Acoustic performance is dependent on a material’s mechanical properties
Mechanical properties: the impact of mechanical loading on a material
Like a mallet striking a xylophone bar!

## Slide 18: Material properties for xylophone bars
Three mechanical properties are key [3]:
Density
Young’s Modulus
Mechanical Loss Coefficient

## Slide 19: Density
Variable=ρ
With a brick and sponge of the same volume, a brick will weigh more
Learn more about material properties and how they differ across material families here

## Slide 20: Young’s Modulus
Variable=E
Can also be referred to as a material’s stiffness or a material’s ability to resist deformation when a force is being applied.
Materials with high stiffness resist deformation more easily than materials with low stiffness

## Slide 21
Learn more about material elasticity here

## Slide 22: Mechanical Loss Coefficient
Mechanical loss-coefficient or damping coefficient (Variable=η) measures the degree to which a material dissipates vibrational energy
Sound waves cause vibrations in materials!

## Slide 23: Different materials have different damping coefficients
Materials with high damping reduce sound vibration in material
think of sound damping foam in a vocal studio
Materials with low damping allow sound to vibrate through the material
think of a bell

## Slide 25: Let’s go back to our acoustic material requirements…
Bars themselves are vibrating
Need a material with:
Good sound quality
Good volume
Nice tone
How do these requirements relate to the properties we just discussed?

## Slide 26: Think about the sound waves interacting with the material
What is happening to the sound waves if I can clearly hear the sound produced by hitting the material?
Sound waves are not absorbed by the material

## Slide 27: What property values prevent sound absorption?
Mechanical Loss Coefficient
Density
Young’s Modulus
If the material has a higher mass per unit volume, there are more atoms  do more atoms help or hurt sound vibration?
Materials with a low Young’s modulus deform easily under force
 Does this help sound waves move through a material?
Does a high or low damping coefficient allow for sound wave vibration?
We want sound to be vibrated through my material!
Notes: For density, we want a higher density of atoms because the atomic bonds will help transfer the sound vibrations through the material. If we have more “space” within an atomic lattice, we lose energy/amplitude of the sound waves  it is absorbed
For young’s modulus, we want lower deformation or a higher Young’s modulus. Imagine hitting a piece of wood vs. a piece of foam with a mallet. The stiffer material (the wood) will not lose the energy from the mechanical hit to deformation. Instead, this energy can be vibrated back as sound. For the foam, I will be losing a lot of this energy as deformation (it is absorbed by the material)
And we already covered mechanical loss coefficient in previous slides– we want a low damping material

## Slide 28: What does values of the key properties do we want?
Mechanical Loss Coefficient
Density
Young’s Modulus
A stiff material, with a dense structure and low mechanical loss coefficient, will have the lowest sound wave absorption
 best performance!

## Slide 29: How else do Young’s modulus and density affect acoustic properties of materials?
Speed of sound through a material
Sound radiation coefficient
(how much the vibration of a body is damped to sound radiation)
c
Notes: Both the speed of sound within a material and the sound radiation coefficient are dependent on the Young's modulus and density of the material  emphasize how important these properties are!

## Slide 30: How do we choose materials?
Need to compare materials with one another based on properties of interest
Learn more about selecting materials using Ashby Charts here
Notes: We can use charts, called Ashby plots, to compare material properties with one another
This visual method is much easier to look at than comparing tables and tables of values!
Note: these charts are made with Ansys Granta EduPack– you can learn more about the software here: https://www.ansys.com/products/materials/granta-edupack?utm_campaign=academic&utm_medium=referral&utm_source=education-resource&utm_content=partner_cross-bu_educator-resource-link_product-page_learn-more_na_en_global&campaignID=7013g000000gv7hAAA

## Slide 31
Need materials with high Young’s Modulus and high density

## Slide 32
We want materials with lower mechanical loss coefficient

## Slide 33: Let’s look at some real materials used for xylophones
Xylophones made from Japanese birch*, rosewood, or synthetic materials [6]
*this is not the specific genus for Japanese birch, but it is in the birch family

## Slide 34: Let’s look at some real materials used for xylophones

## Slide 35: Is xylophone made from the “best” materials in each category?
NO!
And that’s okay!
Notes: Time to discuss how there any many decisions that need to be made when designing a product. Including where we are getting our materials from– maybe we want to use locally sourced materials!

## Slide 36
What if we chose a material that lowered the mechanical loss coefficient?

## Slide 37: Glockenspiel (orchestra bells)
Made from steel bars [8]
Materials → Properties ↓ | Birch | High carbon steel
Density (ρ) [kg/m3] | 612 | 7,800
Young’s modulus (E) [GPa] | 12 | 210
Mechanical loss coefficient (η) [no units] | 0.00796 | 0.0005
*data from Ansys Granta EduPack 2024R1
Notes: See how an instrument can be made with higher density and young’s modulus, but lower mechanical loss coefficient material

## Slide 38: Glass xylophone/marimba (crystallophone)
Materials → Properties ↓ | Birch | High carbon steel | Soda-lime glass
Density (ρ) [kg/m3] | 612 | 7,800 | 2,460
Young’s modulus (E) [GPa] | 12 | 210 | 69.9
Mechanical loss coefficient (η) [no units] | 0.00796 | 0.0005 | 0.000812
*data from Ansys Granta EduPack 2024R1
Notes: And glass xylophones have a lower mechanical loss coefficient than both wood and steel, but their density and young’s modulus is not lower than steel (though it is lower than birch)

## Slide 39
Look on YouTube to find examples of the sounds
for each of these instruments
What are the similarities?
Differences?
Do these instruments sound the same?

## Slide 40
Are the materials you chose dense?
Are they stiff?
Do they absorb sound? Or allow it to resonate?
How does this impact how your instrument makes sound?
Come back to your instrument

## Slide 41: Summary
We’ve learned:
Some basic definitions about music and sound
The Hornbostel-Sachs instrument categorization system
How a material’s performance is dependent on properties, structure, and processing
How we might choose the materials for a xylophone

## Slide 42: References
OnMusic Dictionary -. (n.d.). https://dictionary.onmusic.org/
U. G. K. Wegst, “Wood for sound,” Am J Bot, vol. 93, no. 10, pp. 1439–1448, 2006.
U. G. K. Wegst, “Bamboo and wood in musical instruments,” Annu. Rev. Mater. Res., vol. 38, pp. 323–349, 2008.
sound. (2024). In Merriam-Webster Dictionary. https://www.merriam-webster.com/dictionary/sound
N. J. Conard, M. Malina, S. C. Münzel, and F. Seeberger, “Eine Mammutelfenbeinflöte aus dem Aurignacien des Geissenklösterle: neue Belege für eine musikalische Tradition im Frühen Jungpaläolithikumauf der Schwäbischen Alb,” Archäologisches korrespondenzblatt, vol. 34, no. 4, pp. 447–462, 2004.
https://www.uv.es/clil/ePortfolio/html/jorapra/percussion/xylophone.html#:~:text=The%20Xylophone%20is%20a%20Percussion,Japanese%20birch%20or%20synthetic%20materials.
Materials data and charts from Ansys Granta EduPack, Design Database 24R1
https://usa.yamaha.com/products/musical_instruments/percussion/glockenspiel/yg-250d/index.html

## Slide 43: Ansys Education Resources Feedback Survey
Here at Ansys, we rely on your feedback to ensure the educational content we create is up-to-date and fits your teaching needs.
Please click the link below to fill out a short survey (~7 minutes) to help us continue to support academics around the world utilizing Ansys tools in the classroom.
Feedback Survey Link
Notes: Feedback Survey link for copy-paste method  https://ansys.typeform.com/to/jcattJI5