## Slide 1
1D Dipole Antenna Array in Ansys HFSS
Celia Gómez Molina Dimitris Tzagkas
education@ansys.com

## Slide 2: Introduction
In this Lab Tutorial the method of creating and analyzing a 1D dipole array will be explained.
The arrays created will be
  In the form of dipoles on the same plane and they all have parallel orientation (parallel axis dipoles)
  In the form of dipoles that have their orientation on the same axis (same axis dipoles)
  Pre-requisites:
  Having a ready antenna OR ability to create/import/generate an antenna that will be used as an array element

## Slide 3: Create or load a dipole model
For the tutorial, a dipole model is required. An existing model from previous work can be used.
A reference dipole model is provided with this resource if you prefer to use this reference model for the rest of the tutorial.
OR
Open the file “Dipole_model_ref.aedt” directly in Ansys Electronics Desktop by:
File  Open..  and navigate to the downloaded file location, then select the mentioned file.
Double click the model to open with Ansys Electronics Desktop 

## Slide 4: 1D array Parallel axis Dipole Array

## Slide 5: Create an array
Copy and paste the previous HFSS design and change the Solution Type
A RadiatingSurface will be automatically created
It defines the unit cell

## Slide 6: Boundary Conditions
Delete the AutoOpen1 boundary condition, select the RadiatingSurface object and assign Auto Identify lattice pair
Delete

## Slide 7: Radiation Surface attributes – set dimensions
It is the area in which the radiation is calculated
If not set differently, the boundaries act as perfect reflectors
The dimensions will be used for any array setting
For the points A, B, and C, we set the dimensions of the Radiation Surface padding as where is the array element spacing
The type can be percentage of the total structure dimensions on the respective axis, OR absolute offset
In this example it should be half of the element spacing that is desired.

## Slide 8: Boundary Conditions
Select Global:XY plane and see the primary and secondary lattice pairs that have been created

## Slide 9: Radiation Region
Select top and bottom faces of the RadiatingSurface and assign Radiation Boundary condition

## Slide 10: Create the array
Select Create Array
Change the name and make it Visible. Define the Size of the array

## Slide 11: Create the array
Visualize the created array

## Slide 12: Setups
In the solution setup, just change the option of Save radiated fields only and Validate and Analyze the design

## Slide 13: Magnitude and Phase of the elements
Select the Finite Array Beam Angle option, then click on Calculate and Apply to Sources

## Slide 14: Magnitude and Phase of the elements
Check the values by visualizing the sources

## Slide 15: 3D radiating Sphere
Create a Far Field Setup, Infinite Sphere type

## Slide 16: Exercise: Plot Gain in dB

## Slide 17: Exercise: Plot Gain in dB (solution)
Solution:
Create a 3D Polar Plot and plot the total gain (GainTotal) in dB as shown

## Slide 18: Exercise: Compare the Radiation Pattern
Compare the radiation pattern of the single element and the array. Comment the differences

## Slide 19: Exercise: Compare the Radiation Pattern (solution)
Compare the radiation pattern of the single element and the array. Comment the differences
Solution:
The radiation pattern of the dipole has changed, and the maximum gain has increased

## Slide 20: Visualize Radiation Pattern wit the array
Click on Plot Fields, Radiation Field.. and then select as visible the Gain (dB) plot

## Slide 21: Exercise: Visualize Radiation Pattern
Check the radiation patter for a different scan condition: θ=30deg and φ=60deg

## Slide 22: Exercise: Visualize Radiation Pattern (solution)
Solution:
Modify the value of ScanAngleTheta and ScanAnglePhi variables as desired
φ=60deg
θ=30deg
Check the radiation patter for a different scan condition: θ=30deg and φ=60deg

## Slide 23: 1D array Same axis Dipole Array

## Slide 24: Rotate the dipole
Copy and paste the dipole HFSS design, select all the elements and click on Rotate
The array in HFSS can be created only with periodicity in X and Y axis, therefore, we rotate the dipole to be on X-Y plane
According to our original coordinate system (slide3) this is the Z-oriented array, even that now the periodicity will be in the new x-direction
Now the dipole is in XY plane

## Slide 25: Boundary Conditions
Change the solution type. Then, delete the AutoOpen1 boundary condition and assign Auto Identify lattice pair boundary condition to the RadiatingSurface

## Slide 26: Boundary Conditions
Maintain the Global:XY plane and see the primary and secondary lattice pairs that have been created

## Slide 27: Radiation Region
Select the other faces of the RadiatingSurface and assign Radiation Boundary condition

## Slide 28: Create the array
Select Create Array
Change the name and make it Visible. Define the Size of the array

## Slide 29: Create the array
Visualize the created array

## Slide 30: Setups
In the Solution setup just check the option of Save radiated fields only and Validate and Analyze the model

## Slide 31: Magnitude and Phase of the elements
Select the Finite Array Beam Angle option, then click on Calculate and Apply to Sources

## Slide 32: Magnitude and Phase of the elements
Check the values by visualizing the sources

## Slide 33: 3D radiating Sphere
Create a Far field setup, Infinite Sphere type

## Slide 34: Exercise: Plot Gain in dB

## Slide 35: Exercise: Plot Gain in dB (solution)
Solution:
Create a 3D Polar Plot and plot the total gain (GainTotal) in dB as shown

## Slide 36: Visualize Radiation Pattern with the array
Click on Plot Fields, Radiation Field and then select as Visible the Gain (dB) plot

## Slide 37: Exercise: Compare the Radiation Pattern
Compare the radiation pattern of the single element and both arrays. Comment the differences

## Slide 38: Exercise: Compare the Radiation Pattern (solution)
Solution:
Compare the radiation pattern of the single element and both arrays. Comment the differences

## Slide 39: Exercise: Compare the Radiation Pattern
Compare the radiation pattern of the single element and both arrays. Comment the differences
Solution:

## Slide 40: Change the unit cell
You can easily change the spacing between elements by double-clicking the CreateRegion and changing Z padding
Then, click on Apply and OK

## Slide 41: Conclusions
The tutorial provided in this Academic Resource includes the instructions to follow and fully populated model for reference.
The solutions can be seen only after the analysis is executed for each model, and this can be done by the “Analyze” function.
The model including all the designs is named: “1D_Dipole_array_model_all.aedt”
or here 

## Slide 42: Ansys Education Resources Feedback Survey
Here at Ansys, we rely on your feedback to ensure the educational content we create is up-to-date and fits your teaching needs.
Please click the link below to fill out a short survey (~7 minutes) to help us continue to support academics around the world utilizing Ansys tools in the classroom.
Feedback Survey Link
Notes: Feedback Survey link for copy-paste method  https://ansys.typeform.com/to/jcattJI5