## Slide 1
2D Dipole Antenna Array in Ansys HFSS (with Array Tool analysis)
Celia Gómez Molina Dimitris Tzagkas
education@ansys.com

## Slide 2: Introduction
In this Lab Tutorial the method of creating and analyzing a 2D dipole array will be explained.
The tutorial is developed using the Array Tool that extrapolates the radiation of a single element (post processing) and keeps the analysis time needed low.
In addition, the generation of the Array Factor plot is demonstrated.
Pre-requisites:
Having a ready antenna OR ability to create/import/generate an antenna that will be used as an array element.
This resource should be considered as a continuation of the Array Theory and the 1D Dipole Array tutorial

## Slide 3: Objective: create 2D dipole array
y
z
x
5x5 XY-oriented array
0.5λ
0.5λ
2λ
2λ
Top View of the Array [View from Z-axis]
θ
φ

## Slide 4: Load dipole model
There is a dipole model available in the resource structure that you can load and use:
OR by opening the file “Dipole_model_ref.aedt” directly in Ansys Electronics Desktop by:
File  Open..  and navigate to the downloaded file location, then select the mentioned file.
Double click the model to open with Ansys Electronics Desktop 

## Slide 5: Create an array
Once we have our antenna ready, right-click on Radiation> Antenna Array > Antenna Array Setup…
Choose Parametric Array Setup and enable Array Visibility

## Slide 6: Create an array
Go to Array Geometry menu to define the array setup
To select the coordinates of the center position
In this case: (0,0,0)
To select the direction of the U and V vector
In this case: U corresponds to X and V corresponds to Y
Specify the Layout Type and Frequency
In this case: Rectangular at 2.4GHz
To specify the total length and width of the array and the spacing between elements
In this case: the array is 2λ x 2λ with 0.5λ of spacing between elements
Then, click on Apply and OK
Reference Array

## Slide 7: Create an array
Go to Array Weight menu to setup more characteristics
To select the taper function
In this case: Uniform
To select Sum/Difference Pattern
In this case: No Differential
To specify the scan angles
In this case: both Phi and Theta equal to 0°
Then, click on Apply and OK

## Slide 8: Analyze the array
Check the array model that has been created
Then, Analyze it
We can observe the rectangle 5x5 array with the center in the origin that has been created

## Slide 9: Visualize the Gain in dB and the Directivity

## Slide 10: Directivity with the Array
Plot the Radiation Field

## Slide 11: Explore other phi/theta scan angles
Open the Antenna Array Setup…
In the Array Weight tab, change Phi and Theta angles to 45deg

## Slide 12: Explore other phi/theta scan angles
Visualize the new radiation pattern

## Slide 13: Comparing radiation patterns
Compare the radiation pattern with [Phi=0deg and Theta=0deg] to [Phi=45deg and Theta=45deg]

## Slide 14: Comparing radiation patterns (solution)
The radiation pattern has changed, and the directivity has increased
Compare the radiation pattern with [Phi=0deg and Theta=0deg] to [Phi=45deg and Theta=45deg]

## Slide 15: Comparing radiation patterns
Compare the radiation pattern of just a dipole antenna to the previous array with scan angles Phi=45deg and Theta=45deg

## Slide 16: Comparing radiation patterns (solution)
With the array the directivity can be increased significantly
Compare the radiation pattern of just a dipole antenna to the previous array with scan angles Phi=45deg and Theta=45deg

## Slide 17: Comparing array sizes
How is the radiation pattern affected if two more elements are added (7x7 array)?
0.5λ
0.5λ
3λ
7x7 XY-oriented array

## Slide 18: Comparing array sizes (solution)
Copy the project and click on Antenna Array Visibility. Then, modify the Antenna Array Setup…
Modify the Length and Width of the array. Then, Analyze the model
How is the radiation pattern affected if two more elements are added (7x7 array)?

## Slide 19: Comparing sizes (solution)
The radiation pattern has changed, and the directivity has increased
Visualize the new radiation pattern
(previous 5x5 array)
(new 7x7 array)
How is the radiation pattern affected if two more elements are added (7x7 array)?

## Slide 20: How to plot Array Factor
When using the array tool, the array factor can be plotted on Far Field plots (ArrayFactor vs Angle) using the below method.
Create Far Field plot Create Far Fields Report and then  Radiation Pattern
Create Variable
If the “Far Field report” option does not exist, a Radiation Surface needs to be defined

## Slide 21: Plotting the Array Factor
1
2
3
4
5
6
A
B
C
D
E
F

## Slide 22: Conclusions
The tutorial provided in this Academic Resource includes the instructions to follow and fully populated model for reference.
The solutions can be seen only after the analysis is executed for each model, and this can be done by the “Analyze” function.
The model including all the designs is named: “2D_Dipole_array_model_all.aedt”
or here 

## Slide 23: Ansys Education Resources Feedback Survey
Here at Ansys, we rely on your feedback to ensure the educational content we create is up-to-date and fits your teaching needs.
Please click the link below to fill out a short survey (~7 minutes) to help us continue to support academics around the world utilizing Ansys tools in the classroom.
Feedback Survey Link
Notes: Feedback Survey link for copy-paste method  https://ansys.typeform.com/to/jcattJI5