## Slide 1
Electrical Machines Fundamentals: Electromotive Force Analysis in Depth
Developed and curated by the Ansys Education Team
Angelos Fragkos, Dimitris Tzagkas
education@ansys.com

## Slide 2: Learning Objectives
Intended Learning Outcomes | 
Knowledge and Understanding | Understanding the concept of EMF and validate the theory with simulations.
Skills and Abilities | Conducting simulations, understanding electromagnetics.
Values and Attitudes | Emphasis on accuracy, validation, and bridging theory with real-world applications.
Resources
Introduction to Electrodynamics, by David J. Griffiths, 2nd ed.
Electric Machinery Fundamentals, by Stephen J. Chapman, 5th ed.
Matter & Interactions, by Ruth W. Chabay and Bruce A. Sherwood, 4th ed.
Electromagnetics and Applications, by David H. Staelin (MIT course material)
Further reading/information
  Ansys Academic
  Ansys Innovation Courses
  Ansys Education Resources
Ansys software mentioned | Ansys Maxwell®, an advanced electromagnetic field solver
Built-in Assessment
  Simulation instructions
  Exercises

## Slide 3: Resource purpose
This Ansys Maxwell software educational resource was developed to meet the following objectives:
Familiarize the reader with 3D Design, Material Assignment and Magnetostatic, Transient analysis in Ansys Maxwell software. This is achieved through:
1) A step-by-step analytical tutorial.
2) Practice exercises.
Provide a brief yet analytical presentation of the theory behind EMF (Electromotive Force) through a dedicated theory presentation.
Validate and enhance the reader’s theoretical understanding by replicating a classic textbook example and allow experimentation with multiple variations of the same design.
Understanding theory is crucial — it allows junior engineers to build strong foundations and enhance their expertise. A strong grasp of the fundamentals is key to tackling complex designs and addressing the toughest engineering challenges.
Disclaimer
This is a concept design developed to meet the above conditions. It is not a real-world application engineering design and must not be confused with or compared to one.

## Slide 4: Outline
This presentation
  What is Electromotive Force (EMF)
  Motional EMF
  Induced magnetic/electric fields concepts
  EMF Calculation
Next presentations
  How to create a motional EMF setup in Ansys Maxwell software
  How to solve the setup and study the fields
  How to solve the setup and study EMF

## Slide 5: Basic Theory Glossary
Symbol | Meaning | Unit | Vector/Scalar
 | The force of the source per unit charge |  | Vector
 | Total force per unit charge in the wire |  | Vector
 | Electric Field (Induced or Static) |  | Vector
 | EMF (Electromotive force) | V | Scalar
N or S | Represent North or South pole | - | -
 | Magnetic Laplace force |  | Vector
 | Magnetic field | T | Vector
 | Magnetic flux | Wb | Scalar
 | Time | s | Scalar
w | Rotational frequency | rad/s | Scalar
 | Velocity | m/s | Vector
Symbol | Meaning | Unit | Vector/Scalar
 | The force of the source per unit charge |  | Vector
 | Total force per unit charge in the wire |  | Vector
 | Electric Field (Induced or Static) |  | Vector
 | EMF (Electromotive force) | V | Scalar
N or S | Represent North or South pole | - | -
 | Magnetic Laplace force |  | Vector
 | Magnetic field | T | Vector
 | Magnetic flux | Wb | Scalar
 | Time | s | Scalar
w | Rotational frequency | rad/s | Scalar
 | Velocity | m/s | Vector

## Slide 6: EMF (Electromotive force)
In most of the resources EMF is defined as: the work done, per unit charge, by the source. But what does this definition really mean?
*Do not forget that low frequency and power transfer circuits are represented by TEM mode (Transverse Electric and Magnetic) and most of the times l(length of circuit)<<λ(wavelength) so, in the whole space induced fields are not present and curl remains 0 (electrostatic).
Total force per unit charge
EMF is defined as the line integral of around the circuit :
Units:
Considering a fundamental circuit with a battery. As we know, the forces that are responsible for driving current around the circuit are:
The force of the source , which is confined to one portion of the loop. In this fundamental illustration the chemical force of the battery is responsible for the development of the source force.
The electrostatic force (due to the surface charges) , which serves to smooth out the flow and communicate the influence of the source to distant parts of the circuit.
The Electrostatic Field from surface charges?

## Slide 7: EMF (Electromotive force)
EMF is the electric potential generated by a source to move a unit charge [in a cable/circuit]. The physical agency responsible for can be any one of many different things: -In a photoelectric cell it is light, -In a battery it is a chemical force, -In a piezoelectric crystal mechanical pressure is converted into an electrical impulse, -In a thermocouple it is a temperature gradient that does the job.
Piezoelectric plates
Batteries (AAA, AA, PP3)
Solar panel structure (photoelectric effect)
Piezoelectric Roads Generating Sustainable Electricity
Thermocouple in heater

## Slide 8: Motional-EMF
Thus, EMF is defined as
The most common source of EMF though is the generator which is producing a type of EMF called motional EMF!
It is known that when a conductor moves into a magnetic field that Lorentz force applies:
N
S
ω
It is proven that EMF generated in the loop is minus the rate of change of flux through the loop:
This is known as the flux rule for motional EMF.
💡
Experiment 1: A simple loop of wire rotating within a uniform magnetic field. Loop is moving; magnets are stationary.
a
b
c
d
Wire loop
a
b
c
d
A very large electric diesel generator in factory.

## Slide 9: Induced Electric Field-EMF
ω
N
S
Stoke’s Theorem
Now consider a different experimental set up in which the magnetic field is varying but the loop remains stationary. Will there be an EMF? Which force will be responsible for creating the EMF? Obviously, magnetic forces cannot be the case because the loop has zero velocity. Faraday’s work brought clarity.
A changing magnetic field induces an electric field:
It was experimentally observed that one more time:
This induced electric field is responsible for the development of EMF this time.
.
🤔
This is the Faraday’s law ( flux rule, mechanisms responsible for developing EMFs are totally different)
You are probably wondering how can these different experiments yield the same formula for the EMF ()… This ‘coincidence’ led Einstein to the special theory of relativity.
Experiment 2: Magnets are moving loop is stationary.
(Maxwell’s Third Equation)

## Slide 10: EMF: Reference Frame
E.g. In the first experiment, if you are an observer at a charge’s reference frame (on the wire loop) you have 0 velocity, but you experience a time-varying magnetic field. This results in an induced electric field, as described by faraday’s law and results remain the same✔️(relativity in electromagnetism)
The force responsible for developing EMF depends on the observer’s frame of reference (whether it is magnetic or electric). However, the physical outcome the induced voltage must be the same in all frames.
Reference Frame | First Experiment Force responsible for EMF | Second Experiment Force responsible for EMF
Lab Observer | Magnetic | Induced Electric
Observer on the wire loop | Induced Electric | Induced Electric
Observer on the magnets | Magnetic | Magnetic
💡
In all the above scenarios, the EMF follows the same rule: , whether it is called Faraday’s law or flux role for motional EMF.
.

## Slide 11: EMF: Calculations
The theoretical motional EMF should be calculated when the loop is rotating. This will be done by calculating the Lorentz force’s integral in every part of the loop.
For the ab: In this segment, the velocity of the wire is tangential to the path of rotation, while the magnetic field B points to the right , as shown in Figure 1. The quantity v x B points into the page, which is the same direction as segment ab. Therefore, the induced voltage on this segment of the wire is:
.
Experiment 1: Loop is moving magnets are stationary.
ω
a
b
c
d
+
-
-
+
+
-
l
r
a
b
c
d
0
.
For the bc and da segment: v x B is perpendicular to the length of the segments. Therefore the voltage in these segments be will be zero:
.
.
N
S
For the cd : The quantity v x B points into the page, which is the same direction as segment cd. Therefore, the induced voltage on this segment of the wire is.
a
b
c
d
Vab
Vcd
B
B
ω
Figure 1

## Slide 12: EMF: Calculations
Experiment 1: Loop is moving magnets are stationary.
ω
a
b
c
d
Thus, the total motional EMF can be defined as:
Geometrically, and :
It can be written that: . Also, the tangential velocity of the edges of the loop can be expressed as :
Area of the loop
N
S
Chart: 
3 Periods (3T)
Amplitude of the waveform

## Slide 13: EMF (Electromotive force)
The total motional EMF is written as:
.
In the experiment that will follow Ansy’s software (2025 R1) ‘conveniently ’ operated better when the magnets are rotated instead of the wire. It is necessary to rotate the magnets around the wire. But as it has already been mentioned, the mechanisms for developing EMF may differ drastically and are depended on the frame of reference, but the observable results -the developed EMF- are identical!
💡
It is hence proven that the EMF in the loop follows a sinusoidal waveform and the amplitude of it is determined by the product of the magnetic flux in the loop and the rotational speed. This is also applied is real AC machines. The (back) EMF in a real AC machine is determined by:
The magnetic flux in the machine.
The rotational speed.
A constant which is determined by the construction characteristics of the machine.
🎯
The goals of this experiment are:
Demonstrate the developed EMF and experiment by changing the rotational speed.
Understand the concept of EMF and demonstrate that the Faraday’s law and the flux rule provide the same results (relativity in electromagnetism). Theoretical calculations  Experiment 1.
Ansys Maxwell software setup Experiment 2.

## Slide 14: Basic principle of generator motor operation [simulation example]
How does motion can create Electromotive Force?
Setup consists of:
  Ring magnets,
  rotating around wire loop,
  At frequency ,
  Inducing EMF on wire loop at same frequency
ω
a
b
c
d
N
S

## Slide 15: Ansys Education Resources Feedback Survey
Here at Ansys, we rely on your feedback to ensure the educational content we create is up-to-date and fits your teaching needs.
Please click the link below to fill out a short survey (~7 minutes) to help us continue to support academics around the world utilizing Ansys tools in the classroom.
Feedback Survey Link
Notes: Feedback Survey link for copy-paste method  https://ansys.typeform.com/to/jcattJI5