## Slide 1
Electrical Machines Fundamentals: Electromotive Force Analysis in Depth
Developed and curated by the Ansys Education Team
Angelos Fragkos , Dimitris Tzagkas
education@ansys.com

## Slide 2: Outline
Duplicate design
Change solution type – Transient
Create excitation on wire loop/coil
Create motion/rotation band
Set rotation speed
Setup analysis configuration
Results plotting

## Slide 3: Transient Analysis (1)
Right click on the magnetostatic design and copy it.
1
2

## Slide 4: Transient Analysis (2)
Then right click on the Project and click Paste.
1
2

## Slide 5: Transient Analysis (3)
Then right click on copied design and select solution Type. Change the solution type to Transient.
1
2
3
4

## Slide 6: Transient Analysis: Coil Terminal (1)
Right click on the Wire_Loop and Copy it.
1
3
2

## Slide 7: Transient Analysis: Coil Terminal (2)
Right click anywhere in the viewport and paste it.
Right Click
3
2
1

## Slide 8: Transient Analysis: Coil Terminal (3)
Make only Wire_Loop1 visible in the active view.
1
2

## Slide 9: Transient Analysis: Coil Terminal (4)
Set the Grid Plane to XZ.
Create a rectangle sheet on the XZ plane that intersects (cuts across) Wire_Loop1, i.e., it should fully cross the conductor’s cross-section and extend slightly beyond it
1
2

## Slide 10: Transient Analysis: Coil Terminal (5)
Make sure that your viewport looks like the adjoining one.

## Slide 11: Transient Analysis: Coil Terminal (6)
Select Both objects (make sure to choose the Wire_Loop1) and Intersect.
Left Click +ctrl +Left Click
1
2

## Slide 12: Transient Analysis: Coil Terminal (7)
Click at the surface that you just created and rename it
Creating a surface on the coil volume is required to assign a coil terminal. The coil terminal is where you excite the coil or observe its response - It lets you apply current or voltage or detect an induced EMF.

## Slide 13: Transient Analysis: Coil Terminal (8)
Right click on the Excitation and Add Winding. Then you can change the Name of the winding and click OK.
1
2
3
4

## Slide 14: Transient Analysis: Coil Terminal (9)
First select (left click) the newly created rectangle and right click on the PhaseA. Select Assign Coil Terminal and click OK.
1
2
3
4

## Slide 15: Transient Analysis: Motion Band (1)
Set the Grid Plane to XY and draw a cylinder.
1
2
3
Left-Click at any point
Move the mouse at any direction and left click again to define the rectangle.
Move the mouse and left click again to define the height.

## Slide 16: Transient Analysis: Motion Band (2)
Double click the CreateCylinder option to define its parameters.
1
Double click
2
3
4

## Slide 17: Transient Analysis: Motion Band (3)
Create a second cylinder and configure again.
1
2
3
4

## Slide 18: Transient Analysis: Motion Band (4)
Firstly, select the bigger Cylinder then the smaller, click subtract and OK.
1
2
3
4

## Slide 19: Transient Analysis: Motion Band (5)
Select the new object. Rename it as MotionBand and assign a transparency level of your choice.
Motion Bands are used to determine moving parts in transient simulations.
1
2

## Slide 20: Transient Analysis: Motion Band (6)
First select the Motion_Band and Right click on Model. Select Motion Setup and Assign Band. Select Rotation and move to the next slide to complete the steps.
1
2
3
4

## Slide 21: Transient Analysis: Motion Band (7)
5
6
9
After selecting “Rotation” in the “Type” tab click the “Mechanical” tab and introduce a global variable “$speed_rpm” that will represent the speed. Set the value to 000 rpm and click OK to close both windows.
8
7
The symbol $ is used to define a Global variable. Global variables  Accesible across all designs within the same project.

## Slide 22: Transient Analysis: Motion Band (8)
Right Click on Analysis and select Add Solution Setup. Configure the Stop time and the Time step as shown and move to the next slide to configure the local variable.
1
2
8
3

## Slide 23: Transient Analysis: Motion Band (9)
5
4
In the pop-up window configure the unit to [s].
8
Next Configure the Value as shown and click OK.
6
7
Finally click OK to the Solve Setup window of the previous step.

## Slide 24: Transient Analysis
By clicking at the Project’s name, the global variables appear at the properties window.
You can later change it at any desired reasonable value.
By clicking at the Design’s name, the local variables of the design appear at the properties window. This specific variable it is depended and can not be adjusted.

## Slide 25: Transient Analysis: Simulation (1)
Click on the Simulation tab and validate the Simulation. Notice that everything is validated correctly.
1
2

## Slide 26: Transient Analysis: Simulation (2)
Left Click on the created Setup and select Analyze.
1
2

## Slide 27: Transient Analysis: Results (1)
Right click on results and Create Transient Report  Rectangular Plot.
While the simulation is still running you can observe the waveform of the EMF forming.
1
2
3
4
5

## Slide 28: Transient Analysis: Results (2)
Observe the sinusoidal waveform.
The experimental results match excellently the theoretical predictions!
From the Magnetostatic analysis and the theoretical calculations, we predicted an EMF waveform with minimal harmonic content and amplitude of 3 V
3
4
1) Right click +
2

## Slide 29: Transient Analysis: Results (3)
A sinusoidal waveform with the theoretical amplitude was produced, exactly as predicted by the calculations. However, it is important to note that this waveform resulted from the rotation of the magnets—not the wire loop. This means the EMF was generated by an induced electric field acting on the stationary wire loop, rather than by a magnetic (Laplace) force, as perceived by a lab-frame observer. As previously mentioned, the mechanism responsible for generating EMF depends on the observer's frame of reference—magnetic or electric. Nevertheless, the physical outcome—the induced voltage—remains the same across all frames of reference.
.
Values for 4000 rpm: Theoretical Value = 3.062264 V
Experimental Value = 3.026904 V
Absolute difference = 0.03536 V
Percent difference:

## Slide 30: Transient Analysis – Practice
  Recall the theory about the EMF. Remember that its amplitude is depended on the maximum flux and on the rotational speed. Try change the speed and observe how the EMF responds.

## Slide 31: Transient Analysis: Results (4)
Two tables with the theoretical values and “experimental “ values of EMF amplitudes are presented.
Theoretical Values at different speeds. Magnetostatic Analysis.
Transient Simulation Results. “Experimental” values.

## Slide 32: Transient Analysis: Results (5)
Graph visualizing the data from the two previous tables. The theoretical predictions match the transient simulation results.

## Slide 33: Transient Analysis: Results (6)
Observe the rotating magnets and the magnetic field vector in the wire loop.

## Slide 34: Transient Analysis: Results (7)
Observe the rotating magnets and the magnetic field vector in the horizontal cut – circular surface.

## Slide 35: Design challenges – Keep in mind
Shape of Magnets: The geometry of the magnets is critical. It should suppress rotation of the magnetic field and minimize its magnitude gradient, ensuring the wire loop “sees” a uniform magnetic field at every position during rotation.
Region Size: We must trade off accuracy and time. The solving domain region must be large enough to obtain a correct solution, but at the same time as small as possible to reduce simulation time and memory. The appropriate size depends strongly on the application, and if there are magnetic materials present in the model or not.
Meshing: We should implement mesh operations to increase element count and accuracy. In this design, we applied a mesh operation to the subregion because it’s critical; more elements were needed there to improve accuracy and match the theoretical calculation.

## Slide 36: Ansys Education Resources Feedback Survey
Here at Ansys, we rely on your feedback to ensure the educational content we create is up-to-date and fits your teaching needs.
Please click the link below to fill out a short survey (~7 minutes) to help us continue to support academics around the world utilizing Ansys tools in the classroom.
Feedback Survey Link
Notes: Feedback Survey link for copy-paste method  https://ansys.typeform.com/to/jcattJI5