## Slide 1
Current Loop Simulation using the Ansys Maxwell Software
Pratap Vangol and Dr. Saharnaz Baghdadchi
University of California, San Diego
Dr. Celia Gómez Molina
Academic Development team, Ansys
education@ansys.com

## Slide 2: Learning Objectives
Intended Learning Outcomes | 
Knowledge and Understanding | Fundamental principles of magnetostatics and simulation workflows using the Ansys Maxwell software.
Skills and Abilities | Conducting simulations, visualizing magnetic fields, and validating results using industry-standard software.
Values and Attitudes | Emphasis on accuracy, validation, and bridging theory with real-world applications.
Resources
M. N. O. Sadiku, Elements of Electromagnetics, Oxford University Press, 2001.
Ulaby, Michielssen, and Ravaioli, Fundamentals of Applied Electromagnetics, Seventh Edition, Pearson Education, 2015.
Further reading/information
  Ansys Academic
  Ansys Innovation Courses
  Ansys Education Resources
Ansys software mentioned | Ansys Maxwell®, an advanced electromagnetic field solver
Built-in Assessment
  Simulation instructions
  Exercises

## Slide 3: Magnetostatics
Magnetic fields that do not change with time, produced by steady (time-independent) electric currents or permanent magnets.
In today’s lesson we will study the magnetic field generated by a current-carrying loop.
Magnetostatics can be seen as special case of Maxwell's equations, where we assume that charges are either fixed or move as a steady current.
Commonly used sources that generate static magnetic fields are permanent magnets, current-carrying conductors and electromagnets.
Applications: transformers, inductors, electric motors, generators, magnetic storage devices, medical imaging…

## Slide 4: Analytical Assignment
Consider a loop of radius centered on the x − y plane. Find the magnetic flux density at the point from the loop, when the loop is carrying Amps of current.
Calculate from the Biot-Savart law, the field created by a current-carrying loop
Observation point

## Slide 5: Theoretical derivations
Starting from the Biot-Savart Law:
Now, particularly for our geometry
We finally obtain the magnetic flux density (𝐵) produced at by the current-carrying loop
And considering that
and
(Tesla)
where
is the permeability of free space
is an infinitesimal segment of the current loop
is the vector pointing

## Slide 6: Problem statement
Simulate in Ansys Maxwell software a loop of radius , having a current of flowing through it.
Observe the magnitude of the field created at .
Particularize the previously calculated theoretical solution to this case and compare it with the obtained simulated solution.
Observation point

## Slide 7: Maxwell Setup

## Slide 8: Familiarize yourself with the Ansys Maxwell Software Interface
Draw 3D Objects
Draw 2D Objects
3D Modeller Window
Project Manager window
Configuring the Simulation

## Slide 9: Maxwell Configuration – solution type
Right+Click

## Slide 10: Step 1: Current Carrying Loop
The loop is represented as a Torus

## Slide 11: Step 1: Current Carrying Loop
Move the mouse approximately to the center of the coordinate system and left click
Move the mouse to define the radius of the Torus.

## Slide 12: Step 1: Current Carrying Loop
Move the mouse inwards and left click again to define the inner radius of the torus

## Slide 13: Step 1: Current Carrying Loop
The geometry should look similar to the adjoining figure
Double-click

## Slide 14: Step 1: Current Carrying Loop
Set the center to be (0,0,0)
Set Major Radius to be 1m = 1000mm Set the Minor radius to 10mm
The Minor radius defines the thickness of the wire loop

## Slide 15: Step 2: Defining the Current
Select the drawn Torus and make a copy of it by clicking Ctrl+C and Ctrl+V
We will copy the torus to create a 2D cross section for the planar current source

## Slide 16: Step 2: Defining the Current
The resulting geometry is shown in the adjoining Figure

## Slide 17: Step 2: Defining the Current
Ensure that you are in the Draw strip Select the YZ plane from the adjoining menu

## Slide 18: Step 2: Defining the Current
Select the draw rectangle option and draw an arbitrary rectangle which cuts through the torus once

## Slide 19: Step 2: Defining the Current
On drawing the rectangle, the geometry is as seen in the adjoining image
Note: For drawing the rectangle there is no specific coordinates. Any arbitrary size is acceptable, but has to intersect the torus

## Slide 20: Step 2: Defining the Current
Select the Rectangle and then the Torus. Then select the intersect option
1
2
3
This creates a circular plane which will serve as a planar current source

## Slide 21: Step 2: Defining the Current
The final geometry is illustrated in the adjoining figure

## Slide 22: Step 3: Defining the Excitation
Select Right+Click

## Slide 23: Step 3: Defining the Excitation
Set to 1mA

## Slide 24: Step 3: Defining the Observation Line
Select the Draw Line
Draw an arbitrary line on the plane
In the next slide, the line length is set to be 2m

## Slide 25: Step 3: Defining the Observation Line
Double click
Set point 1 to be at (0,0,0) and point 2 to be at (0,0,2000)

## Slide 26: Step 4: Material Definition
Right+click

## Slide 27: Step 4: Material Definition
Set the loop to be made of Copper

## Slide 28: Step 5: Airbox Definition
Click on the create region command
Draw an arbitrary region. In the next slide, the dimensions will be edited

## Slide 29: Step 5: Airbox Definition
Click on the create region command
And assign 150 as the value of the padding

## Slide 30: Step 6: Solution Setup
Select and Right+Click
Click on OK The default simulation setup is sufficient for this problem

## Slide 31: Step 7: Simulation Validation
(1)
(2)
Ensure that there are no errors in the simulation
If there are any errors, recheck the previous steps

## Slide 32: Step 8: Running the simulation
Finally, analyze the design

## Slide 33: Step 9: Plotting the Results
Right+Click

## Slide 34: Step 9: Plotting the Results
Select the line we drew earlier
We will be plotting B field

## Slide 35: Step 9: Plotting the Results
Note: For the marker Right+Click -> X Marker You can drag it with your mouse along the X axis

## Slide 36: Validation step
Does this value match your theoretical calculations?

## Slide 37: Step 10: Plotting the magnetic field
Select the planes:
-Global: XY
-Global: XZ

## Slide 38: Step 10: Plotting the magnetic field
Right+Click

## Slide 39: Step 10: Plotting the magnetic field
Select Mag_H and click on Done

## Slide 40: Step 10: Plotting the magnetic field
(1) Double-click on the color scale
(2) Select dB

## Slide 41: Step 10: Plotting the magnetic field

## Slide 42: Step 10: Plotting the magnetic field
Select the vacuum Region and Right+Click
Select B_Vector and click on Done

## Slide 43: Results – Magnetic field created by a current loop
From theoretical derivations:
In a current-carrying loop, the magnetic field lines form concentric circles around the conducting wire, in accordance with the right-hand rule.
Analytic results validated through simulation

## Slide 44: Ansys Education Resources Feedback Survey
Here at Ansys, we rely on your feedback to ensure the educational content we create is up-to-date and fits your teaching needs.
Please click the link below to fill out a short survey (~7 minutes) to help us continue to support academics around the world utilizing Ansys tools in the classroom.
Feedback Survey Link
Notes: Feedback Survey link for copy-paste method  https://ansys.typeform.com/to/jcattJI5