## Slide 1
Functional Safety using Ansys SCADE software:
Session II Instructor Guide Presentation
Christoph Edeler, PhD
Ansys Application Engineer
Notes: The 25 PowerPoint Lecture Units For 2021
The Lecture Units developed for teaching in connection with Granta EduPack are listed at the end of this presentation.

## Slide 2: The Task: Follow up with constant distance
Integration
(using a State-Machine)

## Slide 3: The Development Process
Safety-related Software-Specification
Validation
System Design
Integration Tests
Module Design
Module Tests
Coding
Validation
validated
Software
Specification of Safety Functions
Result
Verification
Session I
Session II

## Slide 4: Final Architecture
Software-Integration
Distance-Controller
SiL-Testing (Software-in-the-Loop)

## Slide 5: Session II A 1
Open & observe the draft integration logic: Scademodel_Session_II_A_1\ACC_Scademodel\ACC_Scademodel.vsw (ignore the error «unresolved references» during loading: click ‘No’)
Compare with the requirements:
  a State-Machine shall be used to switch between active and inactive ACC
    a state ‚Control_OFF‘ for pedal control
    a state ‚Control_ON‘ for controller driving throttle and brake
  an input shall switch between pedal and controller steering
    Input name: ‚ControlSwitch_IN‘, type bool
    Input is <true> shall lead to active ACC (‚Control_ON‘), <false> to pedal control (‚Control_OFF‘)
Simulate your changes to ensure they work
Time: 20min

## Slide 6: Session II A 2
Open & observe the integration tests: Scademodel_Session_II_A_2\ACC_Scademodel_Test\ACC_Scademodel_Test.vsw
Review the test content (Procedure_IntegrationTest). What exactly is being tested in
    Record_Integration_Off,
    Record_Integration_On,
    Record_Integration_OnOff?
Is there anything which should be tested in addition?
Time: 10min

## Slide 7: From Integration to Validation
Now we have (partly) finished the integration tests.
Let’s do some validation in a Software-in-the-Loop environment (SiL)!
In this environment, our piece of code ‘feels’ exactly the same as in the field
=> Near-real testing under controlled conditions is possible!

## Slide 8: The Development Process
Safety-related Software-Specification
Validation
System Design
Integration Tests
Module Design
Module Tests
Coding
Validation
validated
Software
Specification of Safety Functions
Result
Verification
Session I
Session II

## Slide 9: Software-in-the-Loop Testing
*Software (or model) under test:
- Software-in-the-Loop (SiL)
- Model-in-the-Loop (MiL)
**virtual hardware & environment: in this exercise we will use the operators for emulation as well to close the control loop
Virtual cars:
masses, forces, preceding car
driving profile, friction etc
throttle, brake
distance
Software-Integration*
Distance-Controller*
Simulated surrounding conditions and actions
Virtual Hardware**:
emulated target
(Chip Emulation)

## Slide 10: Session II B 1
Open & observe the Software-in-the-loop environment: Scademodel_Session_II_B_1\ACC_Scademodel\ACC_Scademodel.etp
Simulate the environment to understand the values
  Speed_preceding_car_IN is the speed of the car ahead of us
  Car_Speed is the speed of our car
  Distance is the resulting distance
  we can regularly drive our car by throttle_IN & brake_IN
  a crash (Distance <= 0.0) leads to CrashDetected_OUT equals to <true> (reset simulation in this case)
Compare with the requirements:
  Average distance to preceding car (control target value): 50 m
  After initialization (first cycle): distance is given with 5 m
  It is impossible to let our car crash (this is clear, isn’t it :-)
Time: 20min

## Slide 11: Session II B 2
Open & observe the SiL tests: Scademodel_Session_II_B_2\ACC_Scademodel_Test\ACC_Scademodel_Test.etp
What is being tested in the tests:
  Record_SiL_Case1?
  Record_SiL_Case2?
  Record_SiL_Case3?
Review the tests:
  What is your opinion?
Time: 20min

## Slide 12: Session II (optional): New Requirement
An ‚Emergency-Brake‘ functionality has been requested:
100% brake when
  distance < current_speed / 3 s-1 and
  speed_Relative > 20 m/s
keep 100% brake until speed is zero
  then brake according to pedal position again
  leave ‚E-brake‘ mode
Design & implement the logic
Create 1-2 test cases
Your colleagues propose two ways:
Extend the distance controller functionality
  „very small distance => hard braking“
Add a new functionality
  controller and e-brake assistant side-by-side, „somehow“
What is the better approach and why?

## Slide 13: Discussion & Wrap-Up
The software development process
Requirements
Model-based software-development
Ansys SCADE suite/test
Dataflow / State-Machines
Testing
Conclusion
Questions/comments?
?
!

## Slide 14: Optional Safety Questions
What happens, if
the distance to the preceding car is high & the preceding car brakes hard?
something works at the unit-level, will it necessarily work at the (software) integration level?
the system state (On/Off) changes during operation? Do we have to prevent special cases?
Creation of formal low-level requirements can be hard!
Notes: In practice, the art is to formulate low-level requirements out of informal and/or high-level requirements. Keywords: Back-to-back testing, black box testing, model coverage etc…

## Slide 15: Discussion & Wrap-Up
What is your „success rate“?
What is your opinion about the workshop?
  Did you understand the principles of safety-critical software development?
  Were the examples understandable?
  Tempo too slow/too high?
Any further feedback?
  Space for improvements?
  General comments?

## Slide 16: End of Session II

## Slide 17
Appendix

## Slide 18: V-Model EN 61508 (13849-1)
Safety-related Software-Specification
Validation
System Design
Integration Tests
Module Design
Module Tests
Coding
Validation
validated
Software
Specification of Safety Functions
Result
Verification

## Slide 19: V-Model ISO 26262

## Slide 20: V-Model ISO 26262-6

## Slide 21: Roles in MBSW (50128): Implementer

## Slide 22: Roles in MBSW (50128): Tester

## Slide 23: Ansys Education Resources Feedback Survey
Here at Ansys, we rely on your feedback to ensure the educational content we create is up-to-date and fits your teaching needs.
Please click the link below to fill out a short survey (~7 minutes) to help us continue to support academics around the world utilizing Ansys tools in the classroom.
Feedback Survey Link
Notes: Feedback Survey link for copy-paste method  https://ansys.typeform.com/to/jcattJI5