## Slide 1
Functional Safety using Ansys SCADE Software:
Activity Overview and Background Information
Christoph Edeler, PhD
Ansys Application Engineer

## Slide 2: Activity Goals:
Implement and analyze a safety-critical functionality
Learn about Automatic Cruise Control (ACC)
  Keep constant distance to vehicle ahead
  Analyze incoming sensor data
  Control Loop Computations
Practice Model-Based Software Development w.r.t. Safety Processes
  V-model: Specification/Requirements, Implementation, Testing & Review
  EN 61508, ISO 26262, …
Learn basics of the Ansys SCADE tool in 3 hours
Notes: The goal here is to have some material to flexibly play with. Of course the focus is on learning the Ansys SCADE software (as a side effect). But aspects of ADAS systems, safety-critical development processes or standards, e.g. 26262, can also be discussed. As kind of a red line, the ACC example is given and several stages of the development cycle will be exercised.

## Slide 3: Activity Content Breakdown
Session I
Introduction & Target
A: Hands-On: Model Implementation “Controller”
B: Analyze Tests => Review => Review Requirements
Wrap-up & Discussion / Outlook
Session II
Introduction and Reminder
A: Hands-On: Integration => Analysis => Test
B: SiL*-Testing => Review (optional new Req. ‘Emerg.-Brake’)
Wrap-up & Discussion
* SiL = Software in the loop
Notes: This is the workshop outline as it has been planned and performed at Hochschule Kempten. However, different formats are possible. You could subdivide into more chapters, e.g. have A and B as individual 45-60min sessions. Or everything could be done in a ½ day activity, preferably with a break somewhere in the middle. Feel free to adapt to your needs.

## Slide 4: The Model – Headway Control
This exercise can be placed here
Notes: We saw the ACC example in the agenda. To understand the safety level and particular importance of this example, a rough categorization is given here. As the standard ACC is clearly SAE level 1, an advanced ACC could also be level 2 or even 3. Imagine also the case that the ACC is coupled with other ADAS functions. E.g. level 4-5, where the set speed comes not from the throttle input but from a path planning algorithm incl. sensor data.
SAE = Scociety of Automotive Engineers

## Slide 5: Documents & models for the workshop
Model Scade_Walkthrough and Scade Walkthrough.pptx (preparation)
FuSi Workshop Scade - Guidance Session I II.pptx (step-by-step instructions)
Scade-Models/Testprojects Session I
  I_A_1
  I_A_2
  I_B_1
  I_B_2
Scade-Models/Testprojects Session II
  II_A_1
  II_A_2
  II_B_1
  II_B_2
Design (dataflow) against requirements & Simulation
Testing against requirements & Review
Integration design (controlflow) against requirements & Simulation
SiL-Testing & Review (optional: new req.: ‚E-brake‘)
Notes: The walkthrough is meant to be handed to the participants in advance. So they can make themselves familiar with the Ansys SCADE tool and play a bit with the different setups (design, debugging/simulation, testing).

## Slide 6: The Task: Follow up with constant distance
Sensor: Distance
Actuator: Throttle
Actuator: Brake
t=0 s
t=4 s
t=8 s
t=11 s
Notes: Now this is the course definition of the environment: The ‚ego car‘ (in black) carries the ACC functionality, thus throttle and brake of the black car are controlled. This scenario shows the acceleratrion of the yellow car ahead. It‘s not exactly defined how the cars should interact. We would expect that the ego car detects the increasing distance and will begin to accelerate.
What would be appropriate parameters?
E.g. how shoud we accelerate,
What should be the target distance to the car ahead?
Again, this is not about exact numbers but to get into the ‚safety thinking‘.
Car image by shutterstock 755763799

## Slide 7: Distance Controller: Interface and Description
Controller will set ego car throttle and break according to the measured distance
In session I (and the dependent exercises), only the controller behaviour will be modelled
PI_Control will be used by the controller
In session II the controller will be embedded in a virtual car environment (CarInertiaSim). This will add basic characteristics such as inertia and friction.
Signal Name | Direction | Type | Description
distance_IN | Input | float32 | [m]
throttle_OUT | Output | float32 | [%] of max. throttle
break_OUT | Output | float32 | [%] of max. break
Notes: - Description of system behaviour => see also the instructor‘s slide deck with requirements for each excercise
- Description of the scope
- Description of the variables/signals used

## Slide 8: Final Architecture
Software-Integration
Distance-Controller
SiL-Testing (Software-in-the-Loop)
Notes: This rather simple diagram shows how basic function design, integration & Testing are organized.
First, the Distance-Controller will be investigated/developed (without any car-specific behaviour)
Second, the integration will be done to see typical car-specific charateristics such as inertia and velocity loss due to friction
Finally, testing activities can be performed. These ones are most ‚interesting‘ from the Integration perspective (at least for academic teaching purposes)

## Slide 9: The Development Process (Simulation Game)
Safety-related Software-Specification
Validation
System Design
Integration Tests
Module Design
Module Tests
Coding
Validation
validated
Software
Specification of Safety Functions
Result
Verification
This is your entry point!
Session I
Session II
Notes: On the one hand this schematic flow exemplarily shows the standard V model. On the other hand (and to ease the entry into the workshop‘s content), the starting point for the workshow is given.
To make it a bit more realistic (as in many companies in practice), the activities do not start with requirement definition but with module design immediately. As kind of a game play, the workshop participant is thrown into the role of a team member getting to his team a little late. So the participants have to really focus on what‘s really necessary. We will not go into endless discussions on requirements ;-)
Note: Just take this scenario as an option. If you want, do a full V-cycle and start with the requirements! Or you could skip the design phase (left hand side) and focus on V&V (right hand side) only. Feel free!

## Slide 10: Scade-Model Session I A 1 (Controller Implementation)
Failures will occur! Can you handle them?
Notes: We are in the game play mode again. Probably „your colleagues“ (the virtual company‘s temmates which prepared this model as a starting point for your work) have been in a hurry and did some mistakes. Can you fix them?

## Slide 11: Scade-Model Session I A 2 (Controller Simulation)
Model I A 2 is the solution of unfinished model I A 1

## Slide 12: Scade-Model Session I B 1 (Controller Test)
Notes: This is the vvalidation and verification activity. The values are close, but the test fails. Why?
(It‘s the tolerance!)

## Slide 13: Scade-Model Session I B 2 (Improved Test Cases)

## Slide 14: End of Session I:
Controller is readily done
Requirements have been improved
Design has been implemented
Design has been successfully simulated
Given tests have been executed and reviewed
Design has been adapted/corrected
Additional tests have been introduced
Notes: This is a list of what an ideal work product of session could look like. Feel free to focus on the aspects you want to shed some light on

## Slide 15: Scade-Model Session II A 1 (Software Integration)
here the previously designed controller will be used
Notes: Now we are in a mode of designing at integration level. It can be easily seen that we are building on the controller functionality we have designed beforehand (yellow block inside the state-machine‘s state ‚Control_ON‘)

## Slide 16: Scade-Model Session II A 2 (Software Integration Test)

## Slide 17: Scade-Model Session II B (from Integration to Testbench)
System Integration has been done:
  Now let‘s test our logic on a (software-based) testbench: Software-in-the-loop SiL (using the Ansys SCADE tool)
Safety-related Software-Specification
Validation
System Design
Integration Tests
Module Design
Module Tests
Coding
Validation
validated
Software
Specification of Safety Functions
Result
Verification
Notes: And now the verification of what has been done on integration level.

## Slide 18: Scade-Model Session II B 1 (SiL Integration)
here the previously designed ‚Software_Integration‘ is used
Notes: As we are now two levels up from the controller function, we can see how the Integration operator is embedded into a simple car-level simulation (CarInertiaSim)

## Slide 19: Scade-Model Session II B 1 (SiL Simulation)
Controller maintains constant distance
Notes: Just play with the debugger (Simulator): This is a typical behaviour of the ego car following a car ahead which accelerated very fast. One can easily see the swing forth and back of the distance under closed-loop control.

## Slide 20: Scade-Model Session II B 1 (SiL Simulation => Issue!)
In some situations a crash occurs!
Notes: Under bad conditions, the distance can become negative (shortly). This indicates a crash. The system has failed! What is the lession learned here?
Btw: There is not THE right answer. It could be all: Improper design, improper testing or just bad requirements. How should the overall process be improved to avoid such behaviour? The goal is to get into a discussion with the participants. What are the right questions to avoid such cases in general?

## Slide 21: Scade-Model Session II B 2 (SiL Tests & Review)

## Slide 22: Scade-Model Session II B 2 (New Req.: Emergency-Brake)
No template – let‘s see how far you can get in ~ 30 min!
?
Notes: This is a placeholder for additional activities, if some (or all) participants have 100% finished the exercises and would like to spend some more time on this. A typical safety feature close to ACC is an emergency brake. This could be even integrated into the existing ACC. Get into a discussion:
Formulate 2-3 requirements for an E-brake assistant
Implement the basic functionality and test it
Continue on integration and integration test level
=> What are your observations? What does it mean for development in general, for development process, for safety considerations?

## Slide 23: End of Session II:
Integration has been implemented (use of operator from session I)
Integration has been tested
A ‘SiL-environment’ is introduced to really see “changing values”
SiL-Testruns have been reviewed:
  Some functionality has been confirmed
  New issues arised
  The consequences of the new issues have been discussed
Optional (if enough time):
  New Requirement ‚Emergency-brake‘ is introduced
  Functionality can be implemented
  Fix of issue can be confirmed by tests
  Possible approach: Split participant teams into two groups: Developers and Testers

## Slide 24: Ansys SCADE Software Content
Controller Implementation
  I/Os & Dataflow
  Simulator
  Unit Testing
Integration + Testing
  State Machine
  Architecture
  Software Integration Tests
  Software-in-the-Loop (SiL)
This course will not contain “confusing” content:
  Last & Default
  Time Operators (except one in library)
  Arrays and Struct
  Map & Fold iterators incl. ‚i‘ & ‚w‘
Models consist only of
  regular inputs & outputs
  float32 & bool types
  Test
  Design
  Simulator
  Design
  Test
  Simulator
Notes: Before the workshop there is only the ‚Walkthrough‘ introduction to get familiar with SCADE. By intention, several important but rather difficult SCADE concepts have been left out.
For being able to use all the SCADE potential the participants would need extended experience or at least an in-depth hands-on training. Otherwise the time in the workshop will be wasted by struggling with e.g. proper iterator design or timing constraints. This should be avoided.

## Slide 25: The Workshop
for a step-by-step workshop guidance see separate document

## Slide 26: Preconditions for a successful workshop
Software Installation
  see the installation instructions „Scade Installation.pptx“
  Installation must be done (common Windows PC, Win 10 or 11, <4GB disc space)
  admin permissions required => creation of a system environment variable
  A temporary license (license file) will be provided in the week before the workshop
  Ansys SCADE software installation takes ~15min per machine
Students have successfully gone through the „SCADE Walkthrough“:
  they can open and modify models and „check“ them
  they can simulate an operator
  they can trigger test runs from test projects
  they have gone through the process of adding a test case (record and scenario file)

## Slide 27: Appendix

## Slide 28: Ansys SCADE software Suite Overview
Notes: A typical view of the tool DIE (Integrated Development Environment)

## Slide 29: Scade-Model “Cruise Control” (Scade Standard Example)

## Slide 30: V-Model EN 61508 (13849-1)
Safety-related Software-Specification
Validation
System Design
Integration Tests
Module Design
Module Tests
Coding
Validation
validated
Software
Specification of Safety Functions
Result
Verification

## Slide 31: V-Model ISO 26262
Notes: Exerpt from ISO 26262

## Slide 32: V-Model ISO 26262-6

## Slide 33: Roles in MBSW (50128): Developer (Implementer)
Notes: Exerpt from rail standard: Focus on different roles in a development process. E.g. ISO 26262 does not really define such roles. However, in practice, virtuelly every software product contributer has a dedicated role such as Developer, Tester, Requirements Engineer, Architect etc

## Slide 34: Roles in MBSW (50128): Tester

## Slide 35: Library CarInertiaSim
MassKg 1600 [kg]
FactorThrottleForce 10 [N/100]
FactorBrakeForce 50 [N/100]
These factors define the mass of our car and the maximum acc- and decceleration force for 100% throttle or brake, respectively.
In addition, the car exhibits friction and thus, if no throttle and no brake is applied, it will moderately deccelerate and finally stop. The controller will set an appropriate throttle value for constant velocity.
Notes: These are the basic simulated car properties of the ego car. They are hardcoded in the CarInertiaSim library. Feel free to adapt them, e.g. to investigate an empty car compared to a fully loaded car or even to make it to be a truck.

## Slide 36: Some feedback (Jan 2019)
Generally the workshop was a great success, the overall content and timing went very well
The walkthrough should be handed out to all of the students 2-3 weeks before the workshop
Dependent on the individual success rate and tempo of the groups there could be one or two more ‚special tasks‘ comparable to the ‚E-brake assistant‘ (e.g. manual oversteering of throttle/brake in On-mode). Eventually the whole level can be increased by introducing additional tasks
Notes: Here some thoughts from experience about what is necessary to have a successful workshop. It just key that people can get familiar with the tool (walkthrough) and that there is a clear central idea during in the workshop. Give the people open questions and support the answers by requesting ‚sharp‘ answers.

## Slide 37: Ansys Education Resources Feedback Survey
Here at Ansys, we rely on your feedback to ensure the educational content we create is up-to-date and fits your teaching needs.
Please click the link below to fill out a short survey (~7 minutes) to help us continue to support academics around the world utilizing Ansys tools in the classroom.
Feedback Survey Link
Notes: Feedback Survey link for copy-paste method  https://ansys.typeform.com/to/jcattJI5