## Slide 1
STEM Racing: How Fluid Flow Simulation Drives Competitive Advantage
Elisabeth Hülse
Ansys (part of Synopsys) Academic Program

## Slide 2: Learning Objectives
Intended Learning Outcomes | 
Knowledge and Understanding | Fluid dynamics, Aerodynamics – with relevance to STEM Racing
Skills and Abilities | Gain the basic knowledge necessary to understand what to look out for doing a CFD simulation on a STEM Racing car
Values and Attitudes | Being able to understand bigger picture concepts and applying those relevant to a specific project
Resources
Built-in Assessment
Further reading/information
  Ansys Academic
  Ansys Innovation Courses
  Ansys Education Resources
Ansys software mentioned | Ansys Discovery™, Ansys Fluent®
N/A

## Slide 3
Hints and tips on the use of this resource
DO NOT PRESENT TO STUDENTS
Start presenting from slide 8.

## Slide 4: Information for the instructor about this resource
<
This slide deck is intended to be presented by the teacher to the student team to provide a basic understanding of fluid flow and aerodynamics, relevant to the use of Ansys Software in the STEM Racing competition.
We recommend hiding slides 3 – 7, as it is only information on the use of this resource, and presenting slides 8 and onwards to the students.
Recommendation

## Slide 5: Learning Track online
These slides give a conceptual summary of essential concepts in fluid dynamics and aerodynamic, laying a foundation for using CFD (Computational Fluid Dynamics) simulation to improve a STEM Racing car’s performance.
For a deeper knowledge and understanding of these concepts, Ansys provides an online learning track for free online.

## Slide 6: Find the relevance for STEM Racing
As you walk your students through the basic concepts of fluid dynamics, aerodynamics, and engineering simulation, it is important to draw connections between these concepts and the relevance for the STEM Racing competition.
<
Look for the “STEM Racing hat”
So, when we “put our STEM Racing hat on” is marked with this hat on the slide.

## Slide 7: From here on …
Present the following slides to your students

## Slide 8
<
Using Ansys in STEM Racing
Ansys is the exclusive global partner for CFD simulation for STEM Racing teams providing access to free software, learning resources and support.

## Slide 9: What to use Ansys for?
With Ansys, you can:
Design and simulate your STEM Racing car in real time
Instantly test aerodynamics, materials, and structural performance
Explore multiple design iterations with live physics feedback
Visualize how your car will perform - before it hits the track
Build critical engineering skills using industry-leading simulation tools

## Slide 10: Know your science behind your car’s performance
The STEM Racing car is racing through air and the air flows around it like a fluid.
Understanding how this fluid flows, how it can slow the car down, and what to do to make the car faster is what will help you improve your car’s performance.
So, you need to understand basic concepts in:
Fluid Dynamics
Aerodynamics
Engineering Simulation

## Slide 11
Basic Concepts in Fluid Dynamics

## Slide 12: What defines a fluid?
As you know, matter exists in three basic states: solid, liquid, and gas.
The word “fluid” describes a behavior, not a state: anything that “flows” is considered a fluid.
Liquids and gases behave differently, but both can flow — that’s why both are called fluids.
When we study how fluids move, we call it “fluid dynamics”.

## Slide 13: Fluids are everywhere
You can find fluids almost everywhere:
Inside machines
Inside the human body
In food and drinks
In rivers, lakes, and the ocean
Fluids do many important jobs, they can:
Help rockets lift off
Carry oxygen through our bodies
Wash away dirt
Heat or cool different systems
Fluids are all around us.
Water, air, steam, paint, blood—these are all examples of fluids we use or see every day.
There are many different fluid flow characteristics. We will look at three of them on the following slides.

## Slide 14: External versus Internal Flow
External Flow
The air moving around the outside of the STEM Racing car is an external flow. This is the main type of flow that shapes how the air behaves around the vehicle.
Different areas around the car experience different air speeds and pressures.
External Flow
Internal Flow
Flow over an object, unconfined
Flow confined by walls or other boundaries

## Slide 15: Uniform versus Non-Uniform Flow
Uniform flow:
The fluid moves at nearly the same speed at all locations of the same flow path, making the airflow more predictable.
For example: a steady flow through a straight pipe of constant diameter
Non‑uniform flow:
This is a flow that is different in different locations of the same flow path, i.e. different speed.
For example: a steady flow through a pipe with bends and/or changes in diameter (Bends and diameter changes will change flow speed, for example.)

## Slide 16: Laminar versus Turbulent Flow
Laminar Flow
At low speeds, fluid particles move in a smooth, layered fashion (“lamina”). The flow appears uniform with no substantial mixing.
Turbulent Flow
At higher speeds, fluid particles move in a more chaotic fashion. The flow appears non-uniform and significant mixing occurs.

## Slide 17: How does this relate to STEM Racing?
How Flow Characteristics Affect Your STEM Racing Car
As your car moves through the air, different airflow patterns develop around it. These patterns influence how the air interacts with the car and how easily the car moves forward.
Why This Matters
Recognizing where smooth or chaotic airflow develops helps you understand which parts of your car move through the air more easily and which don’t. Based on that, you can make changes to your car’s design.
Airflow goal:
As smooth as possible!
(Image taken from this >> case study)
Smoother air flow
More chaotic air flow

## Slide 18
Intro to Aerodynamics

## Slide 19: What is the difference between fluid dynamics and aerodynamics?
Fluid dynamics is the study of how any fluid (like water or air) moves.
Aerodynamics is a part of fluid dynamics that looks at how air moves around things, like cars, bikes, or planes.

## Slide 20: Let’s look at an airplane as an example
How does an airplane take off into the air and stay in the air?

## Slide 21: Forces acting on an airplane
Thrust
Weight
Drag
Lift
The thrust from the engine pushes the plane forward.
The drag force pulls it back because of the air resistance.
.
The weight pulls the airplane to the ground.
The lift force is what keeps the airplane up in the sky.
So, where does this come from?

## Slide 22: The wings are responsible for “Lift”
The shape of the wing does the trick!
The shape is called “Airfoil”
Cross section of wing

## Slide 23: What is “Lift”?
Because of the wing’s shape, the air underneath slows down more than the air above. This creates a higher‑pressure region underneath the wing, which pushes the wing upward and generates lift.

## Slide 24: How does this relate to STEM Racing?
STEM Racing cars have wings too – but they are upside down.
The lift force becomes a downforce, which keeps the car stable and on the ground.
High pressure
Low pressure
DOWNFORCE
While downforce is an important consideration in motorsport, it has only a small impact for STEM Racing, because the track is a straight line.

## Slide 25: And what is “Drag”?
Thrust
Weight
Drag
Lift
The thrust from the engine pushes the plane forward.
The drag force pulls it back because of the air resistance.
.
The weight pulls the airplane to the ground.
The lift force is what keeps the airplane up in the sky.
And what is “Drag”?

## Slide 26: You can feel drag
Imagine riding a bicycle. You can feel the air pushing back against you. The faster you go, the more you can feel it.
That is the drag force.
When you change your seating position on your bike, you can feel how the push-back from the air changes. It feels stronger, when you sit up, and you can feel it less when you bend down.

## Slide 27: A motorsport example of making use of drag
Until 2026, Formula One cars used a technology called the Drag Reduction System (DRS). By opening a flap in the rear wing, the car reduces drag and can reach higher speeds on straight sections.
Drivers can switch DRS on or off. It stays closed in corners because they need the extra downforce for grip and stability while they turn.

## Slide 28
Apply this knowledge to optimize your STEM Racing car

## Slide 29: So, what you need to focus on, for your STEM Racing car
You want your car to be steady and fast…
What keeps it steady?
Generally, the downforce is what keeps the car steady. But since the STEM Racing track is a straight line and the cars are fixed on a line, the downforce has a minimal impact.
What makes it fast?
Keep the drag as low as possible!
How?

## Slide 30: “Streamlined shape”
A streamlined shape is a form designed to let air or water flow around it as smoothly as possible, reducing drag (air resistance or water resistance).
Examples:
<
Key features:
Smooth, curved front that gently parts the fluid (air or water).
Tapered, narrow rear end (like a teardrop) that helps the fluid close back smoothly behind the object.
No sharp edges that would create turbulence.
Symmetry along the direction of motion.

## Slide 31: What is flow separation?
Watch this short video (2 min) to see an example.
Flow separated from shape
Flow attached to shape
Area prone to turbulences
A more streamlined shape keeps the flow attached, avoids turbulences and reduces drag.

## Slide 32: Utilizing simulation to find the optimal performance
STEM Racing Case Study
Download this case study to see how design adjustments lead to improved performance.
Your goals for a high-performing car:
Streamlined shape
Keeping flow attached
Reducing drag
CFD simulation makes the invisible airflow visible and helps you see where you need to make changes.
CFD simulation reveals the numbers and values (such as velocity, pressure, and forces) you need to make design changes and improve performance.

## Slide 33
What is Engineering Simulation?

## Slide 34: Engineering Simulation Step by Step
CAD
Building a 3D model of your product
Input
Information about product (i.e. materials, components, fixtures)
Product Environment
Define boundary conditions (i.e. Is there a flow or a source of heat? Where is it coming from? Are certain parts fixed somewhere? Which parts are loose?
Output
Understanding product response and performance
Engineering Simulation is the computer-based analysis of how a product would perform in real life situations.

## Slide 35: Engineering Simulation Step by Step
Build a 3D model of your car, with the correct measurements
Input all information
i.e. which material each component is made of
Set environment and boundary conditions
i.e. external flow and direction
Understand car’s performance, i.e. velocity, pressure, forces
Watch this short video (14 min) to see a simplified and short example.

## Slide 36
Getting started with Ansys Discovery for STEM Racing

## Slide 37: Recommendation to get started with Ansys Discovery
about
2 hours
1. Learn the general tools in Ansys Discovery
2. Do a simulation on a generic STEM Racing car
about
2 hours
With the basic knowledge you have now, you can get started using Ansys Discovery and applying your knowledge to your STEM Racing car.
You are all set!
Download the software and get started with your own car.

## Slide 38: For higher fidelity use Ansys Fluent
If you run into limitations using Ansys Discovery, take a look at the Tutorial using Ansys Fluent.

## Slide 39
Where to get the Software?

## Slide 40: Get the download
On the Ansys website, there is a landing page dedicated to STEM Racing.
There are 2 options to get Ansys Software:

## Slide 41: Good luck!

## Slide 42: Ansys Education Resources Feedback Survey
Here at Ansys, we rely on your feedback to ensure the educational content we create is up-to-date and fits your teaching needs.
Please click the link below to fill out a short survey (~7 minutes) to help us continue to support academics around the world utilizing Ansys tools in the classroom.
Feedback Survey Link
Notes: Feedback Survey link for copy-paste method  https://ansys.typeform.com/to/jcattJI5