## Slide 1
Lecture Unit
Fundamentals of Dynamic Analysis Using LS-DYNA in Ansys Workbench– Part II
Developed by
Dr. Hesam Moghaddam
In Collaboration with
Dr. Saeid Enayatpour

## Slide 2: Learning objectives for this Lecture Unit
Intended Learning Outcomes | 
Knowledge and Understanding | Knowledge and understanding of dynamic analysis and explicit simulation
Skills and Abilities | Ability to use Ansys LS-DYNA software within the Ansys Workbench platform to solve highly nonlinear, transient, dynamic finite element analysis using explicit time integration.
Values and Attitudes | Awareness of the importance of simulation in dynamic analysis such as impact, crash, blast, etc.
In-Built Assessment
  Exercises:
  Quizzes
Further reading/information
  Ansys Academic
  Ansys Innovation Courses
  Ansys Education Resources
Resources
  Software Release: 2025 R1
  Images: Ansys Inc.
  Source: Ansys Learning Hub
  Collaborator: Dr. Saeid Enayatpour
Ansys software mentioned | Ansys LS-DYNA® nonlinear dynamics structural simulation software Ansys Workbench™, a simulation integration platform Ansys Mechanical™ structural finite element analysis software

## Slide 3: Outline of Lecture Unit
Contact Modeling in LS-DYNA in Ansys Workbench
Post-Processing Results in LS-DYNA in Ansys Workbench
Quasi-Static Analysis

## Slide 4: Contact Modeling in Ansys LS-DYNA in Ansys Workbench
Review of Fundamentals of Connections in Ansys Mechanical Software

## Slide 5: Relevance of Contacts for Impact Simulation
Contacts define how impact energy is transmitted — the heart of any crash simulation
Relevance
Define how bodies interact during collision — critical for accurate force transmission, stress prediction, and energy dissipation.
Governs whether simulation captures reality (penetration, rebound, friction, wear, etc.).
Central to crash, drop, ballistic, and forming analyses.
Impact on Simulation
Accuracy of contact forces → stress & deformation fidelity.
Numerical stability → timestep size and convergence behavior.
Computational cost → number of contact pairs and formulation type..
- velocity sphere A
- velocity sphere B
- contact normal
- contact point
– penetration depth

## Slide 6: Penalty Stiffness and Contact Search
Body Interactions and Contacts are penalty-based contacts
If contact is detected, contact forces F are applied to penetrating node (penetration g) and penetrated segment (element face)
The contact acts like a stiff penalty spring applied between the penetrating node and the target segment.
  Too low stiffness → excessive penetration
  Too high stiffness → reduces stable timestep and may cause contact chatter
To learn more about contact formulation theory, refer to Ansys Documentation [1].
Contact analysis depends on contact stiffness
g
F
k
Notes: [1] https://ansyshelp.ansys.com/account/secured?returnurl=/Views/Secured/corp/v252/en/wb_sim/ds_contact_theory.html?q=penalty%20stiffness
In explicit dynamics, contacts between bodies are modeled using a penalty-based approach.
When two parts come into contact, a force (F) is applied based on the amount of penetration (g) between a node and an element face.
This contact force acts like a stiff spring (with stiffness k) to resist penetration. But this spring is artificial—it doesn't physically exist; it's just a numerical mechanism.
Low contact stiffness can lead to excessive penetration, compromising accuracy. However, too high a stiffness results in high-frequency oscillations, which can destabilize the simulation.
The explicit time step size places an upper limit on contact stiffness—higher stiffness requires smaller time steps for stability.
Choosing the right penalty stiffness is a balance between accuracy and computational efficiency.

## Slide 7: Types of Connections
The Connections folder is used to define how the various bodies of an Explicit Dynamics solution interact with one another
Possibilities include:
  Contact
  Body Interactions
  Spot Welds
  Joints
  Springs / Dampers
  Beams
  SPH to SPH / ISPG to Surface Coupling/ etc. (Unique to Explicit)
Contacts, Joints, Spot Welds and Springs / Dampers behave in a similar manner to those used in implicit Mechanical solutions
The Default connection type for explicit analysis is Body Interactions
SPH to SPH / ISPG to Surface Coupling/ etc are used for fluid-solid interaction and Particle modeling

## Slide 8: Main Types of Connections: Body Interaction and Contact
In explicit dynamics, most interaction among parts occurs through contacts
Two kinds of penalty formulation contacts:
  Contact Region (in short Contact)
  Body Interaction
By default, LS-DYNA in Ansys Workbench adds a Body Interaction scoped to all bodies of the model upon initial geometry update. To learn more about different contact types in Ansys Mechanical software and LS-DYNA in Ansys Workbench, you can refer to these resources . [1-3].
Body Interactions can exist with Contact Regions; Do not use both at the same location Because:
  Contact forces will be split
  Contact stiffness will be doubled
  Frictional and bonded contact might act against each other
Notes: [1] https://ansyshelp.ansys.com/public/account/secured?returnurl=/Views/Secured/corp/v252/en/wb_sim/ds_Contact_Definition.html
[2] https://www.bing.com/videos/search?q=different+contact+types+in+Ansys+Mechanical&view=detail&mid=07676B9A6C62531608C107676B9A6C62531608C1&FORM=VIRE
[3] https://www.bing.com/videos/search?q=different+contact+types+in+Ansys+Mechanical&view=detail&mid=5F43CFD3F61EB1D6A3B05F43CFD3F61EB1D6A3B0&FORM=VIRE

## Slide 9: Body Interaction
In Explicit Dynamics, the solver automatically detects contact between nodes and faces across all bodies in the model—this is powerful but can be computationally expensive.
By default, all bodies are included in contact detection. For large or complex assemblies, it’s best practice to manually scope contact to regions where interaction is expected.
Default Body Interaction uses frictionless penalty contact. Friction can be enabled, but Body Interaction uses a simplified node-to-surface formulation, so dedicated Contact Regions are preferred when friction strongly influences behavior.
Reinforcement contact is used in special cases like concrete or tire modeling, connecting line bodies (like rebar or cords) to solids. Line mesh should match the solid mesh size for accuracy.
Bonded contact, though listed, is NOT supported in Explicit Dynamics when using “Body Interaction” option.
Reinforcement
Frictional
Frictional
Notes: In Explicit Dynamics, the solver automatically detects contact between nodes and faces across all bodies in the model—this is powerful but can be computationally expensive.
By default, all bodies are included in contact detection. For large or complex assemblies, it’s best practice to manually scope contact to regions where interaction is expected.
Default contact behavior is frictionless, but frictional contact is typically more realistic for physical simulations.
Reinforcement contact is used in special cases like concrete or tire modeling, connecting line bodies (like rebar or cords) to solids. Line mesh should match the solid mesh size for accuracy.
Bonded contact, though listed, is not supported in Explicit Dynamics.

## Slide 10: Contact
Contact can be more efficient than Body Interactions
  Provides a means for Bonded behavior, along with additional behavioral controls
Supported Types
  Bonded (no sliding - can be breakable)
  Frictional (sliding possible - static and dynamic friction coefficient)
  Frictionless (sliding possible - not recommended due to unrealistic behavior)
  Although listed, Rough and No Separation are NOT supported in Explicit Dynamics.
Scoping
  Contact: (known as Slave in LS-DYNA)
    Face
    Edge
  Target: (known as Master in LS-DYNA)
    Body
    Rigid Body (or faces of rigid body)
    Face
10
10

## Slide 11: Contact
When creating Contact scoped to Shell body Faces
  Frictional and Frictionless types require Contact Shell Face
  Required by Ansys Mechanical Software, NOT used by Ansys LS-DYNA software
  Select either Top or Bottom, doesn’t matter which
  Contact may occur on top and bottom as appropriate
Contact Formulations
  Penalty: Allows small penetration; fast and stable—ideal for impact and explicit analyses.
  Augmented Lagrange: Iteratively reduces penetration for higher accuracy in nonlinear contact.
  Normal Lagrange: Strictly enforces no penetration using constraint equations; less stable.
  Pure Lagrange: Enforces both normal and tangential constraints exactly; very accurate but computationally expensive.
11
11
Notes: Contact Enforcement Methods in Ansys Mechanical Software
These methods control how contact constraints are enforced between surfaces:
Penalty Method
  Allows small penetration between contact surfaces.
  Contact force = penetration × contact stiffness.
  Fast and stable, suitable for most nonlinear and explicit problems.
  Commonly used in Explicit Dynamics (LS-DYNA).
Augmented Lagrange
  Iteratively adjusts contact pressure to minimize penetration.
  More accurate than penalty but with slightly higher computational cost.
  Useful for static or quasi-static contact problems where convergence matters.
Normal Lagrange
  Enforces zero penetration strictly by introducing additional constraint equations.
  No penetration, but can increase system size and reduce numerical stability.
  Best for small deformation or linear contact cases.
Pure Lagrange (or Full Lagrange Multiplier)
  Enforces both normal and tangential contact constraints exactly.
  Very accurate but computationally expensive and prone to convergence issues.
  Rarely used in large deformation or impact analyses.

## Slide 12: Main Contact Types: Frictional Contact
Frictional contact is the preferred type:
  Most realistic, all real contacts exhibit friction
  Acts as an energy dissipator and stabilizes model
  Applies to both Contact and Body Interactions
  Can be velocity-dependent
    Requires a problem dependent choice of the Decay Constant
    Recommendation: Use Coulomb Friction, specify only the Friction Coefficient
tangential (friction) force normal contact force coefficient of friction
c = decay constant
v = Relative sliding velocity between surfaces
Notes: Introduction
In most engineering applications, contact between surfaces involves friction.
Therefore, frictional contact is the preferred and most realistic contact type to use in simulation.
It provides a more accurate representation of real-world behavior compared to frictionless or bonded contact.
Why Frictional Contact?
All real contacts exhibit friction: Surfaces, even when polished, have microscopic roughness that causes resistance to sliding.
Energy Dissipation: Friction acts as an energy dissipator, converting part of the kinetic energy into heat or deformation work.
Model Stabilization: The presence of friction often improves numerical stability by damping oscillations during contact events.
Where It Applies
Frictional contact can be applied in both:
  Contact interactions (between separate bodies or surfaces), and
  Body interactions (within parts that might deform and self-contact).
Velocity Dependence
In reality, friction can depend on the relative sliding velocity.
Some materials show decreasing friction with increasing speed (typical for lubricated or polymer interfaces).
In simulation, velocity-dependent friction can be modeled to capture this effect.
Decay Constant
The Decay Constant controls how friction transitions between static and dynamic values as sliding velocity increases.
Its value is problem-dependent — there is no universal default.
  Too low → unrealistic sudden slip.
  Too high → excessive damping and stiffness.
Always check sensitivity of results to this parameter when modeling complex contact behavior.
Recommended Practice
Use Coulomb Friction Model, the simplest and most commonly used approach:
where : tangential (friction) force = normal contact force = coefficient of friction
Typically, only the friction coefficient () needs to be specified.
Typical values:
  Steel on steel: 0.3–0.6
  Rubber on concrete: ~1.0
  Lubricated surfaces: < 0.1
Key Takeaways
Frictional contact = realistic, stable, and physically meaningful.
Acts as energy dissipator → helps convergence.
Use Coulomb friction unless a more advanced model is needed.
Choose decay constant carefully if modeling velocity-dependent behavior.
Introduction
In most engineering applications, contact between surfaces involves friction.
Therefore, frictional contact is the preferred and most realistic contact type to use in simulation.
It provides a more accurate representation of real-world behavior compared to frictionless or bonded contact.
Why Frictional Contact?
All real contacts exhibit friction: Surfaces, even when polished, have microscopic roughness that causes resistance to sliding.
Energy Dissipation: Friction acts as an energy dissipator, converting part of the kinetic energy into heat or deformation work.
Model Stabilization: The presence of friction often improves numerical stability by damping oscillations during contact events.
Where It Applies
Frictional contact can be applied in both:
  Contact interactions (between separate bodies or surfaces), and
  Body interactions (within parts that might deform and self-contact).
Velocity Dependence
In reality, friction can depend on the relative sliding velocity.
Some materials show decreasing friction with increasing speed (typical for lubricated or polymer interfaces).
In simulation, velocity-dependent friction can be modeled to capture this effect.
Decay Constant
The Decay Constant controls how friction transitions between static and dynamic values as sliding velocity increases.
Its value is problem-dependent — there is no universal default.
  Too low → unrealistic sudden slip.
  Too high → excessive damping and stiffness.
Always check sensitivity of results to this parameter when modeling complex contact behavior.
Recommended Practice
Use Coulomb Friction Model, the simplest and most commonly used approach:
𝐹_𝑟=𝜇⋅𝐹_𝑛
where 𝐹_𝑟: tangential (friction) force 𝐹_𝑛= normal contact force 𝜇= coefficient of friction
Typically, only the friction coefficient (𝜇) needs to be specified.
Typical values:
  Steel on steel: 0.3–0.6
  Rubber on concrete: ~1.0
  Lubricated surfaces: < 0.1
Key Takeaways
Frictional contact = realistic, stable, and physically meaningful.
Acts as energy dissipator → helps convergence.
Use Coulomb friction unless a more advanced model is needed.
Choose decay constant carefully if modeling velocity-dependent behavior.

## Slide 13: Main Contact Types: Bonded Contact
By default, Contact Type is Bonded and is penalty-based (relies on contact stiffness to “close” gap)
  Available between flexible and rigid bodies
Nodes tied to target side if their distance is within Maximum Offset
  Default : 1e-4 mm, too small for most models!
  Adjust Offset to a value 20-30% larger than physical gap, or
  Maximum Offset = 0.0 relates to a default offset distance, based on mesh size and shell thickness
Large gaps should be avoided
  Gaps cause problems in rigid body rotations
  Moments resulting from the offsets are not properly handled
Notes: Overview
By default, the Contact Type in most solvers (e.g., Ansys Workbench) is set to Bonded.
The Bonded contact assumes that two surfaces remain permanently attached — no separation or sliding is allowed once the contact is established.
It is implemented using a penalty-based formulation, which relies on contact stiffness to keep the surfaces “closed” or joined.
How It Works
The solver introduces a penalty stiffness between the contact and target surfaces.
This stiffness penalizes any relative motion normal or tangential to the interface, effectively keeping the nodes together.
The quality of this enforcement depends on how well the contact stiffness and offset parameters are defined.
Applicability
Bonded contact can be defined between:
  Two flexible bodies (typical structural assemblies), or
  A flexible body and a rigid body (e.g., mounting a component on a fixed support).
Node Association (Maximum Offset)
During contact detection, nodes on the contact surface are tied to the target surface if their distance is within the Maximum Offset value.
Default Maximum Offset: 1e-4 mm
  This value is too small for most models and may cause the solver to miss valid contact pairs.
Setting an Appropriate Offset
Adjust the Maximum Offset to be 20–30% larger than the actual physical gap between parts.
  Example: If the physical gap = 0.5 mm → set offset ≈ 0.6 mm.
Alternatively, if Maximum Offset = 0.0, the solver will use a default offset distance based on:
  The element size and
  The shell thickness (if applicable).
Modeling Recommendations
Avoid large initial gaps. Large or unrealistic gaps can:
  Cause contact detection errors.
  Lead to unstable or inaccurate rigid body rotations.
  Introduce unphysical moments due to incorrect offset geometry.
Always inspect the contact preview and verify contact regions visually before running the simulation.
Key Takeaways
Bonded contact = default, penalty-based, and useful for permanently joined interfaces.
Check and tune the Maximum Offset — default may be too small.
Avoid large gaps to ensure stable and accurate results.
Always verify contact behavior in pre-processing before solving.

## Slide 14: Contact Types, Applications and Formulations
Contact Type | Behavior | Example Use Case
Bonded | No separation or sliding | Welded parts, adhesive bonds
No Separation | Sliding allowed, no opening | Bolted joints under preload
Frictionless | Compression only, no shear transmission | Light contact without friction effects
Frictional | Includes shear resistance (with µ) | Friction-dependent joints
Rough | No slippage allowed | Spline or dovetail-type fits
Formulation | Characteristics & Use Cases
Penalty | Adds virtual spring resistance. Robust but less precise.
Augmented Lagrange | Balanced approach with higher accuracy and good convergence.
Normal Lagrange | Enforces strict no-penetration. Ideal for small contact areas.
Pure Lagrange | Fully constrained but can cause solver issues.
Here we can see type of available contacts and their possible applications and formulations that exist under either Body Connections and Contacts in Ansys Ansys Mechanical software Software [1].
To better understand how different contacts can affect your results, it’s highly recommended to study this example and watch the associated video [2].
Notes: [1] https://innovationspace.ansys.com/courses/wp-content/uploads/sites/5/2019/05/2.5.1-Introduction-on-contact_New_Template_Master.pdf
[2] https://ansyshelp.ansys.com/public/Views/Secured/corp/v251/en/pdf/ANSYS_Mechanical_APDL_Contact_Technology_Guide.pdf

## Slide 15: Example: Rigid Ball Hitting an Aluminum Thin Plate
Normal and Oblique Impacts

## Slide 16: Problem Description - Normal Impact
A rigid ball (D = 30 mm) impacts a deformable aluminum square plate (L = 200 mm) at 100 m/s from a 40 mm height in the Z direction. The plate is fixed is all DOF on all the four edges. The objective is to investigate how different contact definitions influence the simulation results. The thickness of the shell plate is considered at 2 mm.
Body Interaction vs. explicit Contact Definitions
Frictionless, Frictional, and Bonded contacts
The materials are modeled as follows:
Ball (Rigid Body – Steel)
  Density: 7850 kg/m³
  Young’s Modulus: 210 GPa
  Poisson’s Ratio: 0.3
  When defining the ball as a rigid body, the solver treats it as infinitely stiff, therefore the elastic modulus value is ignored.
Plate (Deformable Aluminum)
  Density: 2770 kg/m³
  Young’s Modulus: 71 GPa
  Poisson’s Ratio: 0.33
  Plasticity: Bilinear isotropic hardening
  Yield Strength = 250 Mpa
  Tangent Modulus = 2 GPa
40 mm

## Slide 17: Connection: Body Interaction (Normal Impact)
Open “BallPlate.wbpz file and locate the LS-DYNA system analysis A names” Ball Hitting Plate – normal”.
Click on Engineering Data and Geometry and familiarize yourself with them.
When ready, double click the “Model” option which prompts you into the mechanical project window and you can start analyzing the model set up including the geometry and material assignment. Under “Connection Group”, you see two options:
  Body Connection
  Contact
As mentioned before, we can’t use both at the same time. So, to explore their difference, we will suppress one at a time and use the other one. Let’s suppress contact first and use body interaction.
Run the simulation using “Frictional” with coefficient of friction of 0.3 first. Make note of your observations for the total deformation of the plate, maximum equivalent (von-mises) stress, and directional velocity of the ball in Z direction, as well as Kinetic/internal energy ratio.
Change the “Body Interaction” type to “Frictionless” and make note of your observations.
Compare the two scenarios and discuss.

## Slide 18: Results Interpretation
Averaged Values
Total deformation and Equivalent (Von-Mises) stress values reported in the tables in next slides are based on the averaged deformation and stress values across the plate
They represents the mean deformation and stress levels.
Best used for comparing overall structure response under different loading or boundary conditions.
We will use the averaged values throughout this example.
Maximum Values
Highest stress value found among all displayed result points (usually at nodes, elemental results selected).
Shows worst-case local stress anywhere in your model at that specific time/frame.
Highly localized — can come from one element, a single integration point, or a contact hotspot.
Physically, it identifies where yielding or failure might start, but can be sensitive to numerical noise.
Best used for: Comparing peak values (like “where does yielding initiate”), Safety checks, and evaluating whether your contact algorithm or mesh refinement affects local peaks.
Averaged Von-mises Stress = 265.5 MPa
Maximum Von-mises Stress = 549.5 MPa

## Slide 19: Answers: Body Interaction (Normal Impact)
Contact Type | Total Plate Deformation (Averaged) | Plate Equivalent (von- Mises) Stress (Averaged) | Plate Maximum Kinetic Energy | Plate Maximum Internal energy
Frictionless | 23.5 mm | 268 MPa | 148.9 J | 534.25 J
Frictional | 23.4 mm | 265.5 MPa | 149.5 J | 533.14 J
Question 1:
Why there is not much difference between the stress, deformation, and internal and kinetic energy values?
Total deformation, averaged equivalent (VM) stress contours and Kinetic versus Internal Energy plots for the frictionless scenario
Question 2:
Would using “Contacts” instead of using “Body Interaction” alter the results?
Share your ideas.
Now’s let’s find out in the following slides
NOTE: Total deformation and Equivalent (Von-Mises) stress values reported in the table below are based on the averaged deformation and stress values across the plate.
Notes: Notes regarding the stress and deformation values:
When to use maximum (von-Mises) Stress
This is the highest stress value found among all displayed result points (usually at nodes, unless you select elemental results).
It tells you the worst-case local stress anywhere in your model at that specific time/frame.
It is highly localized — can come from one element, a single integration point, or a contact hotspot.
Physically, it identifies where yielding or failure might start, but can be sensitive to numerical noise.
Comparing peak impact response (like “where does yielding initiate”).
Safety or failure checks (compare to yield strength).
Evaluating whether your contact algorithm or mesh refinement affects local peaks.
Answer to question 1:
1. The impact is dominated by normal (perpendicular) forces Most of the kinetic energy and momentum transfer occur in the normal direction — perpendicular to the plate surface.
The tangential (frictional) forces are much smaller because:
2. The normal pressure dwarfs the tangential shear
Contact pressure during such an impact easily reaches hundreds of MPa to a few GPa
Even with μ = 0.3, the tangential stress is only about 30 % of the normal pressure — and only acts over part of the contact area. The normal momentum exchange dominates both deformation and rebound.
3. Very brief contact time = limited frictional slip
The impact lasts only microseconds, so there isn’t enough time for large tangential slip or heating. Frictional work scales roughly with contact time × tangential velocity × shear stress, all of which are small here.
Answer to question 2:
Using contacts might slightly change some results due to the different formulation

## Slide 20: Connection: Contact
Now suppress “Body Interaction” and use the “Contact” option under Connections.
Run the simulation using “Frictional” contact with coefficient of friction of 0.3 first. Make note of your observations for the total deformation of the plate, maximum equivalent (von-mises) stress, and directional velocity of the ball in Z direction, as well as Kinetic/internal energy ratio.
Change the “contact” type to “Frictionless” and make note of your observations. Finally change the contact type to “Bonded” (This option was not available when using Body Interaction)
Compare the three scenarios and discuss.
Finally report if you noticed any significant difference between the frictionless, and frictional cases when using body interaction versus contacts?

## Slide 21: Answers - Contact (Normal Impact)
Contact Type | Total Plate Deformation (Averaged) | Plate Equivalent (von- Mises) Stress (Averaged) | Plate Maximum Kinetic Energy | Plate Maximum Internal energy
Frictionless | 23.4 mm | 282 MPa | 147.64 J | 532 J
Frictional | 23.4 mm | 280.5 MPa | 148.67 J | 531.31 J
Bonded | 0 | 0 | 0 | 0
Question 1:
Explain the similarities and differences between the values for the 3 contact scenarios?
Impact simulation using Bonded contact (Why nothing happens!!!??)
Question 2:
Comparing the results for frictionless and frictional “Contact” scenarios with same ones from “Body Interaction”, how do you explain the differences?
NOTE: Total deformation and Equivalent (Von-Mises) stress values reported in the table below are based on the averaged deformation and stress values across the plate.
Notes: Answer to question 1:
The impact is governed by normal pressure, not sliding → so frictional effects are negligible.
When a rigid ball hits a plate at high speed (100 m/s), most of the interaction is normal to the surface — the tangential (sliding) motion is small.
In both frictionless and frictional contact, the normal contact stiffness and penetration behavior dominate.
The friction coefficient only affects tangential motion (sliding resistance), not the normal impact.
Since the tangential velocity component is near zero (purely normal hit), friction doesn’t have a significant role — that’s why stress, deformation, and energy values are almost identical between the two.
Using Bonded contact is essentially not enforcing any contact here since, Bonded contact in LS-DYNA is meant to connect two surfaces so they move together.
But it cannot “stop penetration” if one surface is moving fast or is a solid body with high velocity — LS-DYNA needs a proper contact definition that can handle impact/penetration.
Answer to Question 2:
Why deformation and energies are nearly identical
The ball is rigid → almost all kinetic energy is transferred to the plate in the same way, regardless of subtle differences in the contact algorithm.
Deformation and internal energy integrate over the plate → they are dominated by the overall impact, not by small local differences.
Why max von Mises stress differs
Max von Mises stress is local:
  Occurs at the contact interface or at sharp gradients in the mesh.
  Body Interaction uses averaged or approximate contact pressures, so it may slightly underestimate or overestimate the peak stress.
  Frictional/frictionless contact resolves local contact pressures more accurately, producing a slightly higher or lower max stress.
For rigid-on-deformable impacts, using Body Interaction is fine if you only care about global quantities (deformation, energy).
For local stresses or failure predictions, you should use explicit contact — even frictionless — because it resolves the contact interface more accurately.

## Slide 22: Practice: Rigid Ball Hitting a Steel Thin Plate – Oblique Impact
Remember that we discussed that when ball impacted the plate in normal direction only, since the frictional effects were not that much, we did not see much difference between the frictional and frictionless contacts. To verify this and also investigate the effect of friction on results, let’s do an oblique impact where the resultant velocity is still 100 m/s but is hitting the plate at 45 degrees in y-z plane. The velocity components will be vy = -70.711 m/s and vz = -70.711.
Total deformation, equivalent (VM) stress contours and Kinetic/Internal Energy ratio plot for the frictionless scenario

## Slide 23: Exercise: Rigid Ball Hitting a Steel Thin Plate – Oblique Impact
Duplicate the original system analysis for normal impact
Update the velocity components based on the values provided in the last slide.
Run the simulation first using “Body Interaction” – Alternate between frictionless and frictional
Suppress “Body Interaction” and run it using “Contact” – Alternate between frictionless and frictional.
Report maximum deformation, equivalent (VM) stress, kinetic energy, and internal energy for both cases (Body Interaction and Contact)
Compare the results between Body Interaction and Contact.
Share observations and reasons for similarities and differences

## Slide 24: Answers – Contact and Body Interaction (Oblique Impact)
Frictionless
Connection type Type | Total Plate Deformation (Averaged) | Plate Equivalent (von- Mises) Stress (Averaged) | Plate Maximum Kinetic Energy | Plate Maximum Internal energy
Contact | 16.63 mm | 598 MPa | 52 J | 332.68 J
Body Interaction | 16.65 mm | 610 MPa | 52.47 J | 336.71 J
Connection type Type | Total Plate Deformation (Averaged) | Plate Equivalent (von- Mises) Stress (Averaged) | Plate Maximum Kinetic Energy | Plate Maximum Internal energy
Contact | 17.9 mm | 667 MPa | 53.47 J | 335.68 J
Body Interaction | 18 mm | 655 MPa | 54.08 J | 339.78 J
Note:
For simple geometries where two bodies come into contact, both Body Interaction and Contact options typically produce very similar results. However, for complex geometries—such as cases where edges contact other edges or surfaces, or multiple contact types coexist within a region—the Body Interaction option may not accurately capture local contact behavior. In such cases, relying on the dedicated Contact definition is recommended to ensure proper contact detection and accurate force prediction.
NOTE: Total deformation and Equivalent (Von-Mises) stress values reported in the table below are based on the averaged deformation and stress values across the plate
Frictional (coefficient of friction = 0.3)
Notes: Deformation, total kinetic energy, and total internal energy: very similar between Body Interaction and explicit Contact (differences typically small, < ~5–10%) because these are global/integral quantities dominated by total momentum and energy transfer from the rigid ball to the plate.
Max von Mises stress (local): larger differences than the global quantities — expect explicit Contact (frictional) to show the largest local VM peaks, Body Interaction to be slightly different. Differences commonly range from a few percent up to ~10% (or more with coarse meshes or strong tangential
Oblique impact adds a tangential component of momentum. With friction:
More tangential force is transmitted into plate (shear), increasing local deviatoric stress → higher von Mises.
Friction converts some tangential translational KE into plate in
Max von Mises stress is controlled by local contact pressure distribution and shear stresses at the interface.
Explicit contact resolves contact pressure and, if frictional, frictional shear stress — creating localized stress concentrations and a possibly higher VM peak.
Body Interaction is a simplified enforcement. It typically approximates normal/tangential interactions and may average or smooth local pressures, so local peaks differ slightly.
ternal energy (local plasticity) and frictional heating — changing local VM more than global energies.
The rigid ball’s kinetic energy and the plate’s capacity to absorb energy are governed primarily by the normal component of the impact and the plate stiffness. Both Body Interaction and explicit Contact enforce momentum exchange so the integral energy absorption is similar.

## Slide 25: Contact Properties
Body Interaction, Frictional Contact

## Slide 26: Contact Properties
From the LS-DYNA Pre Toolbar, Contacts and Body Interactions can be modified by a Contact Property object
Allows advanced settings not available in the Details of the contacts and body interactions
  Type
    Eroding
    Forming
    Interference
    Mortar
  Common Controls
    Birth/Death
    Viscous damping coefficient
  Advanced Controls
    Optional Thickness effects
Notes: Key Concepts to Emphasize:
Purpose of Contact Property Objects: Used to go beyond default contact options and fine-tune how parts interact during simulation, particularly under nonlinear or high-deformation conditions.
Types of Contact Behaviors:
  Eroding: Useful when elements are expected to be deleted during failure.
  Forming: Designed for metal forming operations.
  Interference and Mortar: Provide alternatives for handling penetration and enforcing contact constraints with different numerical strategies.
Common Controls:
  Birth/Death Options: Enable or disable contact interactions at certain times during simulation.
  Viscous Damping: Adds numerical damping to stabilize contacts and reduce oscillations.
Advanced Controls:
  Thickness Effects: Account for the actual physical thickness of shell or solid parts in contact calculations, which can influence contact force distribution.
Teaching Tips:
Use a real-world example like metal stamping or crash simulations to demonstrate why adjusting contact settings is necessary.
Provide a side-by-side comparison of simulation results with and without advanced contact settings.
Emphasize the computational cost vs. accuracy trade-off when using detailed contact definitions.

## Slide 27: Contact Properties (Body Interactions)
Type changes the Formulation and therefore contact options
Type for Body Interaction
  Program Controlled
  General (for beam-to-beam contact only)
  Eroding (for element erosion only)
  Single Surface (=Program Controlled)
  Mortar (more accurate with higher order elements)
Formulation shows the resulting keyword option.
Upon choosing the “contact Properties” Type, the formulation type appears below it. This refers to formulation keyword used in stand-alone LS-DYNA [1]
[1] https://ftp.lstc.com/anonymous/outgoing/web/LS-DYNA_manuals/DRAFT/DRAFT_Vol_I.pdf
Notes: Program Controlled
  Default and most commonly used setting.
  LS-DYNA automatically selects the most suitable contact formulation based on the model setup (e.g., surface-to-surface or node-to-surface).
  Recommended for general use when you’re not sure which formulation to choose.
General (for beam-to-beam contact only)
  Specialized contact type that handles beam-to-beam or wire-like interactions (e.g., cables, stents, reinforcement wires).
  Uses an algorithm optimized for slender bodies where contact occurs along lines instead of surfaces.
Eroding (for element erosion only)
  Used when elements may fail or be deleted during the simulation (such as in impact, blast, or fracture cases).
  Automatically removes contact contributions from eroded elements, preventing instability or “ghost” forces.
Single Surface (= Program Controlled)
  Equivalent to program-controlled single-surface contact, where multiple parts in a group can contact themselves or each other.
  Useful in scenarios like sheet metal folding or crash simulations where surfaces can fold and re-contact.
Mortar
  A high-accuracy contact formulation especially effective when using higher-order elements (like quadratic shells or solids).
  Provides better pressure continuity and less penetration error, but at higher computational cost.
  Recommended for precision-driven analyses or simulations involving curved or refined geometries.
4. Formulation Keyword
When you select a Contact Type, LS-DYNA automatically sets the Formulation, which appears below it in the GUI.
This Formulation corresponds to the keyword name that LS-DYNA uses in the input deck (for example, *CONTACT_AUTOMATIC_SURFACE_TO_SURFACE or *CONTACT_MORTAR).
So, the GUI is essentially a front-end selector that determines which contact keyword LS-DYNA will use internally.

## Slide 28: Contact Properties (Frictional Contact)
For Frictional contact, four types are available:
  Eroding
  Forming (Flexible body is formed using rigid tool bodies)
  Interference
  Mortar
Forming contacts are used in forming simulations
  Must be used for shell adaptive mesh refinement
  Forming contacts ignore tool shell thickness (can be used with solids too)
  Ensure that tool surface normal points towards the workpiece (segment orientation depends on surface normal)
  Asymmetric contact is recommended (one-way contact)
  Viscous damping (damping ratio), 20% typical
    Damps sliding motion between contact and target
k
c
Notes: When modeling frictional contact in LS-DYNA, there are four main types you can choose from, each suited for different simulation scenarios:
Eroding Contact – Used when one or both contacting bodies can undergo element erosion (e.g., in impact or failure simulations).
Forming Contact – Designed for metal forming processes where a flexible workpiece interacts with rigid tools.
Interference Contact – Handles initial geometric interference between parts, often used to simulate press-fit or preloaded assemblies.
Mortar Contact – A more mathematically accurate contact formulation that provides smoother pressure distribution, especially for high-quality contact in structural applications.
2. Forming Contact Details
Forming contacts are particularly important in sheet metal forming and adaptive meshing scenarios.
Used in Forming Simulations: It’s the preferred option for operations like stamping, deep drawing, or bending where a sheet or flexible body is deformed by rigid dies or punches.
Supports Adaptive Mesh Refinement (AMR): If your model uses adaptive meshing for thin shells, forming contact must be used—other contact types are not compatible with AMR.
Ignores Tool Shell Thickness: The contact algorithm treats the tool as a surface with zero thickness, regardless of the actual mesh. This is particularly useful when using rigid shell tools, but forming contact can also be used with solid tools.
Tool Surface Normal Orientation: Always make sure the tool’s surface normal points toward the workpiece.
  This ensures correct contact detection and force transfer.
  Remember that the segment orientation depends on this normal direction—if it’s reversed, contact may fail.
Asymmetric (One-Way) Contact: Recommended for forming simulations where only the tool acts on the workpiece, not the other way around.
  For example, a rigid die can press the sheet, but the sheet shouldn’t influence the die motion.
  This helps reduce unnecessary computation and avoids numerical instabilities.
Friction and Damping Settings
Viscous Damping: In forming simulations, some viscous damping is often applied to stabilize sliding and reduce oscillations during contact.
  Typical damping ratio: 20%
  It helps damp the sliding motion between contact and target surfaces.

## Slide 29: Contact Properties (Frictional Contact)
Interference contacts are used in press-fit simulations that are initially pre-stressed
  Without interference contacts, LS-DYNA performs nodal interference checks at the start of the simulation to move the nodes and eliminate the interference (stress-free)
  With interference contacts, contact forces develop to remove the interferences; pre-stresses the part
  Can be used during dynamic relaxation
    Dynamic relaxation is when stresses and deformation are initialized to model a preload (gravity, bolt pretension, etc.)
    Stiffness Scale Factor – penalty stiffness scaled gradually until it reaches full value (factor =1)
    Interference End Time – Consistent with Pseudo End Time of Dynamic Relaxation
  Or, Can be used during the transient calculation
    Interference End Time – relative to End Time of simulation

## Slide 30: Example: Contact Properties (Eroding)
Using the ball hitting a plate example, let’s change the plate material to glass, which behaves as a brittle material. Ansys LS-DYNA software will automatically capture the appropriate material response based on the defined material model—showing realistic fracture, element erosion, and material removal as the impact occurs.
However, when adjusting Contact Properties, be cautious: certain contact settings may override or mask element erosion effects, leading to unrealistic results or unaccounted interference between bodies.

## Slide 31: Contact Results Output
In LS-DYNA in Ansys Workbench, you can plot the contact forces after the solution is completed. However, If using “Body Interaction” instead of conacts, you need to set things up before starting to solve the problem for the solver to output “Body Interaction Forces”. The following shows the processes for both scenarios:
Plotting Contact Forces in Ansys Mechanical Software
  Solution Information > Result Trackers > Contact Force
    Select Contact Region
    Select Orientation
  Can be requested before or after solving
Plotting Body Interaction Forces in Ansys Mechanical Software
  Before solving, LSDYNA Pre Toolbar > Trackers > Body Contact Tracker
    Select body
  Solution Information > Result Trackers > Contact Force
    Select Contact Region (Body Interaction)
    Select Orientation
Plotting Contact Forces
Plotting Body Interaction Forces

## Slide 32: Exercise: Plotting Contact Forces for Ball Hitting Plate
Use either the normal or oblique impact of the rigid ball on the aluminum plate, and practice the instructions in the previous slide for plotting the contact forces.
What differences do you observe between the two scenarios or why?
Notes: Upon plotting the contact forces using the Body Interaction Option versus the frictional contact, we see a slight difference between the peak values of the contact forces. This could be attributed to the differences in the contact formulation and numerical treatment between the two output options. Body Interaction output often reports interaction-level forces (integrated over contact couples and influenced by contact smoothing, penalty/contact stiffness, and master-slave selection), whereas the frictional contact output reports local contact forces computed from the friction law at contact integration points.
Step-by-step processes to plot these forces for both scenarios and the output results are shown in the next 2 slides

## Slide 33: Exercise: Contact Force Plots – Possible Answer
Body Interaction Scenario:
Make sure contact is suppressed and only “Body Interaction” is enabled. Ou can choose either “Frictional” or “Frictionless”. Here I chose “Frictional” with coeff = 0.3
Click on “LD-DYNA” in the outline window and then go the top toolbar and click on “LSDYNA Pre” , go to “Trackers” from the drop-down menu, select “Body Contact Tracker”.
Next go to “Solution Information”  Right click  and choose “Contact Force”- under scoping method choose “Body Interaction”
This will plot the contact force between the two bodies

## Slide 34: Exercise: Contact Force Plots – Possible Answer
Contact Scenario:
Make sure Body Interaction is suppressed and only “Frictional Contact” is enabled.
Solve the problem.
Next go to “Solution Information”  Right click  and choose “Contact Force”- under scoping method choose the defined contact for “Contact Region” and Target for “Contact Side”. Choose Z axis for the direction
This will plot the contact force in the z-direction between the plate and the ball

## Slide 35: Contact Analysis Best Practices
Large deformation analysis often requires manual selection of contact surfaces
Turn off “Generate Automatic Connection On Refresh”
  If Scope Method is Automatic, suppress the contact if it’s not needed
  Otherwise, the contact will be added again after refresh
If a Body Interaction is not needed, suppress the Body Interaction
  Otherwise, it is added again after refresh
Use friction
Adjust Maximum Offset for bonded contact, take zero as default
For a first run, try asymmetric contact
  Rigid bodies must be target (otherwise, Flip Contact/Target)
  The finer mesh should be contact
  Sharp edges or curved geometry should be contact
  Overlapping geometry should be target

## Slide 36: Contact Analysis Best Practices
If an LS-DYNA analysis fails, it’s quite likely related to contacts specially in complex geometries
  Review target and contact selection and avoid complex contact situations
    Try to figure out where the problem arises
  Switch to Soft Constraint or Segment Based or vice versa
  Adjust (reduce) penalty stiffness
  Think about symmetric/asymmetric or flip contact and target
  Switch to non-automatic contact (keyword snippet) – problem dependent
  Reduce analysis time step (reduce safety factor from 0.9 to a smaller value)
  Refine mesh

## Slide 37: Contacts Quiz
Question 1:
In LS-DYNA in Ansys Workbench contact definitions, which statement correctly describes the effect of penalty stiffness?
Increasing stiffness improves accuracy and has no effect on stability
Low stiffness leads to instability, while high stiffness increases computational efficiency
Low stiffness causes excessive penetration, while high stiffness reduces time step size and may cause oscillations
Penalty stiffness has no significant effect on accuracy or computation
Question 2:
In an Explicit Dynamics system within Ansys Workbench, which of the following statements is true about default connection behavior?
Default connection type is Contact, using the Augmented Lagrange formulation
Default connection type is Body Interactions, which automatically detects contact between all parts
Default connection type is Frictional Contact, applied only to scoped regions
Default connection type is Bonded Contact, supported for all Explicit analyses
Question 3:
A user finds that their Ansys LS-DYNA simulation fails to converge due to unstable contact behavior in a complex assembly. Which of the following strategies is most appropriate to try first?
Increase penalty stiffness and enable symmetric contact
Reduce penalty stiffness and review target/contact orientation
Change all contacts to bonded and refine mesh globally
Add more friction to increase sliding resistance
Notes: Question 1:
✅ Correct Answer: C Explanation:
Penalty stiffness controls penetration. Too low → large penetrations (inaccuracy); too high → numerical oscillations and very small time steps (instability).
Question 2:
✅ Correct Answer: B Explanation:
The Explicit Dynamics module uses Body Interactions as the default connection type, automatically detecting contact between bodies, though this can be computationally expensive.
Question 3:
✅ Correct Answer: B Explanation:
Unstable contacts often result from poor stiffness tuning or incorrect master/slave assignment. Reducing penalty stiffness and reviewing contact/target setup usually helps stabilize the model.

## Slide 38: Postprocessing Results in Ansys Mechanical Software

## Slide 39: Visualizing Results
Upon running a simulation in Ansys Workbench LS-DYNA, since it is using the LS-DYNA solver, It will create many different types of results in the following TWO categories:
  d3plot for contour results
  ASCII for time history
Many of the such results can be visualized directly and automatically in the Ansys Mechanical workspace and under the Solution tab.
However, for some very specific ones, you might still need to open the LS-PrePost which is the postprocessing tool for stand-alone LS-DYNA (This is out of the scope of this course).
In the following slides, we will show what how d3plots and ASCII time history results can be visualized in Ansys Mechanical software.
Keep in mind that for visualizing some results, you MUST do some preparation and set up BEFORE running the simulation, otherwise you will not be able to see those results.

## Slide 40: Postprocessing Ansys LS-DYNA results in Ansys Mechanical software (1)
Ansys Mechanical software automatically reads d3plot files after solving
  If you set up and did your simulation in LS-DYNA in Ansys Workbench, the results will be automatically available under “Solution” tab.
  If you did the simulation using the standalone Ansys LS-DYNA tool, then you can use Manual d3plot import which is available from the Solution toolbar – see below. This is for when you want to visualize the results of a standalone Ansys LS-DYNA simulation in Ansys Mechanical software.

## Slide 41: Postprocessing Ansys LS-DYNA results in Ansys Mechanical software (2)
Major differences between advertised options and supported options can be found in Solution
  This is related to different result file structure and available results
  Some results require postprocessing in LSPP (stand-alone LS-DYNA Pre-Post Processing)
  Available results also depend on Output Controls in Analysis Settings
  Right click on “Solution” tab in the outline tree and choose your desired variable to be visualized. Look at the contours, the maximum and minimum values, etc.

## Slide 42: Postprocessing Ansys LS-DYNA results in Ansys Mechanical software (3)
Supported results
  Deformation (displacement, velocity, acceleration)
  Stress and Linearized Stress
  Probes: displacement, velocity, acceleration, stress
  Stress Tool
  User Defined Results via Worksheet
Not supported
  Elastic strain (toolbar or worksheet)
  Energy
  Damage
  Coordinate Systems
  Snippets
  Probes other than displacement, velocity, acceleration
  Toolbox items other than Stress Tool

## Slide 43: Postprocessing Ansys LS-DYNA results in Ansys Mechanical software (4)
Displaying Time History from LS-DYNA ASCII files
  Most results can be inserted from the Solution Information Result Trackers toolbar before or after the solution.
  Some results like “Time Increment” and “Energy Summary” are already predefined under Solution Information.
Notes: Bndout geht nicht?
Letztlich sollte man postprocessing in LSPP machen.

## Slide 44: Postprocessing Ansys LS-DYNA results in Ansys Mechanical software (5)
Displaying Time History from LS-DYNA ASCII files
  Inserting some LS-DYNA ASCII results after the solution requires having used a Result Tracker (LS-DYNA Pre) before solving
  Specifically, information in the NODOUT file (deformation, position, velocity, acceleration)
  For noisy results, like accelerations or forces, a Butterworth filter can be applied.
2
1
Under the LSDYNA Pre tab, you find:
Result Tracker tool that "Control which nodes are output into the time histories databases."
This shows the dropdown menu under Result Trackers where you can choose:
Deformation, Position, Velocity Acceleration
3
Snapshot of a Result Tracker's Details for “Directional Acceleration”:
Scope: 1 Node
Type: Directional Acceleration along Y-axis
Minimum / Maximum Values displayed
Notes: Displaying Time History from LS-DYNA ASCII Files
Key Points:
Inserting LS-DYNA ASCII results after the solution:
  Some LS-DYNA results can only be postprocessed if you planned ahead before solving.
  You must define a Result Tracker (LS-DYNA Pre) before running the simulation.
  This step ensures that the solver writes out the required time history data (like node displacement, velocity, etc.) to the appropriate files.
What Data is Needed:
  Time history data is stored in the NODOUT file.
  The NODOUT file contains:
    Deformation (Displacement)
    Position
    Velocity
    Acceleration
Filtering Noisy Results:
  Results such as acceleration and forces can be quite noisy.
  To manage this, apply a Butterworth filter (a type of signal filter that smooths out noise while preserving the signal).
  Filter settings include:
    Type: Butterworth
    Cut Frequency: e.g., 2000 Hz

## Slide 45: Postprocessing Ansys LS-DYNA results in Ansys Mechanical software (6)
Displaying Contact results
  LS-DYNA in Ansys Workbench exports contact results into input.intfor only for contacts, not for Body Interactions
    Body Interactions don’t support keyword snippets
  Supported results using LSDYNA Post Contact Tool
    Normal pressure
    Shear stress
    Nodal force (vector plot)

## Slide 46: Animation of State Variables
When animating state variables in Ansys Workbench tool (e.g., deformation), you may notice motion occurring before actual contact between bodies. For example, in a ball-impacting-plate simulation, you might notice:
  Apparent plate deformation occurs before physical contact due to result interpolation.
  This is Caused by limited output frames
  It’s NOT a modeling or physics error — only a post-processing display artifact
  This is common in high-speed impact simulations where output time steps are coarse
  ✔ Fix: Adjust the number of animation frames to match the actual result steps-
  You can do this by toggling between the two options on the animation pane, “Distributed” and “Results Sets” – Choosing “Results Sets” option will adjust the number of frames, so the deformation happens right when ball hits the plate.
  Look at the picture and the animation provided for reference as how to do this.
Distributed
Result sets
Notes: Ansys Mechanical software interpolates and/or smooths results between output frames when playing an animation. If the animation has more frames than you have actual solution output steps, the software creates intermediate geometry states — which can make the plate look like it deforms before the ball contacts it. Reducing/increasing frames to match the actual output frequency removes the interpolated (fake) frames and the early deformation disappears.
Looking at the animation, we see when the “distributed” option is chosen on animation pane, the number of frames might be at 100 and hence the deformation happens before the ball physically touches the plate. Keep in mind that the plate is not actually deforming before impact — it’s a visual artifact from explicit contact enforcement & animation smoothing.
However, changing the setting to “Results set” will automatically picks the appropriate number of frames which shows the physical phenomenon as it should happen in reality.

## Slide 47: Summary
There are many different result files produced during the LS-DYNA run
  d3plot for contour results
  ASCII for time history
Make sure to output the desired results, i.e. think about ASCII files and Result Trackers
  LSDYNA Pre Result Trackers for nodal displacement, velocity, acceleration (nodout)
  LSDYNA Pre Body Contact Tracker for Body Interaction contact forces (rcforc)
  Solution Information Result Trackers for glstat, matsum, rcforc, spcforc, etc.
The Worksheet allows access to additional user defined results
LS-PrePost (LSPP) extends the LS-DYNA capability and offers full-featured post processing
  Additional training on LSPP can be found in the Anys Learning Hub
    Introduction to Ansys LS-DYNA
    Ansys LS-PrePost Advanced

## Slide 48: Quasi-Static Analysis

## Slide 49: Quasi-static Analysis
Static | Quasi-static | Dynamic
Structural Problems | Metal Forming | Impact Problems
Static | Quasi-static | Dynamic
Structural Problems | Metal Forming | Impact Problems
IMPLICIT METHODS
EXPLICIT METHODS
LS-DYNA
Notes: Ansys LS-DYNA is capable of doing implicit and explicit analysis, but it’s best known for it’s explicit dynamic modeling capabilities. If a load is applied very slowly, the acceleration (inertia) and damping effects become negligible, allowing the dynamic equation to reduce to a quasi-static form. This is why slow processes—like metal forming, creep, or gradual structural loading—are ideal candidates for quasi-static analysis. Dynamic simulations require very small time steps to satisfy the Courant-Friedrichs-Lewy (CFL) condition for numerical stability, which can make them computationally expensive. In contrast, quasi-static simulations allow for larger time steps through techniques like mass scaling or implicit solvers, but to preserve accuracy, loads must be applied very gradually, often resulting in longer total run times.

## Slide 50: Quasi-static Analysis
A solution of the equation of motion be used for quasi-static problems
Applying a load very slowly would yield the following:
So you get a solution which is equivalent to the quasi-static one!
If the process is inherently slow (e.g., metal forming, structural loading, or creep behavior), the inertia and dynamic effects (vibrations, oscillations) should be minimal.
Dynamic simulations require small time steps (CFL) to maintain numerical stability -----> computationally expensive.
Quasi-static allows for increase in the time step (through implicit solvers or mass scaling), Applying loads slower, reduced inertia, but end time increases!
A dynamic simulation might introduce unnecessary oscillations, leading to misleading results.
Dynamic involve high deformation or complex contact and can be unstable while quasi-static more stable (implicit).
≈ 0
≈ 0
Notes: This slide explains how quasi-static solutions can be obtained from the general equation of motion by carefully controlling the load application rate.
If a load is applied very slowly, the acceleration (inertia) and damping effects become negligible, allowing the dynamic equation to reduce to a quasi-static form. This is why slow processes—like metal forming, creep, or gradual structural loading—are ideal candidates for quasi-static analysis.
Key point: You’re still solving the equation of motion, but under conditions where inertial forces (𝑀𝑎) are nearly zero, so the solution resembles that of a static analysis.
Dynamic simulations require very small time steps to satisfy the Courant-Friedrichs-Lewy (CFL) condition for numerical stability, which can make them computationally expensive.
In contrast, quasi-static simulations allow for larger time steps through techniques like mass scaling or implicit solvers, but to preserve accuracy, loads must be applied very gradually, often resulting in longer total run times.
One risk of using a dynamic simulation for a slow process is that it can introduce artificial oscillations or instability, which do not reflect the true physical behavior—this could mislead interpretation of the results.
Also note that dynamic problems often involve large deformations or complex contact interactions, which can be less stable than quasi-static problems, especially if using explicit solvers.

## Slide 51: Verification of quasi-static analysis
Energy Ratio Plot: For explicit quasi-static conditions, as a rule of thumb the kinetic energy should remain much lower than internal energy — typically < ~5%, and ideally ≤ 2–5% during most of the solution. A graph displaying kinetic energy and internal energy over time, highlighting periods where the kinetic energy remains below 2% of the internal energy, indicating quasi-static behavior. We anticipate that this will be the case for most of the analysis time [1]
Force Equilibrium Chart: A plot showing applied forces versus reaction forces in the x, y, and z directions over time, demonstrating the maintenance of equilibrium throughout the analysis.
Animation Snapshot: A still image or short clip from an animation of the simulation results, showing smooth, non-oscillatory deformation, supporting the quasi-static assumption.
2%
Notes: https://www.sciencedirect.com/science/article/pii/S0379711217302473
Note: While several resources may indicate that it’s appropriate to have Kinetic Energy / Internal Energy ratio between 5-10 % for the analysis to be verified as quasi static, we should keep in mind that this could be different for different applications and analysis types and to be on the safe side, one should consider 2% as the safe lower benchmark to evaluate the energy ratio results.

## Slide 52: Kinetic to Internal energy Ratio
fast loading slow loading
Rescaling the y-axis for better visualization
Energy Ratio = 2%
Energy Ratio = 2%
Notes: This slide shows how the rate of load application impacts the distribution of kinetic and internal energy in a simulation.
On the left, we have a graph where the load was applied too quickly.
  Notice the significant spikes in kinetic energy throughout the simulation. These are a result of inertia effects becoming prominent due to fast loading.
  The kinetic/internal energy ratio in this case exceeds 2-5%, which means the system is experiencing dynamic behavior, not quasi-static. These oscillations can distort the physical accuracy of the results. While 5% can also be considered a threshold for quasi static, it’s best to run the data against the 2% threshold.
On the right, the graph corresponds to a simulation where the load was applied very slowly.
  Here, the kinetic energy remains minimal—just a small fraction of the internal energy throughout the process.
  The energy ratio stays below 1%, which is a key indicator that quasi-static conditions are satisfied and inertial effects are negligible.
This contrast clearly demonstrates the importance of monitoring energy plots to assess the nature of your simulation. If you're targeting a quasi-static response:
  Make sure the kinetic energy remains much lower than the internal energy.
  If you see energy spikes like in the left plot, consider slowing the load application or using mass scaling/implicit solvers to dampen dynamic effects.

## Slide 53: Equilibrium of Applied load & Reaction forces
For static analysis, applied loads and reaction force must be in equilibrium
Inertia forces are responsible for the difference between load and reaction
Time scaling is required to run quasi-static analysis more efficiently
End time must be chosen by the user to
  Achieve short run times
  Reduce/eliminate dynamic effects
User must verify if the analysis behavior is quasi-static
  Kinetic energy is < 2-5% of internal energy for most of the analysis time
  Check force equilibrium in all directions for applied and reaction forces
Finally, the only proof is a run with an increased end time
Fast Loading - Impact
Very slow loading – Quasi-static
Notes: In a static or quasi-static analysis, the applied loads and the reaction forces should be in equilibrium. Any difference between them is due to inertia forces, which are characteristic of dynamic behavior.
Since we're using explicit dynamics to approximate a quasi-static response, we need to scale the time appropriately. That means choosing a sufficiently long end time to apply the load slowly, helping to suppress inertia effects.
The end time must be carefully selected by the user to achieve two goals:
  Reduce or eliminate dynamic effects (like oscillations or energy spikes).
  Keep simulation runtime efficient—not too long, but long enough to avoid artificial dynamics.
But how do we verify that our simulation truly behaved quasi-statically?
  First, check that the kinetic energy stays below 5% of the internal energy for most of the simulation time—this is a strong indicator that inertia is negligible.
  Second, check that the sum of applied and reaction forces are in balance across all directions (x, y, and z). Imbalance suggests the presence of inertia forces, i.e., a more dynamic response.
Finally, the most definitive check is to re-run the simulation with a longer end time. If the results don't change significantly, it confirms that quasi-static conditions were achieved in your original run.

## Slide 54: Verifying Quasi-static Analysis: 3-point bending example
In the example on the right, a 3-point bending problem is shown. The simulation were run for a longer duration of0.5 seconds and its quasi-static behavior was verified for the longer duration analysis in terms of kinetic/internal energy ratio and contact force equilibrium as shown.
3-point bending (Impact on Tubes)– problem set-up
Quasi-static analysis – Contact force equilibrium
Kinetic/Internal Energy Ratio <2%
Velocity Profile – for longer duration simulation for 0.5 ms
Notes: Simulation of two nested tubes which are hit by an impactor with an initial velocity of 30 m/s.
Two nested tubes are hit by an impactor with an initial velocity of 30 m/s
  Tubes are connected at the outer ends through caps
  Supported by rotatable cylinders (3-Point Bending)
Symmetry used
Loading :
A displacement of -300 mm, duration of 0.50 s, and ramp duration of 0.05 s creating a step load

## Slide 55: Sheet Metal Punching Example
Energy Summary
Thickness Distribution
Notes: This slide explores how to simulate sheet metal punching using Ansys Explicit Dynamics, with a focus on capturing quasi-static behavior.
The goal of the analysis is to represent gradual deformation without introducing artificial dynamics.
Key recommendation: apply displacement slowly using velocity or load curves to avoid large inertia forces. This helps maintain a low kinetic-to-internal energy ratio—under 1% is ideal.
When using explicit solvers for inherently slow processes (like punching or forming), time control and mass scaling are essential tools for increasing timestep size and reducing computational time.
Watch for hourglass modes, mesh quality, and energy imbalance, which can distort results.
Damping or soft contact parameters may be useful for stabilizing the simulation if oscillations occur.

## Slide 56: Best Practices for Explicit Analysis in Quasi-Static Problems
  Prescribe motion instead of force or pressure
  Apply velocity instead of displacement (angular velocity instead of angle)
  Ramp up velocity, avoid jumps in velocity
  If contacts close at high velocity, the impact will cause dynamic effects. velocity needs to be reduced if contact is closing too rapidly
  Smooth curves recommended for loading
  Position parts with minimal gaps
  End time for quasi-static problems is dependent upon the corresponding natural frequencies: Loading must be much slower than the period of the smallest natural frequencies
  Run the first analysis with a small end time. Later, end time can be increased for verification

## Slide 57: Quasi-Static Example
Explicit Analysis of a Sooda Can Crushing Under Dynamic Loading

## Slide 58: Problem Description
  A small punch impacts a soda can that is resting on a rigid die. The soda can is modelled as a shell body made of aluminum and the punch and die are considered rigid bodies made of structural steel.
  To explore quasi-static behavior and eligibility, different velocity profiles and simulation times are tested, starting with a very short duration impact at 120 m/s over 0.6 milliseconds which causes about 59 mm of displacement through the width of the can.
  This velocity profile is adjusted to provide the same displacement over 0.06, 0.6, and 3 seconds, to observe the effects of loading duration on the mechanical response of the can.
  Explicit analysis is performed using LS-DYNA in Ansys Workbench with frictional contacts between the punch and can as well as can and the die with a coefficient of friction of 0.3.
Punch
Can
Die
CAD Model and Meshing
Velocity profile used for fast loading (short duration impact)

## Slide 59: Simulation Set-up
Open the supplied archive file “Cancrush.wbpz” and go to LS-DYNA analysis system, and double click to open Model named” “Can Crush – Fast Loading (0.6 ms). You can use this system analysis or alternatively:
  To preserve the analysis settings, duplicate the analysis by clicking on the down arrow and choosing “Duplicate” as shown on the top pictures.
When prompted into the LS-DYNA in Ansys Workbench environment in Ansys Mechanical software, look through the geometry, materials, connections (Body Interaction OR Contacts), boundary conditions, loading (velocity profile) and familiarize yourself with the problem set up in Ansys LS-DYNA. Different setting options are shown on the bottom picture.
Check that under “Solution Information”, Contact Force Tracker as well as “Kinetic Energy” and “Internal Energy” has been chosen to graph them. Make sure you use “Contact” OR “Body Interaction as explained in the last section of this resource. When using one, make sure to “Suppress” the other option to disable it. If using Body Interaction, You need to add “Body Contact Tracker” before solving the problem.
Check geometry parts and assign their materials
Set up Contacts
Mesh the parts
Set simulation time, define initial conditions (velocity, displacement profile)
Boundary conditions
Solution Information: Set Trackers for Internal energy and contact forces
Result contours for different state variables: Stress, Strain, deformation , etc
How to duplicate Analysis System
LS-DYNA in Ansys Workbench Environment and setting options

## Slide 60: Graphing Results
For the fast-loading scenario (t = 0.0006 seconds) which replicates an impact situation, the following velocity profile is used:
Run the simulation and look at the results.
Select both “Contact Force” together under “Solution Information” together to see the force equilibrium. Is Newton’s 3rd Law of Motion, Action and Reaction, satisfied here? Why? Explain your observations
Select both Internal and Kinetic Energy Graphs to compare the Kinetic/Inertial Energy Ratios. Does the Quasi-static assumption hold? Why? Explain your observation.
The Figures show example graphs for force equilibrium (top) and Kinetic/Inertial Energy Ratio for the highspeed impact.
Contact forces comparison (punch – Can contact versus Can-Die contact)
Kinetic and Internal Energy graphs for the can.

## Slide 61: Exercise
Now, think about how you can modify the simulation to make it eligible for quasi-static.
Would using a smoother ramping of velocity help with the quasi-static verification, like the one shown in the figure here? This is for loading time of 0.06 seconds (100X times slower)
Using the sample velocity profile shown here, start slowing the loading. How much should you slow it down? Try increasing the simulation run by two orders of magnitude (end time = 0.06 seconds) and adjust the velocity values accordingly (you can use the velocity profile shown here). Check the Kinetic/Internal energy ratio and look at the force equilibrium and see if that is enough? Share your observations and explain why?
If still not quasi-static, increase the simulation time by another order of magnitude (end time = 0.6 seconds)- Don’t forget to adjust the velocity values in the velocity profile table!
How about going further and make the simulation 5 times slower with the end time = 1.2 seconds? Adjust the velocity values!
Share your observations again for Kinetic/Internal energy ratio and force equilibrium and explain why?
Notes: Students to use the given velocity profile and increasing end time to 0.06 times and then look at kinetic/internal energy.
Then they can start increasing the time to 0.6 s and 3 seconds and adjusting the velocity profile values accordingly.
The velocity profiles and sample force equilibrium and KE/IE graphs are provided in next slides

## Slide 62: Velocity Profiles for Different Scenarios
Slow loading
t = 0.06 seconds
Slower loading
t = 0.6 seconds
Slowest loading
t = 1.2 seconds

## Slide 63: Sample Results - Contact Force Equilibrium & Energy Ratios
Slower loading
t = 0.6 seconds
Slowest loading
t = 1.2 seconds
(A) Contact Force Equilibrium
(B): Kinetic Energy (KE) versus Internal Energy (IE)
(KE/IE) > 2%
(KE/IE) < 2%
(KE/IE) < 2%
Slow loading
t = 0.06 seconds
(C) KE/IE Ratio – Zoomed in and Rescaled
2%
2%
2%
Notes: This graphs show the contact force equilibrium and KE/IE rations for three different durations, t = 0.06 s, t= 0.6 s, and t = 3 s.
We have used a smoother ramping of velocity to avoid sudden jumps and changes in velocity compared to the original profile
As observed, increasing the duration and using a smoother ramping of velocity has helped with force equilibrium and the KE/IE ratio.
This shows how quasi static analysis for such a dynamic loading can be achieved using smoother ramping of velocity and increasing the final velocity
Column A – Force Equilibrium
As we see in the graphs in column A, we look at the force equilibrium between the punch and the can versus can and the ground. As the loading starts to get to be applied slower and have smoother transitions in the loading pattern, the force equilibrium shows more static behavior confirming that quasi static conditions are more dominant.
Column B: Kinetic Energy (KE) Versus Internal energy (IE) results
In this column, we observe the kinetic energy and internal energy graphs for all 3 loading scenarios. We can clearly see that in the first scenario (slow loading) on the top, the kinetic energy shows some significant values at the bottom and hence not meeting the criteria of KE/IE <2%. However, as the loading becomes slower, we observe that the criteria is met.
Column C: KE/IE Ratio – Zoomed in and Rescaled
In this column, we established a graph that shows the RATIO of KE/IE to confirm that it is under 2%. We adjusted the axis values and, in a way, “zoomed in” so this will be more visible.
In the slow loading scenario (t = 0.06 s) , we can see that a significant part of analysis (about 25%) have KE/IE> 2% and hence further slowing down is needed. However, as we make the analysis slower, we can see how we reach KE/IE <2% for most of the analysis.
However, the reason we still needed to do a slowest loading scenario (t = 1.2 s) is that the force equilibrium is not quite matching in the slower loading scenario (t = 0.6 s)

## Slide 64: Sample Results - Stress & Strain Contours
Total Deformation
Equivalent (Von-mises) Stress
Strain

## Slide 65: Quasi Static Analysis Quiz
Question 1:
In a quasi-static analysis, which condition must be satisfied to confirm that dynamic effects are negligible?
Reaction forces must always be zero
Kinetic energy should remain below 2% of internal energy for most of the simulation time
Applied force must increase linearly with time
Deformation should always be elastic
Question 2:
Why is a quasi-static approach often preferred over a fully dynamic simulation for slow processes (e.g., metal forming, structural loading, creep)?
It eliminates the need to consider material properties
It avoids unnecessary oscillations, allows larger time steps, and is more stable
It always gives faster results regardless of the process
It ensures the structure remains purely elastic
Question 3:
Which of the following practices helps minimize dynamic effects when setting up a quasi-static analysis using explicit methods?
Applying step changes in velocity to speed up simulation
Prescribing force instead of motion
Using smooth loading curves and ramping up velocity gradually
Starting with large gaps between parts to avoid contact
Notes: Question 1:
✅ Correct Answer: B Explanation:
Kinetic energy should remain below 2% of internal energy for most of the simulation time.
Question 2:
✅ Correct Answer: B Explanation:
It avoids unnecessary oscillations, allows larger time steps, and is more stable
Question 3:
✅ Correct Answer: C Explanation:
Using smooth loading curves and ramping up velocity gradually

## Slide 66: Ansys Education Resources Feedback Survey
Here at Ansys, we rely on your feedback to ensure the educational content we create is up-to-date and fits your teaching needs.
Please click the link below to fill out a short survey (~7 minutes) to help us continue to support academics around the world utilizing Ansys tools in the classroom.
Feedback Survey Link
Notes: Feedback Survey link for copy-paste method  https://ansys.typeform.com/to/jcattJI5