## Slide 1
Optimization of a Steel Hook using Ansys optiSLang and Ansys Mechanical software
Nicolas Martin
Ansys Academic Development Team

## Slide 2: Learning Objectives
Intended Learning Outcomes | 
Knowledge and Understanding | What is process integration and how Machine learning algorithms can enhance model predictions
Skills and Abilities | How to perform design optimization and result analysis for a simple problem
Further reading/information
  Introduction to Methods for PIDO in Ansys optiSLang
  Parametric Analysis and Optimization using Ansys optiSLang
Ansys software mentioned | Ansys Mechanical™, a structural finite element analysis software. Ansys Workbench™, simulation integration platform Ansys optiSLang®, process integration and design optimization software

## Slide 3: Introduction
In this Lab Tutorial, you will apply basic Process Integration and Design Optimization (PIDO) in Ansys optiSLang tool using a simple structural application example
The 2 main tutorial parts will have you
  Run parametric sensitivity analyses of the system
  Use Machine learning algorithms to optimize design with mass as an objective and Max stress as a limit
The computational time needed to run the sensitivity analyses is expected to be 1-2hours depending on your machine
  Pre-requisites:
  Being able to run a simple structural analysis using Ansys Mechanical module within the Ansys Workbench interface; having basic functional concepts in PIDO with Ansys optiSLang tool (see slide 6)

## Slide 4: Problem Description
The task is to re-design a steel hook such that:
The von-Mises stress under a defined load does not exceed 300 MPa (This would have factor of safety >1.4 which is good general practice)
The mass is as small as possible
Certain geometry parameters are within the predefined bounds.
In this tutorial the following are performed:
Setup of the required solver chain
Sensitivity analysis
Optimization on Metamodel of Optimal Prognosis

## Slide 5: Before You Start
Please use Release 2025 R1 (Service Pack 1) or newer
For background concepts, we recommend the following Ansys Innovation Courses (~60 minutes)
  Introduction to Methods for PIDO in Ansys optiSLang
  Parametric Analysis and Optimization using Ansys optiSLang
Important: do not save the files of this project in a folder with cloud auto-save functionality (like OneDrive) as it will make the solvers fail to run

## Slide 6: Key Best Practice to prepare model(s) for Process Integration
What are parameters and responses of your model?
  Parameters include all geometric feature, physics conditions and design requirement variables which could help to reach performance objectives. Does my parameter range conflict with manufacturing scenario? With the rest of the system if it is a sub-component?
  Responses are model outputs which should be optimized (objectives) or monitored (constraints)
Is it a mature simulation model that runs well with varying parameters?
  Test a few cases to ensure that you obtain a converged solution (meaning that the underlying partial differential equations are solved) in different parts of the design space
What is the computational cost of running a design point?
  Process integration and later optimization can require a significant number of design points to be calculated. Can you cover this cost or adapt the model to reduce it?
1.

## Slide 7: Solver: Ansys Mechanical Software
In Ansys workbench, open the hook_structural_analysis.wbpj file provided with this tutorial (make sure it is located in the same folder as the hook_structural_analysis_files folder)
In Ansys Workbench interface, we use Ansys Mechanical software as a solver.
2.
1.

## Slide 8: Input Parameters: Geometry
Connection_Angle (120-150°)
Thickness (15-25 mm)
Depth (15-25 mm)
Lower_Radius (45-55 mm)
Right-click on the Geometry cell and open Discovery to review the Design parameters.
History tracking records your changes in block of script – you can play back the operations and makes changes to settings and parameters.
In history tracking, expand the sketch section to visualize steps that have been defined as parameters

## Slide 9: Note on Named Selections in the Ansys Discovery tool
To maintain geometric association of the loads, boundary conditions, and mesh settings in the Ansys Mechanical software, Named Selections are created in the Ansys Discovery tool as part of the History Tracking
Close the Ansys Discovery software

## Slide 10: Boundary Conditions
Review the solution setup in Ansys Mechanical software (double-click on the Model cell A4, then click on ‘Static Structural’ in the left-hand tree menu to review the solution setup)
Loading force F = 6000 N applied to hook’s end
Cylindrical support applied, where tangential direction is free.

## Slide 11: Meshing set up
element size = 3mm
Initial mesh performance analysis has identified the need for a local meshing
Overall mesh is set to element size of 50 mm while a localize mesh has been created on the inner surface of the hook with element size of 3 mm

## Slide 12: Output Parameters
Responses in Ansys Mechanical software:
For the objective function and constraint condition, the following are parameterized:
the Maximum stress and
the Mass
Close Ansys Mechanical software window (not shown)
2.
1.

## Slide 13: Update and Go to Ansys optiSLang tool
Click Update Project to ensure it runs without issue
Right-click on the Static Structural System and issue the Clear Generated Data command in order to reset the output variables and remove the outdated files Deleting the generated data helps reduce the amount of data that must be copied. This will facilitate the rest of the workflow
Press the Go to optiSLang button
Save the project when prompted
A .opf file will be created in the same folder as where the workbench project is being stored
3.
1.
2.

## Slide 14: Process Integration in Ansys optiSLang tool

## Slide 15: Project Status
You should have an Ansys optiSLang software project as shown to the right – you might need to actively open it from the working folder
There will be one Parametric System, with an Ansys Workbench tool IntegrationPlugin solver node
The project name defaults to the Ansys Workbench tool project’s name.

## Slide 16: Process Integration
Double click on the IntegrationPlugin node to open the interface.
The input and output variables are automatically identified and turned into Parameters and Responses
The input parameters from Discovery History Tracking are named with “__[Blockname]_[DiscoveryParameterID]__[Parameter Name]_[WBParameterID]” – for example __B1_D5_Thickness_P41
Click OK to close this interface

## Slide 17: Definition of Input Parameters
Double click on the Parametric System to open the interface
Do a right mouse click on the Name and select Resize to contents to better view the Parameter names
Specify the following ranges of the geometry parameters
Press OK
1.
2.
3.

## Slide 18: Rename System
Right click on the System and rename it to Hook_optimization
Right click on the Node and rename it to Hook_optimization

## Slide 19: The Solver Chain
Save the project and perform a test run of the solver chain. The system turns green when it’s finished.
Check the response values:
Double Click on the system Hook_optimization
Go to the Result designs tab and review the results – the results values of stress and mass should be real and non zero.
1.
2.
3.
1.
2.
Note on Computational cost: the test run will give you an indication of the time needed later on to run the sensitivity analysis, where at least 54 design points will be simulated. If run time of one design point is too long, consider increasing the size of the mesh shell either locally or globally

## Slide 20: Sensitivity Analysis using the Adaptive MOP (Metamodel of Optimal Prognosis)

## Slide 21: Sensitivity Analysis
Drag the Sensitivity wizard onto the head of the solver chain and let it drop

## Slide 22: Parameterize Inputs
Because we already set the parameter ranges for the single solve with the Parametric System, no additional changes are required on this screen of the Sensitivity Wizard.
Click Next >

## Slide 23: Definition of Objectives and Constraints
Drag the Geometry_Mass_P35 response and hover it over the Objective icon; it gets split into two segments,
Drop the response on Minimize
A new objective is created
1.
2.

## Slide 24: Definition of Objectives and Constraints
Drag the stress response over the Constraint and drop it on Less.
Input the limit value 300 in the Limit field.
  Mind the right units and scale objective and constraint to the same order of magnitude.
  In the image to the right, the stress value of 1.75618e+08 hints that the Mechanical unit system was set to Pa instead of MPa. The Unit system can be changed by opening the solver node and editing the WB file, or the Response in Ansys optiSLang tool can be scaled into the same units as in the Ansys Mechanical software
  See next slide for scaling
1.
2.

## Slide 25: Scaling of Objectives and Constraints
While not necessary, it is best practice for all objectives and constraints to be of similar scale : sensitivity analysis and optimization in Ansys optiSLang tool uses Machine Learning algorithms in the back end. High values attract the algorithm, which may make the procedure less efficient, so rescaling will overcome this limit.
Modify the Expression and Limit for the Stress so that both fall in the 0.1-10 range.
  Expression needs to be divided by 1e6 to convert from Pa to MPa, and then by another 1e2 to scale into the target range.
  The Limit needs to be divided by 1e2 to bring the 300 Limit into the target range.
1.

## Slide 26: Definition of Design of Experiments Scheme
Press Next to advance to the Sampling Method screen.
Keep the default Adaptive Metamodel of Optimal Prognosis (AMOP) – see next slide for background on AMOP
Press Next
1.
2.

## Slide 27: Adaptative Metamodel of Optimal Prognosis for Sensitivity analysis and Optimization
To run the sensitivity analysis, Ansys optiSLang tool :
(1) Does Design of experiment sampling and investigates each response using the solver(s)
Uses Regression methods to approximate different response surfaces on all calculated design points.
(2) Provides a Metamodel of Optimal Prognosis (MOP) which is the best fitting response surface. Its forecast quality is Evaluated with a Coefficient of Prognosis (COP)
(3) If COP threshold is not met, an additional set of design points are solved to improve response surface models

## Slide 28: Definition of Design of Experiments Scheme
Activate Show postprocessing during algorithm run (min. 4)
Finish the sensitivity settings by pressing Finish
1.
2.

## Slide 29: The Sensitivity Flow
The old system, which was used as a solver chain template for setting up the sensitivity, is inactive (dark grey)
The Sensitivity flow is shown in the layout
2.
1.

## Slide 30: Tips for Sensitivity analysis
Adjust the number of samples according to your solver run time and the number of parameters you have, keeping in mind:
  Use 2 times more samples than input variables (if possible) to reduce input correlation errors
  Use at least 50 to 100 samples in order to get suitable estimates of variance-based input variable importance
After the analysis, in the MOP postprocessing check that:
  the number of failed designs should not exceed 20-30%
  global Coefficient of Prognosis should be >80%

## Slide 31: MOP Settings
Double Click on the AMOP System (not shown)
Go to the Adaption tab
Checkmark Show advanced settings
Change Start iteration number of samples to 54*
Change number of Maximum Iterations to 4
Change the Refinement to 16
Press OK
* Number should be > 50 design for good single CoP .
2.
3.
5.
6.
7.
4.

## Slide 32: Configuring parallel computing and license usage
By default Ansys optiSLang tool will run parallel computation if your machines allow. This will consume multiple licenses at the same time, which may lead to errors if you do not have multiple licenses available (or are using Ansys Student which does not allow this)
To avoid troubleshooting go to the project menu>project settings, and change the maximum number of threads to 1 as shown
This will result in the AMOP solving more slowly, as it can only run one solution at a time

## Slide 33: Running the Sensitivity Analysis
Start the sensitivity analysis using the Run button
Now, the system in running, the DOE is created in the background, all designs are calculated, and finally the MOP is generated
  Approximate runtime with 1 parallel computation: 1-2hours depending on the machine hardware
1.
2.

## Slide 34: Results of the Sensitivity Analysis
After the first iteration the Target CoP is achieved
The approximation quality is excellent for both output variables (CoP > 99%)
The influence of the angle and the lower radius is relatively small

## Slide 35: Optimization with One-Click-Optimization (OCO) on Metamodel of Optimal Prognosis (MOP)

## Slide 36: Ansys optiSLang tool Optimization Algorithms: Concepts
3 families of optimization algorithms are used:
  Gradient-Based Methods
  Nature-Inspired Optimization
  Surrogate-based Optimization
The choice of the proper algorithm is assisted by the Optimization wizard in the software and based on insights gained by sensitivity analysis.

## Slide 37: Optimization using MOP
Drag the Optimization wizard onto the AMOP System and let it drop

## Slide 38: Optimization using MOP
Parameters are linked automatically to the sensitivity system
All parameters are automatically considered as non constant
Press Next >

## Slide 39: Checking of Objectives and Constraints
Check the objective and constraints
Press Next >
1.

## Slide 40: Optimization using MOP
We can keep the optimization on the MOP as the CoP is >90%
Suggested algorithm is OCO
Start point (Best Design from AMOP System) is automatically selected
Press Next >
Note: a Coefficient of Prognosis of 0.9 is satisfactory. When that is not the case, one needs to calculate additional design points which will update the MOP and CoP, or to do an optimization on real run which will have much higher computational cost.
1.
2.
3.
4.

## Slide 41: Optimization using MOP
Validation of the best design is automatically set and the solver chain from the AMOP System is used
Press Finish
1.
2.

## Slide 42: Optimization using MOP
The Optimization workflow is shown in the scenery (you can click on the Layout optimal button of the tool bar to rearrange the layout
Start the optimizer by using RUN-Button
Optimization on MOP
Validating Best Design Chain with real simulation run

## Slide 43: Optimization using MOP
The optimizer converges and performs the validation in about two minutes
The optimization has stopped after a defined number of design estimation using MOP, with constraints fulfilled, has been reached (in our case 400)
The responses and objective/constraints of the best design are verified: if constraints are violated, the next best design is verified
Validating best design is very important for the optimization on the MOP

## Slide 44: Optimization using MOP
Ansys optiSLang tool should have automatically opened the post-processing, otherwise you can double click on « Validator post-processing ». You should access this view:
History graph displays progress towards design objective at each iteration of AMOP optimization. Best calculated design is also visible
Design parameter of selected design is visible here
Response data of MOP vs calculated for the selected design is given here
Criteria data of MOP vs calculated for the selected design are given here
3.
1.
2.
4.

## Slide 45: Optimization using MOP
Parameter Values for Best Design
Relative Size to Criteria range based on full data set
Responses of Best Design
Validation shows that the mass of the simulation of the best design is higher than the one predicted by the metamodel
The reason is that the parameters reach their boundaries (end of parameter space and metamodel), in this areas the prediction quality reduced
Increasing the parameter space when generating the metamodel of Optimal Prognosis helps, default parameter bounds can then be applied to the optimization.

## Slide 46: Initial vs. Optimal Design
Initial Design Optimal Design: Geometry Optimal Design: Eqv. Stress
Mass = 1.268kg Mass = 0.711kg (-44%) Equivalent Stress = 176MPa Equivalent Stress = 299MPa
Factor of safety=2.4 Factor of Safety=1.4
By considering hundreds of possible alternative designs, and optimizing to find the best, Ansys optiSLang tool has exploited the maximum equivalent stress of 300MPa which we allowed and gives a solution within permitted constraints which achieves a 44% mass reduction.

## Slide 47: Summary of Tutorial and extension
Summary:
  The solver chain was configured to perform further analysis
  The sensitivity analysis was performed to generate a MOP
  The optimization was conducted using OCO on the MOP with a validation analysis
Alternative scenario to extend the case study:
  Add max displacement as a parameter in the Ansys Mechanical software, and use it as a second objective/constraint in the Ansys optiSLang tool process
  Include the material as a discrete parameter of the system and rerun the Ansys optiSLang tool process – be careful about the max stress constraint definition! To chose the grade You can either perform Materials selection in the Ansys Granta EduPack software, or use the Al6061 and Ti6Al4V grades available in the Ansys Granta Materials for Simulation sample library of Ansys Mechanical software

## Slide 48: Ansys Education Resources Feedback Survey
Here at Ansys, we rely on your feedback to ensure the educational content we create is up-to-date and fits your teaching needs.
Please click the link below to fill out a short survey (~7 minutes) to help us continue to support academics around the world utilizing Ansys tools in the classroom.
Feedback Survey Link
Notes: Feedback Survey link for copy-paste method  https://ansys.typeform.com/to/jcattJI5