## Slide 1
Lab Tutorial on Communication example using Ansys HFSS™ SBR+ Simulation
Dimitris Tzagkas Celia Gomez Molina
education@ansys.com

## Slide 2: Received Power for Comms scenario
Receiver Antenna
Transmitter system
Receiver system
Transmitter Antenna
Propagation path
Assumptions:
Tx and Rx Antennas are impedance-matched
Tx and Rx Antennas are polarization-matched
Tx and Rx Antenna radiation efficiency is 1
where
Friis Transmission Equation
Notes: In this slide you can see the equations used to reach the Friis equation. The equations use the transmit power, the power density and the antenna parameters such as the gain (G) and the directivity (D).

## Slide 3: How to simulate the setup with Ansys HFSS SBR+
Parameters used:
Antenna model(s) in HFSS
  Identical Horn Antenna at ,
  with efficiency ,
  with maximum gain at boresight of 20.92 (13.2 dB),
  excitation power
Link and Setup configuration
  Identical horn antennas for transmitter and receiver,
  Antennas are aligned facing each other at maximum gain angle (boresight),
  Variable distance between them R ,
Tx
Rx
R
This tutorial uses Ansys HFSS™, the high-frequency electromagnetic simulation software

## Slide 4: Friis equation scenario implemented in Ansys HFSS software
Example visualization
Antenna Coupling depending on the distance between the Tx and Rx antennas

## Slide 5
How to create a communication scenario in Ansys HFSS Software

## Slide 6: Antenna Design
Use an existing antenna OR generate using the ACT Antenna Toolkit in Ansys HFSS View ACT Extensions  Launch Wizards HFSS Antenna Toolkit  Any Antenna needed  Set parameters Synthesis  Finish The example next uses a pyramidal Horn Antenna at 2.4 GHz center frequency.
Excitations (right click)  Set Far-Field Phase Reference..
And then set a Far-Field Phase Reference point for the antenna.

## Slide 7: Analyze Antenna
Make sure Save Fields is checked…… Setup Freq Sweep ... and… Analyze
Step A
Step B
Step C
You can set sweep to specific frequencies OR even a single specific frequency

## Slide 8: Antenna Parameters extraction
From Excitations we can set the input power [1 W in this case]
From Results we can get the Total Gain [20.9 or 13.2 dB]

## Slide 9: Setting Up the System Setup
Create New HFSS Design
Change Solution Type to SBR+
Create Antenna Component via Link to Source Design..
Name Appropriately the Antenna

## Slide 10: Setup Link – Working in the SBR+ design now
General Tab
Model Visualization Tab
Make sure you choose the correct Sweep
OK, Next and Finish

## Slide 11: Before Linking Receiver Antenna …
Change Units to appropriate scale..
Add parametric Relative Coordinate System ..
* R1 = 10 meter
You can add the Relative CS anywhere and then modify the attributes as shown below

## Slide 12: Adding the Receiver Antenna Instance
Select the RelativeCS1 and then add the receiver antenna (Rx) as a Link to Source Design shown previously When done  you will get the below setup
Make sure the antennas are facing each other..
Rotate antenna by 180 deg
Select the Rx antenna and then rotate

## Slide 13: Assign Tx and Rx behaviors
Assign port and behavior type as shown below

## Slide 14: Setup Analysis and Run Analysis
Error?? Check next slide

## Slide 15: Important note!
A model/component should exist in SBR+ design… So for an antenna coupling example, a simple model is required.. Thus, we add a very small sized sphere very far away from the setup..
e.g.
Try to Analyze again now!

## Slide 16: Analyze for different distance R1
Add Parametric setup for R1
You can define the start/stop/step accordingly. More steps mean more simulation time

## Slide 17: Plotting results

## Slide 18: Results – Compared to calculated Friis equation (imported)
Example visualization
Antenna Coupling depending on the distance between the Tx and Rx antennas
Notes: For a side by side comparison you can export the simulation data OR import the calculated theoretical data in order to compare the simulated and calculated data in a single graph. In this example the calculated data are imported in HFSS

## Slide 19: Creating animated picture
OR
THEN

## Slide 20: Creating animated picture
Setup animation and steps
Animate
Export (*.avi OR *.gif file)

## Slide 21: Ansys Education Resources Feedback Survey
Here at Ansys, we rely on your feedback to ensure the educational content we create is up-to-date and fits your teaching needs.
Please click the link below to fill out a short survey (~7 minutes) to help us continue to support academics around the world utilizing Ansys tools in the classroom.
Feedback Survey Link
Notes: Feedback Survey link for copy-paste method  https://ansys.typeform.com/to/jcattJI5